## Slide 1
Notes: Figure 1.1: Blackbody radiation curves for a temperature of 5800 K corresponding to the Sun and 290 K roughly corresponding to the Earth. The peak in the solar radiation (scaled by 10−6 ) is centered on the visible part of the spectrum between 400 and 800 nanometers. The peak in the Earth’s thermal radiation occurs in the thermal infrared (TIR) between 3 and 15 micrometers.

## Slide 2
Notes: Figure 1.2: Percent transmission of EM waves through the Earth’s atmosphere as a function of wavelength. There are three main windows where the atmosphere is mostly transparent. They are the visible (shaded red) centered at 0.5 micrometer, the thermal infrared (shaded blue) centered at 8 micrometers with prominent windows at 3.5 and 10 micrometers, and the microwave (shaded green) at wavelengths between 0.6 cm an 30 cm. Note that EM waves at wavelengths greater than about 30 cm are strongly distorted and reflected by the ionosphere. The microwave region has bands noted by letters. The most common bands for radar interferometry are X, C, S, and L. The K-band is mainly used for radar altimetry and microwave radiometry.

## Slide 3
Notes: Figure 1.3: Schematic diagram of a SAR satellite in orbit. The SAR antenna has its long axis in the flight direction (also called the azimuth direction) and the short axis in the range direction. The radar sends pulses to one side of the ground track that illuminate the Earth over a large elliptical footprint. The reflected energy returns to the radar where it is recorded as a function of fast time in the range direction and slow time in the azimuth direction.