## Slide 1: Digital Design: A Systems Approach Lecture 2: Combinational Logic Design

## Slide 2: Readings
L2: Chapters 6 & 7
L3: Chapters 8 & 9

## Slide 3: Review
Lecture 1
  The world is digital
    Analog at the edges, hardware for demanding problems, 100x per decade
  Digital signals
    Encode discrete states in a continuous signal
    Reject noise
  Representations
    Binary, set, continuous, compound
  Boolean Algebra (0,1,,)
    Axioms, properties, duality
    Logic equations express binary functions
  Combinational logic
    Output is a function only of current input
  Verilog
    Defines hardware modules, assign, case

## Slide 4: Today
How to implement combinational logic by hand
  Given a description of a logic function
  Generate a gate-level circuit that realizes that function
Everyone needs to do this once
  To understand how its done
  Demystifies what the synthesis tools do
  Better understanding of what synthesis tools can and can’t do
In practice you will rarely have to do this by hand
General practice is:
  Design using Verilog
  Simulate with test cases
  Generate gates with synthesis program

## Slide 5: English language description of a combinational logic function
F(d,c,b,a) is true if input d,c,b,a is prime

## Slide 6: Truth Table
F(d,c,b,a) is true if input d,c,b,a is prime

## Slide 7: Equation
F(d,c,b,a) is true if input d,c,b,a is prime

## Slide 8: Schematic Logic Diagram
Equation:
Schematic Logic Diagram:

## Slide 9: Cube representation (3-bit prime)
å
=
cba
m
f
)
7
,
5
,
3
,
2
,
1
(

## Slide 10: 4-D Hypercube (4-bit prime)

## Slide 11: 4-bit Prime Number Function (cont)
f = (a d) V (b c d) V (a b c) V (a b c)
V
V
V
V
V
V
V
¯
¯
¯
¯
¯

## Slide 12: Karnaugh Map of 4-bit Prime
0
1
1
1
0
1
1
0
0
1
3
2
4
5
7
6
8
9
1
1
1
0
1
2
1
3
1
5
1
4
0
0
0
1
1
1
1
0
a
b
c
d
0
1
0
0
0
0
1
0
00
01
11
10
dc
ba
a
b
c
d

## Slide 13
Position of minterms on a 4-bit Karnaugh map
0
1
3
2
4
5
7
6
ba
a
12
13
15
14
8
9
11
10
00
01
11
10
00
01
11
10
d
b
c
dc
Karnaugh Map of 4-bit Prime: Minterms

## Slide 14
0000
00
01
11
10
0001
0011
0010
0100
0101
0111
0110
1100
1101
1111
1110
1000
1001
1011
1010
Adjacent minterms differ in exactly one bit
Every positive minterm is an implicant
ba
a
00
01
11
10
d
b
c
dc
Karnaugh Map of 4-bit Prime: Implicants

## Slide 15
0000
00
01
11
10
0001
001X
0100
X101
0111
0110
1100
1111
1110
1000
1001
1011
1010
Can combine adjacent minterms into implicants
ba
a
00
01
11
10
d
b
c
dc
Karnaugh Map of 4-bit Prime: Larger Implicants

## Slide 16
0000
00
01
11
10
0001
0010
0100
X101
0111
0110
1100
1111
1110
1000
1001
X011
1010
X011
Can combine adjacent minterms into implicants
Note edges wrap around
ba
a
00
01
11
10
d
b
c
dc
Karnaugh Map of 4-bit Prime: Adjacency

## Slide 17
0000
00
01
11
10
0XX1
0010
0100
0110
1100
1101
1111
1110
1000
1001
1011
1010
A larger implicant
ba
a
00
01
11
10
d
b
c
dc
Karnaugh Map of 4-bit Prime: 0XX1

## Slide 18
00
01
11
10
a
b
c
d
0
0
0
0
0
0
1
1
1
1
1
1
0
0
1
0
ba
dc
00
01
11
10
00
01
11
10
a
b
c
d
0
4
12
6
8
9
1
5
7
3
2
13
15
14
11
10
ba
dc
001X
X101
0XX1
00
01
11
10
X011
Why make implicants overlap?
Two reasons:
  Larger implicants have fewer gates, or gates with fewer inputs.
  2. Hazards. More on them later.

## Slide 19
00
01
11
10
a
b
d
0
0
0
0
0
0
1
1
1
1
1
1
0
0
1
0
ba
dc
001X
X101
0XX1
00
01
11
10
X011
In practice, CMOS gates are always
inverting, so the real circuit might look
like this

## Slide 20: Decimal prime number function – includes don’t cares
00
01
11
10
00
01
11
10
a
b
c
d
0
0
x
0
0
0
1
1
1
1
1
x
x
x
x
x
ba
dc

## Slide 21
Decimal prime number function K-Map
11
10
01
11
a
b
d
0
0
x
0
0
0
1
1
1
1
1
x
x
x
x
x
ba
dc
X1X1
00
01
11
10
X01X
0XX1
XX11
c

## Slide 22
Cover:
0XX1
X01X
f = (a d) V (b c)
V
V
¯
¯
Decimal prime number function – circuit
00
01
11
10
a
b
d
0
0
x
0
0
0
1
1
1
1
1
x
x
x
x
x
ba
dc
00
01
11
10
X01X
0XX1
c

## Slide 23: Revisiting some definitions (and some new ones)
Minterm: a product term that includes each input of a circuit or its complement.
Implicant: a product term that if true implies the function is true.
Prime Implicant: is an implicant that cannot be made any larger and still be an implicant.
Essential Prime Implicant: the only prime implicant that contains a particular minterm of the function.
Distinguished One: is a minterm that is contained in only one implicant.
00
01
11
10
a
b
d
0
0
0
0
0
0
1
1
1
1
1
1
0
0
1
0
ba
dc
00
01
11
10

## Slide 24: Product-of-Sums Implementation
Sum-of-Products circuit: focus on inputs states where truth table is a 1.
Product-of-Sums: focus on input states where truth table is a 0.
1
1
1
1
1
1
1
1
0
1
3
2
4
5
7
6
8
9
11
10
12
13
15
14
00
01
11
10
ba
dc
1
0
1
1
0
1
0
0
a
b
c
d
1
0
0
1
1
1
1
1
d
c
a
Ú
Ú

## Slide 25: Product-of-Sums Example: Decimal Prime
0
1
1
1
0
1
1
0
0
1
3
2
4
5
7
6
8
9
11
10
12
13
15
14
00
01
11
10
ba
dc
1
0
1
1
0
1
0
0
a
b
c
d
x
x
x
x
0
0
x
x
d
c
a
Ú
b
a
Ú
Fix this equation – 11 and 15 in both

## Slide 26: Hazards
0
0
1
1
0
1
1
0
0
1
3
2
4
5
7
6
0
0
0
1
1
1
1
0
b
a
c
1
0
a
b
c
Static-1 hazard
c
b
c
a
v
v

## Slide 27: Cover transitions to eliminate hazards
0
0
1
1
0
1
1
0
0
1
3
2
4
5
7
6
0
0
0
1
1
1
1
0
b
a
c
1
0
a
b
c
c
b
c
a
b
a
v
v
v

## Slide 28: Reminder: 4-bit Prime Number Function
00
01
11
10
a
b
d
0
0
0
0
0
0
1
1
1
1
1
1
0
0
1
0
ba
dc
001X
X101
0XX1
00
01
11
10
X011
c

## Slide 29: 4-bit Prime Number Function in Verilog Code – Using case
module prime(in, isprime) ;
input [3:0] in ; // 4-bit input
output isprime ; // true if input is prime
reg isprime ;
always @(in) begin
case(in)
1,2,3,5,7,11,13: isprime = 1'b1 ;
default: isprime = 1'b0 ;
endcase
end
endmodule

## Slide 30: 4-bit Prime Number Function in Verilog Code – Using casex
module prime1(in, isprime) ;
input [3:0] in ; // 4-bit input
output isprime ; // true if input is prime
reg isprime ;
always @(in) begin
casex(in)
4'b0xx1: isprime = 1 ;
4'b001x: isprime = 1 ;
4'bx011: isprime = 1 ;
4'bx101: isprime = 1 ;
default: isprime = 0 ;
endcase
end
endmodule

## Slide 31: 4-bit Prime Number Function in Verilog Code – Using assign
module prime(in, isprime) ;
input [3:0] in ; // 4-bit input
output isprime ; // true if input is prime
wire isprime = (in[0] & ~in[3]) |
(in[1] & ~in[2] & ~in[3]) |
(in[0] & ~in[1] & in[2]) |
(in[0] & in[1] & ~in[2]) ;
endmodule

## Slide 32: Which is a better description?
Using case
Using casex
Using assign

## Slide 33: 4-bit Prime Number Function in Verilog Code – Result of synthesizing description using case
module prime ( in, isprime );
input [3:0] in;
output isprime;
wire n1, n2, n3, n4;
OAI13 U1 ( .A1(n2), .B1(n1), .B2(in[2]), .B3(in[3]), .Y(isprime) );
INV U2 ( .A(in[1]), .Y(n1) );
INV U3 ( .A(in[3]), .Y(n3) );
XOR2 U4 ( .A(in[2]), .B(in[1]), .Y(n4) );
OAI12 U5 ( .A1(in[0]), .B1(n3), .B2(n4), .Y(n2) );
endmodule

## Slide 34: Synthesis Reports
****************************************
Report : area
Design : prime
Version: 2003.06
Date : Sat Oct 4 11:38:08 2003
****************************************
Library(s) Used:
XXXXX
Number of ports: 5
Number of nets: 9
Number of cells: 5
Number of references: 4
Combinational area: 7.000000
Noncombinational area: 0.000000
Net Interconnect area: undefined (Wire load has zero net area)
Total cell area: 7.000000
Total area: undefined
****************************************
Report : timing
-path full
-delay max
-max_paths 1
Design : prime
Version: 2003.06
Date : Sat Oct 4 11:38:08 2003
****************************************
Operating Conditions:
Wire Load Model Mode: enclosed
Startpoint: in[2] (input port)
Endpoint: isprime (output port)
Path Group: (none)
Path Type: max
Des/Clust/Port Wire Load Model Library
------------------------------------------------
prime 2K_5LM XXXXX
Point Incr Path
-----------------------------------------------------------
input external delay 0.000 0.000 r
in[2] (in) 0.000 0.000 r
U4/Y (EX210) 0.191 0.191 f
U5/Y (BF051) 0.116 0.307 r
U1/Y (BF052) 0.168 0.475 f
isprime (out) 0.000 0.475 f
data arrival time 0.475
-----------------------------------------------------------
(Path is unconstrained)

## Slide 35: Constraint File
create_clock "clk" -name clk -period 2 -waveform {0 1.7}
set_clock_uncertainty 0.2 clk
set_fix_hold all_clocks()
set_load -pin_load 5 {isprime}
set_input_delay 0.5 -clock clk {in}
set_output_delay -max 0.8 -clock clk {isprime}

## Slide 36: Test bench
module test_prime ;
reg [3:0] in ;
wire isprime ;
// instantiate module to test
prime p0(in, isprime) ;
initial begin
in = 0 ;
repeat (16) begin
#100
$display("in = %2d isprime = %1b",in,isprime) ;
in = in+1 ;
end
end
endmodule

## Slide 37: Test benches use a very different style of verilog
Initial statements
$display
Repeat and other looping constructs
#delay
Don’t use these constructs in synthesizable modules

## Slide 38: Testing Result
# in = 0 isprime = 0
# in = 1 isprime = 1
# in = 2 isprime = 1
# in = 3 isprime = 1
# in = 4 isprime = 0
# in = 5 isprime = 1
# in = 6 isprime = 0
# in = 7 isprime = 1
# in = 8 isprime = 0
# in = 9 isprime = 0
# in = 10 isprime = 0
# in = 11 isprime = 1
# in = 12 isprime = 0
# in = 13 isprime = 1
# in = 14 isprime = 0
# in = 15 isprime = 0

## Slide 39
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Wave output

## Slide 40
module prime_dec(in, isprime) ;
input [3:0] in ; // 4-bit input
output isprime ; // true if input is prime
reg isprime ;
always @(in) begin
casex(in)
0,4,6,8,9: isprime = 1’b0 ;
1,2,3,5,7: isprime = 1’b1 ;
default: isprime = 1’bx ;
endcase
end
endmodule

## Slide 41: Summary
To minimize logic
  Write K-map
  Find all prime implicants
  Pick a minimal set of prime implicants that covers the function
Hazards (output glitches) can be eliminated by covering transitions
Verilog
  Can represent with case, casex, assign, or structurally
  Use representation that is readable and maintainable
    case for truth tables
    assign for equations
    Don’t try to do the logic design yourself
  Synthesis tool will do the optimization
  Test benches check that implementation meets its specification
    Test benches use a different style of Verilog

## Slide 42: Next Time
Combinational building blocks