## Slide 1: Chapter 3 Medium Access Control
Email list: https://groups.google.com/forum/#!forum/mobile-miao

## Slide 2: Overview
Multiple terminals need to communicate at the same time
MAC protocols
  Share channel
  Multiplex several data streams of different terminals
MAC design
  Initially for wired communications (copper fiber optics)
    Reliable channel with abundant bandwidth
      BER<10e-6
    Packet loss in wired networks is mainly due to collisions and the MAC designs are relatively simple.

## Slide 3: Challenges for Wireless Networks
A radio signal may experience reflection, diffraction, or scattering before reaching its receiver.
  Fading deteriorates the signal and incur the variation of signal quality in time, frequency, and space.
  BER>10e-3
Broadcast nature of wireless channels.
  The stronger the transmission power or the closer the neighbor terminals, the stronger the interference will be.
Half-duplex

## Slide 4: MAC Types
Contention free
  Efficient in QoS guarantee
  Improve network throughput and reduce network response for heavily loaded networks
  Dynamic schemes have high complexity
Contention based
  Inevitable packet collisions
  Good performance in low-traffic networks
  Low complexity

## Slide 5: MAC Types

## Slide 6: Communications Model
Bursty data traffic, depending on traffic types
Message model: deterministic arrival, random Poisson arrival.

## Slide 7: Performance Measures
Delay
  Delay between arrival time and time the message sent to receiver.
  Di=bi-ai.
Quality of data received:
  BER
    Send msg: 1 1 0 0 1 0 0 1
    Receive msg: 0 1 0 1 1 0 1 1
    Number of bit errors: 3.
    BER: 3/8=37.5%
    In practice, bit error probability, pBER.
    Factors: noise, interference, synchronization problems, fading, and so forth.
    Improvement: higher power, lower modulation order, more robust channel coding

## Slide 8: Performance Measures
Quality of data received:
  PER
  Packet dropping
Notes: all packets consist of the same number of bits and in each packet, bit errors are independently and identically distributed

## Slide 9: Performance Measures
Throughput: expected number of messages delivered to the receiver per unit time
Individual:
System throughput:

## Slide 10: Performance Measures
Throughput:
  An alternative definition
  Normalized link delay
File size
Time to send all bits
Notes: Capital Lambda

## Slide 11: Contention-Free Access Protocols

## Slide 12: Contention-Free Access Protocols
Contention-free access protocols
  Each terminal sends packets using predetermined time slots, frequency bands, or codes.
  A central scheduler coordinates the transmissions of different terminals, and there will be no collisions in the network.
Types:
  Static access protocols
  Dynamic access protocols

## Slide 13: Resource Assignment Techniques
Wireless resources can be divided into orthogonal partitions called channels and these channels can be assigned to different terminals.
Fundamental resource partitioning techniques
  TDMA
  FDMA
  OFDMA
  CDMA
  SDMA
Illustration assuming static resource allocation:
  Each link is assigned some fixed channels throughout its communication session.

## Slide 14: FDMA
Oldest way of static resource allocation
Not efficient for traffic with different rate requirements

## Slide 15: TDMA
All terminals are synchronized
More flexible in handling different rate requirements

## Slide 16: OFDMA
Based on orthogonal frequency division multiplexing (OFDM).

## Slide 17: OFDM Spectrum
  Orthogonal subcarriers to send multiple data symbols in parallel and achieves high spectral efficiency.

## Slide 18: OFDM Properties
Pros
Easy implementation
Robust against multi-path fading and inter-symbol interference.
Low sensitivity to time synchronization errors.
Cons
Very sensitive to frequency-domain errors like Doppler shift and frequency synchronization problems.
High PAPR

## Slide 19: OFDMA
Multiple access is achieved in OFDMA
  Assign subsets of subcarriers to individual users.
  For example a subcarrier can be allocated to the user with relatively the best channel condition.
Scheduling flexibility in another dimension, the frequency domain.
  By assigning different numbers of subcarriers to different users, differentiated qualify of service can be easily supported.
A kind of FDMA in a wide sense.
  OFDMA incorporates the orthogonality without guard bands, allows overlapping adjacent spectrum bands and therefore is much more spectrum efficient.

## Slide 20: SDMA
Mobile users are located far away.
Uses the spatial separation to reuse the frequency spectrum for higher network capacity.
The simplest form of SDMA
  Reusing the same frequency in different cells
  Cells with the same frequency should be sufficiently separated in space.
  Limit how many cells a region may be divided into and network reuse factor

## Slide 21: SDMA
More advanced SDMA:
  Frequency reuse within each cell
Use smart antenna arrays and intelligent signal processing techniques to steer the antenna beam to the desired users and places nulls in the direction of other users.
Notes: User 1 is located at a null or minimum gain point of the beam pattern of user 2 and vice versa

## Slide 22: SDMA
SDMA differs from FDMA, TDMA, and OFDMA in that a perfect spatial separation of users can not be guaranteed in general.
The orthogonality of different users depends on the spatial correlation among the channels of the users.
  When spatial sub-channels are not close to orthogonal, it may result in excessive co-channel interference and degraded performance.
SDMA algorithms
  cope with correlated subchannels and multiplex data streams of different users only when their channels are sufficiently uncorrelated.
The number of available spatial channels
  depend on the environment and the number of transmit and receive antennas.

## Slide 23: Hybrid Access

## Slide 24: Resource-Sharing Conflicts (1)
Use FDMA
Symbols are transmitted at a rate

## Slide 25: Resource-Sharing Conflicts (2)
Only one user
  Each message has Nm symbols and the message duration is
  System throughput: # of messages per unit time
Mo users
  Split the bandwidth into Mo identical channels
    Symbol duration of each channel: MoTb
  Message duration:
  Throughput of a user:

## Slide 26: Dynamic Access Protocols
Network resources can be dynamically allocated using a central scheduler to achieve better network performance.
Good performance in heavy traffic
QoS guarantee
Higher complexity and cost
Not scalable.
Examples:
  Poll-based access protocols
  Token-based access protocols

## Slide 27: Poll-based Access Protocols
Designate device as a channel access administrator, i.e. the central controller
  Example: base station in cellular networks, access point in WLAN.
To get data from a terminal
  The controller sends a request for data to the terminal and then receives the data from what the terminal sends, if any.
  The controller then polls another terminal and receives the data from that one, and so forth.

## Slide 28: Poll-based Access Protocols
Terminals linked to the controller in many different configurations.
  For example a star topology, where the controller is the hub and all other terminals are the points of the star.
The network configuration limits how long each terminal can transmit on each poll.
Higher overhead as polling consumes a lot of bandwidth and turnaround time increases time overhead

## Slide 29: Token-Ring Based Access Protocols
A small frame, called token, is passed in an orderly fashion from one terminal to another
  The terminal holding the token has the channel access

## Slide 30: Reservation schemes.
In almost all modern communication systems, one tries to emulate a dynamic assignment schemes, i.e. striving for some type of adaptation of the resource allocation to the present demand
A part of the resources
  collect information about the communication demands of the terminals
  Can be done on separate channels or on dedicated time slots.
  Overhead
The rest of the resources
  perfectly scheduled transmissions of the messages.
Long messages/big data packets: negligible overhead
Short packets: low throughput, higher overhead

## Slide 31: Performance Comparison
Fixed assignment(FA), dynamic assignment (DA), and perfect dynamic assignment (PS)
Notes: Note that systems with fixed assignment
have a comparatively high delay at low arrival rates. In these cases, this system
is practically empty, and only a few messages arrive from time to time. Since
each station is allowed to use only its dedicated fraction of the bandwidth,
the transmission time will be long. On the other hand, at high arrival rates, the
entire bandwidth will be effectively utilized. The maximum throughput for this
system is thus high. The system using dynamic allocation will have (almost)
all the bandwidth at its disposal and yields a very low delay at low traffic loads. the system is empty, an arriving message can be transmitted at once at
a considerably higher rate than in the FA system. On the other hand, when
the traffic load is increased, more resource sharing transmissions are required
and the maximum throughput is considerably lower.

## Slide 32: Contention-Based Access Protocols

## Slide 33: Contention-Based Access Protocols
Contention-based access protocols allow terminals to access channel randomly when they have packets to send.
With random access or contention-based methods, no terminal is superior to another station and none is assigned the control over another
At each instance, a terminal that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send.
Examples: Aloha, CSMA, CSMA/CA/CD, reservation, etc.

## Slide 34: Pure ALOHA(1)
In the late 1960s, the ALOHA protocol was developed at the University of Hawaii.
  Algorithm devised for a VHF-radio system to connect remote terminals on the many islands with a central computer site.
  Control signaling, i.e. ACK, is sent on an independent control channel.
Not synchronized
• Step 1: If there is a message to send, send it;
• Step 2: If the transmission succeeds, remove the message from the queue and go to Step 1.
If the transmission fails, wait a random time interval, i.e. backoff randomly, and go to Step 1.
Notes: Very high frequency (VHF) is the radio frequency range from 30 MHz to 300 MHz.

## Slide 35: Pure ALOHA(2)
Transmission failure due to a collision.
  Paramount importance that the terminals do not wait identical time intervals after a collision, otherwise, another collision.
  Backoff scheme determines the efficiency of pure ALOHA.
  When the total traffic is low, pure ALOHA works well; otherwise, the performance is poor
2 consecutive frame durations needed to send one frame

## Slide 36: Slotted ALOHA
All terminals are synchronized and time is assumed to be slotted
Terminals can send packets only at the beginning of slots
One frame duration needed and efficiency doubles.

## Slide 37: Performance of Slotted ALOHA (1)
M terminals, each with Poisson arrival messages
Success probability: q
Collided messages will be stored and sent out later, approximated by Poisson arrival with rate
Notes: the compound process of retransmitted and new messages will also form a
Poisson process

## Slide 38: Performance of Slotted ALOHA (2)
The system is in a stable equilibrium
  the average number of messages arriving to the system has to be equal to the average number of departing messages. Otherwise the system will either contain an ever-increasing number of packets or become empty.

## Slide 39: Performance of Slotted ALOHA (3)

## Slide 40: Performance of Slotted ALOHA (4)
The relationship between total message arrival rate, i.e. network throughput, and the total rate of attempts.

## Slide 41: Performance of Slotted ALOHA (5)

## Slide 42: Carrier Sense Multiple Access (CSMA)
We can abort transmissions as soon as a collision is detected.
  Once two packets start colliding, it is useless to continue their following transmissions
  Otherwise, it will lead to a waste of bandwidth and energy.
Detect collision while transmitting a packet.
Carrier Sense Multiple Access (CSMA)
  popular in asynchronous (non-slotted) wireless networks with low propagation delays.
  Terminals measure the signal level to detect transmission
    Existing transmission: defer its transmission attempt
    Otherwise, transmit data

## Slide 43: Different CSMA Algorithms
• Step 1: If the channel is sensed idle, transmit a packet immediately;
• Step 2: If the channel is sensed busy, wait a random amount of time and go to Step 1.
Non-persistent CSMA
1-persistent CSMA
• Step 1: If the channel is sensed idle, transmit a packet immediately;
• Step 2: If the channel is sensed busy, continue sensing until the channel is idle; then transmit a packet immediately.

## Slide 44: Different CSMA Algorithms
p-persistent CSMA (p determines the performance)
  How to choose p?
• Step 1: If the channel is sensed idle, transmit a packet with probability p; With probability 1 − p, delay its transmission by one time slot and repeat this Step.
• Step 2: If the channel is sensed busy, continue sensing until the channel is idle; then go to Step 1.

## Slide 45: Effect of Detection Delay
Detection delay: time span between transmission time, t, and detection time, t+to.
With large detection delay compared to the message size,
  Useless carrier sensing information since it is only able to describe the state of the channel some time ago.
  Two terminals may both sense that the channel is empty and start their respective transmissions.
Notes: This delay includes the carrier measurement delay, the switch time from reception to transmission, and
the propagation delay.
If the detection delay approaches zero, almost all collisions can be avoided.

## Slide 46: CSMA w/ Collision Detection
With CSMA, if a terminal decides to send a packet, it will send the whole packet.
  It there is a collision, the resources, time, frequency, and energy, sending the whole packet are wasted.
CSMA/CD is designed to reduce these wastes.
  Each transmitting terminal will also monitor its own transmission.
  If it detects a collision, it stops transmission immediately and instead sends a jam signal to indicate that there has been a collision.
CSMA/CD widely used in wired networks

## Slide 47: Backoff in CSMA-CD
Backoff grows to reduce collision probabilities
  After a collision, a terminal involved in the collision will retransmit its packet after waiting for a random time period.
  If another collision occurs, the time window from which the random waiting time is selected is increased step-by-step.
Exponential back off:
  In the first backoff, random backoff time is chosen randomly between [0; t];
  In the Nth collision, the random backoff time is chosen randomly between [0, tN], where tN=min(2N-1 t; tMax), where tMax is the maximum window size

## Slide 48: Challenges of in Wireless Networks
CSMA/CD not appropriate for wireless networks
  CSMA/CD detects collisions at senders not receivers.
    The signal strength is almost the same for wired networks but varies dramatically in wireless networks.
    In wireless networks, the transmission power is usually much higher than the reception power and collision detection by the sender is very difficult and not possible in practice.
    The collision at the receiver will not be detected by the sender.
In wireless networks
  A signal should reach the receiver without any collision
    The receiver needs to detect collision.

## Slide 49: Hidden Terminal Problems
Both A and B sense the channel idle and send.

## Slide 50: Exposed Terminal Problem
A and C can send packets to B and D at the same time
  But they won’t because C will sense channel busy and not transmit

## Slide 51: CSMA w/ Collision Avoidance
CSMA/CA
  Avoid collisions
  w: exponential back off after each transmission failure
Step 0: For each new transmission, choose a backoff counter randomly between [0, w-1].
Step 1: Sense the channel: idle for a DIFS period, go to step 2; otherwise, continue sensing until it is idle for a DIFS period.
Step 2: The backoff counter counts down as long as the channel remains idle. If the channel is sensed busy, go to Step 1. If the counter is zero, transmit data immediately.
Notes: DIFS (Distributed Inter-Frame Space)

## Slide 52: CSMA/CA
Request To Send/Clear To Send (RTS/CTS) in CSMA/CA
  Both RTS/CTS carry the time length for data transmission
  Solves hidden terminal problem.

## Slide 53: CSMA/CA
RTS/CTS also solves the exposed terminal issue.

## Slide 54: Example- Another way to solve the hidden-node problem
Assume an independent control channel. Time is slotted.
  Sense: When the transmitter wants to send a packet to the receiver, the transmitter checks if the control channel is idle for one slot, defined as slot t.
  Request: If so, in time slot, t + 1, it sends a request on the control channel to the receiver.
  Busy announcement: After receiving the request, the receiver sends the busy signal on the control channel continuously until the transmitter finishes its packet transmission.
  Transmission: After receiving the busy signal, the transmitter starts sending data at time t + 2 on the data channel. All other transmitters hearing the busy signal keep silent.
Question: Assume two transmitters are sending data to an access point. In each idle slot, each transmitter would like to send a packet with probability p. Each packet transmission lasts M slots. What is the throughput of the network?

## Slide 55: Example- Another way to solve the hidden-node problem
For each transmitter, the throughput is
E: expected time for successful packet transmissions
B: expected busy time, including both collisions and successful transmissions.
I: expected idle time.

## Slide 56: Example- Another way to solve the hidden-node problem
The expected idle time is

## Slide 57: Example- Another way to solve the hidden-node problem
Busy transmission: either transmit or collision in a slot
The expected number of busy transmissions is

## Slide 58: Example- Another way to solve the hidden-node problem
Each failed transmission:
  Need two slots for the signaling exchange
Each successful transmission:
  Need M+2 slots: data + signaling
The expected busy time is
where the success probability is

## Slide 59: Example- Another way to solve the hidden-node problem
The expected time for successful packet transmissions is
Network throughput:

## Slide 60: Conflict Resolution Algorithms
CSMA defers data transmission when the channel is busy
CRA: resolves conflicts and users are scheduled using a distributed algorithm.
Example: tree-search algorithm
  Each terminal is numbered with a unique integer with base q.
  As soon as a conflict occurs, the system enters the conflict resolution mode and remains in this mode until the conflict has been resolved. Then it returns to the free access mode.
Notes: In the first time slot after the collision, only stations having a zero as the final digit in their station IDs are allowed to transmit. If another collision occurs, the station with final digits equal to 00 is enabled to transmit. However, if the next slot is empty, or if it contains a successful transmission, we proceed with stations with IDs ending with a 1.

## Slide 61: Conflict Resolution Algorithms
  In the first time slot after the collision, only stations having a zero as the final digit in their station IDs are allowed to transmit
  If another collision occurs, the station with final digits equal to 00 is enabled to transmit.
    However, if the next slot is empty, or if it contains a successful transmission, we proceed with stations with IDs ending with a 1.

## Slide 62: Reservation-Based Protocols
Costly to lose one long data packet if a collision happens
Reservation-based protocols
  Reserve resources, time slots, frequency, etc., for data transmission without conflicts
  Two phases:
    Reservation phase
    Data phase

## Slide 63: Reservation-Based Protocols
Two categories
  Scheduling based
    In the contention phase, a central scheduler collects network information and then schedule the resources for all users to transmit in the data phase.
    Discussed in more detail in the Chapter 5 Scheduling.
  Contention based
    Use short reservation packets to contend for resource allocation
      Packets as small as possible
      ALOHA, CRA, and other random access protocols can be used to decide resource reservation

## Slide 64: Reservation ALOHA
Use slotted ALOHA in the reservation phase
All terminals in the range of each other

## Slide 65: Bit-Map Protocol
Terminals numbered from 1 to N
All terminals are in the coverage area of each other
Send a short packet in the corresponding slot if a terminal has data to send
Send data in the data phase following the order in reservation phase

## Slide 66: Efficiency of Bit-Map Protocol
Low load, only one user has a packet in each data phase
d: number of bits in the packet; N: number of terminals. One bit in each reservation packet.
Efficiency  1with d>>N, which is true in most scenarios

## Slide 67: Efficiency of Bit-Map Protocol
High load, all terminal have packets
Efficiency  1with d>>1, which is true in most scenarios

## Slide 68: Efficiency Limit
Critical Factors for High Efficiency
  Ideal synchronization
  Each reservation slot as small as possible
    Limited by sync capability, necessary amount of information, channel capacity, etc.
  Number of reservation slots as small as possible
  Allow long data transmission.
A special type of network
  all terminals in the coverage of each other
  Bit-Map Protocol
  Efficiency  1

## Slide 69: Efficiency Limit
General types of wireless networks
  Terminals have different coverage areas
  Any distribution or density of terminals
  [G. W. Miao et al., 2012]: The efficiency for networks of any type or size can approach 1 using the designed CAD-MAC (channel-aware distributed MAC).

## Slide 70: System Examples: WiFi
IEEE 802.11 Wireless Local Area Network (WLAN)
  Also called WiFi
Asynchronous, best effort, connectionless
Access: CSMA/CA
Carrier sensing: measure the RF energy at the antennas and determining the strength of the received signal
  Signal strength below a threshold-> channel available

## Slide 71: System Examples: WiFi
Notes: DIFS (Distributed Inter-Frame Space)
PIFS: PCF Interframe Space
SIFS: Short Interframe Space. used for the highest priority transmissions enabling stations with this type of information to access the radio link first.
The period of time following immediately a busy channel state is of the highest probability of collisions.
After a busy channel, a minimum time gap between frames for each terminal. Once a frame has been sent and the channel goes
from the busy state to the idle, a terminal must wait until the time gap is up to try a transmission.

## Slide 72: System Examples: WiFi
To further avoid collisions:
  virtual carrier-sense mechanism
  network allocation vector (NAV)
    limits the need for physical carrier sensing to save power.
    A counter
    Predicts future traffic and busy channel, and thus avoid channel sensing
    Can be exploited by using RTS, CTS, ACK, and data transmission frames sequentially.

## Slide 73: System Examples: WiFi

## Slide 74: MAC Types