## Slide 1: Chapter 10 Long Term Evolution
Email list: https://groups.google.com/forum/#!forum/mobile-miao

## Slide 2: History of Cellular Standards
1G
2G
3G
4G
2.5G
1980s, 28KBPS
1990s, 100KBPS
2000s, 2MBPS
2010s, 100MBPS

## Slide 3: Introduction
In November 2004 3GPP began a project to define the long-term evolution of UMTS cellular technology.
Related specifications are formally known as the evolved UMTS terrestrial radio access (E-UTRA) and evolved UMTS terrestrial radio access network (E-UTRAN).
First version is documented in Release 8 of the 3GPP specifications.

## Slide 4: Introduction
First commercialization:
  TeliaSonera in Stockholm and Oslo on December 14, 2009.
Adoption of LTE technology as of Dec 7, 2014.
Red: Countries with commercial LTE service
Blue: Countries with commercial LTE network deployment on-going or planned
Grey: Countries with LTE trial systems (pre-commitment)

## Slide 5: LTE Targets
Higher data rate
  100 Mbit/s peak downlink, 50 Mbit/s peak uplink
  1G for LTE Advanced
  Faster cell edge performance
  Reduced latency (to 10 ms) for better user experience
  Scalable bandwidth up to 20 MHz
Backwards compatible
  Works with GSM/EDGE/UMTS systems
  Utilizes existing 2G and 3G spectrum and new spectrum
  Supports hand-over and roaming to existing mobile networks
Reduced capex/opex via simple architecture
  reuse of existing sites and multi-vendor sourcing
Wide application
  TDD (unpaired) and FDD (paired) spectrum modes
  Mobility up to 350kph
  Large range of terminals (phones and PCs to cameras)

## Slide 6: LTE Architecture

## Slide 7: Protocol Layers
Packet Data Convergence Protocol (PDCP)
  IP header compression based on Robust Header Compression (ROHC)
  ciphering and integrity protection of transmitted data
Radio Link Control (RLC)
  segmentation/concatenation
  retransmission handling
  in-sequence delivery to higher layers
Medium Access Control (MAC)
  handles hybrid-ARQ retransmissions
  uplink and downlink scheduling at the eNodeB
Physical Layer (PHY)
  coding/decoding
  modulation/demodulation (OFDM)
  multi-antenna mapping
  other typical physical layer functions

## Slide 8: OFDM (1)

## Slide 9: OFDM (2)
Symbols to be sent on the nth OFDM symbol:
N-point IFFT:
  Usually N>K, based on:
Before sending d[n], a guard period is created at the beginning of d[n].
  Eliminate inter-symbol interference

## Slide 10: OFDM (3)
Guard period obtained by adding the Cyclic Prefix (CP) to the beginning of d[n].
Assume the guard period has G samples.
CP is the duplicate of the last G elements of d[n].

## Slide 11: OFDM (4)
The receiver is well synchronized in both the time and frequency domains
Reverse operation for decoding
  Remove the first G CP samples
  Pass the remaining N samples to the FFT for transformation back to the frequency domain
The symbols on the modulated K subcarriers are chosen out of the N output subcarriers
  further processed, e.g. demodulated and decoded, for the desired bit stream

## Slide 12: OFDM (5)
ISI elimination

## Slide 13: OFDM (6)
CP longer than the longest channel impulse response
  None of the replica of the preceding symbol may spill over into the FFT period of the current symbol
After discarding the CP samples
  only signals of time-staggered replicas of the current symbol, based on which the receiver can apply an equalizer to recover the original transmitted signal.

## Slide 14: OFDM (7)
  The CP of OFDM changes the linear convolution of the multipath channel into a circular one
  With the FFT operation, the circular convolution is transformed into a multiplicative operation in the frequency domain
  The frequency-selective multipath channel is converted into an N-parallel orthogonal flat-fading channel in the frequency domain
  Receiver will estimate channel and correct channel distortion on a per-subcarrier basis.

## Slide 15: OFDMA
LTE downlink employs OFDMA as the multiplexing scheme because of its efficiency in managing resources and low latency in sending packets.
Difference between OFDM and OFDMA
  OFDM: a single user on all subcarriers (a modulation scheme)
  OFDMA: each user is allocated a specific number of subcarriers for a predetermined amount of time

## Slide 16: LTE Generic Frame Structure

## Slide 17: Resource Grid in LTE

## Slide 18: Channel Resources
The number of subcarriers
  depend on system bandwidth: 1.4 MHz to 20 MHz
PRB: 12 consecutive subcarriers for one slot
  84 REs
With MIMO
  A resource grid for each antenna

## Slide 19: Scheduling
A PRB is the smallest scheduling element.
Scheduling is based on the channel state information of all users
The PRBs of different users may have different channel qualities.
Adaptive allocation can be used to improve the total network spectral efficiency compared to single-user OFDM systems by exploiting multiuser diversity.
The minimum scheduling interval is 1 ms, corresponding to the 1 ms subframe, to enable low latency.

## Slide 20: SC-FDMA (1)
OFDMA
  not favorable for the uplink communications because of its weak peak-to-average power ratio (PAPR) properties
  poor uplink coverage and high power consumption of mobile terminals.
The uplink transmission
  sufficiently low PAPR to avoid excessive cost and power consumption of power amplifiers.
LTE uses Single Carrier Frequency Division Multiple Access (SC-FDMA) in the uplink
  better PAPR properties than OFDMA.

## Slide 21: SC-FDMA (2)

## Slide 22: SC-FDMA (3)
Different users are assigned different sets of subcarriers
Multi-path distortion
  Handled the same as that in OFDM
Difference between OFDMA and SC-FDMA
  OFDMA: Each subcarrier carries information of only one specific modulation symbol
  SC-FDMA: each allocated subcarrier contains information of all transmitted modulation symbols
    The information of the symbols has been spread out across all subcarriers by FFT
    Single carrier as the subcarriers are not independently modulated
    Much lower PAPR in the time domain.

## Slide 23: MIMO (1)
Multiple Input Multiple Output (MIMO) is essential for LTE to achieve high spectral efficiency.
Both eNB and UE may have multiple antennas
Support of different modes in LTE
  (i) Single-antenna transmission;
  (ii) Transmit diversity;
  (iii) Open-loop spatial multiplexing (no CSI feedback needed);
  (iv) Closed-loop spatial multiplexing (CSI feedback needed);
  (v) Multi-user MIMO.

## Slide 24: MIMO (2)

## Slide 25: MIMO (3)
Transmit diversity mode
  Use MIMO to exploit diversity and increase transmission robustness
  Default mode of LTE
  Each antenna transmits the same information
    Replicas of the same signal are received
    Improved received SNR and robustness

## Slide 26: MIMO (4)
  Antenna-specific coding may be applied to further improve the robustness
Two transmit antennas at the eNB
  Space frequency block code (SFBC): a frequency-based version of the Alamouti code
  The transmitted streams are orthogonal to each other
  the optimal SNR can be achieved with a linear receiver

## Slide 27: MIMO (5)
Four transmit antennas at the eNB
  A combination of SFBC and frequency switched transmit diversity (FSTD)
  Different antennas use different sets of subcarriers

## Slide 28: MIMO (6)
Spatial multiplexing
  Different streams of data are sent simultaneously on the same RBs by exploiting the spatial-domain channel characteristics.
  The number of independent data streams
    Determined by the rank of H.
    Channels of different antennas should be sufficiently de-correlated.
    The singular values of H determines if SM should be employed.
  SU-MIMO
    All data streams are allocated to a single user
    Increase the throughput of an individual user
  MU-MIMO
    The data streams are assigned to two or more users
    Improve overall network capacity

## Slide 29
Interference coordination in LTE (1/2)
Motivation for inter-cell interference coordination (ICIC)
LTE provides orthogonality to users within a cell
However, users (particularly at cell edge) are susceptible to interference from other cells
Conventional frequency reuse reduces system capacity too much

## Slide 30
Interference coordination in LTE (2/2)
Various levels of interference coordination (ICIC)
Static ICIC
  Rules for resource block allocation restricting the usage of resource (bandwidth or power) in some part of the cell
  Similar to reuse partitioning
Adaptive ICIC
  Adaptive selection of predefined configurations
Dynamic ICIC
  Multi-cell cooperation (termed CoMP)

## Slide 31
Static ICIC schemes
1
2
3
Power
Frequency
Cell 1
Cell 2
Cell 3
1
2
3
Power
Frequency
Cell 1
Cell 2
Cell 3
1
2
3
Power
Frequency
Cell 1
Cell 2
Cell 3
1
2
3
Power
Frequency
Cell 1
Cell 2
Cell 3
Frequency reuse of 1
Frequency reuse of 3
Soft frequency reuse
Partial frequency reuse

## Slide 32
SFR: Example 10.3
Cell area is divided into two
inner-cell: K=1 (all available resources can be allocated)
outer-cell: K=3 (only a part of resources is allowed)
Resource division in frequency domain
cell-center band: reduced power, only available for inner-cell users
cell-edge band: amplified power, available for all users in the cell
1
2
3
Power
Frequency
Cell 1
Cell 2
Cell 3

## Slide 33
SFR: Example 10.4 (1/2)
Consider a terminal moving towards cell edge
SIR of cell center band < SIR of K=1
SIR of cell edge band < SIR of K=3
r
Cell j
Dj(r)

## Slide 34
SFR: Example 10.4 (2/2)
SFR strikes a balance between the performances of center user and boundary user
When a mobile can claim all the available resources at each location, its achievable capacity is

## Slide 35
Coordinated multi-point transmission (1/3)
Joint processing between neighboring cells (a cluster)
Coordinated scheduling
  One entity assumes the scheduling decision of all cells in the cluster
Coordinated beamforming
  Precoding of transmitted signal for interference cancellation
  Requirements: precise CSI, fast and reliable backhaul
Joint transmission (see next slide)

## Slide 36
CoMP (2/3)
Joint transmission
  APs share data stream to be transmitted.
Three categories depending on CSI and synchronization accuracy
  Dynamic point selection
    Selection diversity is obtained (similar to instantaneous handover)
  Non-coherent transmission
    Signal power is combined similarly to the downlink of CDMA soft handover
  Coherent Transmission
    The cluster can be regarded as a single cell with geographically separated multiple antenna with extremely accurate CSI and phase synchronization

## Slide 37
CoMP (3/3)
Challenges
Inter-BS communications (backhaul)
  Fast, reliable, and high capacity
Channel estimation and feedback
  Accuracy
  Overhead
Inter-cluster interference management