## Slide 1: Chapter 4 Scheduling
Email list: https://groups.google.com/forum/#!forum/mobile-miao

## Slide 2: Background
Wireless networks are evolving from analog, small-capacity, voice services to digital, large-capacity, data services.
Users have different service requirements:
  With unlimited wireless resources: all problems solved
    Never going to happen!
  A flexible service architecture to integrate different types of services on a single air-interface;
    Optimized only for one type of service, other types will experience poor service qualities.
  Effective QoS management schemes
    QoS metrics differ between different applications that may even be of the same type.
      Video telephony has a strict delay requirement but the detailed parameters can be different.
      With different resolutions of videos, the delay requirements differ.

## Slide 3: Resource Allocation
Contention-based access protocols
  Protocol itself decides the resource allocation, e.g. time slots when a packet should be transmitted
  Example: Pure ALOHA determines when a packet transmitted and how much spectrum, the whole sys bandwidth, will be used.
  The design determines the efficiency of resource utilization
    Inefficient in practice (50% ~65% at most)
    Terrible performance with heavy traffic
  Not efficient when many terminals access the network
    Frequent in cellular networks
    High efficiency needed in cellular networks
Reservation-based access protocol with centralized scheduling
  Most commonly used access protocol in wireless cellular networks
  High efficiency as well as flexibility in managing wireless resources.

## Slide 4: A Reservation-based Protocol
PDCCH: conveys control information for each user.
PDSCH: multiplex the data of all terminals; each user will transmit on a unique set of OFDM symbols and frequency blocks.
Reservation phase: PDCCH. Data phase: PDSCH.

## Slide 5: Role of Scheduling
Reservation phase:
  Estimate channel Feedback Scheduling

## Slide 6: Issues in Wireless Scheduling
Support of mixed classes of traffic desiring different QoS

## Slide 7: Perceived QoS

## Slide 8: Issues in Wireless Scheduling
Flexible in allocating network resources.
  Achieved using scheduling algorithms.

## Slide 9: Issues in Wireless Scheduling
Channel Variation
  Shadowing, fading, noise, interference, and user mobility
  Unstable, error-prone, and hard to predict
  Capacity of each link varies significantly in different time periods and locations
Even the scheduler knows QoS requirements
  Difficult to estimate the amount of resources needed
  An adaptive procedure is needed to assure QoS considering the requirement and channel variation.

## Slide 10: Wireless Packet Scheduling Algorithms
Benefit of using scheduling in wireless networks
  Flexible in adaptation to QoS and channel
  A single air-interface to integrate various service types
  Significant performance improvement w/o more spectrum
Model: M users served on a single channel; TDMA, one user in one slot; each user has a buffer.

## Slide 11: Queuing Modeling
At time t, the queue of user i changes following
Number of bits in the queue
Number of new bits arriving
Number of bits scheduled to transmit, determined by scheduling.

## Slide 12: Round-Robin Scheduling
Users are scheduled in a round robin, i.e. cyclic order, manner
i[t]: user scheduled at time t.
RR scheduler:
  i[t+1]=i[t]+1.
Fair: all users scheduled the same amount of time.

## Slide 13: Round-Robin Scheduling
Performance
  All users are allocated the same amount of network resources
  What’re the throughput of all users in the following network?

## Slide 14: Max Throughput Scheduling
Objective: maximize total network throughput
If user i is scheduled, the expected data rate is
The total expected network throughput is
Schedule the user with the highest expected data rate
  Estimate:
  Max SINR or Max C/I scheduler (a channel-aware scheduler)
Slot length
Expected number of bits that can be successfully delivered
Scheduling indicator: 1 scheduled, 0 otherwise.

## Slide 15: Max Throughput Scheduling
Main drawbacks
  Unfairness
  Coverage limitation
  Most users may never be served

## Slide 16: Proportional Fair Scheduling
PF scheduling: a compromised policy to balance the competing interests of network throughput and minimum service level
Objective: maximize
Si: long-run throughput, which can be predicted using
PF scheduler: schedule the user with the highest

## Slide 17: Proportional Fair Scheduling
Meet the proportional fairness criterion:
xi: the optimal value; For any other feasible value, the sum of proportional changes is non-positive, i.e.
Indication: when the scheduling result is already proportional fair, we change the scheduling such that the throughput of any user is increased by a%, there will be more than a% cumulative decrease of the throughputs of other users.

## Slide 18: Proportional Fair Scheduling
Why proportional fair

## Slide 19: Max-Min Scheduling
Objective: maximize the minimum user throughput
A scheduling result is max-min fair if and only if a further increase of throughput of one user will result in the decrease of a user with a smaller throughput
Schedule the user with the minimum , i.e. the one with the smallest throughput at time t-1.

## Slide 20: Max-Min Scheduling
M empty cylindrical buckets (users), all with the same radius but different heights.
Allocate water

## Slide 21: Max-Min Scheduling
M empty cylindrical buckets (users), all with the same radius but different heights.
Allocate water

## Slide 22: Can these schedulers deal with QoS?

## Slide 23: Max Utility Scheduling
Previous schedulers do not consider QoS
Utility-based scheduling
  Utility quantifies the satisfaction of each user given the allocated resources
  Model the QoS perception of users
  Objective: maximize the sum utility of all users, i.e. total network satisfaction
Utility functions: model how user perceives services

## Slide 24: Fairness and Efficiency
Different utility functions can be designed.
In addition to QoS modeling, different utility functions can be designed to reflect fairness and efficiency.
Max-throughput (highest efficiency):
Proportional fair:

## Slide 25: Alpha Fair Utility
More generic definition: fair scheduling
measures how fair the scheduling result is
  0: Max throughput;
  1: Proportional fair;
  2: equivalent to minimizing
    Minimize the total potential delay
  Infinity: Most fair, max-min scheduler.

## Slide 26: Alpha Fair Utility

## Slide 27: Utility Functions with QoS Consideration
Determined based on traffic characteristics
a: best effort; b: real time with tight delay requirement; c: real time with loose delay requirement.
Notes: a. Best effor

## Slide 28: How to Schedule Users
Equivalent objective:
Schedule the user with the largest:

## Slide 29: Performance Comparison
In a cellular network, users requesting different types of services from the BS. Ten users dropped randomly in each cell.

## Slide 30: Performance Comparison

## Slide 31: Performance Comparison

## Slide 32: Performance Comparison

## Slide 33: Scheduling in OFDMA Systems
One more dimension of resources
  Subcarrier allocation
Different users experience independent wireless channels and their subcarriers may experience substantially different channel gains because of the frequency selectivity in the channels.
Theoretically it is possible to set the data rate for each sub-carrier based on its channel quality and power allocated.

## Slide 34: Scheduling in OFDMA Systems
Subcarrier in deep fading for one user may not be used by this user as sending bits on these subcarriers cost too much power.
  May be in good channel conditions to other users and can be used by them instead.
Scheduling of subcarriers in an adaptive way based on the instantaneous channel qualities.
OFDMA systems typically use adaptive subcarrier assignment, power allocation, modulation and coding to exploit the diversity in multiple users and frequency to improve the network performance.

## Slide 35: System Model

## Slide 36: Signaling in OFDMA Scheduling
Additional signal overhead is necessary as all users need to feed back CSI
The base station has to inform all users the resource allocation result.
The overhead is rather small, especially in slow-fading channels, and the resource allocation may be updated once every many OFDM symbols.
Besides there are also many other techniques to further reduce the signaling overhead, like bundling of adjacent subcarriers.

## Slide 37: Max-Throughput OFDMA Scheduling
Round-robin, max-throughput, PF, max-min, and max-utility scheduling can all be done for OFDMA.
Take max-throughput scheduling as an example.
  Schedule the users such that the total network throughput is maximized
The expected throughput of user i in the tth OFDM symbol is

## Slide 38: Max-Throughput OFDMA Scheduling
Each subcarrier is assigned to only one user and we have the following constraint
The overall network throughput
W/o and w/ power adaptation

## Slide 39: W/o power adaptation
Assume no adaptive power allocation
In order to maximize the network throughput, subcarrier i should be allocated to the user whose SINR on this subcarrier is the highest among all users.

## Slide 40: W/ power adaptation
Assume adaptive power allocation
Subcarrier allocation
  Each subcarrier should be assigned to the user with the highest , as the rate increase by using any amount of power on any subcarrier will be maximized if the subcarrier has the highest .
How much power should be used on each subcarrier?

## Slide 41: W/ power adaptation
The BS has a total power constraint
where Po is the total transmit power limit of the BS power amplifier.
Concave problem and the Lagrangian method can be used to find the optimal power allocation.

## Slide 42: W/ power adaptation
Water-filling power allocation

## Slide 43: Other OFDMA Schedulers
Max-throughput OFDMA scheduling also suffers unfairness and coverage limitations
  Users closer to the BS have more subcarrier assignment
  Users at cell edges may never be served.
Fair scheduling algorithms for OFDMA systems can be designed.
QoS consideration further complicates the scheduling
  Mixed types of traffic, utility based scheduling should be used
  Much more complicated than the schedulers we have introduced so far in this chapter.
  Refer to the references for more details.