## Slide 1: Chapter 7 Interference Management
Email list: https://groups.google.com/forum/#!forum/mobile-miao

## Slide 2
Why interference management?
Radio spectrum is a finite resource
It should be shared with many others
Radio wave is a broadcast medium
Your signal is interference to the others

## Slide 3
In cellular systems,
Radio resource allocation is usually on a per-cell basis
Orthogonal resource assignment within each cell
Therefore, what matters is inter-cell interference management

## Slide 4
Classifying Interference Management Techniques (1/3)
Interference avoidance
Relies on separation of users in space (reuse distance)
  exploiting exponential decay of radio propagation
Time/frequency division can be used to separate users in the vicinity
Most fundamental and common
Interference randomization
Interference cancellation

## Slide 5
Classifying Interference Management Techniques (2/3)
Interference avoidance
Interference randomization
Randomly spreading interference over time or frequency
Good for handling sudden interference fluctuation
Distributed interference mitigation is possible
Interference cancellation

## Slide 6
Classifying Interference Management Techniques (3/3)
Interference avoidance
Interference randomization
Interference cancellation
Transmitter and receiver techniques to make interference less harmful
“Known” interference is not harmful anymore

## Slide 7
Key Elements of Interference Management (1/2)
It is a tool to investigate practical ways to improve the performance of the system

## Slide 8
Key Elements of Interference Management (2/2)
Adaptivity to traffic
Long-term variation in average traffic
Real-time traffic fluctuation
Adaptivity to channel condition
Average propagation loss due to terrain and buildings
Instantaneous channel state
Resource reusability
What to do with the traffic and channel information?
You can deal with time, frequency, modulation and coding, power, and more

## Slide 9: Interference avoidance
Frequency reuse is a rudimentary interference avoidance technique
Use of the same frequency channel with reuse distance to meet SINR requirement
When reuse factor is K, only 1/K of system bandwidth is utilized at each cell
f1
f3
f2
f1
f3
f2
f1
f3
f2
f1
f3
f2
Example of frequency reuse with K=3.

## Slide 10
Better interference avoidance?
How to improve the resource utilization under the interference avoidance principle?
Numerous studies have been performed and are ongoing
We will look into two representative techniques
  Reuse partitioning
  Multi-cell scheduling

## Slide 11
Reuse partitioning: introduction (1/2)
A close look at geographic characteristics of a cell
Inner cell (close to AP): stronger signal, weaker interference
Outer cell (far from AP): weaker signal, stronger interference
Inner cell can easily achieve higher SIR, and thus requires less reuse distance

## Slide 12
Reuse partitioning: introduction (2/2)
Each cell is divided into two or more co-centric subcells with different reuse distance
Cell boundary: low SIR → large reuse factor needed
Cell center: high SIR → small reuse factor available
1,2,3
4,5,6
7,8,9
Channels 1-9
1,2,3
1,2,3
1,2,3
4,5
6,7
8,9
Num. channels per cell: 3
Num. channels per cell: 5

## Slide 13
Reuse partitioning: subcell radius
How to determine subcell radius?
Let Ki be reuse factor of L subcells
Then,
Radius of subcell i is
Zone 1
Zone 2
Zone 3
Zone L
d1
d2
d3
dL

## Slide 14
Reuse partitioning: resource allocation (1/2)
How does the reuse partitioning increase the capacity?
Let c be channel allocation vector for L subcells
The choice of c vector is constrained by the total number of available channels C
Considering the frequency reuse factors, the number of available channels per cell is

## Slide 15
Reuse partitioning: resource allocation (2/2)
How does the reuse partitioning increase the capacity?
For example, Let C=100 and K=(1,3,4,7,9).
  Then, c=(2,4,2,6,4).
  Thus, c0 = 18.
Under conventional frequency reuse,
Therefore, the cell capacity has increased from 11 to 18 channels!

## Slide 16
Example 7.1
Despite the capacity increase, the reuse partitioning may lead to more assignment failures
Fragmentation results in reduced trunking efficiency (higher assignment failure rate)

## Slide 17
Example 7.1
Frequency reuse
Cell traffic load M is accommodated by cell capacity c0
Reuse partitioning
Possible mismatch between and
Assignment failure rates; C = 100.

## Slide 18
Need for dynamic approach
Reuse partitioning falls into static resource allocation
No further interaction between cells after frequency allocation
  No adaptivity to traffic variation in multi-cell level
Cells normally exhibit very different traffic profiles both in long-term and short-term
What can be achieved if neighboring cells collaborate?

## Slide 19
Multi-cell scheduling: concept
Assume a cluster of N cells share real-time traffic information within the cluster
It would be possible to make coordinated scheduling decisions
Radio resources can be pooled together to cope with the traffic fluctuation in the cells

## Slide 20
Multi-cell scheduling: an example
Assume only one cell in the cluster is allowed to transmit at each scheduling epoch
The chosen cell can utilize the whole resources (N times larger than the conventional frequency reuse)
Conventional system: N independent M/M/1 queues
  Arrival rate λ, service rate μ
Multi-cell scheduling: a single M/M/1 queue with N times faster server
  Arrival rate , service rate

## Slide 21
Example 7.2
Assume that the same sojourn time is allowed
Thus,
How much traffic can multi-cell scheduling accomodate?
Traffic load that multi-cell scheduling can accomodate as a function of N; µ = 1.

## Slide 22
Challenges for multi-cell scheduling
What are obstacles to realizing the full potential of multi-cell scheduling?
Backhaul connection
  Fast and reliable inter-cell communication is required to exchange real-time scheduling information
Inter-cluster coordination
  How to prevent performance degradation at cluster borders?

## Slide 23
Interference randomization
It randomly spreads signal power over frequency
so that the signal looks like a noise to the others
Frequency
Power spectral density
Frequency
Power spectral density

## Slide 24
Why using randomization?
For general benefit
Robustness to fading (particularly multi-path fading)
Inherent encryption capability
Easy multiplexing of bursty sessions
For interference management
To combat hostile interferer (jammer)
When you ”cannot” avoid interference (lack of coordination)

## Slide 25
Frequency hopping (Example 7.3)
Non-orthogonal FH
Hopping patterns are not coordinated among the pairs
1 |  | 2 |  |  | 
 | 1 |  |  | 1 | 
 | 2 |  | 1,2 |  | 
2 |  |  |  |  | 
 |  |  |  | 2 | 1,2
 |  | 1 |  |  | 
time
frequency

## Slide 26
Interference cancellation
”Known interference” can be deducted from received signal or can be erased in the beginning
Challenges are
  How to ”know” interference
  How to ”cancel” interference

## Slide 27
Successive interference cancellation (1/2)
Successive interference cancellation is the most well known technique at the receiver side
It decodes strongest interference, eliminate it, and reconstruct the received signal; repeat it until no interference remaining
Precise knowledge about instataneous CSI is required
Decoding error may propagate if cancellation not perfect

## Slide 28
Successive interference cancellation (2/2)
Received signal
After extracting the strongest interference
Reconstruction of the received signal after jth extraction

## Slide 29
Transmit beamforming
Multiple transmitters collaborate to ”precode” transmitted signal so that receivers do not notice interference
The simplest method is zero-forcing
If you know the channel gain matrix (H),

## Slide 30
Heterogeneous Networks
It refers to a layered deployment for macro and small cells
Why heterogeneous networks?
  To provide higher capacity with less cost
Challenge in heterogeneous networks
  Co-tier and cross-tier interference management

## Slide 31
Example 7.4 Open vs. Closed access (1/2)
Closed access may cause a serious interference problem
Why heterogeneous networks?
  To provide capacity with less cost

## Slide 32
Example 7.4 Open vs. Closed access (2/2)
  Marco cell only: r={5.14, 8.64, 2.50, 0.34} Mbps
  Open access: r={17.6, 32.2, 41.9, 16.1} Mbps
  Closed access: r={8.8, 32.2, 0.007, 32,2} Mbps