## Slide 1: Chapter X CDMA
Email list: https://groups.google.com/forum/#!forum/mobile-miao

## Slide 2: Code-Division Multiple-Access Digital Cellular Systems
Introduction to cellular DS-CDMA
DS-CDMA digital cellular networks
Capacity calculations of DS-CDMA cellular systems
Multi-rate DS-CDMA systems
Power Control in DS-CDMA cellular systems
Soft-handoff in DS-CDMA cellular systems
Summary

## Slide 3: Direct-Sequence Spread Spectrum

## Slide 4: DS-CDMA Cellular systems
In DS-CDMA systems, the processing gain allows a universal reuse (K=1)
No frequency planning is needed.

## Slide 5: DS-CDMA Cellular systems
Power control is a basic requirement in DS-CDMA systems.
  Constant Received Power (CRP) in the uplink.
  Power allocation type in the downlink.
Soft and softer handoffs.
DS-CDMA systems use a two-layered spreading code allocation.
  Short orthogonal codes (channelization codes).
    Increase system capacity.
  Long PN sequences (scrambling codes)
    Reduce interference between different cells.
    Reduce uplink interference.

## Slide 6: DS-CDMA Cellular systems
North American DS-CDMA Digital Cellular System (IS-95), 1993
  Bandwidth: W=1.25 MHz.
  Information (speech) data rate: Rs=9.6 kbps.
  Processing gain of Lc=PG=128.
3rd Generation: W-CDMA, 2001
  Bandwidth: W=5 MHz.
  Variable data rate: Rs=9.6, 144, 384, 2048 kbps.
  Variable processing gain: 4-256.

## Slide 7: Sequences in IS-95 and WCDMA Cellular Networks

## Slide 8: Sequences in IS-95 and WCDMA Cellular Networks
 | CDMA (IS-95) | 
 | Forward Link | Reverse Link
Channelization code | Walsh sequences of length 64 | -
Scrambling code | Different offsets of m-sequences, chips. A common PN for all users of a cell. | Different offset of m-sequence, chips. A distinct offset for each user.
 | CDMA (IS-95) | 
 | Forward Link | Reverse Link
Channelization code | Walsh sequences of length 64 | -
Scrambling code |  | 
 | WCDMA | 
 | Forward Link | Reverse Link
Channelization code | OVL sequences | OVL sequences
Scrambling code | Gold sequences, chips. A common PN for all users of a cell. | Vary large set of Kasami sequences. Optional: Gold sequence, chips.
 | WCDMA | 
 | Forward Link | Reverse Link
Channelization code | OVL sequences | OVL sequences
Scrambling code |  | 

## Slide 9: Uplink of DS-CDMA systems
The received signal at the base station can be written as follows:
is the received signal from mobile within the same cell.
is the received signal from mobile in a neighbor cell.
The signal energy-to-noise power spectral density , for user is
is the received signal from mobile .
is the user data rate.
is the system bandwidth.
is the required threshold.

## Slide 10: Single Cell Capacity of DS-CDMA Systems
For a single cell, the signal energy-to-noise power spectral density, becomes,
With perfect Constant Received Power (CRP), we get
The capacity is estimated as
is the after despreading.

## Slide 11: Multiple Cell Capacity of DS-CDMA Systems
The signal energy-to-noise power spectral density at the base station is given by
With perfect CRP, we have

## Slide 12: Multiple Cell Capacity of DS-CDMA
The capacity is obtained by computing the time availability
.
The capacity can be approximated from the average as
  We define the interference factor as :
The capacity of multi-cell DS-CDMA systems becomes:
The external interference is about (with ) of the internal interference, i.e.,

## Slide 13: Sectorization in DS-CDMA Cellular systems
The capacity of DS-CDMA system can be improved by reducing the interference
  Sector antennas improve the capacity of DS-CDMA
  is the number of antennas per cell.

## Slide 14: Voice Activity Detection in DS-CDMA Systems
Voice activity monitoring can improve the capacity of DS-CDMA.
  Modeling the talk spurt and silence as exponential with means and s , respectively. The voice activity factor can be written as
  The transmission rate of a given mobile can be modeled as a stochastic process with average transmission rate
  The average received power from such user is .
The multicell capacity of DS-CDMA becomes

## Slide 15: Pole Capacity of DS-CDMA Systems
The pole capacity is obtained when the user stations power approaches infinity
  Real systems operate below the pole capacity.
We define the system load as follows:
We define as the stability factor of the CDMA system as
  This analysis neglects the effects of imperfect power control and the dynamics of the systems.
  To account for these variations, a system should not run too close to the capacity pole.

## Slide 16: Coverage-Capacity Tradeoff in the Reverse Link
When the mobile users are transmitting at maximum power, loading should not be permitted to increase.
Conversely, if the loading is allowed to increase, then the mobile users can no longer reach the required target .
  The cell shrinks due to loading.
This phenomenon couples coverage and loading.
Loadings of to are an appropriate compromise between loading and coverage.

## Slide 17: Traffic-Based Capacity Evaluation of DS-CDMA Systems
The number of channels (codes) in CDMA is very large.
Blocking occurs due to bad links and not to lack of available codes.
In CDMA, each cell can be modeled as an queue.
For a single cell, the number of users is modeled as a Poisson random variable having mean equal to the cell offered traffic, .
    With voice activity detection, the number of users is still Poisson but with reduced traffic load
The multiple cell case can also be seen as a single cell with a higher traffic load.
The number of active mobiles is modeled as Poisson RV with

## Slide 18: Traffic Variations – Erlang Capacity of DS-CDMA
With users, at a given base station for user is
The assignment failures occur when the total interference experienced by any user exceeds the background noise by an amount .

## Slide 19: Multi-Rate DS-CDMA Systems
DS-CDMA can provide multimedia services by using variable rate spreading codes.
The signal-to-noise power spectral density for user is written as:
The required power for user is the given by
The capacity of multi-rate DS-CDMA systems is such that

## Slide 20: Power Control in DS-CDMA Systems
DS-CDMA cellular systems require good and accurate power management.
Bandwidth allocation power allocation.
Power control ensures that each user receives and transmits enough energy to properly convey information while interfering with other users no more than necessary.
Power control reduces the required transmitted power
Power control increases the capacity of DS-CDMA cellular systems.
  Better battery life.
  Less interference.
Uplink and downlink power control are required (lack of reciprocity).

## Slide 21: Reverse Link Power Control in DS-CDMA Systems
Power control is very critical for DS-CDMA cellular systems.
  Path loss effects (dynamic range in the order of 80 dB)
  Fading multipath effects (fluctuations of 20 to 30 dB)
The reverse link power in DS-CDMA constitutes of three loops
  Open loop power control
  Fast closed loop power control.
  Outer loop power control.

## Slide 22: Open Loop Power Control
The mobile estimates the path loss to the base station by measuring the received signal level.
  Measurements based on an analog AGC voltage.
The mobile unit adjusts its transmitted power according to
Required accuracy of about in normal conditions.
Problem of reciprocity in FDD cellular networks.

## Slide 23: Closed Loop Power Control
Closed loop power control is a sort of “fine tuning” to the open loop power control.
  The base station measures the received , for each mobile.
  Compares this estimate to the desired threshold, .
  If , a “down” command is sent to the mobile.
  If , an “up” command is sent to the mobile.
  Power control frequency: 800 Hz, 1600 Hz.
  Power up/down “step size”: 0.5-1 dB.
There is no “do nothing” command (to reduce overhead).

## Slide 24: Outer Loop Power Control
The outer loop power control aims at providing the required quality: no worse, no better.
  Adjust target to the required FER (or BER).
This loop ensures that the fast power control strategy is operating correctly.
  Uplink only is IS-95.
  Both uplink and downlink in WCDMA.

## Slide 25: Forward Link Power Control in DS-CDMA
The forward link may be subject to poor reception conditions.
  Mobile near the border of the cell.
  Mobile located where several strong multipath signals arrive.
The mobile can request an increase/decrease in the power transmitted to it by the base station.
  Mobile has the capability to measure received signal-to-total interference ratio.
Slow rate of forward link power adjustment:
  Once per 15-20 ms.
Limited dynamic range:
  About dB around the nominal power.

## Slide 26: Soft Handoff in DS-CDMA Cellular Systems
Soft handoff is a technique whereby mobile units in transition between one cell and its neighbor transmit to and receive the same signal from both base stations simultaneously.
On the downlink, the RAKE receiver at the mobile can achieve MRC of the two coming signals.
On the uplink, the mobile switching center must resolve which base station is receive the stronger signal and hence better replica and decide in its favor ( selection diversity).

## Slide 27: Soft Handoff Extends CDMA Cell Coverage
With hard handoff, the required fade margin is given by

## Slide 28: Soft Handoff Extends CDMA Cell Coverage
With soft handoff (7 closest base stations only), the required fade margin is such that

## Slide 29: Soft Handoff Increases CDMA Uplink Capacity
With perfect power control, the received at base station 0, for a given user, is given by
  B is the number of base stations.
  M is the number of users per cell.
With a candidate set for soft handoff of cells, we have
The capacity can be approximated from the average as follows:
  A frequency reuse factor dependent on the number of cells in the candidate set for handoff.

## Slide 30: Soft Handoff Increases CDMA Uplink Capacity
The uplink capacity of DS-CDMA cellular systems with soft handoff becomes:
The frequency reuse factor, , for different values of and
Standard Deviation |  |  |  | 
0 | 1.44 | 1.44 | 1.44 | 1.44
2 | 1.48 | 1.43 | 1.43 | 1.43
4 | 1.67 | 1.47 | 1.45 | 1.45
6 | 2.13 | 1.56 | 1.49 | 1.49
8 | 3.38 | 1.77 | 1.57 | 1.55
10 | 7.17 | 2.28 | 1.75 | 1.66
12 | 20.8 | 3.62 | 2.17 | 1.91
0 | 1.44 | 1.44 | 1.44 | 1.44
2 | 1.48 | 1.43 | 1.43 | 1.43
4 | 1.67 | 1.47 | 1.45 | 1.45
6 | 2.13 | 1.56 | 1.49 | 1.49
8 | 3.38 | 1.77 | 1.57 | 1.55
10 | 7.17 | 2.28 | 1.75 | 1.66
12 | 20.8 | 3.62 | 2.17 | 1.91

## Slide 31: Example
Let us consider the IS-CDMA system with and
Compute the capacity for different values of as a function of the standard deviation Neglect the noise.

## Slide 32: Soft Handoff in IS-95
Soft handoff in IS-95 is based on Pilot set maintenance:
  Mobile continuously monitors pilot channel signals
  Active set, Candidate set, Neighbor set, remaining set.
Soft handoff in IS-95 is based on absolute values of received pilots.
  Load dependent active set updating.

## Slide 33: Soft Handoff in WCDMA
Soft handoff in WCDMA is based on relative handover thresholds between received pilots.
  Load independent active set updating.

## Slide 34: Soft Handoff in WCDMA
Pilot strength exceeds : Mobile station sends a Pilot Strength Measurement Message and transfers pilot to the candidate set.
Base station sends a Handover Direction Message.
Mobile station transfers pilot to the active set and sets a Handover Completion Message.
Pilot strength drops below : Mobile station starts the handover drop timer.
Handover drop timer expires: Mobile station sends a Pilot Strength Measurement Message.
Base station sends a Handover Direction Message.
Mobile station moves pilot from the active set to the neighbor set and sends a Handover Completion Message.

## Slide 35: Summary
DS-CDMA cellular networks are interference limited systems.
DS-CDMA cellular networks require very accurate power management especially in the uplink.
DS-CDMA cellular networks have the possibility to trade coverage for capacity and vice versa.
Assignment failures in DS-CDMA cellular networks are due to signal outage and not the lack of available channels.
Power control allows DS-CDMA to properly convey information while interfering with other users no more than necessary.
Uplink and downlink power control are necessary in DS-CDMA cellular systems.
Soft handoff extends DS-CDMA cell coverage.
Soft handoff increases uplink capacity (base station diversity).
Soft handoff improves signal quality for mobiles in bad positions but causes slight loss in downlink capacity.