## Slide 1: Chapter 8 Association and Handover
Email list: https://groups.google.com/forum/#!forum/mobile-miao

## Slide 2
Association is a part of RRM problem
To each active terminal, we need to assign
Transmit power
Waveform
Base stations
in order to maximize system utility
Association on the move: handover

## Slide 3
Mobility management
While inactive
Tracking location of terminal and waking it up when necessary
  Location area updates
  Paging
While connection in progress
Handover (or handoff)
It refers to timely selection (transition) of base stations based on signal quality measurements

## Slide 4
Handover types
Networks involved
Horizontal handover
  Within a single network of homogeneous radio access technologiy
Vertical handover (or network selection)
Simultaneous connections
Hard handover
  Only one base station serving at a time
Soft handover
  Multiple base stations can simultaneously serve a mobile terminal

## Slide 5
Handover phases
Handover measurement & decision
Decides when & where to handover
Handover resource management
Radio resource available in receiving cell?
Handover execution
Reliable handover signaling (handshaking) procedure

## Slide 6
Handover decision
When and where to handover?
Signal fluctuates a lot in practical environments

## Slide 7
Performance metric
We will consider two metrics
Handover failure probability
  A measure of how often a handover fails
  The probability that signal quality is below the required value for more than a given time interval
Handover frequency (or rate)
  A measure indicating how frequently handover decisions are made
Easy to notice a tradeoff between handover frequency and failure probability

## Slide 8
Example 8.1 (1/2)
Three handover decision algorithms are to be studied:
Algorithm I: instantaneous decision
  AP with the highest signal level is chosen at any sample point
Algorithm II: moving average
  Average over the last 10 samples determines the serving AP
Algorithm III: expected value
  In fact, only one handover at the mid-point

## Slide 9
Example 8.1 (2/2)
Illustration of a realization

## Slide 10
Handover decision criteria
Received signal strengh (RSS)
Detecting cell boundaries
Designed for (low capacity) macro-cellular systems (noise-limited)
Signal to interference ratio (SIR)
Efficient in micro-cellular environments (interference-limited)

## Slide 11
Example 8.2
Limitation of RSS-based handover in microcells
Rapid RSS level changes at street corners
RSS is not a good indicator of connection quality in microcells

## Slide 12
Practical handover algorithm (Example 8.3)
Typical hard handover decision in LTE system
Hysteresis & time-to-trigger
Note that it is the very basic handover mode in LTE

## Slide 13
Handover resource management
Resource reservation for handover
Are there resources available in the receiving cell?
Protection of ongoing services is much more important than accepting new services
  Particularly for voice services
Its significance depends on the delay tolerance of the service
  In the voice era, it was one of the most important RRM issues
  Less important for data services

## Slide 14
Example 8.4 (delay-sensitive service)
State-transition diagram can be drawn under Markovian assumption
Birth-death process
Solve balance equations

## Slide 15
Example 8.4: result
New call blocking and handover dropping probabilities

## Slide 16
Example 8.5 (delay-tolerant service)
What’s different from the previous example?

## Slide 17
Example 8.5: result
New call blocking and handover dropping probabilities

## Slide 18
Handover execution
It is mostly about signaling procedure
The system and mobile should reach agreement on
  Which AP?
  Which waveform? (frequency, timeslot, code, etc)
  Authentication
The signaling should be fast & reliable
  Handover is performed under critical SIR conditions

## Slide 19
Soft handover
Simultaneous connections to multiple APs
Enhanced coverage due to diversity gain
Possible capacity increase due to reduced inter-cell interference
Possible capacity decrease due to duplicated resource consumption

## Slide 20
Soft handover in IS-95 system
Soft handover in IS-95 is based on Pilot set maintenance
Handover decision is based on absolute values of received pilots
  Load dependent active set updating

## Slide 21
Soft handover in WCDMA system
Soft handover in WCDMA is based on relative handover thresholds between received pilots
  Load independent active set updating

## Slide 22
Fade margin improvement by soft handover
Soft handover reduces outage probability at the cell edge

## Slide 23
Effect of soft handover on capacity

## Slide 24
Association: load balancing
Motivation for load balancing
  Traffic load fluctuates a lot over time
  My neighbor cell may have much lighter load at the moment
  Why not switching edge users to the neighbor cell?
Cell breathing
  Adjust output power of cell-specific reference signal

## Slide 25
Example 8.7
For a highway with 8 km length,
Traffic intensity follows a location-dependent Poisson distribution with intensity
Load balancing handover point can be determined by

## Slide 26
Association in heterogeneous network
Mismatch occurs in the uplink/downlink association
Cell range extension (CRE): an artificial bias to small cells