## Slide 1: Chapter 11 Introduction to Wireless Infrastructure Economics
Email list: https://groups.google.com/forum/#!forum/mobile-miao

## Slide 2: What is Wireless Infrastructure Economics?
Costs, Prices, Revenues, Profits
Money related to capabilities and resources
Distribution of costs, cost structure models, and analysis
Trade-offs between
Costs, Prices, Revenues, Profits
Money related to capabilities and resources

## Slide 3: TODAY, two main parts
First part is about overall picture, problems and challenges
Second part is about network dimensioning, trade-offs, relationships and different solutions
Cost
Capacity
Spectrum

## Slide 4: TODAY, the first part
First part is about overall picture, problems and challenges
Where are the costs?
  In the fixed/Broadband networks?
  In the Mobile Networks?
  In the Radio Access Network of the Mobile networks?
  In the Core Network of the Mobile Networks?
  For a Mobile Operator in general?
Where are the revenues? What kind of services?
  Voice
  Messages
  Data
  Music
  Other services

## Slide 5: The “last mile” problem: Most investments in Access Networks
Backbone network shared by many
Access network individual
Example: 2 cities, 50000 user each
Access network: 100 m/user
Trunk network: 1 m/user
(=100km/100000 users)

## Slide 6: Cellular networks in rural areas
Large coverage areas per base station
Few base stations per area unit

## Slide 7: Range limitations
Typical ranges (NLOS):
  10 kbit/s (GSM) 25+ km
  500 kbit/s (EDGE) 5-10 km
  2 Mbit/s (UMTS) 2-3 km
  10 Mbit/s (HSPA) 500 m
  100 Mbit/s (LTE/WLAN) 50-150 m
Coverage limited system

## Slide 8: Cellular network in urban areas
Many base stations per area unit

## Slide 9: Cost structure of radio access networks
It is not only costs for the base station equipment (the radio) but also for the transmission & sites.
Chart: 
| Macro | Micro | Pico | WLAN/Femto
Radio equipment, O&M, Power | 0.37 | 0.17 | 0.08 | 0.03
Site buildout, installation + lease | 0.43 | 0.2 | 0.015 | 0.005
Backhaul transmission | 0.2 | 0.2 | 0.09 | 0.03
From
Klas Johansson
PhD thesis 2007

## Slide 10: The infrastructure cost for capacity limited systems
Spectrum limitation
  is available bandwidth
  is spectral reuse efficiency

## Slide 11: Spectrum, capacity and cost
High bandwidth means high capacity per site, i.e., less number of base station sites

## Slide 12: TODAY, the first part
First part is about overall picture, problems and challenges
Where are the costs?
  In the fixed/Broadband networks?
  In the Mobile Networks?
  In the Radio Access Network of the Mobile networks?
  In the Core Network of the Mobile Networks?
  For a Mobile Operator in general?
Where are the revenues? What kind of services?
  Voice
  Messages
  Data
  Music
  Other services

## Slide 13: One motivation for our research: New services require new solutions
Years
Revenues
Voice services
Mobile Broadband
New services

## Slide 14: One motivation for our research: New services require new solutions
Years
Revenues
Voice services
Mobile Broadband
New services

## Slide 15: Revenues for mobile voice services in Sweden 2000-2008
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008
Telia Sonera (EUR) | 36.5 | 31 | 28.5 | 27 | 25 | 23 | 22 | 21 | 19.75
ARPU Sweden (EUR) | 31.75 | 29 | 26.75 | 24 | 22 | 21.25 | 20.75 | 21 | 19
From Mölleryd, Markendahl, Werding and Mäkitalo
conference paper presented at CTTE 2010, May 2010

## Slide 17: The revenue gap “decoupling of traffic and revenues”
Flat rate tariffs create large increase of data trafficMany GB per user per month
  Data traffic up >100% per year
  Revenues do not follow
Traffic
Network cost
Revenues
Voice is dominating
Data is dominating
Time
Amount of
traffic
revenues
costs
?
?

## Slide 18: Traffic, prices and revenues
Chart: revenues
| SMS + MMS | Mobile data | Voice
 | 0.11 | 0.08 | 0.81
Chart: Traffic
| Voice | Mobile data
 | 0.25 | 0.75
Traffic and revenue for different services at the Swedish market Q4 2008
EUR per MB | 2007 | 2008
Voice | 1.46 | 1.36
SMS | 439.5 | 351.6
Mobile data (laptop) | 0.014 | 0.011
Estimated price per Mbyte for voice, SMS and data for one Swedish operator

## Slide 19: One big data challenge
=
Corresponding data consumption
1 kr
23 000 kr
5 min clip
115 000
Revenues

## Slide 20: Traffic, prices and revenues
Amount of voice data 10 - 20 MB per month
Amount of mobile broadband data 1 - 20 GB per month
  The of mobile broadband bits are 100 - 1000 more than the number of voice bits.
But we pay more or less the same, i.e., the price per data bit is 100 - 1000 times lower => the cost per bit must be 100 - 1000 lower.

## Slide 22: One motivation for our research: New services require new solutions
Years
Revenues
Voice services
Mobile Broadband
New services

## Slide 23: “New” services

## Slide 24: “New” services

## Slide 26: Operator challenges – business related
Traffic
Revenues
Revenue gap
MBB Profitability
Voice
Chart: 
| Voice | Data
 | 1 | 5
Chart: 
 | 5 | 1
Investments
5x
5x
Network Investments
Revenues
Data
Voice
Voice services
Mobile broadband
New services ??
Revenue mix
The business landscape

## Slide 27: TODAY, the second part
Second part is about relationships and different solutions

## Slide 28: Operator challenges – network related
Scalability
Data rate depends on range
Spectrum allocation
Chart: 
| Macro | Micro | Pico | WLAN/Femto
Radio equipment, O&M, Power | 0.37 | 0.17 | 0.08 | 0.03
Site buildout, installation + lease | 0.43 | 0.2 | 0.015 | 0.005
Backhaul transmission | 0.2 | 0.2 | 0.09 | 0.03
Cost structure

## Slide 29: GSM Coverage
Tele2
Telenor
Telia
~70% covered area
~65% covered area
~90% covered area

## Slide 30: Coverage maps – Telia webpage

## Slide 31
From Ericsson:
Capital markets day, May 2008

## Slide 32
From Ericsson:
Capital markets day, May 2009

## Slide 33: To improve the spectral efficiency - i.e. more bits/second per Hz of spectrum
Peak data rate ~10 - 20 bps per Hz
Cell border rate < 0,10 bps per Hz
Average data rate ~1 -2 bps per Hz
Distance from base station
Average
Cell border

## Slide 34: Bit rate and range – Bandwidth and Radio Access Technology (RAT)
Macro BS
For twice the amount
of Spectrum (2 X MHz)
For a given amount of Spectrum
( e.g. X MHz)

## Slide 35: “Offered” bit rate vs coverage & load
”promised” data rate
at ”low” level
”promised” data rate
at ”higher” level

## Slide 36: Marketing by mobile operators

## Slide 37: Spectral efficiency
Peak data rate
~10 - 20 bps per Hz
Average data rate
~1 -2 bps per Hz
Cell border rate
< 0,10 bps per Hz

## Slide 38: Spectral efficiency and cylinder model

## Slide 39: Spectral efficiency and cylinder model

## Slide 40
From Ericsson:
Capital markets day, May 2008

## Slide 41: Cellular systems – low data rates
Cellular systems - low data rates

## Slide 42: Cellular systems – high data rates, the same sites
Cellular systems - high data rate, the same sites

## Slide 43: Zander formula
  the number of access points (base stations)
  the number of users
  the average data rate of users
  the service area covered (volume indoors)
  a function of the required Quality of Service.

## Slide 44: Amount of spectrum and number of sites
Chart: 
| 5 | 10 | 15 | 20 | 40
Spectral eff = 1.70 (LTE type) | 39 | 19.5 | 13 | 10 | 5
Spectral eff = 0.70 (HSPA type) | 95 | 47 | 31 | 23 | 11
Used spectrum (MHz)
Number of sites
Example: New Kista area, 10 000 office workers

## Slide 45: Short exercise – work in 4 groups
How many base station sites need to be deployed in the following cases?
  Operator A, LTE in the 2.6 GHz
  Operator B, HSPA in the 2.6 GHz
  Operator C + D, LTE in the 2.6 GHz band and share network
  Operator E, LTE using unlicensed 1800 MHz band.
  You are allowed to ask me one question per group

## Slide 46: Number of base station sites
Chart: 
| 5 | 10 | 15 | 20 | 40
Spectral eff = 1.70 (LTE type) | 39 | 19.5 | 13 | 10 | 5
Spectral eff = 0.70 (HSPA type) | 95 | 47 | 31 | 23 | 11
Used spectrum (MHz)
Number of sites
Cases for different
Swedish operators
using 2.6 GHz band

## Slide 47: Number of base station sites
Chart: 
| 5 | 10 | 15 | 20 | 40
Spectral eff = 1.70 (LTE type) | 39 | 19.5 | 13 | 10 | 5
Spectral eff = 0.70 (HSPA type) | 95 | 47 | 31 | 23 | 11
Used spectrum (MHz)
Number of sites
Brazil operators
UK operators

## Slide 48: Cost structure of radio access networks
It is not only costs for the base station equipment (the radio) but also for the transmission & sites.
Chart: 
| Macro | Micro | Pico | WLAN/Femto
Radio equipment, O&M, Power | 0.37 | 0.17 | 0.08 | 0.03
Site buildout, installation + lease | 0.43 | 0.2 | 0.015 | 0.005
Backhaul transmission | 0.2 | 0.2 | 0.09 | 0.03
From
Klas Johansson
PhD thesis 2007

## Slide 49: Cost structure, bandwidth and capacity
Radio
Site and Trans
Capacity of
radio base
station site
~ 10 Mbps
HSPA year 2008
5 MHz
~ 20 k€
~ 100 k€

## Slide 50: Cost structure, bandwidth and capacity
Radio
Site and Trans
Total cost
for new site
~ 200k€
Capacity of
radio base
station site
~ 40 Mbps
HSPA year 2008
20 MHz

## Slide 51: Cost of radio equipment is decreasing rapidly
512 MSEK (50 MEuro)
~6 KEuro per base station
~ 750 MSEK

## Slide 52: Cost structure, bandwidth and capacity
Radio
Site and Trans
Total cost
for new site
~ 200k€
Capacity of
radio base
station site
~ 40 Mbps
HSPA year 2008
20 MHz

## Slide 53: Cost structure, bandwidth and capacity
Trans
Radio
Site and Trans
Radio
Capacity of
radio base
station site
~ 100 Mbps
Capacity of
radio base
station site
~ 100 Mbps
Cost for
upgrading
an existing
site ~ 30k€
Total cost
for new site
~ 110k€
Assuming 3 sector site
20 MHz of bandwidth
and cell average
spectral efficiency
0,7 bps per Hz (HSPA)
1,7 bps per Hz (LTE)
Radio
Site and Trans
Total cost
for new site
~ 200k€
Capacity of
radio base
station site
~ 40 Mbps
HSPA year 2008
20 MHz
LTE year 2010
20 MHz
LTE year 2010
20 MHz

## Slide 54: Base station site location in urban areas
from PTS “Transmitter map” web page, December 2009
Kista Industry Area
Downtown Stockholm

## Slide 55: Examples of Base station densities (Urban areas in Sweden)
Name and type of area | Total density of sites | Typical densities for operators
Residential area in Uppsala | ~6 per km2 | 1 - 3 per km2
Residential area Akalla | ~14 per km2 | 3 - 5 per km2
Central part of Uppsala | ~20 per km2 | 3 - 8 per km2
Industry area Kista | ~50 per km2 | 7 - 20 per km2
Central part of Stockholm | ~130 per km2 | 20 - 40 per km2

## Slide 56: The capacity needs to be increased at least 1000 times in the coming years
Contributions
  One enabler is “more spectrum”
  Another contribution comes from “better technology” (improved spectral efficiency)
  A third contribution is from “denser network”
3 minute discussion – discuss in groups
  How do you think the different aspects contribute?

## Slide 57: Cooper’s law
“the number of conversations” than can theoretically be conducted over a given area in all of the useful spectrum is doubled every two-and-a-half years
  The improvement in spectrum utilization has been over a trillion times in the last 90 years and a million times in the last 45 years.
“Of the million times improvement in the last 45 years,
  25 times were the result of being able to user more spectrum.
  5 times can be attributed to the ability to divide the radio spectrum into narrower slices
  Modulation techniques like FM, SSB, time division multiplexing, another 5 times or so.
  The remaining sixteen hundred times improvement was the result of confining the area used for individual conversations to smaller areas, what we call spectrum reuse.”

## Slide 58: Operator challenges – network related
Scalability
Data rate depends on range
Spectrum allocation
Chart: 
| Macro | Micro | Pico | WLAN/Femto
Radio equipment, O&M, Power | 0.37 | 0.17 | 0.08 | 0.03
Site buildout, installation + lease | 0.43 | 0.2 | 0.015 | 0.005
Backhaul transmission | 0.2 | 0.2 | 0.09 | 0.03
Cost structure