## Slide 1: Chapter 6 Transmitter Power Control
Email list: https://groups.google.com/forum/#!forum/mobile-miao

## Slide 2: Radio Resource Allocation problem
To each active terminal, assign
Base station
Waveform (“Channel”)
Transmitter power
such that Link Quality & power constraints are satisfied for as many terminals as possible

## Slide 3: Why Transmitter Power Control?
Reduce terminal power consumption
Mitigate near/far effects
  Efficient handling of mobility
Reduce interference/Improve quality
Radio resource management tool
  Low complexity/Local Measurement
  Fast (Real-time)

## Slide 4: Interference Models
Arbitrary collection of wireless links
Propagation conditions on link (i,j) characterized by Gji, the instantaneous link gain
  Prx, j= GjiPtx, i
Link gain matrix (BXM)

## Slide 5: Performance Measure
Q transmitters assigned to a channel co.
Effective Signal-to- Interference(+Noise) Ratio (“C/I”)
The transmitter i is said to be supported if
Outage probability

## Slide 6: Special Case: Cellular Systems, Orthogonal Signals
Per-channel analysis
At most one mobile per cell active
Simplify indices
Separate uplink/downlink analysis

## Slide 7: Conditions of Availability
The minimal power that the transmitter i should use to achieve the target SIR, assuming the other transmitters' powers are fixed.

## Slide 8: Two User Case

## Slide 9: Optimum Power Control
What can be done in terms of system capacity by controlling the transmitter power?

## Slide 10: Objective
How to maximize the number of supported terminals by selecting transmission powers appropriately?
  Capacity maximization
The goal of power control
  Find a power vector such that the number of supported users is maximized

## Slide 11: Problem Formulation-Vector Notation
I: identity matrix.

## Slide 12: Achievability
has a non-negative power solution

## Slide 13: Achievable Conditions
Proof: has non-negative solutions.
  If , exists and above 0.
  Therefore
  If , I-H becomes a singular matrix and only the case is valid with multiple solutions.

## Slide 14: Achievable Conditions

## Slide 15: Centralized Power Control
A central scheduler controls the power of all transmitters

## Slide 16: SIR balancing
Maximizes the minimum SIR in all links.
  Achieved by making every transmitter's received SIR balanced (equalized) while keeping the balanced SIR as high as possible.
Introduce matrix A:
What is the maximum achievable?

## Slide 17: Maximum Achievable SIR: Zander’s Proposition
Proof: Proposition 6.1,
Zander’s Proposition: The largest for which there exists a non-negative power vector such that all the active links can be supported is given by [J. Zander, 1992]
where is the dominant (largest) eigenvalue of the matrix A.

## Slide 18: Maximum Achievable SIR-Noiseless Case
Proposition: The inequality has solutions if and only if
The optimum power vector P* is the eigenvector corresponding to the eigenvalue .

## Slide 19: Example: 2 links
Notes: Shadow is the part not allowed.

## Slide 20: Example: 2 links

## Slide 21: Power Constraints
Maximum power constraint

## Slide 22: Transmitter Removal
With SIR balancing
  If the maximum achievable SIR is larger than the target SIR, all links have acceptable performance
  If the maximum achievable SIR is smaller than the target SIR
    Disastrous!
    All links useless!
    More connections than can be supported by the channels!

## Slide 23: Optimum Power Control
Theorem 2: The power vector P that minimizes the outage probability has the following property
where P* is a C/I balancing power vector
“If you cannot communicate, the least you can do is to shut up”
-Tom Lehrer

## Slide 24: Stepwise Removal Algorithm
Algorithm:
  1) C/I balance system
  2) If all links are supported - stop
    else Remove “as few links as possible” and repeat 1)
  Remove: Set Pk = 0

## Slide 25: SIR Balancing and Transmitter Removal

## Slide 26: Distributed Power Control
How to control power without the knowledge of G?
Power control based on link measurements only

## Slide 27: Distributed Power Control
Power control based on local (SIR) measurements only
where is the power control algorithm implemented at transmitter
Example: DPC

## Slide 28: Convergence of DPC
Define the error vector to be
Feasible assumption: SIR achievable and receiver noise positive.
DPC will converge to P* whenever the given target is achievable.

## Slide 29: Yate’s Sufficient Conditions of Convergence
Yate’s Proposition 6.4 (Theorem 2 in [R. Yates, 1995]) If the system
has a unique non-negative solution P∗, a distributed power
control algorithm based on a standard interference function will
have a sequence of power vectors that converges to the solution
of , starting with any non-negative power vector.
DPC: standard interference function.
Interference function
Notes: Convergence with good power control functions.

## Slide 30: Convergence in Sufficiently Weak Interference Channels: Miao’s Convergence Theorem
Miao’s Convergence Theorem (Theorem 4 [G. W. Miao et al., 2011]):
If for any transmitter i,
where sup is the supremum on all non-negative cumulative interference Ii , the distributed power control algorithm will converge to a unique power vector P∗. If the interference function is linear in the cumulative interference Ii , the above sufficient condition is equivalent to
Total sum of squares of interference channel gains on the left directly determines whether a distributed power control algorithm can converge to a unique optimal solution or not.
: Threshold, independent of any ,
solely determined by
Notes: Convergence with good network conditions.

## Slide 31: Convergence Speed of DPC
The values of the gain matrix as well as the size of the matrix are changing continuously
  mobile movement and propagation condition change.
A good power control algorithm should quickly and distributively converge to the state where the system supports as many users as possible.

## Slide 32: Distributed Constrained Power Control
Transmitters have maximum power limits:
DCPC:
A general scheme: different users have different SIR targets

## Slide 33: Performance of DCPC

## Slide 34: Power Control for Wireless Data
How to handle power control when different users have respective data rate requirements?

## Slide 35: Achievable Region
Rate adaptation mechanism
where f is a monotonically increasing and strictly concave modem (waveform set/coding) dependent function.
The SIR of user i is:

## Slide 36: Two Data Rate Examples
Case A: corresponds to case where the available bandwidth is unlimited and the same waveform is scaled to achieve a constant Eb/N0 to provide a constant link quality in terms of bit error probability,
Case B: the Shannon limit for a band-limited channel.

## Slide 37: Achievable Region
A rate vector is instantaneously achievable if there exists a positive power vector
A rate vector is achievable in the average sense if
where all Rk are instantaneously achievable rate vectors

## Slide 38: Optimization Problem
Each link requires a minimum data rate
Assume that any excess data rate provided to the user is potentially consumed
Non-real time traffic,

## Slide 39: Two-User Case
where

## Slide 40: Rate Region
Further apply the rate-SIR relationship
Non-convex rate region
Maximum power
Minimum rate region
Notes: Relative maximal powers 5, 10 and 15.
the achievable instantaneous rate regions (as indicated by the region below the solid lines) are not
convex, but the average sense rate regions (as indicated by dotted lines) are.
The figure also illustrates a minimum rate requirement ri > ri,min (i.e.
within the rectangle in the upper right corner). In this example, it can be seen
that for the maximal power 5, there is no rate pair meeting the constraints, neither
instantaneously nor in the average sense. For the maximal power 10 the
rate requirements can be achieved in the average sense but not instantaneously.

## Slide 41: Rate Region
Further apply the rate-SIR relationship
Concave in the low-power region
  Simultaneous transmission to maximize
  the sum rate
  Convex in the high-power region
  Time multiplex to maximize the sum rate
Maximum power

## Slide 42: Distributed Power Control for Wireless Data

## Slide 43: Problem Modeling
Maximize overall network throughput

## Slide 44: Difficulty in Centralized Power Control
Non-concave and many local maxima may exist depending on channel conditions
Two user case

## Slide 45: Two User Case
Interference limited region
MAC and scheduling protocols and algorithms are designed to coordinate the orthogonal transmissions of all users in these interference-limited systems

## Slide 46: Two User Case
Noise limited region
Non-orthogonal schemes have advantages and power control algorithms are needed to determine the transmission power values

## Slide 47: Generally…
A centralized algorithm requires complete channel knowledge, including the interference channels.
Non-concave
Exponential complexity to search for the global optimum

## Slide 48: Distributed Power Control
Each transmitter decides its power level based on local observations
Local measurement at time n.

## Slide 49: For Real-Time Traffic
Allocate a power value such that the SIR target is just met in iteration n+1 based on the observation in iteration n
A generalization of the DPC algorithm

## Slide 50: For Non-Real-Time Traffic
Can we control the power such that:
All users will simply use the highest power possible
The network performance might be poor because of excessive interferences.

## Slide 51: Power Control with Pricing
The pricing mechanism introduces a cost for each user to use a certain amount of power
  Regulates the aggressive power control behavior to reduce interferences.

## Slide 52: Control Effect of Utility Functions

## Slide 53: Convergence
In general hard to analyze the convergence
The number of equilibria is determined by how strong interference channel gains and signal channel gains are
  Different equilibria may have different performance
According to Miao’s Convergence Theorem, there is a unique equilibrium when for each transmitter,

## Slide 54: Summary
Reduce terminal power consumption (energy efficiency)
Reduce interference/Improve quality
Radio resource management tool
Low complexity/Local Measurement
Fast (real-time)
Improve overall network performance