## Slide 1: Supplement e08.1: A look at a severe winter event using different sensors and products

## Slide 2: Context
In the book, an example of how to use scanning radars to obtain valuable information for forecasting widespread systems was provided.
In this example, the focus will instead be on the complementarity of information coming from different sensors/products.
The event studied is a winter storm arriving from the SW that affected the Montreal area many years ago.
GOES visible imagery
1999/03/03 16:02
Image courtesy of NASA
Montreal
250 km

## Slide 3: Approaching snow: A scanning radar view
On scanning radars, the snow appears further ahead at high levels than at lower levels.
This is best seen on vertical sections: snow is above the radar, but reaches the surface 40+ km away.
A
B
Ground clutter (ignore)
Clutter
A
B

## Slide 4: Approaching snow: Vertically pointing radar (VPR) view
From a collocated VPR, we see that this is due to turbulent sublimation of snow at low levels, near-surface winds being relatively dry from the SE.

## Slide 5: Reflectivity CAPPI animation: Snow changing to (freezing) rain
Following several hours of smooth-looking snow, precipitation echoes become more textured (and slightly convective).
Snow then changes to rain around 23:00.

## Slide 6: Vertically pointing radar sequence: Snow changing to (freezing) rain
On the VPR, different signatures betray the action of dynamical and microphysical processes occurring within the storm: K-H waves riding on the warm front, the increase in vertical motions, the change to rain…

## Slide 7: Doppler velocity PPI animation: The evolving wind profile
In parallel, sequences of Doppler velocity PPIs illustrate how the wind changes with time.
Here, winds are strengthening overall, with surface winds switching from the SE to ENE.

## Slide 8: Doppler velocity PPI: Turbulent wind signatures
Only by paying considerable attention to detail can one spot the Doppler signature of the strong K-H waves on the PPI.

## Slide 9: Studying the evolving wind profile: The VAD time series perspective
Later, the echo movement shifted from a SW-NE movement to a SSE-NNW movement. This was associated with a change in the upper-level flow observed on this time series of VAD-derived winds.

## Slide 10: Exercise: Using the VAD time series to reconstruct pressure patterns
The sequence of wind profiles obtained can actually be used to reconstruct the pressure or height patterns that caused those winds. Here, I have done it with 5.5 km (50 kPa) winds, and they suggest a deep trough; remember that “early” profiles are to the east, the storm coming from the west. Try it at other levels.

## Slide 11: On the next day…
Then, on 4 March 1999 in the afternoon, the center of the low passes over the radar coverage.
GOES visible imagery
1999/03/04 18:02
Image courtesy of NASA
Montreal
250 km

## Slide 12: Reflectivity CAPPI animation: Circulation/precipitation changes
As the center of the low pressure system passes near the Montreal radar, the direction of echo movement changes from the south to the west.
The winds at all levels also change.

## Slide 13: Vertically pointing radar sequence: Shower, then gradually back to snow
On the VPR, after a shower, the cold rain stops after the passage of the low and precipitation changes to snow. In the cold sector of the low, surface winds increase, leading to increasing turbulence at low levels.

## Slide 14: Completing the evolving wind profile from the VADs
The wind profile evolution for the whole event is now shown. The time of front passage can be clearly seen.

## Slide 15: Completing the evolving wind profile from the VADs
Q: Based on this sequence of winds alone, would you stay that the storm was mature or occluded?