## Slide 1: Digital Design: A Systems Approach Lecture 5: Combinational Review

## Slide 2: Review
Lecture 1 – Digital abstraction
Lecture 2 – Combinational logic design
Lecture 3 – Combinational building blocks
Lecture 4 – Numbers and arithmetic
Lecture 5 – Quiz 1 Review

## Slide 3: Digital Signals
Noise margins
  VOL = 0.1V, VOH = 0.9V, VIL = 0.5V, VIH = 0.7V
  What are the high and low noise margins?
  How much variation in power supply (with GNDs equal) can be tolerated?
  How would you adjust these settings?
    Assume VIH-VIL >= 0.2V.

## Slide 4: Digital Signals
Representation
  A single signal can represent a _________
  Represent a set with a ________
    Can be either _____ or _______
Example
  Represent a chessboard

## Slide 5: Boolean Algebra
Simplify the expressions
  f = (x y  z)  (x  y)  (x’  y  z)
  f = (x y  z)  (x  y’)  (x  z’)

## Slide 6: Duals and Complements
Given a function f(a,b,c)
Its complement is f’(a,b,c)
Its dual is f’(a’,b’,c’)
Example - f = AND, complement is _____, dual is _____
Example - f = 3-bit prime number function
  f is one at 1,2,3,5,7
  f’ is one at _______
  fD is one at _______

## Slide 7: Manual Combinational Design
Start with a specification
Write K-map
Find all prime implicants
Pick a minimal set of prime implicants that covers the function
Example,
  4-bit Fibonacci circuit

## Slide 8
Consider a 4-input Fibonacci circuit
True when input = 1,2,3,5,8, or 13
Implicants (dcba)
1000 x101 0x01 00x1 001x
Three are essential
Combinational Logic Design – Karnaugh maps are one method

## Slide 10
What function does this realize?

## Slide 11
Starting at input, write equations (or k-maps) for signals

## Slide 14
What function does this realize?

## Slide 16
1

## Slide 17: Building Block Combinational Logic
Raise the abstraction layer of design using building blocks rather than directly with K-maps
  Assemble combinational circuits from pre-defined building blocks
  Decoder – converts codes (e.g., binary to one-hot)
  Encoder – encodes one-hot to binary
  Multiplexer – select an input (one-hot select)
  Arbiter – pick first true bit
  Comparators – equality and magnitude
  ROMs
Divide and conquer to build large units from small units
  Decoder, encoder, multiplexer
Logic with multiplexers or decoders (basis of LookUp Table in FGPAs)
Bit-slice coding style

## Slide 18
Maximum unit
How to change this to a minimum unit?
Change this to less than
min
How to determine the middle of three numbers?
Min
Min
A
B
C
Max
middle
Min
Max

## Slide 19: Example building block problems
Circuit accepts 4 4-bit one-hot numbers, output the number with a one in the most significant position. Circuit accepts 4 4-bit numbers (of any kind) output the number with the smallest number of 1s

## Slide 20: Numbers and Arithmetic
Binary numbers – bit i weighted 2i
2’s complement – MSB weighted -2i
  -x represented by 2n-1 – x (mod 2n-1)
  makes subtraction easy
  To negate, invert and add one
    The add one can use the carry in of the least significant bit
Multiplication accomplished by adding shifted versions of the multiplier
  The shift is an implicit multiply by a power of 2
  Example, 7 x 5
1 1 1 x 1 0 1
1 1 1 0 0 0
1 1 1 1 0 0 0 1 1
Number representations do not have infinite ability to express all possible values
accuracy and resolution help quantify the error
Fixed versus floating point

## Slide 21: Examples
Design a circuit that computes -2a given input a
  Shift a left 1-bit, (2x) and negate – complement and add 1
Convert 35.6 to 8.3 floating point
  First convert to binary 100101.10011…
  Then take 8 MSBs as mantissa .10010110
  Need to shift binary point six places .10010110e110
  With an implied leading 1 1.00101100e101

## Slide 22: Next Lectures – Sequential Logic