## Slide 1: Digital Design: A Systems Approach Lecture 1: The Digital Abstraction Combinational Logic Verilog

## Slide 2: Readings
Lecture 1: Chapters 1, 3, 7.1, Appendix A
L2: Chapters 6, 7 for L2

## Slide 3: Today
The Digital Abstraction
  Representation
  Noise
Combinational Logic
  Output function of current input
  Acyclic composition
  Representations - description, truth table, equation
  Boolean algebra
Verilog

## Slide 4: Moore’s Law

## Slide 5: The Digital Abstraction

## Slide 6: Voltages Ranges of Binary Signals
0
1
?
Voltage
Damage
Damage
Vmin
V0
VIL
VIH
V1
Vmax
-0.3V
0.0V
0.7V
1.7V
2.5V
2.8V
2.5V LVCMOS Logic

## Slide 7: Representing Information with Digital Signals
Binary Information
Light On/Off: 1/0
Element of a set
000 | White
001 | Red
010 | Blue
011 | Yellow
100 | Purple
101 | Orange
110 | Green
111 | Black
Continuous Quantities
000 | 68
001 | 70
010 | 72
011 | 74
100 | 76
101 | 78
110 | 80
111 | 82
0000000 | 68
0000001 | 70
0000011 | 72
0000111 | 74
0001111 | 76
0011111 | 78
0111111 | 80
1111111 | 82

## Slide 8: How would you represent
A Date ?
  Days since Jan 1 0000 (20 bits)
  Month, day, year (4 + 5 + 12 bits)
  Month, day, year, day of week (4 + 5 + 12 + 3 bits)
    This representation is _________
A playing card ?
  Number in deck (6 bits)
  Suit, Number (2 + 4 bits)
  Decoded suit, decoded number (4 + 13 bits)
A 5-card hand ?
Pick a representation based on operations required

## Slide 9: Example
Pick representation of colors to support the operation of subtractive color mixing (e.g., red + blue = purple)
  No colors - white
  Primary colors – red, blue, yellow
  Derived colors – orange, purple, green, black
How would you represent this?

## Slide 10: Effect of Noise on Analog & Digital Signals
V
Input
+
e
Noise
V+
e
f
f(V+
e)
Output
Noise added to Input
Error at Output
Analog Signals
Digital Signals
V
1
Input
+
e
Noise
V
1
+
e
f
f(V
1
)
Output
Noise added to Input < Noise Margin
Correct Value at Output

## Slide 11: Input & Output Voltage Ranges

## Slide 12: Restoration of Digital Signals
Noise
+
e
1
Noise Accumulation
V
a
+
e
1
Noise
+
e
2
V
a
+
e
1
+e
2
V
a
Noise
+
e
3
Noise
+
e
1
V
a
+
e
1
Noise
+
e
2
V
a
+
e
2
V
a
V
a
Noise
+
e
3
V
a
+
e
3
V
a
V
a
Signal Restoration
V
a
+
e
1
+e
2
+e
3

## Slide 13: DC Transfer Curve for a Logic Module

## Slide 14: Combinational Logic

## Slide 15: Combinational Logic Circuit
Output is a function of current input
Example – digital thermostat

## Slide 16: Sequential logic circuit
Includes state (memory, storage)
Makes output a function of history as well as current inputs
Synchronous sequential logic uses a clock
Example, calendar circuit

## Slide 17: Combinational logic is memoryless
o = f(i)

## Slide 18: Can compose digital circuits

## Slide 19: Closure
Combinational logic circuits are closed under acyclic composition.
CL1
CL2
CL12

## Slide 21
Combinational
NOT
Combinatorial

## Slide 22: Combinational not Combinatorial
Combinational
Combinatorial
mathematics of counting
combinational logic circuit
combines inputs to generate
an output

## Slide 23: Several ways to describe a combinational logic function
Example – Majority Circuit
English Language Description
  Outputs 1 if more inputs are 1 than are 0
Logic equation
  q = (a b)  (a  c)  (b  c)
Truth table
abc | q
000 | 0
001 | 0
010 | 0
011 | 1
100 | 0
101 | 1
110 | 1
111 | 1

## Slide 24: Boolean Algebra
Boolean Algebra:
  algebra over 2 elements: {0,1}
  3 operators: AND (), OR (), NOT ()
AND Operation:
  a  b = 1 iff a=1 and b=1
OR Operation:
  a  b = 1 if a=1 or b=1
NOT Operation:
  a = 1 iff a=0
a | b | a&b | a¦b
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 1
a | ~a
0 | 1

## Slide 25: Note on Notation
For AND logic function:
  use  or &
  don’t use x nor .
For OR logic function:
  use  or |
  don’t use +

## Slide 26: Axioms of Boolean Algebra
Axioms: a set of mathematical statements that we assert to be true.
Identity:
  0  x = 0
  1  x = 1
Idempotence:
  1  x = x
  0  x = x
Negation:
  0 = 1
  1 = 0

## Slide 27: Useful Boolean Properties (all can be derived from the axioms)
Communicative | x  y = y  x | x  y = y  x
Associative | x  (y  z) = (x  y)  z | x  (y  z) = (x  y)  z
Distributive | x  (y  z) = (x  y)  (x  z) | x  (y  z) = (x  y)  (x  z)
Idempotence | x  x = x | x  x = x
Absorption | x  (x  y) = x | x  (x  y) = x
Combining | (x  y)  (x  y) = x | (x  y)  (x  y) = x
DeMorgan’s | (x  y) = x  y | (x  y) = x  y

## Slide 28: DeMorgan’s Law
(x  y) = x  y (x  y) = x  y
Proof by perfect induction
x | y | (x  y) | x  y
0 | 0 | 1 | 1
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0

## Slide 29: DeMorgan Graphically

## Slide 30: Applying Boolean Properties
f(a,b,c) = (a  c)  (a  b  c)  (a  b  c)  (a  b  c)
f(a,b,c) = (a  c)  (a  b  c) 
(a  b  c)  (a  b  c) 
(a  b  c)  (a  b  c)
f(a,b,c) = (a  c) 
(a  b  c)  (a  b  c) 
(a  b  c)  (a  b  c)
f(a,b,c) = (a  c)  (b  c)  (a  b)
Apply Absorption Property
Apply Combining Property

## Slide 31: Verilog

## Slide 32: Verilog
A hardware description language (HDL)
Used as an input to:
  Synthesis – implement hardware with gates, cells, or FPGAs
  Simulation – see what your hardware will do before you build it
Basic unit is a module
Modules have
  Module declaration
  Input and output declarations
  Internal signal declarations
  Logic definition
    Assign statements
    Case statements
    Module instantiations

## Slide 33: Example, Verilog for Thermostat
module Thermostat(presetTemp, currentTemp, fanOn) ;
input [2:0] presetTemp, currentTemp ; // temperature inputs, 3 bits each
output fanOn ; // true when current > preset
wire fanOn ;
assign fanOn = (currentTemp > presetTemp) ;
endmodule

## Slide 34: Example, Verilog for Thermostat
module Thermostat(presetTemp, currentTemp, fanOn) ;
input [2:0] presetTemp, currentTemp ; // temperature inputs, 3 bits each
output fanOn ; // true when current > preset
wire fanOn ;
assign fanOn = (currentTemp > presetTemp) ;
endmodule
Module declaration
I/O list
Declare I/Os
A wire is a signal set with an assign statement or connected to a module
3-bit wide signals
An assign statement defines a signal with an equation

## Slide 35: Example, Days in Month Function
module DaysInMonth(month, days) ;
input [3:0] month ; // month of the year 1 = Jan, 12 = Dec
output [4:0] days ; // number of days in month
reg [4:0] days ;
always @(month) begin // evaluate whenever month changes
case(month)
2: days = 5’d28 ; // February has 28
4,6,9,11: days = 5’d30 ; // 30 days have September ...
default: days = 5’d31 ; // all the rest have 31...
endcase
end
endmodule

## Slide 36: Example, Days in Month Function
module DaysInMonth(month, days) ;
input [3:0] month ; // month of the year 1 = Jan, 12 = Dec
output [4:0] days ; // number of days in month
reg [4:0] days ;
always @(month) begin // evaluate whenever month changes
case(month)
2: days = 5’d28 ; // February has 28
4,6,9,11: days = 5’d30 ; // 30 days have September ...
default: days = 5’d31 ; // all the rest have 31...
endcase
end
endmodule
Reg defines a signal set in an always block. It does NOT define a register.
Always block evaluates each time activity list changes. In this case each time month changes
Case statement selects statement depending on value of argument. Like a truth table.
Default covers values not listed.
Can have multiple values per statement

## Slide 37: Verilog design style – for synthesizable modules
Combinational modules use only
  Assign statements
  Case or Casex statements (with default)
  If statements – only if all signals have a default assignment
  Instantiations of other combinational modules
Sequential modules use only
  Combinational logic
  Explicitly declared registers (flip-flops)
Do not use
  Loops
  Always blocks except for case, casex, or if
Do use
  Signal concatenation, e.g., {a, b} = {c, d}
  Signal subranges, e.g., a[7:1] = b[6:0] ;
Logic is organized into small modules
  Leaf modules not more than 40 lines
  If it could be made two modules, it should be

## Slide 38: Verilog design style – for synthesizable modules (page 2)
Use lots of comments
  Comments themselves
  Meaningful signal names – tempHigh, not th
  Meaningful module names – DaysInMonth, not Mod3
Activation lists for case statements include ALL inputs (or use *)
Constants
  All constants are `defined if used more than once
  Width of all constants is specified 5’d31, not 31
Signals
  Buses (multi-bit signals) are numbered high to low
    e.g., wire [31:0] bus
  All signals should be high-true (except primary inputs and outputs)
Visualize the logic your Verilog will generate.
  If you can’t visualize it, the result will not be pretty

## Slide 39: Summary
The world is digital
  Systems are digital at their core, only analog on the edges
Representing information
  Binary signals, sets, continuous values
Digital signals reject noise
  Voltage range divided into discrete states
  Noise margins
Combinational logic
  Output depends only on input (no state)
Boolean algebra
  Rules to manipulate logic equations
Verilog
  Describe hardware for simulation and synthesis

## Slide 40: Next Time
Fun with Karnaugh maps
  Manual design of combinational circuits
In real life you will synthesize these, but everyone needs to manually design a combinational circuit – just once.