## Slide 1: Digital Design: A Systems Approach Lecture 10: System Design

## Slide 2: Announcements
L10: Chapters 21, 22, & 20
L11: Chapter 23

## Slide 3: System Design – a process
Specification
  Understand what you need to build
Divide and conquer
  Break it down into manageable pieces
Define interfaces
  Clearly specify every signal between pieces
  Hide implementation
  Choose representations
Timing and sequencing
  Overall timing – use a table
  Timing of each interface – use a simple convention (e.g., valid – ready)
Add parallelism as needed (pipeline or duplicate units)
Timing and sequencing (of parallel structures)
Design each module
Code
Verify
Iterate back to the top at any step as needed.

## Slide 4: Specification
Write the user’s manual first
Putting it on paper means that there are no misunderstandings about operation
  In practice, this also serves to validate the specification with users/customers
Spec includes
  Inputs and outputs
  Operating modes
  Visible state
  Discussion of “edge cases”
Most of design is done writing English-language documents – with associated drawings. Coding comes later.
  Don’t start coding until your design is complete.

## Slide 5: Divide and Conquer –common themes
Task
  Divide system into a network of tasks
  One module per task
  Model-view-controller: tasks are:
    The ‘guts’ (model)
    Output modules that ‘view’ the model
    Input modules that affect the model
State
  Divide system by state
  Separate module for each set of state variables
Interface
  Module for each external interface

## Slide 6: Divide and Conquer
Example 1 – Pong
  Model-view-controller
  Model – ball and paddle position FSMs, score
  View – VGA display and sound
  Controller – inputs to control paddles

## Slide 7: Pong Decomposition
Pong
RGBSync
Buttons

## Slide 8: Pong Decomposition
Pong
RGBSync
Buttons
VGA Display
Input Logic
Main
FSM
Ball
FSM
Paddle
FSM
Score
FSM
left pad y
right pad y
ball pos
mode
left pad y
right pad y
mode
ball pos
mode
ball pos
score
score
serve,start
left up/down
right up/down

## Slide 9: Each block is now small enough to design
Example, Ball FSM
  State: x, y, vx, vy
  Serve: {x, y} = middle, vy = 0, vx = dir ;
  Bounce off top/bottom: vy = -vy ;
  Bounce off paddle: vx = -vx ; adjust vy ;
  Otherwise: x = x+vx, y = y+vy ;
Simple datapath FSM

## Slide 10: Divide and Conquer
Example 2 – DES Cracker
  Task pipeline:
    Generate keys
    Sequence ciphertext
    Decrypt plaintext
    Check plaintext

## Slide 11: DES Example

## Slide 12: Divide and Conquer
Example 3 – Music Synthesizer
  State x task
    Tone generator
      Generate harmonics, generate addresses, lookup sine wave, weight for each harmonic
    Envelope generator
      Generate envelopes, multiply by samples
    Combiner

## Slide 13: Simple Music Synthesizer

## Slide 14: With Harmonics and Attack/Decay

## Slide 15: Define Interfaces
For standard modules, already defined for you
  DES module (from OpenCores library)
  AC97 CODEC
For your own modules, interfaces must specify every signal
  Each Data “Port”:
    Data signals – how wide, what representation, when valid
    Flow control – specifies when data transfers take place
  Other control and status
  Example – Sine Wave Generator
    Next (in) – goes high one clock each data sample
    Freq (in) – 16-bits – u0.16 specifies an interval between samples in the sine table. A value of 1 specifies an interval of pi.
    Value (out) – 16-bits s0.15 format, on sample pulse
    NextNote (out) – goes high when current note has been held for 100ms

## Slide 16: Example decision
Suppose we need 15 sine-wave generators
  3 notes x 5 harmonics each
Do we share a single quarter sine table or use 15 tables?
In favor of sharing
  We have time
    Sample rate is 48KHz, clock is 100MHz.
    2,083 cycles per sample
  It will take less chip area
Opposed to sharing
  Dedicated BRAMs are simpler
  We have lots of BRAMs.
Which would you do?

## Slide 17: System Design – a process (reminder)
Specification
  Understand what you need to build
Divide and conquer
  Break it down into manageable pieces
Define interfaces
  Clearly specify every signal between pieces
  Hide implementation
  Choose representations
Timing and sequencing
Add parallelism as needed (pipeline or duplicate units)
Timing and sequencing (of parallel structures)
Design each module
Code
Verify
Iterate back to the top at any step as needed.

## Slide 18: Timing and Sequencing
Work out exactly when and in what order things happen
Account for pipeline delays
Account for multi-cycle operations
Draw a timing diagram (or a table)
Example: DES Cracker

## Slide 19: Example, DES Cracker Timing
Cycle | KeyGen | CT Seq | DES | Check
0 | firstKey | firstBlock |  | 
1 | Key0 | CT Block 0 | Round 1 | 
2 |  |  | Round 2 | 
… |  |  | … | 
16 |  | nextBlock | Round 16 | 
17 |  | CT Block 1 | Round 1 | PT Block 0
18 |  |  | Round 2 | 
… |  |  | … | 
32 |  | nextBlock | Round 16 | 
33 |  | CT Block 2 | Round 1 | PT Block 1
… |  |  | … | 
112 |  | nextBlock | Round 16 | 
113 |  | CT Block 7 | Round 1 | PT Block 6
… |  |  | … | 
128 | nextKey | firstBlock | Round 16 | 
129 | Key1 | CT Block 0 |  | PT Block 7

## Slide 20: DES Example

## Slide 21: Example, DES Cracker Timing – if a PT block fails, go on to next key
Cycle | KeyGen | CT Seq | DES | Check
0 | firstKey | firstBlock |  | 
1 | Key0 | CT Block 0 | Round 1 | 
2 |  |  | Round 2 | 
… |  |  | … | 
16 |  | nextBlock | Round 16 | 
17 |  | CT Block 1 | Round 1 | PT Block 0
18 | nextKey | firstBlock | --- | 
19 | Key1 | CT Block 0 | Round 1 | 
 |  |  | Round 2 | 
… |  |  | … | 
34 |  | nextBlock | Round 16 | 
35 |  | CT Block 1 | Round 1 | PT Block 0
… |  |  | … | 

## Slide 22: Example timing – Music Synthesizer with Harmonics
Cycle | NextNote | NextSample | NextHarmonic | Ready | Comment
0 | 1 | 1 |  |  | Start – look up note, convert to freq
1 |  | 1 |  |  | Freq valid this cycle, read value
2 |  | 1 |  | 1 | Value of fundamental
3 |  |  | 1 |  | Read 2nd harmonic
4 |  |  | 1 | 1 | Value of 2nd harmonic (2x freq)
5 |  |  | 1 |  | Read 3rd harmonic
6 |  |  | 1 | 1 | Value of 3rd harmonic (3x freq)
… |  |  |  |  | Idle until next 48KHz request
2084 |  | 1 |  |  | Read fundamental for next sample
2085 |  | 1 |  | 1 | Value of fundamental
2086 |  |  | 1 |  | Read 2nd harmonic
2087 |  |  | 1 | 1 | Value of 2nd harmonic (2x freq)
2088 |  |  | 1 |  | Read 3rd harmonic
2089 |  |  | 1 | 1 | Value of 3rd harmonic (3x freq)
… |  |  |  |  | Repeat above 4800 times per note
X+0 | 1 | 1 |  |  | Read next note
X+2 |  | 1 |  |  | Freq valid, read value
X+3 |  | 1 |  | 1 | Value of fundamental

## Slide 23: With Harmonics and Attack/Decay

## Slide 24: System Design – a process (reminder)
Specification
  Understand what you need to build
Divide and conquer
  Break it down into manageable pieces
Define interfaces
  Clearly specify every signal between pieces
  Hide implementation
  Choose representations
Timing and sequencing
Add parallelism as needed (pipeline or duplicate units)
Timing and sequencing (of parallel structures)
Design each module
Code
Verify
Iterate back to the top at any step as needed.

## Slide 25: Basic principle
Keep it simple (KIS)
Add complexity only when your design absolutely needs it
A corollary:
If its not broken, don’t fix it
Don’t optimize something unless there is something wrong with the simple design

## Slide 26: System Design – a process (reminder)
Specification
  Understand what you need to build
Divide and conquer
  Break it down into manageable pieces
Define interfaces
  Clearly specify every signal between pieces
  Hide implementation
  Choose representations
Timing and sequencing
Add parallelism as needed (pipeline or duplicate units)
Timing and sequencing (of parallel structures)
Design each module
Code
Verify
Iterate back to the top at any step as needed.

## Slide 27: Some comments on Coding
Don’t start coding until your design is done.
Don’t even think about coding until your design is done
Code a separate module for every block in your block diagrams
Unit test each module before moving on to the next module
Follow good Verilog coding practice
  All state should be explicitly declared DFFs
  Assign and case/casex for combinational logic
  Don’t forget its hardware
Debug in Modelsim before coming into the lab

## Slide 28: Verification
Basic principle
  If you didn’t test it, it doesn’t work
    All modules
    All states
    All transitions between states
    All “edge” conditions
Accelerate tests
  Initialize to just before the state you’re testing
  Shorten counters (for testing, don’t forget to lengthen for real operation)

## Slide 29: Debugging
Thinking your design through ahead of time will avoid most bugs
  Work out timing
  Keep it simple
Be a detective to track down the few bugs that slip through
  Start with known working logic
  Follow signals to the point where something first goes wrong
  Run simplest possible test case
  Unit test modules
Make sure you don’t have compilation or simulation warnings
  Check that your logic meets timing
Do not just randomly change Verilog code - stop and think

## Slide 30: System Design – Overview
Specification
  Understand what you need to build
Divide and conquer
  Break it down into manageable pieces
Define interfaces
  Clearly specify every signal between pieces
  Hide implementation
  Choose representations
Timing and sequencing
Add parallelism as needed (pipeline or duplicate units)
Timing and sequencing (of parallel structures)
Design each module
Code
Verify
  Debug
Iterate back to the top at any step as needed.