## Slide 1: Digital Design: A Systems Approach Lecture 4: Numbers and Arithmetic

## Slide 2: Readings
L4: Chapters 10 & 11
L5: Review Lectures 1-4

## Slide 3: Numbers
Digital logic works with binary numbers
  Each bit has a value based on its position
  e.g., 10101
    1+4+16 = 21
    Or 1+4-16 = -11

## Slide 4: From Decimal To Binary
Example: 1710
Convert number to binary base:
17 ÷ 2 = 8 remainder 1
8 ÷ 2 = 4 remainder 0
4 ÷ 2 = 2 remainder 0
2 ÷ 2 = 1 remainder 0
1 ÷ 2 = 0 remainder 1
1710 = 100012
MSB
LSB

## Slide 5: From Decimal To Binary To Hexadecimal
Example: 196310
196310 = 0111 1010 10112
7
A
Bhex

## Slide 6
Binary addition
1-bit 0+0 = 0, 1+0 = 1, 1+1 = 10
1
  6 110 + 3 011
  5 101 +7 111
0_
10_
01
001
110_
1001
9
0
1_
00
11_
100
111_
1100
12

## Slide 7: One bit of an adder
Counts the number of “1” bits on its input
Outputs the result in binary
For a half-adder, 2 inputs, output can be 0, 1, or 2
For a full-adder, 3 inputs, output can be 0, 1, 2, or 3

## Slide 8: Half Adder
// half adder
module HalfAdder(a,b,c,s);
input a,b ;
output c,s ; // carry and sum
wire s = a ^ b ;
wire c = a & b ;
endmodule
# 00 00
# 01 01
# 10 01
# 11 10

## Slide 9
// full adder - from half adders
module FullAdder1(a,b,cin,cout,s) ;
input a,b,cin ;
output cout,s ; // carry and sum
wire g,p ; // generate and propagate
wire cp ;
HalfAdder ha1(a,b,g,p) ;
HalfAdder ha2(cin,p,cp,s) ;
or o1(cout,g,cp) ;
endmodule
# 000 00
# 001 01
# 010 01
# 011 10
# 100 01
# 101 10
# 110 10
# 111 11

## Slide 10: Full adder from a truth table

## Slide 11: Full adder from truth table
// full adder - logical
module FullAdder2(a,b,cin,cout,s) ;
input a,b,cin ;
output cout,s ; // carry and sum
wire s = a ^ b ^ cin ;
wire cout = (a & b)|(a & cin)|(b & cin) ; // majority
endmodule

## Slide 12: CMOS Version of Full Adder

## Slide 13: Multi-bit Adder

## Slide 14: Adder in verilog - behavioral
// multi-bit adder - behavioral
module Adder1(a,b,cin,cout,s) ;
parameter n = 8 ;
input [n-1:0] a, b ;
input cin ;
output [n-1:0] s ;
output cout ;
wire [n-1:0] s;
wire cout ;
assign {cout, s} = a + b + cin ;
endmodule

## Slide 15: Ripple-carry adder – bit-slice notation
// multi-bit adder – with vectors
module Adder2(a,b,cin,cout,s) ;
parameter n = 8 ;
input [n-1:0] a, b ;
input cin ;
output [n-1:0] s ;
output cout ;
wire [n-1:0] p = a ^ b ;
wire [n-1:0] g = a & b ;
wire [n:0] c = {g | (p & c[n-1:0]), cin} ;
wire [n-1:0] s = p ^ c[n-1:0] ;
wire cout = c[n] ;
endmodule

## Slide 16: Negative Integers
Thus far we have only addressed positive integers. What about negative numbers?
3 ways to represent negative integers in binary:
  Sign Magnitude
  One’s complement
  Two’s complement
Example: Consider +23 –23
  Sign Magnitude 0 10111 1 10111
  One’s complement 0 10111 1 01000
  Two’s complement 0 10111 1 01001

## Slide 17: Why do we all use 2’s complement?
2’s complement makes subtraction easy
Represent negative number, –x as 2n – x
All arithmetic is done modulo 2n so no adjustments are necessary
x + (– y) = x + (2n – y) (mod 2n)
consider 4-bit numbers
4 – 3 = 4 + (16 – 3) (mod 16) = 4 + (15 – 3 + 1) = 0100 + (1111 – 0011) + 0001 = 0100 + 1100 + 0001 = 0001

## Slide 18: 2’s Complement

## Slide 21
// add a+b or subtract a-b, check for overflow
module AddSub(a,b,sub,s,ovf) ;
parameter n = 8 ;
input [n-1:0] a, b ;
input sub ; // subtract if sub=1, otherwise add
output [n-1:0] s ;
output ovf ; // 1 if overflow
wire c1, c2 ; // carry out of last two bits
wire ovf = c1 ^ c2 ; // overflow if signs don't match
// add non sign bits
Adder1 #(n-1) ai(a[n-2:0],b[n-2:0]^{n-1{sub}},sub,c1,s[n-2:0]) ;
// add sign bits
Adder1 #(1) as(a[n-1],b[n-1]^sub,c1,c2,s[n-1]) ;
endmodule

## Slide 22
# 57 + 28 = 7f ovf = 0
# 57 - 28 = 2f ovf = 0
# 58 + 28 = 80 ovf = 1
# e9 - 17 = d2 ovf = 0
# e9 + 97 = 80 ovf = 0
# e9 - 6a = 7f ovf = 1
// test script
module test2 ;
reg [7:0] in0, in1 ;
wire [7:0] out ;
reg sub ;
wire ovf ;
AddSub #(8) a(in0,in1,sub,out,ovf) ;
initial begin
in0 = 8'd87 ; in1 = 8'd40 ; sub = 0 ;
#100 $display("%03h + %03h = %03h ovf = %b", in0, in1, out, ovf) ;
in0 = 8'd87 ; in1 = 8'd40 ; sub = 1 ;
#100 $display("%03h - %03h = %03h ovf = %b", in0, in1, out, ovf) ;
in0 = 8'd88 ; in1 = 8'd40 ; sub = 0 ;
#100 $display("%03h + %03h = %03h ovf = %b", in0, in1, out, ovf) ;
in0 = 8'he9 ; in1 = 8'h17 ; sub = 1 ; /* -23 - 23 */
#100 $display("%03h - %03h = %03h ovf = %b", in0, in1, out, ovf) ;
in0 = 8'he9 ; in1 = 8'h97 ; sub = 0 ; /* -23 - 105 = -128 no ovf */
#100 $display("%03h + %03h = %03h ovf = %b", in0, in1, out, ovf) ;
in0 = 8'he9 ; in1 = 8'd106 ; sub = 1 ; /* overflow */
#100 $display("%03h - %03h = %03h ovf = %b", in0, in1, out, ovf) ;
end
endmodule

## Slide 23
reg [8:0] ref, in0, in1 ; // reference result, inputs kept longer
Reg rovf ;
…
initial begin
// generate test cases
// check each against reference
if(sub) ref = in0-in1 ;
else ref = in0+in1 ;
rovf = (ref[8] != ref[7]) ;
#100
if ((out != ref[7:0])||(ovf != rovf)) $display("ERROR") ;
// more cases
end

## Slide 24
Compare two numbers with subtraction
diff = a – b if diff is negative (sign bit = 1), a<b
If diff is zero, a=b
Example, compare a = 0101 and b = 0110
diff = a – b = 1111 => a<b
Compare a=0111 and b = 0111, diff = 0 => a=b

## Slide 25: Multiplication
Multiplication
Shifting left multiplies by 2
e.g., 5 = 101, 10 = 1010, 20 = 10100
To multiply by 3, compute 3x = x + 2x
Example, 7 x 5
1 1 1 x 1 0 1
1 1 1 0 0 0 1 1 1 1 0 0 0 1 1

## Slide 26
First generate partial products: pij = ai  bj has weight i+j

## Slide 27
Then sum partial products to get sum

## Slide 28
// 4-bit multiplier
module mul4(a,b,p) ;
input [3:0] a,b ;
output [7:0] p ;
// form partial products
wire [3:0] pp0 = a & {4{b[0]}} ; // x1
wire [3:0] pp1 = a & {4{b[1]}} ; // x2
wire [3:0] pp2 = a & {4{b[2]}} ; // x4
wire [3:0] pp3 = a & {4{b[3]}} ; // x8
// sum up partial products
wire cout1, cout2, cout3 ;
wire [3:0] s1, s2, s3 ;
Adder1 #(4) a1(pp1, {0,pp0[3:1]}, 0, cout1, s1) ;
Adder1 #(4) a2(pp2, {cout1,s1[3:1]}, 0, cout2, s2) ;
Adder1 #(4) a3(pp3, {cout2,s2[3:1]}, 0, cout3, s3) ;
// collect the result
wire [7:0] p = {cout3, s3, s2[0], s1[0], pp0[0]} ;
endmodule

## Slide 29
// test script
module test3 ;
reg [3:0] in0, in1 ;
wire [7:0] out ;
Mul4 mul(in0,in1,out) ;
initial begin
in0 = 0 ;
repeat (16) begin
in1 = 0 ;
repeat (in0+1) begin
#100 $display("%03d * %03d = %03d",in0,in1,out) ;
in1 = in1 + 1 ;
end
in0 = in0 + 1 ;
end
end
endmodule

## Slide 30
# 0 * 0 = 0
# 1 * 0 = 0
# 1 * 1 = 1
# 2 * 0 = 0
# 2 * 1 = 2
# 2 * 2 = 4
# 3 * 0 = 0
# 3 * 1 = 3
# 3 * 2 = 6
# 3 * 3 = 9
# 4 * 0 = 0
# 4 * 1 = 4
# 4 * 2 = 8
# 4 * 3 = 12
# 4 * 4 = 16
# 5 * 0 = 0
# 5 * 1 = 5
# 5 * 2 = 10
# 5 * 3 = 15
# 5 * 4 = 20
# 5 * 5 = 25
# 6 * 0 = 0
# 6 * 1 = 6
# 6 * 2 = 12
# 6 * 3 = 18
# 6 * 4 = 24
# 6 * 5 = 30
# 6 * 6 = 36
# 7 * 0 = 0
# 7 * 1 = 7
# 7 * 2 = 14
# 7 * 3 = 21
# 7 * 4 = 28
# 7 * 5 = 35
# 7 * 6 = 42
# 7 * 7 = 49
# 8 * 0 = 0
# 8 * 1 = 8
# 8 * 2 = 16
# 8 * 3 = 24
# 8 * 4 = 32
# 8 * 5 = 40
# 8 * 6 = 48
# 8 * 7 = 56
# 8 * 8 = 64
# 9 * 0 = 0
# 9 * 1 = 9
# 9 * 2 = 18
# 9 * 3 = 27
# 9 * 4 = 36
# 9 * 5 = 45
# 9 * 6 = 54
# 9 * 7 = 63
# 9 * 8 = 72
# 9 * 9 = 81
# 10 * 0 = 0
# 10 * 1 = 10
# 10 * 2 = 20
# 10 * 3 = 30
# 10 * 4 = 40
# 10 * 5 = 50
# 10 * 6 = 60
# 10 * 7 = 70
# 10 * 8 = 80
# 10 * 9 = 90
# 10 * 10 = 100
# 11 * 0 = 0
# 11 * 1 = 11
# 11 * 2 = 22
# 11 * 3 = 33
# 11 * 4 = 44
# 11 * 5 = 55
# 11 * 6 = 66
# 11 * 7 = 77
# 11 * 8 = 88
# 11 * 9 = 99
# 11 * 10 = 110
# 11 * 11 = 121
# 12 * 0 = 0
# 12 * 1 = 12
# 12 * 2 = 24
# 12 * 3 = 36
# 12 * 4 = 48
# 12 * 5 = 60
# 12 * 6 = 72
# 12 * 7 = 84
# 12 * 8 = 96
# 12 * 9 = 108
# 12 * 10 = 120
# 12 * 11 = 132
# 12 * 12 = 144
# 13 * 0 = 0
# 13 * 1 = 13
# 13 * 2 = 26
# 13 * 3 = 39
# 13 * 4 = 52
# 13 * 5 = 65
# 13 * 6 = 78
# 13 * 7 = 91
# 13 * 8 = 104
# 13 * 9 = 117
# 13 * 10 = 130
# 13 * 11 = 143
# 13 * 12 = 156
# 13 * 13 = 169
# 14 * 0 = 0
# 14 * 1 = 14
# 14 * 2 = 28
# 14 * 3 = 42
# 14 * 4 = 56
# 14 * 5 = 70
# 14 * 6 = 84
# 14 * 7 = 98
# 14 * 8 = 112
# 14 * 9 = 126
# 14 * 10 = 140
# 14 * 11 = 154
# 14 * 12 = 168
# 14 * 13 = 182
# 14 * 14 = 196
# 15 * 0 = 0
# 15 * 1 = 15
# 15 * 2 = 30
# 15 * 3 = 45
# 15 * 4 = 60
# 15 * 5 = 75
# 15 * 6 = 90
# 15 * 7 = 105
# 15 * 8 = 120
# 15 * 9 = 135
# 15 * 10 = 150
# 15 * 11 = 165
# 15 * 12 = 180
# 15 * 13 = 195
# 15 * 14 = 210
# 15 * 15 = 225

## Slide 31
Accuracy
Resolution

## Slide 32: Value and Representation functions
R(x) is binary number representing real number x
V(b) is value of binary number b
Absolute error
  ea= |V(R(x)) - x|
Relative error
  er = |(V(R(x)) - x)/x|

## Slide 33: Example
Suppose you need to represent temperatures from 0 to 100C to 0.1C
What representation would you use?
  What is the resolution of this representation?
  What is its maximum absolute error?

## Slide 34: Example
Suppose you need to represent distances from 1mm to 1m with an accuracy of 0.1%
How many bits are required to do this with a binary fixed-point number?
How many bits are needed with binary floating point?
What floating-point representation is needed?

## Slide 35
Binary Floating Point
Floating-Point Representation
S
Exponent
Mantissa
Floating-Point Format: (-1)S x M x 2E
0
22
23
30
31
8 bits
23 bits
IEEE 754 Floating-Point Representation
Floating-Point Format: (-1)S x (1 + M) x 2(E-Bias)
S
Exponent
Mantissa
0
22
23
30
31
8 bits
23 bits

## Slide 39: Summary
Binary number representation
Add numbers a bit at a time
2’s complement –x = (2n – x) = (2n – 1) – x + 1 = neg(x) + 1
Subtract by 2’s complement and add
Multiply – form partial products pij and sum
Number representation – accuracy and resolution.
Fixed and floating point