## Slide 1: Principles of Plasma Physics for Scientists and Engineers
Lecture 8: Hydrodynamic (Fluid) Equations for a Plasma
Covers Material from Chapter 4 (4.4-4.5) and Chapter6 (6.1-6.2)*
*Material corresponds to Principles of Plasma Physics for Engineers and Scientists by
U. S. Inan and M. Gołkowski, Cambridge University Press, 2011

## Slide 2: Fluid Equations for a Plasma
Zeroth Moment of the Boltzmann Equation: Continuity Equation(s)
First Moment of the Boltzmann Equation: Momentum Transport Equations
The Second Order Moment: Energy Transport Equation
Systems of Macroscopic Equations: Cold and Warm Plasma Models
  The cold plasma model
  The warm plasma model
The single-fluid equations for a fully ionized plasma
  Equations of mass and charge conservation
  Equation of motion
  Generalized Ohm’s law

## Slide 3: Zeroth Moment of the Boltzmann Equation
Zeroth moment is a statement of conservation of particles, i.e., of mass and charge.
First term is rate of change of charge (or mass), second term is loss of charge (or mass) from the volume element via escaping particles, i.e., divergence of charge (or mass) flow.
Number of charged particles is not always conserved; in partially ionized gases (electrons, ions, and neutrals), various gain or loss mechanisms can lead to loss or gain of particles.
Collision phenomena can be elastic and inelastic. In elastic collisions, mass, momentum, and energy is conserved and there is neither creation or annihilation of particles.
In an inelastic collision, electrons may recombine with ions to form neutral atoms, or can attach to neutrals to form a much heavier (than an electron) negative ion.
Collisions may also result in raising the energy state of electrons in an atom so that new electrons are stripped off, in a process referred to as ionization.

## Slide 4: Zeroth Moment of the Boltzmann Equation (cont’d)
If only one species of positive ions are present, the rate of recombination is proportional to Ne and Ni , with NeNi. Loss rate due to recombination processes is −αN2.
Rate of electron attachment is proportional to Ne and Nn. In a weakly ionized gas Nn can be considered constant, so that attachment loss rate is given by −νaN.
Rate at which electrons are added due to ionization is given by −νiN.
where both the density N and the fluid velocity u are understood to be functions of r and t, and the pressure tensor is given by Ψ = Nm<w>.

## Slide 5: First Moment of the Boltzmann Equation
The first moment of the Boltzmann equation expresses the conservation of momentum
where both the density N and the fluid velocity u are understood to be functions of r and t, and the pressure tensor is given by Ψ = Nm<w>.
Terms on the left constitute the total derivative as a function of time and represent the rate of increases of momentum per unit volume.
First term on the right represents the loss of momentum of the volume element through escaping particles, i.e., divergence of momentum flow.
Second term on the right is electromagnetic force density, while the last term Sij represents the total momentum transferred (gained) by the species i via its collisions with species j. In this context, we neglect inelastic collisions. In most cases, we can assume that the plasma is isotropic, so that Ψ is diagonal and ∇・Ψ = ∇p, with p being the scalar pressure.

## Slide 6: First Moment of the Boltzmann Equation (cont’d)
Dominant collision process in low pressure discharges and in the lower heights of the ionosphere are collisions of electrons with neutrals. Rate of momentum transfer to species i due to collisions with neutrals is described by setting Sij = −∑mNνj (ui− uj ), where the summation is to be carried over all the neutral species j.
When plasma can be assumed isotropic, having only one neutral species assumed to be stationary (uj = 0), the momentum transport equation reduces to

## Slide 7: Second Order Moment: Energy Transport Equation
Second order moment of the Boltzmann equation, i.e., equation of energy conservation, is obtained multiplying with (1/2)mv2 and integrating over velocity space.
Scoll ≠0, due to energy transfer between species, although total energy is conserved.
Energy conservation equation can be also written as:

## Slide 8: Second Order Moment: Energy Transport Equation (cont’d)
For isotropic plasma Ψ reduces to p, and noting that average energy of plasma is 1/2 m<w・w>= 3/2 kBT and using p=N kBT we find 3/2 p= 1/2Nm<w・w>, i.e., energy density (in J/m3).
Quantity 3/2pu represents the flow of energy density at the fluid velocity so that it is the macroscopic energy flux (in units of Watts/m2).
The third term p∇ ・u (in units of Watts/m3) represents the heating or cooling of the fluid due to compression or expansion of its volume.
Quantity q is heat flow vector (in units of Watts/m2), representing microscopic energy flux, and is related to particle random velocity as q = (N/2)m<w2w>.
For steady-state low pressure discharges, the macroscopic energy flux is balanced against the collisional processes, resulting in a simpler equation

## Slide 9: System of Macroscopic Equations: Cold and Warm Plasma Models
We can evaluate higher order moments of the Boltzmann equation. However, moments involving the third or higher powers of v lack simple physical meaning and have no utility.
Equations of conservation of particles, momentum and energy are useful general statements, but they cannot be considered as a closed system of plasma equations.
In analyzing plasmas, e.g., to determine the degree of heating/transport, or characteristics of EM waves at a given frequency, we need to solve Boltzmann equation in the presence of other physical constraints, such as external forces and/or Maxwell’s equations.
It is difficult to solve Boltzmann’s equation to determine our ultimate goal of f (r, v, t).
Short of f (r, v, t), we may set out to determine its moments, realizing that, velocity distribution function is known once we now all of its moments.
It is likely that we do not need f (r, v, t) itself but instead require that we estimate some of its bulk properties, such as number density N, fluid velocity u, and pressure tensor Ψ.

## Slide 10: System of Macroscopic Equations: Cold and Warm Plasma Models (cont’d)
In order to determine such macroscopic parameters, we can deduce equations satisfied by these quantities by taking the moments of the Boltzmann equation.
However, everytime we obtain a new equation a new unknown appears so that the number of equations is never sufficient for the determination of all the macroscopic quantities. The number of unknowns always exceed the number of equations.
It is thus necessary to truncate the system of equations at some point in the hierarchy of moments, by making simplifying assumptions.
Of the several different sets of macroscopic equations used to describe plasmas, the two most commonly used ones are the so-called cold plasma and the warm plasma models.

## Slide 11: Cold Plasma Model
The simplest set of macroscopic equations can be obtained by introducing the truncation at the momentum transfer equation.
The physical assumption adopted is to neglect the thermal motions of the particles, which is achieved by setting the kinetic pressure tensor to zero, i.e., Ψ = 0
The only remaining macroscopic variables are then the number density N and fluid velocity u, which are described by the two equations:
In general, a suitable method for evaluation of the collision term Sij is needed in order for the above equations to be useful in analysis of plasma dynamics.

## Slide 12: Collisions in Cold Plasma
One common method is to view the collisions as an impediment to motion, causing a rate of decrease in momentum as determined by an ‘effective’ collision frequency:

## Slide 13: Warm Plasma Model
Next we truncate at the energy conservation equation. Thermal motions are included but viscous forces are neglected,Ψ is diagonal with equal terms, ∇・Ψ = ∇p.
The system is not closed, since p is a third variable. Energy conservation equation can be used for p, but it contains a fourth unknown, namely heat flux q.
To truncate the system at this point we adopt simplifying assumptions, to either make energy transport equation unnecessary or reduce it to simpler forms in terms of p.
Use thermodynamic equation of state to relate p to N. The isothermal equation of state:
holds for relatively slow time variations, allowing temperatures to reach equilibrium. The plasma fluid can exchange energy with its surroundings.

## Slide 14: Warm Plasma Model (cont’d)
Adiabatic equation of state, C =const. and γ=1 + 2/nd, nd being number of degrees of freedom, holds for fast time variations, such as for plasma waves.
Plasma fluid does not exchange energy with its surroundings and a separate energy conservation equation is not needed. The use of adiabatic gas law is equivalent to assuming no energy interchange (and no heat flow) due to collisional interactions.
When explicit use of energy equation is required, heat flux vector q is the outstanding unknown, and we need to adopt a physical assumption in order to close the finite number of moment equations.

## Slide 15: The Single-fluid Equations for a Fully Ionized Plasma
In a plasma with multiple species (e.g., electrons gas and ions), there is a set of continuity/ momentum transport equations for each species:
and
where ∇ is obviously in configuration space (i.e., already integrated over velocity space).
The collision term Sei (Sie) represents total momentum transferred to electrons (ions) per unit volume per unit time by collisional interactions with ions (electrons).

## Slide 16: The Single-fluid Equations for a Fully Ionized Plasma (cont’d)
For fully ionized two species plasma with no neutral gas, the total momentum must be conserved in collisional interactions between two species, i.e.,
Due to the difference between electron and ion masses, the characteristic time scales of the phenomena is substantially different. The characteristics frequencies ωp and ωc are much larger for electrons. The equations are solved simultaneously to account for the coupling between ion and electron motions.
For plasma phenomena that are large scale (L >> λD) and at low frequencies (ω<<ωpe and ω<<ωce), plasma is on average electrically neutral (Ni~Ne) and the movement of electrons independently of ions is not important.
In such cases, the plasma can be treated as a single conducting fluid, whose inertia is provided primarily by mass of ions; dynamics of the plasma is then no different than any other conductive fluid, such as liquid mercury.

## Slide 17: The Single-fluid Equations for a Fully Ionized Plasma (cont’d)
Macroscopic variables of electrons and ions are lumped together to obtain macroscopic parameters describing the ionized gas as a whole. Governing equations for new set of macroscopic parameters is obtained by combining constituent equations
For partially ionized plasmas, the above should also contain terms corresponding to neutral particles.
To obtain macroscopic equations for the single plasma fluid, we linearize the equations.
Assume the fluid velocity u, the electric field E, and the kinetic pressure Ψ to be small perturbations, and neglect higher order terms resulting from any products of these.

## Slide 18: The Single-fluid Equations for a Fully Ionized Plasma (cont’d)
Particle density and magnetic field are small perturbations on ambient values:
any products of perturbation terms ˜N , ˜B with one another or with u, E and Ψ are neglected.
The linearized versions of the continuity eqautions are thus obtained as follows:

## Slide 19: The Single-fluid Equations for a Fully Ionized Plasma (cont’d)
The linearized versions of momentum equations are:
To obtain the equation of continuity of electric current (i.e., the equation of charge conservation), we can multiply the linearized versions of the contiuity equations respectively with qe and qi and add. We find
where J is the linearized form of the electric current density given by
whereas ρ is the electric charge density ρ = Neqe + Niqi.
Notes: <number>

## Slide 20: Equations of Mass and Charge Conservation
By multiplying the linearized versions of the momentum equations with me and mi we find the equation of mass conservation, namely
where ρm = Ne0me +Ni0mi is the linearized mass density, and um is the linearized mass velocity given by

## Slide 21: Equation of Motion
The equation of motion of the bulk plasma gas can be obtained by adding the linearized versions of the individual momentum transport equations . We find
where we have taken advantage of the fact that Sei = −Sie for fully ionized plasma.
Note that the second term on the right is proportional to the ambient value of the electric charge density namely ρ0 = Ne0qe +Ni0qi, which is zero since the plasma is macroscopically neutral. We thus arrive at the equation of motion
which is identical to the general equation of motion for an arbitrary conducting fluid, such as mercury, when we substitute for the mass density ρm = Ne0me +Ni0mi and the total pressure tensor Ψ = Ψe + Ψi.
For an isotropic plasma, we have ∇ ・Ψ = ∇p, so that the first term on the right is the negative gradient of the total pressure p = pe + pi.

## Slide 22: Generalized Ohm’s Law
A consequence of our assumption of electrical neutrality of the bulk plasma is that the local charge density ρ is assumed to be zero everywhere to first order (ρ = ρ0 + ˜ρ, with ρ0 = 0), which means that Gauss’s law, is no longer useful for determining the electric field E, since we have ∇・E ≈ 0.
Note that theoretically ˜ρ = 0, so that one might think that Poisson’s equation ∇2Φ = −˜ρ/ε0 can be solved for the electric potential Φ (which would then be used to find E = −∇Φ).
However, typically ˜ρ Neqe and reliable calculation of E is nearly impossible. Alternate equation used for determining E in a plasma is the Generalized Ohm’s Law.
We start by multiplying the linearized versions of individual momentum transport equations by qe/me and qi/mi, and adding together to find

## Slide 23: Generalized Ohm’s Law (cont’d)
Noting that for an electrically neutral plasma we have |qeNe0|≈|qiNi0|, we can rewrite the above as
Note that mi >>me, so that (qe/me)>>(qi/mi), and that (Ne0qe2/me)>>(Ni0qi2/mi).
Also assume plasma to be near thermal equilibrium, so that the kinetic pressures of the electrons and ions are similar (i.e., Ψe ≈ Ψi), so that (qe/me)Ψe >> (qi/mi), Ψi.
Physically, total momentum transferred to electrons per unit volume in unit time (as a result of collisions with ions) should be proportional to relative average velocity (ui− ue).

## Slide 24: Generalized Ohm’s Law (cont’d)
Since collisions in a fully ionized plasma are Coulomb collisions, Sei is proportional to Coulomb force or qe2 , as well as to Ne0 and the density of scatterers Ni0 =Ne0 :
where η is constant with units of ohms, known as the specific resistivity of the plasma, and νei is the collision frequency for momentum transfe
νei is not necessarily the actual rate at which collisions occur; it is a ‘fudge factor’, accounting for collision cross sections, effectiveness of momentum transfer, etc..r from the ions to the electrons.
Noting that qi = −qe, and Ne0 = Ni0, we can write
More generally, a magnetized plasma is anisotropic so that the resistivity is a tensor

## Slide 25: Generalized Ohm’s Law (cont’d)
Substituting in we arrive at the so-called generalized Ohm’s law:
For a steady current in a uniform plasma with no steady magnetic field, we have ∂J/∂t = 0, ∇・Ψ = 0, and B0 = 0, and the resistivity tensor reduces to a scalar so that
Thus our use of the terminology Generalized Ohm’s Law
The electric field E can be explicitly found from

## Slide 26: Generalized Ohm’s Law (cont’d)
First term is the motional electric field term associated with frame of reference of the fluid. In a frame of reference moving with the fluid at speed um, the electric field does not include this term and is given instead by E = E + um × B0.
Second term on the right is the Hall effect term and is often neglected.
Third term on the right is the so-called ambipolar polarization term and describes the electric field that arises due to gradients in plasma density along the magnetic field.
Fourth term is the ohmic loss term
Last term represents contribution of electron inertia to current flow.
Note that for collisionless plasma the resistivity is zero and the conductivity is infinite and plasma fluid behaves much like a liquid metal, or mercury.