## Slide 1: Absorption Spectroscopy of Gases
Fundamentals

## Slide 2: The Beer-Lambert Law
where s is the cross-section and a is the absorption coefficient

## Slide 3: Parameters of Absorption Lines

## Slide 4: Line Shape Functions
Doppler Broadened: Gaussian
Collisional Broadened: Lorentzian
Voigt Line Shape: Convolution of Gaussian and Lorentzian Profiles

## Slide 5: Gas Parameters and Line Shape
Measurement of the half-width, γ, and line centre depth, dc, of an absorption line yields information on the gas concentration, pressure or temperature.
For example for a Lorentzian line we have the relationships:
Temperature may be obtained through measurements on two absorption lines of the same gas:

## Slide 6: Molecular Vibrations
Molecular vibration modes may be viewed on the web site:
https://www.chemtube3d.com/category/structure-and-bonding/molecular-vibrations-ir/

## Slide 7: Rotation & Vibration of CO2 Molecule
The three axes of rotation
Vibrations of CO2 Molecule
(b) Symmetric stretch (c) Anti-symmetric stretch (d) Bending mode
Rotations of CO2 Molecule

## Slide 8: Energy Levels of Anharmonic Oscillator

## Slide 9: Near-IR Rovibrational Absorption Lines

## Slide 10: The HITRAN Database
An extremely useful source of information on spectral line parameters is the HITRAN database:
http://www.hitran.org
Absorption spectra may be modelled with various adjustable parameters such as temperature, pressure, line shape (Voigt, Lorentz, or Doppler), path length, wavenumber range, etc. using the HITRAN application sites:
The HITRAN Application Programming Interface (HAPI)
http://www.hitran.org/hapi
HITRAN on the Web
http://hitran.iao.ru/home

## Slide 11: Near-IR Lines of CO
Transmission=exp(-aCl) with Cl=1cm

## Slide 12: Near-IR Lines of CO2 (1.6mm region)
Transmission=exp(-aCl) with Cl=1cm

## Slide 13: Near-IR Lines of CO2 (2mm region)
Transmission=exp(-aCl) with Cl=1cm

## Slide 14: Near-IR Lines of C2H2
Transmission=exp(-aCl) with Cl=1cm

## Slide 15: Near-IR Lines of CH4
Transmission=exp(-aCl) with Cl=1cm

## Slide 16: Near-IR Lines of H2O (1.4mm region)
Transmission=exp(-aCl) with Cl=1cm

## Slide 17: Near-IR Lines of NH3
Transmission=exp(-aCl) with Cl=1cm

## Slide 18: Near-IR Lines of H2S (1.6mm region)
Transmission=exp(-aCl) with Cl=1cm

## Slide 19: Near-IR Lines of H2S (1.9mm region)
Transmission=exp(-aCl) with Cl=1cm

## Slide 20: Line Centre Attenuation for Pure Gas
Gas Molecule | Absorption Line Wavelength (µm) | α0 (cm-1) | Attenuation at line centre (dB/cm)
Carbon Monoxide (CO) | 1.5680 | 0.0025 | 0.011
Carbon Dioxide (CO2) | 1.5723 2.0035 | 0.0014 0.1 | 0.006 0.434
Acetylene (C2H2) | 1.5201 | 0.69 | 2.99
Methane (CH4) | 1.6510 | 0.36 | 1.56
Water Vapour (H2O) | 1.3827 | 0.36 | 1.56
Ammonia (NH3) | 1.5139 | 0.27 | 1.19
Hydrogen Sulphide (H2S) | 1.5781 1.9250 | 0.019 0.05 | 0.08 0.22

## Slide 21: Summary & Conclusions
The basic principles and parameters of gas absorption spectroscopy have been reviewed.
Line-shape measurements may be used to determine concentration, pressure or temperature in a variety of situations.
Optical sensors based on near-IR lines can be highly flexible and relatively inexpensive.
However for high sensitivity use of mid-IR lines is essential.