## Slide 1: Supplement e06.2: Fuzzy logic and target identification

## Slide 2: Identification and rule-based logic A recipe for failure
Consider these two images of Z and ρco of weather and insects.
While it may visually be easy to distinguish weather from insects, it is difficult to write a simple algorithm for it. This is because some values of Z and ρco are common to both, defeating simple rule-based logic such as “if Z < 10 dBZ and ρco < 0.95, then it can only be an insect”.

## Slide 3: Introducing fuzzy logic, or accepting “maybe” as a answer
Sometimes, as is the case here, the information may not be sufficient.
In such instances, instead of taking a decision immediately, one can gradually accumulate evidence and delay the decision until all the information has been considered.
Fuzzy logic has been designed to ease the implementation of such an approach.

## Slide 4: Identification based on fuzzy logic Overview
* Step 1: Use different data sources, such as:
- Radar reflectivity (intensity, texture, vertical gradient),
- Doppler velocity and spectrum width (magnitude, texture),
- Dual-polarization quantities (magnitude and texture), and
- Context information (altitude, temperature, time of day/year…),
to score how “compatible” their values are with different types of targets (rain, snow, hail, ground targets, insects, etc.);
* Step 2: Aggregate or combine the different scores;
* Step 3: Determine one (or several possible) winner(s).

## Slide 5: Step 1: “Fuzzification”, or obtaining “membership functions”
A membership function defines how the different values of data from every source, or their combination, are compatible with different types of targets. There is hence a membership function for each type of target and each type of input data used. Examples of simple membership functions are illustrated below. Given a measurement of reflectivity and of Zdr, these functions evaluate how plausibly such values could be caused by three types of targets (insects, rain, hail).
0
1
Membership or
compatibility functions
Data source 1 (e.g., reflectivity)
0
50 dBZ
Insects
Rain
Hail
0
1
Membership or
compatibility functions
Data source 2 (e.g., Zdr)
0
5 dB
Hail
Rain
Insects

## Slide 6: Step 1: “Fuzzification”, or obtaining “membership functions”
The key to membership functions is to use the full range of values between 0 (very unlikely) and 1 (very possible), and allow for the possibility that a) sometimes a value may only be partially compatible with a target type, and b) multiple positive answers may be acceptable.
Trapezoidal functions are simple to design, but not as good as more complex functions that are based on probability of occurrence. They nevertheless are the most commonly used in the early 21st century.
0
1
Membership or
compatibility functions
Data source 1 (e.g., reflectivity)
0
50 dBZ
Insects
Rain
Hail
0
1
Membership or
compatibility functions
Data source 2 (e.g., Zdr)
0
5 dB
Hail
Rain
Insects

## Slide 7: Step 1: “Fuzzification”
For example, based simply on the reflectivity test, the two echoes near 20 dBZ could very possibly be rain (rain score of 1), possibly be strong insects (insect score near 0.5), but not hail (hail score of 0).
Only with additional tests (e.g., with Zdr, ρco, etc.) will the left echo get gradually higher insect scores, while the middle echo will keep getting better rain scores.
The same process is repeated for all echoes.
0
1
Membership or
compatibility functions
Data source 1 (e.g., reflectivity)
0
50 dBZ
Insects
Rain
Hail

## Slide 8: Step 2: Aggregation or combining results
The scores of the different tests must then be combined. Often, each test score is weighted by a constant, e.g. WeightZ_test, that depends on how good a test is at separating different categories, the quality of the data used, and possibly the redundancy of the different tests. Those weighted scores are then often combined as a sum, e.g.:
Additional inputs can then be taken advantage of to promote or invalidate different target types. For example, the altitude of observation with respect to a detected bright band can be used to eliminate some echo categories such as rain and insects above the bright band, or snow below.

## Slide 9: Step 3: Winner selection
Once all the scores are computed, the target category with the highest score is generally chosen as the target type at that location.
Scoreinsects = 0.82
Scorerain = 0.64
Scorebirds= 0.51
Scoreground_clutter = 0.27
…

## Slide 10: Generation of a target ID map
Some categories may sometimes be regrouped (e.g., birds and insects into “biological”), and maps of target ID can then be generated.
Scorebiological = 0.82
Scorerain = 0.64
Scoreground_clutter = 0.27
…
These maps are useful as is, but they also often help clean the input data used by other algorithms such as for precipitation estimation or severe weather detection.