## Slide 1: Supplement e06.1: The fluctuating radar signal at dual-polarization

## Slide 2: Remember this?
In the supplement e02.6, we investigated how the signal from multiple targets combined to provide the basic amplitude and phase data from which reflectivity and Doppler velocity are derived.
Now, let us consider what can be obtained when a second polarization is added.

## Slide 3: Case 1: Targets with similar shapes
Two copolar signals are obtained, one at horizontal and one at vertical polarization.
Let us first assume that all targets are Rayleigh scatterers and have the same shape, and focus on the differences between H and V:
1) In this case where a lot of rain was in the path, the V transmit wave is slightly ahead of the H. This will lead to a systematic 2-way differential propagation phase Φdp between H and V returns.

## Slide 4: Case 1: Targets with similar shapes
2) Because all target shapes are identical, the amplitude AH of the signal from every target at horizontal polarization is a constant factor Zdr.5 larger than the amplitude AV at vertical polarization. When these amplitudes will be used to compute power and reflectivity, the ratio of the two powers at H and V will be Zdr.
Now let us get all targets moving.

## Slide 5: Case 1: Targets with similar shapes
Since the returns from every target have a) a constant amplitude ratio Zdr.5 and b) a constant phase difference Φdp, the final combined signal does so too, all the time.
Therefore, the time series of amplitudes and phases at H and V are perfectly correlated. The magnitude ρco of the complex copolar correlation coefficient between these time series can be evaluated; here, ρco would be 1.

## Slide 6: Case 2: Targets with different shapes
Now let us alternate between targets having identical shapes, and targets having different shapes and compare the two (here, only the V returns are changing).
1) Because of changes in shapes, the signal from each target at V polarization is also changing, but differently for each target. As a result, the final signal is different from what it was with similar-shaped targets, but most importantly different from the V signal.

## Slide 7: Case 2: Targets with different shapes
Thanks to the variety in the Zdr of each target, the combined H and V signals are not perfectly correlated in time anymore. ρco is now less than 1.
The copolar correlation coefficient ρco is hence a measure of the uniformity in target shapes, returns from Rayleigh targets of similar shapes having high ρco, and lower ρco being associated with targets with varying shapes.

## Slide 8: Case 3: Targets with different scattering delays
And if differential delays on scattering also change from target to target (more common for Mie or larger targets), ρco is lowered further (see the amplitude plot).