## Slide 1: Digital Design: A Systems Approach Lecture 6: Sequential Logic

## Slide 2: Readings
L6: Chapter 14
L7: Chapter 16

## Slide 3: Today
Sequential logic: circuits with state
  Synchronizes state transitions to a clock
D Flip-flops (DFF)
Finite state machines (FSMs)
  One-hot
  Binary
Desigining state machines
  State/input tables
FSMs in Verilog
  Style
  Explicit state declaration

## Slide 4: Sequential logic has state
Combinational Logic
Sequential Logic

## Slide 5: D Flip-Flop
Input: D
Output: Q
Clock
Q outputs a steady value
Edge on Clock changes Q to be D
Flip-flop stores state
Allows sequential circuits to iterate
D
Q
^
d
q
clk
D
Q
^
s
s
clk
d
q

## Slide 6: Synchronous Sequential Logic
A
B
C
B
C
D
A
B
C

## Slide 7: Example Sequential Circuit: Increment
Adder
n
n
n
1
clk
^
  Q
  D
Increment a count on every clock tick
Just wrap around on overflow
Maintaining state has a lot more uses than arithmetic

## Slide 8: Example: A Traffic-Light Controller
carew

## Slide 9: Traffic Light FSM Behavior
Reset to green in north-south direction
If light is green or yellow in one direction, it must be red in the other
A light must be yellow between changing from green to red
If there is a car waiting east-west, then east-west should become green before returning to green north-south

## Slide 10: Traffic Light FSM
Finite state machine is specified by
  States, Inputs, Outputs
Four states
  Green north-south (red east-west)
  Yellow north-south (red east-west)
  Green east-west (red north-south)
  Yellow east-west (red north-south)
Input
  Carew: is there a car waiting on the east-west road
  Reset: return to initial state (need not go through yellow)
Output: Two 3-bit traffic light signals (1-hot) (gyr gyr)
  100 001: NS green, EW red; 001 010 NS red, EW yellow

## Slide 11: Complete Traffic Light State machine
gns
100 001
yns 010 001
gew
001 100
yew
001 010
¬carew | rst
carew & ¬rst
¬rst
¬rst
*
state output
= gyr gyr
ew
ns
carew = car east-west sensor active
rst = reset
rst
rst

## Slide 12: State Table (ignoring reset for now)
¬carew
carew
¬carew
carew

## Slide 13: State Assignment
Assign values to encode each state (gns, yns, gew, yew) on state and next_state signals

## Slide 14: One-Hot State Assignment

## Slide 15: Translating No-Reset FSM To One-Hot Controller
gns
100 001
yns 010 001
gew
001 100
yew
001 010
¬carew
carew
*
*
D
Q
^
D
Q
^
D
Q
^
D
Q
ns
ew
*
^
c
clk
*

## Slide 16: Binary State Assignment (Gray Code)

## Slide 17: Encoded state table and next-state K-maps
ns0 = (s0 | c) & ¬s1
ns1 = s0
c
s1s0
00
01
0
1
11
10
s0
a1
ns1
c
c
s1s0
00
01
0
1
11
10
s0
s1
ns0
c
0
1
1
0
0
1
1
0
0
1
0
0
0
0
1
1
¬carew
carew

## Slide 18: Logic Equations
¬carew
carew
ns1 = s0
ns0 = (s0 | carew) & ¬s1
lgns = ¬s0 & ¬s1
lyns = s0 & ¬s1
lrns = s1
lgew = s0 & s1
lyew = ¬s0 & s1
lrew = ¬s1

## Slide 19: Implementation of traffic-light controller with binary state assignment
carew

## Slide 20: Another Example - Divide by 3 FSM
Output: (out) goes high once for each third cycle that input (in) is high
Example
  IN: 0101010011100
  OUT: 0000001000010
  Note one cycle delay

## Slide 21: Another Example - Divide by 3 FSM
Output: (out) goes high once for each third cycle that input (in) is high
Example
  IN: 0101010011100
  OUT: 0000001000010
  Note one cycle delay
Draw state diagram
  How many states do we need?
  What are the transitions?
  What are the outputs?
How do we make the output go high in the same cycle as the third input 1?

## Slide 22: FSMs in Verilog (Style guide)
All feedback through explicitly instantiated DFF module!
Next state and output functions are combinational – case or assign
  No “inferred latches”
Make sure you can reset your FSM
Use defines for state encoding (and width)

## Slide 23
//---------------------------------------------
// FSM Example for Lecture 7
// Bill Dally 1/30/03
//---------------------------------------------
// define state assignment - one hot
//---------------------------------------------
`define SWIDTH 4
`define GNS 4'b1000
`define YNS 4'b0100
`define GEW 4'b0010
`define YEW 4'b0001
//---------------------------------------------
// define output codes
//---------------------------------------------
`define GNSL 6'b100001
`define YNSL 6'b010001
`define GEWL 6'b001100
`define YEWL 6'b001010
//---------------------------------------------
// define flip-flop
//---------------------------------------------
module DFF(clk, in, out) ;
parameter n = 1; // width
input clk ;
input [n-1:0] in ;
output [n-1:0] out ;
reg [n-1:0] out ;
always @(posedge clk)
out = in ;
endmodule
//------------------------------------------------------
// Traffic_Light
// Inputs:
// clk - system clock
// rst - reset - high true
// carew - car east/west - true when car is waiting in east-west direction
// Outputs:
// lights - (6 bits) {gns, yns, rns, gew, yew, rew}
// Waits in state GNS until carew is true, then sequences YNS, GEW, YEW
// and back to GNS.
//------------------------------------------------------
module Traffic_Light(clk, rst, carew, lights) ;
input clk ;
input rst ; // reset
input carew ; // car present on east-west road
output [5:0] lights ; // {gns, yns, rns, gew, yew, rew}
wire [`SWIDTH-1:0] state, next ; // current and next state
reg [`SWIDTH-1:0] next1 ; // next state w/o reset
reg [5:0] lights ; // output - six lights 1=on
// instantiate state register
DFF #(`SWIDTH) state_reg(clk, next, state) ;
// next state and output equations - this is combinational logic
always @(state or carew) begin
case(state)
`GNS: {next1, lights} = {(carew ? `YNS : `GNS), `GNSL} ;
`YNS: {next1, lights} = {`GEW, `YNSL} ;
`GEW: {next1, lights} = {`YEW, `GEWL} ;
`YEW: {next1, lights} = {`GNS, `YEWL} ;
endcase
end
// add reset
assign next = rst ? `GNS : next1 ;
endmodule
¬carew
carew

## Slide 24: Feedback (state) in explicitly declared DFF module
//---------------------------------------------
// FSM Example for Lecture 7
// Bill Dally 1/30/03
//---------------------------------------------
// define state assignment - one hot
//---------------------------------------------
`define SWIDTH 4
`define GNS 4'b1000
`define YNS 4'b0100
`define GEW 4'b0010
`define YEW 4'b0001
//---------------------------------------------
// define output codes
//---------------------------------------------
`define GNSL 6'b100001
`define YNSL 6'b010001
`define GEWL 6'b001100
`define YEWL 6'b001010
//---------------------------------------------
// define flip-flop
//---------------------------------------------
module DFF(clk, in, out) ;
parameter n = 1; // width
input clk ;
input [n-1:0] in ;
output [n-1:0] out ;
reg [n-1:0] out ;
always @(posedge clk)
out = in ;
endmodule
//------------------------------------------------------
// Traffic_Light
// Inputs:
// clk - system clock
// rst - reset - high true
// carew - car east/west - true when car is waiting in east-west direction
// Outputs:
// lights - (6 bits) {gns, yns, rns, gew, yew, rew}
// Waits in state GNS until carew is true, then sequences YNS, GEW, YEW
// and back to GNS.
//------------------------------------------------------
module Traffic_Light(clk, rst, carew, lights) ;
input clk ;
input rst ; // reset
input carew ; // car present on east-west road
output [5:0] lights ; // {gns, yns, rns, gew, yew, rew}
wire [`SWIDTH-1:0] state, next ; // current and next state
reg [`SWIDTH-1:0] next1 ; // next state w/o reset
reg [5:0] lights ; // output - six lights 1=on
// instantiate state register
DFF #(`SWIDTH) state_reg(clk, next, state) ;
// next state and output equations - this is combinational logic
always @(state or carew) begin
case(state)
`GNS: {next1, lights} = {(carew ? `YNS : `GNS), `GNSL} ;
`YNS: {next1, lights} = {`GEW, `YNSL} ;
`GEW: {next1, lights} = {`YEW, `GEWL} ;
`YEW: {next1, lights} = {`GNS, `YEWL} ;
endcase
end
// add reset
assign next = rst ? `GNS : next1 ;
endmodule

## Slide 25: Next-state and output functions are combinational
//---------------------------------------------
// FSM Example for Lecture 7
// Bill Dally 1/30/03
//---------------------------------------------
// define state assignment - one hot
//---------------------------------------------
`define SWIDTH 4
`define GNS 4'b1000
`define YNS 4'b0100
`define GEW 4'b0010
`define YEW 4'b0001
//---------------------------------------------
// define output codes
//---------------------------------------------
`define GNSL 6'b100001
`define YNSL 6'b010001
`define GEWL 6'b001100
`define YEWL 6'b001010
//---------------------------------------------
// define flip-flop
//---------------------------------------------
module DFF(clk, in, out) ;
parameter n = 1; // width
input clk ;
input [n-1:0] in ;
output [n-1:0] out ;
reg [n-1:0] out ;
always @(posedge clk)
out = in ;
endmodule
//------------------------------------------------------
// Traffic_Light
// Inputs:
// clk - system clock
// rst - reset - high true
// carew - car east/west - true when car is waiting in east-west direction
// Outputs:
// lights - (6 bits) {gns, yns, rns, gew, yew, rew}
// Waits in state GNS until carew is true, then sequences YNS, GEW, YEW
// and back to GNS.
//------------------------------------------------------
module Traffic_Light(clk, rst, carew, lights) ;
input clk ;
input rst ; // reset
input carew ; // car present on east-west road
output [5:0] lights ; // {gns, yns, rns, gew, yew, rew}
wire [`SWIDTH-1:0] state, next ; // current and next state
reg [`SWIDTH-1:0] next1 ; // next state w/o reset
reg [5:0] lights ; // output - six lights 1=on
// instantiate state register
DFF #(`SWIDTH) state_reg(clk, next, state) ;
// next state and output equations - this is combinational logic
always @(state or carew) begin
case(state)
`GNS: {next1, lights} = {(carew ? `YNS : `GNS), `GNSL} ;
`YNS: {next1, lights} = {`GEW, `YNSL} ;
`GEW: {next1, lights} = {`YEW, `GEWL} ;
`YEW: {next1, lights} = {`GNS, `YEWL} ;
endcase
end
// add reset
assign next = rst ? `GNS : next1 ;
endmodule
Case statement concatenation to assign next state and outputs

## Slide 26: Explicit reset
//---------------------------------------------
// FSM Example for Lecture 7
// Bill Dally 1/30/03
//---------------------------------------------
// define state assignment - one hot
//---------------------------------------------
`define SWIDTH 4
`define GNS 4'b1000
`define YNS 4'b0100
`define GEW 4'b0010
`define YEW 4'b0001
//---------------------------------------------
// define output codes
//---------------------------------------------
`define GNSL 6'b100001
`define YNSL 6'b010001
`define GEWL 6'b001100
`define YEWL 6'b001010
//---------------------------------------------
// define flip-flop
//---------------------------------------------
module DFF(clk, in, out) ;
parameter n = 1; // width
input clk ;
input [n-1:0] in ;
output [n-1:0] out ;
reg [n-1:0] out ;
always @(posedge clk)
out = in ;
endmodule
//------------------------------------------------------
// Traffic_Light
// Inputs:
// clk - system clock
// rst - reset - high true
// carew - car east/west - true when car is waiting in east-west direction
// Outputs:
// lights - (6 bits) {gns, yns, rns, gew, yew, rew}
// Waits in state GNS until carew is true, then sequences YNS, GEW, YEW
// and back to GNS.
//------------------------------------------------------
module Traffic_Light(clk, rst, carew, lights) ;
input clk ;
input rst ; // reset
input carew ; // car present on east-west road
output [5:0] lights ; // {gns, yns, rns, gew, yew, rew}
wire [`SWIDTH-1:0] state, next ; // current and next state
reg [`SWIDTH-1:0] next1 ; // next state w/o reset
reg [5:0] lights ; // output - six lights 1=on
// instantiate state register
DFF #(`SWIDTH) state_reg(clk, next, state) ;
// next state and output equations - this is combinational logic
always @(state or carew) begin
case(state)
`GNS: {next1, lights} = {(carew ? `YNS : `GNS), `GNSL} ;
`YNS: {next1, lights} = {`GEW, `YNSL} ;
`GEW: {next1, lights} = {`YEW, `GEWL} ;
`YEW: {next1, lights} = {`GNS, `YEWL} ;
endcase
end
// add reset
assign next = rst ? `GNS : next1 ;
endmodule
Separate assign for reset

## Slide 27: Use defines for state assignment and width Defines for output codes are a good idea too.
//---------------------------------------------
// FSM Example for Lecture 7
// Bill Dally 1/30/03
//---------------------------------------------
// define state assignment - one hot
//---------------------------------------------
`define SWIDTH 4
`define GNS 4'b1000
`define YNS 4'b0100
`define GEW 4'b0010
`define YEW 4'b0001
//---------------------------------------------
// define output codes
//---------------------------------------------
`define GNSL 6'b100001
`define YNSL 6'b010001
`define GEWL 6'b001100
`define YEWL 6'b001010
//---------------------------------------------
// define flip-flop
//---------------------------------------------
module DFF(clk, in, out) ;
parameter n = 1; // width
input clk ;
input [n-1:0] in ;
output [n-1:0] out ;
reg [n-1:0] out ;
always @(posedge clk)
out = in ;
endmodule
//------------------------------------------------------
// Traffic_Light
// Inputs:
// clk - system clock
// rst - reset - high true
// carew - car east/west - true when car is waiting in east-west direction
// Outputs:
// lights - (6 bits) {gns, yns, rns, gew, yew, rew}
// Waits in state GNS until carew is true, then sequences YNS, GEW, YEW
// and back to GNS.
//------------------------------------------------------
module Traffic_Light(clk, rst, carew, lights) ;
input clk ;
input rst ; // reset
input carew ; // car present on east-west road
output [5:0] lights ; // {gns, yns, rns, gew, yew, rew}
wire [`SWIDTH-1:0] state, next ; // current and next state
reg [`SWIDTH-1:0] next1 ; // next state w/o reset
reg [5:0] lights ; // output - six lights 1=on
// instantiate state register
DFF #(`SWIDTH) state_reg(clk, next, state) ;
// next state and output equations - this is combinational logic
always @* begin
case(state)
`GNS: {next1, lights} = {(carew ? `YNS : `GNS), `GNSL} ;
`YNS: {next1, lights} = {`GEW, `YNSL} ;
`GEW: {next1, lights} = {`YEW, `GEWL} ;
`YEW: {next1, lights} = {`GNS, `YEWL} ;
endcase
end
// add reset
assign next = rst ? `GNS : next1 ;
endmodule

## Slide 28
# 0 x xxxx xxxxxx
# 1 0 xxxx xxxxxx
# 0 0 1000 100001
# 0 0 1000 100001
# 0 0 1000 100001
# 0 1 1000 100001
# 0 0 0100 010001
# 0 0 0010 001100
# 0 0 0001 001010
# 0 0 1000 100001
# 0 0 1000 100001
# 0 0 1000 100001
# 0 1 1000 100001
# 0 1 0100 010001
# 0 1 0010 001100
# 0 1 0001 001010
# 0 1 1000 100001
# 0 1 0100 010001
# 0 1 0010 001100
# 0 1 0001 001010
//-----------------------------------------------
// test bench
//-----------------------------------------------
module test_fsm1 ;
reg clk, rst, carew ;
wire [5:0] lights ;
traffic_light tl(clk, rst, carew, lights) ;
// clock with period of 10 units
initial
forever
begin
#5 clk = 1 ; #5 clk = 0 ;
$display("%b %b %b %b",
rst, carew, tl.state, lights ) ;
end
// input stimuli
initial begin
#10 rst = 0 ; // start w/o reset to show x state
#20 rst = 1 ; carew = 0 ; // reset
#10 rst = 0 ; // remove reset
#30 carew = 1 ; // wait 3 cycles, then car arrives
#10 carew = 0 ; // car leaves
#60 carew = 1 ; // wait 6 cycles then car comes and stays
#80 // 8 more cycles
$stop ;
end
endmodule

## Slide 29
# 0 x xxxx xxxxxx
# 1 0 xxxx xxxxxx
# 0 0 1000 100001
# 0 0 1000 100001
# 0 0 1000 100001
# 0 1 1000 100001
# 0 0 0100 010001
# 0 0 0010 001100
# 0 0 0001 001010
# 0 0 1000 100001
# 0 0 1000 100001
# 0 0 1000 100001
# 0 1 1000 100001
# 0 1 0100 010001
# 0 1 0010 001100
# 0 1 0001 001010
# 0 1 1000 100001
# 0 1 0100 010001
# 0 1 0010 001100
# 0 1 0001 001010
//-----------------------------------------------
// test bench
//-----------------------------------------------
module test_fsm1 ;
reg clk, rst, carew ;
wire [5:0] lights ;
traffic_light tl(clk, rst, carew, lights) ;
// clock with period of 10 units
initial
forever
begin
#5 clk = 1 ; #5 clk = 0 ;
$display("%b %b %b %b",
rst, carew, tl.state, lights ) ;
end
// input stimuli
initial begin
#10 rst = 0 ; // start w/o reset to show x state
#20 rst = 1 ; carew = 0 ; // reset
#10 rst = 0 ; // remove reset
#30 carew = 1 ; // wait 3 cycles, then car arrives
#10 carew = 0 ; // car leaves
#60 carew = 1 ; // wait 6 cycles then car comes and stays
#80 // 8 more cycles
$stop ;
end
endmodule
State starts at X need to reset

## Slide 30
# 0 x xxxx xxxxxx
# 1 0 xxxx xxxxxx
# 0 0 1000 100001
# 0 0 1000 100001
# 0 0 1000 100001
# 0 1 1000 100001
# 0 0 0100 010001
# 0 0 0010 001100
# 0 0 0001 001010
# 0 0 1000 100001
# 0 0 1000 100001
# 0 0 1000 100001
# 0 1 1000 100001
# 0 1 0100 010001
# 0 1 0010 001100
# 0 1 0001 001010
# 0 1 1000 100001
# 0 1 0100 010001
# 0 1 0010 001100
# 0 1 0001 001010
//-----------------------------------------------
// test bench
//-----------------------------------------------
module test_fsm1 ;
reg clk, rst, carew ;
wire [5:0] lights ;
traffic_light tl(clk, rst, carew, lights) ;
// clock with period of 10 units
initial
forever
begin
#5 clk = 1 ; #5 clk = 0 ;
$display("%b %b %b %b",
rst, carew, tl.state, lights ) ;
end
// input stimuli
initial begin
#10 rst = 0 ; // start w/o reset to show x state
#20 rst = 1 ; carew = 0 ; // reset
#10 rst = 0 ; // remove reset
#30 carew = 1 ; // wait 3 cycles, then car arrives
#10 carew = 0 ; // car leaves
#60 carew = 1 ; // wait 6 cycles then car comes and stays
#80 // 8 more cycles
$stop ;
end
endmodule
Car arrives on east-west road

## Slide 31: Change the state assignment with defines
//----------------------------------
// define state assignment - Gray code
//----------------------------------
`define SWIDTH 2
`define GNS 2'b00
`define YNS 2'b01
`define GEW 2'b11
`define YEW 2'b10

## Slide 32
# 0 x xx xxxxxx
# 1 0 xx xxxxxx
# 0 0 00 100001
# 0 0 00 100001
# 0 0 00 100001
# 0 1 00 100001
# 0 0 01 010001
# 0 0 11 001100
# 0 0 10 001010
# 0 0 00 100001
# 0 0 00 100001
# 0 0 00 100001
# 0 1 00 100001
# 0 1 01 010001
# 0 1 11 001100
# 0 1 10 001010
# 0 1 00 100001
# 0 1 01 010001
# 0 1 11 001100
# 0 1 10 001010

## Slide 33: Summary
Sequential logic
  State feedback around combinational logic
Synchronous sequential logic
  State register synchronizes state transitions with a clock
  All bits of state are updated at the same time on the rising edge of the clock
  Reduces synchronous machine design to combinational design of next-state function
State diagram and table describe next-state and output functions
State assignment
  Assign binary codes to states – one hot or binary
Implementation
  Design combinational logic for next-state and output functions
Verilog
  Explicitly instantiate flip-flops
  Case (or casex) statement for next-state function
  Use defines for state assignment

## Slide 34: Next Time
Data Path FSMs