## Slide 1: Supplement e13.2: Received power, signal and noise

## Slide 2: Signal and noise: The theory
Equation (3.4) describes the power of the signal Pr that we need to compute Ze while (13.3) does the same for the competing noise PN.
These equations are valid at the antenna. But this is not what the radar really measures.
Pr
PN

## Slide 3: Signal and noise: The reality
The signal and noise powers P’r and P’N that are really seen by the radar are those detected and computed by the signal processor. In between, many radar components transform the original powers Pr and PN.
P’r
P’N
Pr
PN

## Slide 4: Going from Pr and PN to P’r and P’N: Understanding the receiver
P’r
P’N
Pr
PN
To compute P’r, P’N, and the true signal-to-noise ratio (SNR) requires a conceptual understanding of what every receiver component does to signal and noise. This will also serve as our motivation to explore a bit deeper how the receiver operates.

## Slide 5: Key sections of the receiving system: 1) The path to the first amplifier
P’r
P’N
Pr
PN
Received signals are extremely weak. To further process or analyze them, they must be amplified as quickly as possible. But there is a necessary distance and number of components between the antenna and the first amplifier. Over that path, losses occur.

## Slide 6: Key sections of the receiving system: 2) The first (low-noise) amplifiers
P’r
P’N
Pr
PN
Radio frequency (RF) low-noise amplifiers do just that: they try to amplify the signal and noise they receive on input as accurately as possible. Each amplifier has a specific gain (the multiplicative factor by which they amplify the signal) and also introduces some noise.

## Slide 7: Key sections of the receiving system: 3) The mixing system
P’r
P’N
Pr
PN
intermediate frequency (IF) signal also introduces losses and noise, hence the need for additional amplifiers behind.
Except perhaps for wind profilers, radio frequencies oscillate too rapidly to be digitized at a reasonable cost with the current technology. The frequency of the RF signal must hence be reduced using a process known as mixing. This transformation of the RF signal into an

## Slide 8: Key sections of the receiving system: 4) The digitizer and signal processor
P’r
P’N
Pr
PN
Finally, the digitizer converts the IF analog signal into numbers.
These are then passed to the signal processor that must interpret them and compute the signal and noise powers. These computed quantities are finally used to estimate Ze and other radar measurements.

## Slide 9: The outcome of signal and noise: Opening the receiver black box
P’r
P’N
Pr
PN
We now go over each of those key sections to understand what happens to signal and noise.
For illustration purposes, we will assume a typical value for PN at a few degrees elevation (noise temperature TA of 50 K, bandwidth B of 1 MHz,
leading to PN = kBTA of about 7*10−16 W), and a weak signal Pr such that Pr = PN.

## Slide 10: Component specifications jargon: A brief introduction (I)
The transformation of the signal by different components can be described by a set of characteristics that these components have. These include:
Losses: Components are not perfect conductors; losses occur. Losses L are generally expressed in dB such that:
Pout = Pin 10−L/10.
A circulator for example may have a loss of about 0.3 dB. In that case, the signal power will be reduced to 10 −0.3/10 or 93% of its original value.
Some components such as waveguides and cables have losses per unit distance, e.g., 0.045 dB/m for copper waveguides at C-band. A 40-m waveguide run from the feed to the receiver at the base of the radar tower would hence have a loss of 40*0.045 = 1.8 dB, reducing the signal Pin by one-third (note that that same loss also occurs on transmit).

## Slide 11: Reminder: Effects of losses on signal vs. noise
An attenuator is also an emitter (see Kirchoff’s Law). Therefore, any component that reduces signal also adds to noise in the process.
At microwave frequencies, that added noise is a linear function of the absorptivity of the component (1 – 10−L/10) and of its physical temperature Tcomponent in K.
As a result, a component with a loss L modify signal and noise by:
Pr-out = Pr-in 10−L/10, and
PN-out = PN-in 10−L/10 + kB (1 – 10−L/10)Tcomponent,
k being the Boltzmann constant (1.381 × 10−23 J/K), and B the
bandwidth of the receiver (here, 1,000,000 Hz).
Therefore, all along the receiver path, noise gradually gains on signal.

## Slide 12: Component specifications jargon: A brief introduction (II)
The transformation of the signal by different components can be described by a set of characteristics that these components have. These include:
Gain: Amplifiers have gains G, also expressed in dB, such that:
Pout = Pin 10G/10.
An amplifier with a 40 dB gain amplify all inputs by a factor 10,000.
Noise value: Amplifiers also add to the noise. This is expressed as a noise value N (in dB of course).
The net result is that amplification is different for signal and noise:
Pr-out = Pr-in 10−N/1010(G+N)/10 = Pr-in 10G/10, and
PN-out = [PN-in 10−N/10 + kB (1 – 10−N/10)Tcomponent]10(G+N)/10.

## Slide 13: Calculations of final signal power
Computing signal and noise at every step is a long process.
But there are shortcuts: For computing the signal power at different stages of the receiver, losses and gains of all the components in dBs prior to that stage can be added to ease calculations because:
P3 = P2 10B/10 = (P1 10A/10) 10B/10 = P1 10 (A+B)/10.
For noise, a similar shortcut is possible but a) for sections with passive components only (no gain involved), and b) if the temperatures of all the components are similar:
P3 = P2 10L2/10 + kB (1 – 10−L2/10)Tcomponent
= {[P1 10L1/10 + kB (1 – 10−L1/10)Tcomponent] 10L2/10 + kB (1 – 10−L2/10)Tcomponent}
= P1 10(L1+L2)/10 + kB [1 – 10−(L1+L2)/10]Tcomponent
It is now time to compute signal and noise strengths at different stages.

## Slide 14: Noise and power in the receiver 1) At the low noise amplifier input
P’r
P’N
Pr
PN
Let us only consider a 40-m C-band copper waveguide, and a circulator at room temperatures (290K). There are no active components; the losses can hence be summed to simplify calculations:
L = Lwaveguides + Lcirculator = 40*0.045+ 0.3 = 2.1 dB. Hence:
Pr(up-to-LNA) = Pr 10L/10 = 0.62 Pr ≈ 4.3*10 −16 W
PN(up-to-LNA) = PN 10L/10 + kB (1 – 10−L/10)Tcomponent
= 0.62PN + 0.38kBTcomponent ≈ 2*10 −15 W
Time to reflect: Just with waveguides and circulator, we went from a signal-to-noise ratio of 1 (0 dB) to one around 0.215 (−6.6 dB). It gets worse.

## Slide 15: Noise and power in the receiver 2) Contribution from the LNA
A good low-noise amplifier (LNA) at S- or C-band has a noise figure N of about 0.8 dB for a gain G of 40 dB. This will then lead to:
Pr(after LNA) = Pr(up-to-LNA) 10G/10 ≈ 4.3*10−12 W, and
PN(after LNA) = [PN(up-to-LNA) 10−N/10 + kB (1 – 10−N/10)Tcomponent]10(G+N)/10
= [2*10−15 10−0.8/10 + kB (1 – 10−0.8/10)290]10(40.8)/10
≈2.8*10−11 W  SNR ≈ 0.154 or −8.1 dB.
The relative increase of noise compared to signal essentially stops here: if the LNA gain is sufficient, additional noise contributions should be small compared to the existing amplified noise.
Notes: 1.66 10-15 +

## Slide 16: Noise and power in the receiver 3a) The mixing system explained
Mixers multiply the oscillating signal from two sources. Given the received signal of frequency f and an internal reference of frequency fLO,
sin(2πft+φ) cos(2πfLOt) = ½ {sin[2πt(f+fLO)+φ)] + sin[2πt(f−fLO)+φ)]}:
The output of a mixer is hence two superposed waves of frequencies f−fLO and f+fLO. If fLO is chosen to be close to f, the intermediate frequency fIF = f−fLO is much smaller than f (often 60 MHz), while the much higher f+fLO can be subsequently filtered.
Also note that any phase shift φ in the input signal is preserved by mixing and does not affect our ability to make Doppler measurements.

## Slide 17: Noise and power in the receiver 3b) The mixing system and noise
Mixers have considerable losses, of the order of 8 dB. And in the process of removing the unwanted signal, the subsequent filters also reduce the wanted signal by about 1 dB.
In parallel, the digitizer that follows the mixing requires the signal to have enough voltage (and hence power) to be measured; a last amplification stage is therefore needed, often another 30 dB of gain.
Given Pr(after LNA) ≈ 4.3*10−12 W and PN(after LNA) ≈2.8*10−11 W, one should finally get P’r ≈ 5.4*10−10 W and P’N ≈3.5*10 −9 W, with no significant change to the SNR.
Notes: Pr(post filter) = Pr(after LNA) 10(8+1)/10 ≈ 5.4*10−13 W; After a 30 dB gain, P’r then becomes 5.4*10−10 W.
PN(post filter) = PN(after LNA) 10(8+1)/10 + kB (1 – 10−(8+1)/10)Tcomponent ≈ 3.5*10−12 + 3.5*10−15 ≈ 3.5*10−12 ; new noise is tiny wrt old.

## Slide 18: Conclusion and implications (I)
P’r
P’N
Pr
PN
calculations must therefore include the contribution of receiver components.
The signal power P’r measured at the signal processor is obviously very different from the signal Pr received by the antenna, but since we know the components gains and losses, we can computed Pr.
Noise also changed, and increased more than signal. Proper SNR

## Slide 19: Conclusion and implications (II)
P’r
P’N
Pr
PN
Pr(up-to-LNA) = Pr 10L/10 vs. PN(up-to-LNA) = PN 10L/10 + kB (1 – 10−L/10)Tcomponent
For a given radar pulse length and bandwidth, two courses of action are possible to minimize the degradation of SNR in the receiver: reduce losses (shorter/better waveguides, better LNAs, etc.) or have a cooled
receiver (smaller Tcomponent). Radio-telescopes use these techniques, but they are often not compatible with low-maintenance operational systems.

## Slide 21: On the treatment of bandwidth and noise in this discussion
P’r
P’N
Pr
PN
In all latter calculations, I assume that noise has a constant relatively narrow bandwidth B of 1 MHz. Purists will accurately comment that noise actually has a wide bandwidth that gets reduced by filters in the receiver. I chose to consider “noise after frequency filtering” in all
calculations not to further complicate this already fairly technical discussion.
Back to the black box slide.