## Slide 1: Supplement e13.1: Phasing antennas

## Slide 2: Reflector antenna
Traditional “reflector antenna” generally use a single source, the feed, and a parabolic reflector to focus the energy in one direction. To scan, feed and reflector must rotate together.

## Slide 3: Reflector antenna and antenna arrays
At its basis, the “focusing” of the energy is achieved because the reflector acts as a multitude of point antennas. These work together in such a way that the reflections from each element of the reflector combine constructively in one direction, and destructively in others.
The same can be achieved by having a large number of emitting antennas, known as antenna arrays.

## Slide 4: Antenna arrays and wind profilers
Most wind profilers are designed as antenna arrays because they are simpler to build and more flexible to use then the giant reflectors that would be needed to achieve the same beam width.
See, for example, this photo (and the enlarged section) of the MU Radar.

## Slide 5: “Pointing” an antenna array
Transmit phase φk
Position x
Consider the set of emitting antennas shown in red ( ). Let us also assume that they all transmit pulses simultaneously with the same phase (as in the previous illustrations, black lines illustrate the position of the waves’ crests).
Mathematically, we can write the transmit signal from antenna k as:
V(k) = Ak sin(2πft+φk),
where Ak is the amplitude of the transmit signal, f is the transmit frequency, t is time, and φk is the phase shift of the transmit pulse from each antenna with respect to an internal reference wave of frequency f. In this first scenario, φk is identical for all k.
k= 1 2 3 4 5 6

## Slide 6: “Pointing” an antenna array
Transmit phase φk
If the transmit phase shift is identical for all antennas (φk = constant for all k), and all antennas are on a plane, then the combined wave propagates perpendicular to that plane (here, vertically).
This is best seen at far ranges where the emissions from all antennas interfere constructively in the vertical direction and more or less destructively in others.
Position x
k= 1 2 3 4 5 6

## Slide 7: “Pointing” an antenna array
Transmit phase φk
For example, let us vary the transmit phase shift φk such that:
φk = a x(k) + φo
where a is a constant, x(k) is the position of the antenna k, and φo a constant identical for all k.
This is illustrated on the image on the lower left.
What will now happen to the constructive interference pattern from all the antennas at far range?
Position x
k= 1 2 3 4 5 6
There is no special reason why the transmit phase shift φk should be identical for all antennas. In fact, the real value of antenna arrays lies in our ability to have a different φk for each antenna.
This forms the basis behind phased array antennas.

## Slide 8: “Pointing” an antenna array
Transmit phase φk
In this case, the constructive interference propagates with an angle θ compared to previously. For −λ < a < λ, that angle is determined by:
θ = sin−1(a/λ)
where λ is the radar wavelength.
Therefore, by changing the transmit and receive phase shifts of individual antennas, it is possible to “point” the radar antenna array in different directions.
“Scanning” therefore becomes as quick as the speed at which φk can be changed.
k= 1 2 3 4 5 6
Position x