## Slide 1: Digital Design: A Systems Approach Lecture 7: Data Path State Machines

## Slide 2: Readings
L7: Chapter 16
L8: Chapter 17

## Slide 3: Review
Lecture 1 – Digital abstraction
Lecture 2 – Combinational logic design
Lecture 3 – Combinational building blocks
Lecture 4 – Numbers and arithmetic
Lecture 5 – Quiz 1 Review
Lecture 6 – Sequential Logic, FSMs
Lecture 7 – Datapath FSMs
Lecture 8 - Factoring FSMs
Lecture 9 - Microcode

## Slide 4: An FSM is a state register and two functions

## Slide 5: A Simple Counter
Suppose you want to build an FSM with the following state diagram

## Slide 6
module Counter1(clk,rst,out) ;
input rst, clk ; // reset and clock
output [4:0] out ;
reg [4:0] next ;
DFF #(5) count(clk, next, out) ;
always@(rst, out) begin
casex({rst,out})
6'b1xxxxx: next = 0 ;
6'd0: next = 1 ;
6'd1: next = 2 ;
6'd2: next = 3 ;
6'd3: next = 4 ;
6'd4: next = 5 ;
6'd5: next = 6 ;
6'd6: next = 7 ;
…
6'd30: next = 31 ;
6'd31: next = 0 ;
default: next = 0 ;
endcase
end
endmodule
State | Next State | 
 | ~rst | rst
0 | 1 | 0
1 | 2 | 0
2 | 3 | 0
. . . |  | 
30 | 31 | 0
31 | 0 | 0

## Slide 7: Datapath Implementation
You can describe the next-state function with a table
However, it can more compactly be described by an expression:
next = r ? 0 : state + 1 ;
This “counter” is an example of a sequential “datapath” – a sequential circuit where the next state function is generated by an expression rather than a table.
State | Next State | 
 | ~rst | rst
0 | 1 | 0
1 | 2 | 0
2 | 3 | 0
. . . |  | 
30 | 31 | 0
31 | 0 | 0

## Slide 8: Verilog description
module Counter(clk, rst, count) ;
parameter n=5 ;
input rst, clk ; // reset and clock
output [n-1:0] count ;
wire [n-1:0] next = rst? 0 : count + 1 ;
DFF #(n) count(clk, next, count) ;
endmodule

## Slide 9: Make Table Symbolic
State | Next State | 
 | ~rst | rst
0 | 1 | 0
1 | 2 | 0
2 | 3 | 0
. . . |  | 
30 | 31 | 0
31 | 0 | 0
State | Next State | 
 | ~rst | rst
a | a+1 | 0

## Slide 10: Alternate description (symbolic table)
module Counter1(clk,rst,out) ;
input rst, clk ; // reset and clock
output [4:0] out ;
reg [4:0] next ;
DFF #(5) count(clk, next, out) ;
always@(rst, out) begin
case(rst)
1'b1: next = 0 ;
1'b0: next = out+1 ;
endcase
end
endmodule
module Counter1(clk,rst,out) ;
input rst, clk ; // reset and clock
output [4:0] out ;
reg [4:0] next ;
DFF #(5) count(clk, next, out) ;
always@(rst, out) begin
casex({rst,out})
6'b1xxxxx: next = 0 ;
6'd0: next = 1 ;
6'd1: next = 2 ;
6'd2: next = 3 ;
6'd3: next = 4 ;
6'd4: next = 5 ;
6'd5: next = 6 ;
6'd6: next = 7 ;
…
6'd30: next = 31 ;
6'd31: next = 0 ;
default: next = 0 ;
endcase
end
endmodule

## Slide 11: Schematic
A simple counter
next_state = rst ? 0 : state + 1

## Slide 12: Sequential Datapath

## Slide 13: An Up/Down/Load (UDL) Counter
A Deluxe Counter that can:
  count up (increment)
  count down (decrement)
  be loaded with a value
Up, down, and load guaranteed to be one-hot. Rst overrides.
if rst, next_state = 0 if (!rst & up) next_state = state+1 if (!rst & down) next_state = state-1 if (!rst & load) next_state = in else next_state = state

## Slide 14: Table Version
State | Next State |  |  | 
 | rst | up | down | load
0 | 0 | 1 | 31 | in
1 | 0 | 2 | 0 | in
2 | 0 | 3 | 1 | in
. . . |  |  |  | 
30 | 0 | 31 | 29 | in
31 | 0 | 0 | 30 | in

## Slide 15: Symbolic Table Version
State | Next State |  |  |  | 
 | rst | up | down | load | else
q | 0 | q+1 | q-1 | in | q
State | In | Rst | Up | Down | Load | Next
q | x | 1 | x | x | x | 0
q | x | 0 | 1 | 0 | 0 | q+1
q | x | 0 | 0 | 1 | 0 | q-1
x | y | 0 | 0 | 0 | 1 | y
q | x | 0 | 0 | 0 | 0 | q

## Slide 16: Schematic of UDL Counter

## Slide 17
module UDL_Count1(clk, rst, up, down, load, in, out) ;
parameter n = 4 ;
input clk, rst, up, down, load ;
input [n-1:0] in ;
output [n-1:0] out ;
wire [n-1:0] out ;
reg [n-1:0] next ;
DFF #(n) count(clk, next, out) ;
always@(rst, up, down, load, out) begin
casex({rst, up, down, load})
4'b1xxx: next = {n{1'b0}} ;
4'b0100: next = out + 1'b1 ;
4'b0010: next = out - 1'b1 ;
4'b0001: next = in ;
4’b0000: next = out ;
default: next = {n{1’bx}} ;
endcase
end
endmodule

## Slide 18
module UDL_Count1(clk, rst, up, down, load, in, out) ;
parameter n = 4 ;
input clk, rst, up, down, load ;
input [n-1:0] in ;
output [n-1:0] out ;
wire [n-1:0] out, outpm1 ;
reg [n-1:0] next ;
DFF #(n) count(clk, next, out) ;
assign outpm1 = out + {{n-1{down}},1'b1} ; // down ? -1 : 1
always@(rst, up, down, load, in, out, outpm1) begin
casex({rst, up, down, load})
4'b1xxx: next = {n{1'b0}} ;
4'b01xx: next = outpm1 ;
4'b001x: next = outpm1 ;
4'b0001: next = in ;
default: next = out ;
endcase
end
end
endmodule

## Slide 19: Timer module
load – loads count done – asserted when count = 0 count decrements unless load or done is true

## Slide 20
module Timer(clk, rst, load, in, done) ;
parameter n=4 ;
input clk, rst, load ;
input [n-1:0] in ;
output done ;
wire [n-1:0] count, next_count ;
wire done ;
DFF #(n) cnt(clk, next_count, count) ;
always@(rst, load, in, out) begin
casex({rst, load, done})
3'b1xx: next_count = 0 ; // reset
3'b001: next_count = 0 ; // done
3'b01x: next_count = in ; // load
default: next_count = count-1’b1; // count down
endcase
end
assign done = (count == 0) ;
endmodule

## Slide 21: Shift Register
next_state = rst ? 0 : {state[n-2:0],sin} ;

## Slide 22
module Shift_Register1(clk, rst, sin, out) ;
parameter n = 4 ;
input clk, rst, sin ;
output [n-1:0] out ;
wire [n-1:0] next = rst ? {n{1'b0}} : {out[n-2:0],sin} ;
DFF #(n) cnt(clk, next, out) ;
endmodule

## Slide 23
module LRL_Shift_Register1(clk, rst, left, right, load, sin, in, out) ;
parameter n = 4 ;
input clk, rst, left, right, load, sin ;
input [n-1:0] in ;
output [n-1:0] out ;
reg [n-1:0] next ;
DFF #(n) cnt(clk, next, out) ;
always @(*) begin
casex({rst,left,right,load})
4'b1xxx: next = 0 ; // reset
4'b01xx: next = {out[n-2:0],sin} ; // left
4'b001x: next = {sin,out[n-1:1]} ; // right
4'b0001: next = in ; // load
default: next = out ; // hold
endcase
end
endmodule

## Slide 24
rst down done lrlsrout
load sin udlcout
up cout srout
# 1 0 1 0 1 0000 1 0000 0000 0000
# 0 0 1 0 1 0000 1 0000 0000 0000
# 0 0 1 0 1 0001 1 0001 0001 0001
# 0 0 1 0 1 0010 1 0010 0011 0011
# 0 0 0 1 1 0011 1 0011 0111 0111
# 0 0 0 1 1 0100 1 0010 1111 1011
# 0 1 0 0 1 0101 1 0001 1111 1101
# 0 0 0 0 0 0110 0 0101 1111 0101
# 0 0 1 0 1 0111 0 0101 1110 0101
# 0 0 1 0 1 1000 0 0110 1101 1011
# 0 0 1 0 1 1001 0 0111 1011 0111
# 0 0 1 0 1 1010 0 1000 0111 1111
# 0 0 1 0 1 1011 1 1001 1111 1111
# 0 0 1 0 1 1100 1 1010 1111 1111

## Slide 25: Datapath/Control Partitioning
Datapath state – determined by a function – e.g., mux, arithmetic, … Control state – determined by state diagram or state table

## Slide 26: Consider a vending machine controller
Receives coins (nickel, dime, quarter) and accumulates sum
When “dispense” button is pressed serves a drink if enough coins have been deposited
Then returns change – one nickel at a time.
Partition task
Datapath – keep track of amount owed user
Control – keep track of sequence – deposit, serve, change

## Slide 27: State diagram for control portion

## Slide 28: Block diagram of data path

## Slide 29
//----------------------------------------------------------------------
// VendingMachine - Top level module
// Just hooks together control and datapath
//----------------------------------------------------------------------
module VendingMachine(clk, rst, nickel, dime, quarter, dispense, done, price,
serve, change) ;
parameter n = `DWIDTH ;
input clk, rst, nickel, dime, quarter, dispense, done ;
input [n-1:0] price ;
output serve, change ;
wire enough, zero, sub ;
wire [3:0] selval ;
wire [2:0] selnext ;
VendingMachineControl vmc(clk, rst, nickel, dime, quarter, dispense, done,
enough, zero, serve, change, selval, selnext, sub) ;
VendingMachineData #(n) vmd(clk, selval, selnext, sub, price, enough, zero) ;
endmodule

## Slide 30
//----------------------------------------------------------------------
module VendingMachineControl(clk, rst, nickel, dime, quarter, dispense, done,
enough, zero, serve, change, selval, selnext, sub) ;
input clk, rst, nickel, dime, quarter, dispense, done, enough, zero ;
output serve, change, sub ;
output [3:0] selval ;
output [2:0] selnext ;
wire [`SWIDTH-1:0] state, next ; // current and next state
reg [`SWIDTH-1:0] next1 ; // next state w/o reset
// outputs
wire first ; // true during first cycle of serve1 or change1
wire serve1 = (state == `SERVE1) ;
wire change1 = (state == `CHANGE1) ;
wire serve = serve1 & first ;
wire change = change1 & first ;
// datapath controls
wire dep = (state == `DEPOSIT) ;
// price, 1, 2, 5
wire [3:0] selval = {(dep & dispense),
((dep & nickel)| change),
(dep & dime),
(dep & quarter)} ;
// amount, sum, 0
wire selv = (dep & (nickel | dime | quarter |
(dispense & enough))) |
(change) ;
wire [2:0] selnext = {!(selv | rst),selv,rst} ;
// subtract
wire sub = (dep & dispense) | change ;
// only do actions on first cycle of serve1 or change1
wire nfirst = !(serve1 | change1) ;
DFF #(1) first_reg(clk, nfirst, first) ;
// state register
DFF #(`SWIDTH) state_reg(clk, next, state) ;
// next state logic
always @(state or zero or dispense or done or enough) begin
casex({dispense, enough, done, zero, state})
{4'b11xx,`DEPOSIT}: next1 = `SERVE1 ; // dispense & enough
{4'b0xxx,`DEPOSIT}: next1 = `DEPOSIT ;
{4'bx0xx,`DEPOSIT}: next1 = `DEPOSIT ;
{4'bxx1x,`SERVE1}: next1 = `SERVE2 ; // done
{4'bxx0x,`SERVE1}: next1 = `SERVE1 ;
{4'bxx01,`SERVE2}: next1 = `DEPOSIT ; // ~done & zero
{4'bxx00,`SERVE2}: next1 = `CHANGE1 ; // ~done & ~zero
{4'bxx1x,`SERVE2}: next1 = `SERVE2 ; // done
{4'bxx1x,`CHANGE1}: next1 = `CHANGE2 ; // done
{4'bxx0x,`CHANGE1}: next1 = `CHANGE1 ; // ~done
{4'bxx00,`CHANGE2}: next1 = `CHANGE1 ; // ~done & ~zero
{4'bxx01,`CHANGE2}: next1 = `DEPOSIT ; // ~done & zero
{4'bxx1x,`CHANGE2}: next1 = `CHANGE2 ; // done
endcase
end
// reset next state
assign next = rst ? `DEPOSIT : next1 ;
endmodule

## Slide 31
module VendingMachineData(clk, selval, selnext, sub, price, enough, zero) ;
parameter n = 6 ;
input clk, sub ;
input [3:0] selval ; // price, 1, 2, 5
input [2:0] selnext ; // amount, sum, 0
input [n-1:0] price ; // price of soft drink - in nickels
output enough ; // amount > price
output zero ; // amount = zero
wire [n-1:0] sum ; // output of add/subtract unit
wire [n-1:0] amount ; // current amount
wire [n-1:0] next ; // next amount
wire [n-1:0] value ; // value to add or subtract from amount
wire ovf ; // overflow - ignore for now
// state register holds current amount
DFF #(n) amt(clk, next, amount) ;
// select next state from 0, sum, or hold
Mux3 #(n) nsmux({n{1'b0}}, sum, amount, selnext, next) ;
// add or subtract a value from current amount
AddSub #(n) add(amount, value, sub, sum, ovf) ;
// select the value to add or subtract
Mux4 #(n) vmux(`QUARTER, `DIME, `NICKEL, price, selval, value) ;
// comparators
wire enough = (amount >= price) ;
wire zero = (amount == 0) ;
endmodule

## Slide 32: Waveforms for vending machine
Deposit Nickel
Deposit Dime
Attempt Dispense
Two Quarters
Dispense
Serve Drink
Return First Nickel
Return Second Nickel

## Slide 33: Summary
Datapath state machines
  Next state function specified by an expression, not a table
    next = rst ? 0 : (inc ? next + 1 : next) ;
  Common “idioms”
    Counters
    Shift registers
Datapath and control partitioning
  Divide state space into control (deposit, serve, change) and data
  FSM determines control state
  Datapath computes amount
    Status and control signals
  Special case of factoring