## Slide 1: Detection and Estimation of Buried Objects Using GPR
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
A.J. Devaney
Department of Electrical and Computer Engineering
Northeastern University
email: devaney@ece.neu.edu
Talk motivation: GPR imaging for buried targets
Talk Outline
Overview
Review of existing work
New work
Simulations
Future work and concluding remarks
Notes: Presented at the MITRE corporation in 2004. This talk examines the use of time reversal imaging to detecting buried objects using ground penetrating radar (GPR).
<number>

## Slide 2: Time-reversal Imaging for GPR
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
Intervening medium
Intervening medium
Without time-reversal compensation
With time-reversal compensation
In time-reversal imaging a sequence of illuminations is used such that each
incident wave is the time-reversed replica of the previous measured return
First illumination
Final illumination
Intermediate illumination
Intervening medium
Goal is to focus maximum amount of energy on target
for purposes of target detection and location estimation
Notes: <number>
Time-reversal imaging is a standard method used in ultrasound medical and industrial imaging. It is customarily performed experimentally where a target is illuminated (insonified) in a first experiment with a plane wave (all transducers pulsed in phase) and then the target is re-illuminated with the transducers now pulsed using the time-reversed measured waves, etc. The net result after such a sequence of experiments is a set of waveforms, one for each transducer element, such that if these waveforms are used to excite the transducers in the array the transmitted wave will focus on the target—irrespective of the properties of the intervening medium between transducer array and target.
Although the name “time-reversal” connotes the use of broad band wave fields (short time pulses) this is not necessary and the method works equally well with narrow band wave fields. For narrow band illumination the time-reversal process is identical to phase conjugation.
Time-reversal imaging can be performed computationally without actually performing the sequence of experiments outlined above. To do this the multi-static response matrix K must be measured. This quantity is an NXN matrix, where N is the number of antenna (or transducer) elements. From this quantity the time-reversal matrix T=K*K (* standing for complex conjugate) is computed and each eigenvalue, eigenvector pair correspond to a different target. The eigenvalues give the scattering strength of the targets and the eigenvectors give the required exciting waveforms to focus on the associated target.

## Slide 3: Computational Time-reversal
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
Time-reversal processor
Computes measured returns that would
have been received after time-reversal compensation
Multi-static data
Return signals from
sub-surface targets
Target detection
Time-reversal compensation can be performed without actually
performing a sequence of target illuminations
Target location estimation
Time-reversal processing requires no knowledge
of sub-surface and works for sparse
three-dimensional and irregular arrays and
both broad band and narrow band wave fields
Notes: <number>
Multi-static data: Measured returns at each antenna element for pulse transmission from each element. Normally obtained by sequentially pulsing each antenna and measuring returns at all other elements. In TechSat 21 it is proposed to measure the multi-static data array K=Ki,j by simultaneously pulsing all elements using orthogonal coded waveforms or similar means. It is important to note that time-reversal processing does not require broad band waveforms and works equally well with narrow band or broad band signals.
Time-reversal processor: Computes eigenvalues and eigenvectors of time reversal matrix which is equal to K*K. Eigenvalues are used for target detection and eigenvectors for target location estimation and imaging.
Doppler: Used to isolate return from moving ground or air targets.
Time reversal processing requires only the measured multi-static array K and, thus, needs no apriori knowledge of propagation medium (e.g., ionosphere), array geometry, etc.
Target detection also requires no knowledge of propagation medium or array geometry, etc. However, target location estimation and other imaging tasks do require such knowledge. In practice (e.g., in ultrasound time-reversal imaging) it is customary to use homogeneous medium estimates of the required background Green functions for these purposes.

## Slide 4: Research Program
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
Unresolved Issues
Scale and geometry
  How does time-reversal compensation perform at the range and wavelength
  scales and target sizes envisioned for sub-surface GPR?
Clutter rejection
  How does extraneous targets degrade performance of time-reversal algorithms?
Data acquisition
  How does the use of CDMA or similar methods for acquiring the multi-static
  data matrix affect time-reversal compensation?
Phased array issues
  How many separate antenna elements are required for adequate time-reversal
  compensation?
Sub-surface
  Can the background Green functions for the sub-surface be estimated from
  first arrival backscatter data or conventional diffraction tomography?
Notes: <number>
Scale and geometry: Time reversal has been used principally with ultrasound imaging applications. How it performs at the long ranges and wavelength scales of TechSat21 is not known.
Clutter Rejection: Time reversal has poor clutter rejection properties on its own. In particular, it requires that the number of targets be less than the total number of antenna elements. Thus, the use of doppler will be important in applications.
Data Acquisition: In the normal use of time reversal the multi-static matrix is measured directly; e.g., by separately pulsing and receiving at each and every antenna element in the array. In TechSat21 CDMA (coded division multiple access) or similar schemes will be used to acquire this quantity. How this affects the performance of time reversal compensation is not known.
Phased array issues: The chief question here is whether the TechSat21 antenna configurations give the necessary diversity required to yield good time-reversal compensation. Questions to be answered include whether the antenna elements in each antenna module will need to be actively phased or whether they can be hard-wired and phased as units.

## Slide 5: Array Imaging
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
High quality image
Illumination
Measurement
Backpropagation
In conventional scheme it is necessary to scan the
source array through entire object space
Time-reversal imaging provides the focus-on-transmit without scanning
Also allows focusing in unknown inhomogeneous backgrounds
Focus-on-transmit
Focus-on-receive

## Slide 6: Time-reversal Imaging
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
Illumination #1
Measurement
Phase conjugation
and re-illumination
If more than one isolated scatterer present procedure will converge
to strongest if scatterers well resolved
Repeat …

## Slide 7: Using Mathematics
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
Anything done experimentally can be done computationally
if you know the math and physics
Kl,j=Multi-static response matrix
output from array element l for unit amplitude
input at array element j.
Single element
Illumination
Single element
Measurement
= K e
Applied array
excitation vector e
Arbitrary
Illumination
Array output

## Slide 8: Mathematics of Time-reversal
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
Multi-static response matrix = K
Array excitation vector = e
Array output vector = v
v = K e
T = time-reversal matrix = K† K = K*K
K is symmetric (from reciprocity) so that K†=K*
= K e
Applied array
excitation vector e
Arbitrary
Illumination
Array output
Each scatterer (target) associated with different m value
Target strengths proportional to eigenvalue
Target locations embedded in eigenvector
The iterative time-reversal procedure converges to the eigenvector
having the largest eigenvalue

## Slide 9
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
Processing Details
Time-reversal processor
computes eigenvalues and eigenvectors
of time-reversal matrix
Multi-static data
Return signals from ground
or sub-surface targets
Eigenvalues
Eigenvectors
Standard detection scheme
Location estimation
using MUSIC

## Slide 10: Multi-static Response Matrix
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
Specific target
Green Function Vector

## Slide 11: Time-reversal Matrix
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
Single Dominant Target Case

## Slide 12: Focusing With Time-reversal Eigenvector
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
Intervening Medium
Image of target located at r0
Array point spread function
Need the Green functions of the medium to perform focusing operation
Quality of “image” may not be good—especially for sparse arrays

## Slide 13: Vector Spaces
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
Signal Subspace
Noise Subspace

## Slide 14: Music
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
Pseudo-Spectrum
Steering vector
Pseudo-spectrum peaks at scatterer locations

## Slide 15
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 16
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 17
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 18
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 19
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 20
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 21: Computer Simulation Model
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
x
x
z
xn
x0
l0
l1
Sub-surface interface
Thin phase screen model
Down-going wave
Up-going wave

## Slide 22: GPR
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
x
z
Antenna Model

Uniformly illuminated slit of width 2a with Blackman Harris Filter

## Slide 23
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 24: Ground Reflector and Time-reversal Matrix
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 25: Approximate Reflector Model
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 26
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 27
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 28
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 29
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 30
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 31
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 32
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 33: Earth Layer
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
1


## Slide 34: Down Going Green Function
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
z=z0

## Slide 35
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 36
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 37
December 04, 2000
A.J. Devaney--Mitre presentation
<number>

## Slide 38: Future Work
December 04, 2000
A.J. Devaney--Mitre presentation
<number>
Finish simulation program
  Include sub-surface interface
  Employ extended target
  Include clutter targets
Compute eigenvectors and eigenvalues for realistic parameters
Compare performance with standard ML based algorithms
Broadband implementation