## Slide 1: Computational Time Reversal
02/01
JASA 01
<number>
Anthony J. Devaney
Department of Electrical and Computer Engineering
Northeastern University
Boston, MA 02115
email: devaney@ece.neu.edu
Motivation
Non-well resolved targets and sparse sensor arrays
Non-co-linear transmit and receive arrays
Non-reciprocal backgrounds
Super resolution Imaging
Notes: Talk reviewing the basic formulation of time reversal imaging and time reversal MUSIC treated in Chapter 10 of book.
<number>

## Slide 2: Time-Reversal Imaging
02/01
JASA 01
<number>
Illumination #1
Measurement
Phase conjugation
and re-illumination
If more than one scatterer will converge to strongest
if scatterers well resolved
Repeat …

## Slide 3: Using Mathematics
02/01
JASA 01
<number>
Kl,j=Multi-static response matrix
output from array element l for unit amplitude
input at array element j.
= K e
Single element
Illumination
Single element
Measurement
Applied array
excitation vector e
Arbitrary
Illumination
Array output

## Slide 4: Doing it Mathematically
02/01
JASA 01
<number>
Multi-static response matrix = K
Array excitation vector = e
Array output vector = v
v = K e
Time reversal: what e leads to a v = *e* => *e* = K e
K is symmetric (from reciprocity) so that K†=K*
K† (K e)= * K*e* = *(K e)* = | |2 e =  e
T e =  e
T = time-reversal matrix = K† K = K*K

## Slide 5: Multi-static Response Matrix
02/01
JASA 01
<number>
Linearly independent
under very weak conditions

## Slide 6: Time-Reversal Matrix
02/01
JASA 01
<number>

## Slide 7: Array Point Spread Function
02/01
JASA 01
<number>
Backpropagated field from scatterer located at Xm’
evaluated at field location r

## Slide 8: Well-resolved Targets
02/01
JASA 01
<number>
Backpropagated field from scatterer located at Xm’
vanishes at all other scatterer locations

## Slide 9: Vector Spaces for W.R.T.
02/01
JASA 01
<number>
Signal Subspace
Noise Subspace
S
Time reversal eigenvectors
equal to Green function vectors
in well resolved case
Sum of outer products

## Slide 10: Focusing with Time-reversal
02/01
JASA 01
<number>

## Slide 11: Non-well Resolved Targets
02/01
JASA 01
<number>
Theorem: Green function vectors are linearly
independent and span Signal Subspace
S
Noise Subspace
Time reversal eigenvectors
equal to linear combinations of
Green function vectors
in non-well resolved case

## Slide 12
02/01
JASA 01
<number>
Focusing with in Non-well Resolved Case
Time reversal eigenvectors
equal to linear combinations of
Green function vectors
in non-well resolved case
Time-reversal Image equal to sum of images of targets

## Slide 13: MUSIC
02/01
JASA 01
<number>
Pseudo-Spectrum
Green function vectors lie in Signal Subspace

## Slide 14
02/01
JASA 01
<number>

## Slide 15
02/01
JASA 01
<number>

## Slide 16
02/01
JASA 01
<number>

## Slide 17
02/01
JASA 01
<number>

## Slide 18
02/01
JASA 01
<number>

## Slide 19
02/01
JASA 01
<number>

## Slide 20
02/01
JASA 01
<number>

## Slide 21
02/01
JASA 01
<number>

## Slide 22
02/01
JASA 01
<number>
Generalized Time-reversal Processing
Multi-static data
Return signals from
targets
Multi-static matrix K at one or more frequencies contains
all available measured data. All estimates of target presence
and/or location are to be determined from K.
Basic Premise
Approach
Perform a singular value decomposition (SVD)
of K: the singular values are related to scatterer (target)
strengths and the singular vectors to target locations.
Once the SVD is performed the singular vectors
can be employed in conventional imaging
(backpropagation) or used in a vector subspace
algorithm such as MUSIC for target location estimation.
The new formulation does not require the background medium to be reciprocal
and applies to non-collocated transmitting and receiving sensor elements.

## Slide 23: Formulation
02/01
JASA 01
<number>
Inhomogeneous medium
Transmitting sensor
Receiving sensor
Down-going Green function vector
Up-going Green function vector
Multi-static Data Matrix
Perform a singular value decomposition (SVD)
of K: the singular values are related to scatterer (target)
strengths and the singular vectors to target locations.
Down-going
Up-going
Target located at

## Slide 24: Singular System of Multi-static Matrix
02/01
JASA 01
<number>
Above formulation reduces to conventional time-reversal for the case of a
symmetric multi-static data matrix (reciprocal background with full multi-static capability)
Each scatterer (target) associated with different j value
Target strengths proportional to eigenvalue
Target locations embedded in eigenvector
Normal Equations

## Slide 25: SVD of Multi-static Data Matrix
02/01
JASA 01
<number>
Each scatterer (target) associated with different j value
Target strengths proportional to square of singular values
Target locations embedded in singular vectors

## Slide 26: Vector Subspace Methods
02/01
JASA 01
<number>
Vector space of applied voltages
to transmitter sensor elements
Vector space of applied voltages
to receiver sensor elements
MUSIC is based on the fact that the complex conjugate of the downgoing Green function
vectors are orthogonal to Ej and the upgoing Green function vectors are orthgonal to Vj

## Slide 27: MUSIC
02/01
JASA 01
<number>
Steering Vectors
Test Target Location
Pseudo-spectrums