## Slide 1: Detection and Estimation of Buried Objects Using GPR
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
A.J. Devaney
Department of Electrical and Computer Engineering
Northeastern University
email: devaney@ece.neu.edu
Web Site: www.ece.neu.edu/faculty/devaney
Talk motivation: GPR imaging for buried and concealed targets
Talk Outline
Overview
Review of existing work
New work
Simulations
Future work and concluding remarks
Tech Sat 21 AFOSR Arje Nachman
AFOSR MURI, Mitre Corporation, DOE – Idaho Falls
Notes: Given at the 2002 annual meeting of the AFOSR group on EM research.
<number>

## Slide 2: Time Reversal Using Limited Apertures
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
Full Aperture
Half Aperture
Half Aperture
with reflector
Reflecting boundary
Hypothesis: Use of reflecting boundary results in an increased effective aperture

## Slide 3: Time-reversal Imaging for Tech Sat 21
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
Without time-reversal compensation
With time-reversal compensation
In time-reversal imaging a sequence of illuminations is used such that each
incident wave is the time-reversed replica of the previous measured return
Ionosphere
Ionosphere
First illumination
Final illumination
Intermediate illumination
Ionosphere
Goal is to focus maximum amount of energy on target
for purposes of target detection and location estimation
Notes: <number>
Time-reversal imaging is a standard method used in ultrasound medical and industrial imaging. It is customarily performed experimentally where a target is illuminated (insonified) in a first experiment with a plane wave (all transducers pulsed in phase) and then the target is re-illuminated with the transducers now pulsed using the time-reversed measured waves, etc. The net result after such a sequence of experiments is a set of waveforms, one for each transducer element, such that if these waveforms are used to excite the transducers in the array the transmitted wave will focus on the target—irrespective of the properties of the intervening medium between transducer array and target.
Although the name “time-reversal” connotes the use of broad band wave fields (short time pulses) this is not necessary and the method works equally well with narrow band wave fields. For narrow band illumination the time-reversal process is identical to phase conjugation.
Time-reversal imaging can be performed computationally without actually performing the sequence of experiments outlined above. To do this the multi-static response matrix K must be measured. This quantity is an NXN matrix, where N is the number of antenna (or transducer) elements. From this quantity the time-reversal matrix T=K*K (* standing for complex conjugate) is computed and each eigenvalue, eigenvector pair correspond to a different target. The eigenvalues give the scattering strength of the targets and the eigenvectors give the required exciting waveforms to focus on the associated target.

## Slide 4: Computational Time-reversal
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
Time-reversal processor
Computes measured returns that would
have been received after time-reversal compensation
Multi-static data
Return signals from
moving ground targets
Target detection
Time-reversal processing employs Doppler
processing to isolate returns from
moving targets
Time-reversal compensation can be performed without actually
performing a sequence of target illuminations
Target location estimation
Time-reversal processing requires no knowledge
of ionosphere properties and works for sparse
three-dimensional and irregular arrays and
both broad band and narrow band wave fields
Notes: <number>
Multi-static data: Measured returns at each antenna element for pulse transmission from each element. Normally obtained by sequentially pulsing each antenna and measuring returns at all other elements. In TechSat 21 it is proposed to measure the multi-static data array K=Ki,j by simultaneously pulsing all elements using orthogonal coded waveforms or similar means. It is important to note that time-reversal processing does not require broad band waveforms and works equally well with narrow band or broad band signals.
Time-reversal processor: Computes eigenvalues and eigenvectors of time reversal matrix which is equal to K*K. Eigenvalues are used for target detection and eigenvectors for target location estimation and imaging.
Doppler: Used to isolate return from moving ground or air targets.
Time reversal processing requires only the measured multi-static array K and, thus, needs no apriori knowledge of propagation medium (e.g., ionosphere), array geometry, etc.
Target detection also requires no knowledge of propagation medium or array geometry, etc. However, target location estimation and other imaging tasks do require such knowledge. In practice (e.g., in ultrasound time-reversal imaging) it is customary to use homogeneous medium estimates of the required background Green functions for these purposes.

## Slide 5: Research Program
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
Clutter rejection
  How do extraneous targets degrade performance of time-reversal algorithms?
  How can effects of clutter be reduced.
Data acquisition
  How does the use of CDMA or similar methods for acquiring the multi-static
  data matrix affect time-reversal compensation?
Phased array issues
  How many separate antenna elements are required for adequate time-reversal
  compensation? Can the method work for non-coincident arrays.
Sub-surface
  Can the background Green functions for the sub-surface be estimated from
  first arrival backscatter data or conventional diffraction tomography or other-
  wise modeled.
Non-reciprocal media
  Does the method extend to non-reciprocal media such as the ionosphere
Notes: <number>
Scale and geometry: Time reversal has been used principally with ultrasound imaging applications. How it performs at the long ranges and wavelength scales of TechSat21 is not known.
Clutter Rejection: Time reversal has poor clutter rejection properties on its own. In particular, it requires that the number of targets be less than the total number of antenna elements. Thus, the use of doppler will be important in applications.
Data Acquisition: In the normal use of time reversal the multi-static matrix is measured directly; e.g., by separately pulsing and receiving at each and every antenna element in the array. In TechSat21 CDMA (coded division multiple access) or similar schemes will be used to acquire this quantity. How this affects the performance of time reversal compensation is not known.
Phased array issues: The chief question here is whether the TechSat21 antenna configurations give the necessary diversity required to yield good time-reversal compensation. Questions to be answered include whether the antenna elements in each antenna module will need to be actively phased or whether they can be hard-wired and phased as units.

## Slide 6: Doppler Processed Multi-static Data
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
MGT
Illuminated ground patch
from single antenna element
Ionosphere
Doppler shifted
Clutter signal
MGT signal
Doppler Rejection
MGT signal
Dopper Processed Multi-static Data Matrix
Goal: Derive an optimal scheme for
Detecting and locating MGT
Time gating
Notes: <number>
The slide shows six TechSat 21 antenna modules with antenna module k excited by an input voltage ek() (frequency domain) and antenna module j measuring the return signal Vj(). Each separate antenna module is actually a phased array in its own right and the figure shows that all modules are focused on a single ground patch. It is also assumed that the relative velocity of the ground patch to the antennas is known so that a Doppler rejection filter can be employed that filters out all ground clutter (i.e., all scattered signals from targets that are stationary on the earth). The Doppler filtered return vj() is thus output from the Doppler rejection filter and is assumed to have contributions only from moving ground targets (MGT).
The Doppler processed multi-static data matrix relates the Doppler filtered returns vj() to the excitation signals ek(): v=Ke. The classical time-reversal matrix is simply K+K where the + indicates the Hermitian adjoint.
The Doppler processed multi-static data matrix K is the key essential ingredient to all of TechSat 21. This quantity is measured either by alternately pulsing each antenna module and receiving at all other modules or by using CDMA or similar schemes to obtain this quantity.
The goal of our work is to use the multi-static matrix K in an optimal fashion to detect and located moving ground targets (MGT). Time-reversal processing with the use of MUSIC is one possible way to do this.

## Slide 7: Generalized Time-reversal Processing
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
Multi-static data
Return signals from
moving ground targets
Multi-static matrix K at one or more frequencies contains
all available measured data. All estimates of target presence
and/or location are to be determined from K.
Basic Premise
Approach
Perform a singular value decomposition (SVD)
of K: the singular values are related to scatterer (target)
strengths and the singular vectors to target locations.
Once the SVD is performed the singular vectors
can be employed in conventional imaging
(backpropagation) or used in a vector subspace
algorithm such as MUSIC for target location estimation.
The new formulation does not require the ionosphere to be reciprocal and applies
to non-collocated transmitting and receiving antenna modules.

## Slide 8: Formulation
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
Ionosphere
Transmitting antenna
Receiving antenna
Down-going Green function vector
Up-going Green function vector
Multi-static Data Matrix
Perform a singular value decomposition (SVD)
of K: the singular values are related to scatterer (target)
strengths and the singular vectors to target locations.
Down-going
Up-going
MGT located at

## Slide 9: Singular System of Multi-static Matrix
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
Above formulation reduces to conventional time-reversal for the case of a
symmetric multi-static data matrix (reciprocal ionosphere with full multi-static capability)
Each scatterer (target) associated with different j value
Target strengths proportional to eigenvalue
Target locations embedded in eigenvector
Normal Equations
Well Resolved Targets

## Slide 10: SVD of Multi-static Data Matrix
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
Each scatterer (target) associated with different j value
Target strengths proportional to square of singular values
Target locations embedded in singular vectors
Well Resolved Targets

## Slide 11: Single Dominant Target
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
Ionosphere
These correspond to the conventional time-reversed images
generated by back propagating the eigenvectors of the time-reversal matrix.
Transmitter array PSF
Receiver array PSF

## Slide 12: Vector Subspace Methods
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
Vector space of applied voltages
to transmitter antenna elements
Vector space of applied voltages
to receiver antenna elements
MUSIC is based on the fact that the complex conjugate of the downgoing Green function
vectors are orthogonal to Ej and the upgoing Green function vectors are orthgonal to Vj

## Slide 13: MUSIC
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
Steering Vectors
Test Target Location
Pseudo-spectrums

## Slide 14
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>

## Slide 15
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>

## Slide 16
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>

## Slide 17
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>

## Slide 18
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>

## Slide 19
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>

## Slide 20: Computer Simulation Model
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
x
x
z
xn
x0
l0
l1
Sub-surface interface
Thin phase screen model
Down-going wave
Up-going wave

## Slide 21: GPR Antenna Model
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
x
z
Antenna Model

Uniformly illuminated slit of width 2a with Blackman Harris Filter

## Slide 22
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>

## Slide 23: Ground Reflector and Time-reversal Matrix
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>

## Slide 24: Approximate Reflector Model
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>

## Slide 25
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>

## Slide 26
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>

## Slide 27
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>

## Slide 28: Earth Layer
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
1


## Slide 29: Down Going Green Function
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
z=z0

## Slide 30
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>

## Slide 31
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>

## Slide 32
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>

## Slide 33: Future Work
Jan 18, 02
A.J. Devaney-AFOSR San Antonio Annual Meeting
<number>
Finish simulation program
  Include sub-surface interface
  Employ extended target
  Include clutter targets
  Foliage
Compute eigenvectors and eigenvalues for realistic parameters
Compare performance with standard ML based algorithms
Broadband implementation