## Slide 1: Time reversal processing for Tech Sat 21
April 29, 2003
SMARTS Workshop 2003
<number>
A.J. Devaney
Department of Electrical and Computer Engineering
Northeastern University
Boston, MA 02116
Email:devaney@ece.neu.edu
Web Site: www.ece.neu.edu/faculty/devaney
AFOSR (Arje Nachman)
Graduate Students: Mike Dennison and Tim Havens
Preprints available on Web site
A.J. Devaney, “Time reversal imaging of obscured targets from multi-static data,” IEEE Trans Ant. Prop. (submitted)
Notes: Presented at a workshop in 2003 that investigated the use of sparse systems of satellite born microwave antennas for ground surveillance. This talk proposed the use of time reversal based algorithms for detecting ground targets in clutter.
<number>

## Slide 2: Background
April 29, 2003
SMARTS Workshop 2003
<number>
A.J. Devaney, “Super-resolution processing of multistatic data using time
reversal and MUSIC,” JASA (accepted)
H. Lev-Ari and A.J. Devaney, “The time reversal techniques re-interpreted:
Subspace based signal processing for multistatic target location,” Proc. IEEE Sensor
Array and Multichannel Signal Workshop, Cambridge, MA March 2000, pp509-513
S. Lehman and A.J. Devaney, “Transmission mode time reversal imaging
with MUSIC,” JASA (to appear May 03)
A.J. Devaney, “Imaging and target detection from unstructured and sparse antenna
arrays,” ASAP workshop proceedings, Lincoln Lab March 03.
A.J. Devaney, “Time Reversal imaging of obscured targets from
Multistatic data,” IEEE Trans Ant. Prop. (submitted)
A.J. Devaney and M. Dennison, “Inverse scattering in inhomogeneous
background media, Inverse Problems (submitted)

## Slide 3: Generalized Direction Finding
April 29, 2003
SMARTS Workshop 2003
<number>
Proposed approach can be considered to be a generalized form
of direction finding using active phased antenna arrays rather
than passive arrays and for coherent targets rather
than incoherent (uncorrelated) sources
Standard beam forming as well as subspace methods
such as MUSIC used to form images of discrete targets
Method can be used in the presence of distorting media
(ionosphere) and for sparse and irregular 3D arrays
Applies to both narrow and wide band sources
Yields estimates of both target strengths and locations

## Slide 4: Tech Sat 21
April 29, 2003
SMARTS Workshop 2003
<number>
Unstructured Phased Array
Centimeter wavelength
5 to 15 independent antennas
kilometer or more deployment radius
multi-static data acquired
detection and tracking of MGT
Clutter suppression performed using
time-gating and Doppler filtering
Narrow frequency band Very large sparse 3D array
Intervening ionosphere (multipath)
Ionosphere
Transmitting antenna
MGT located at
Receiving antenna

## Slide 5: Doppler and range gated multi-static data matrix
April 29, 2003
SMARTS Workshop 2003
<number>
MGT
Illuminated ground patch
from single antenna element
Ionosphere
Doppler shifted
Clutter signal
MGT signal
Doppler Rejection
MGT signal
Dopper and range gated Multi-static Data Matrix
Doppler and range gated multi-static
data matrix is assumed in analysis
Range Gate
Notes: <number>
The slide shows six TechSat 21 antenna modules with antenna module k excited by an input voltage ek() (frequency domain) and antenna module j measuring the return signal Vj(). Each separate antenna module is actually a phased array in its own right and the figure shows that all modules are focused on a single ground patch. It is also assumed that the relative velocity of the ground patch to the antennas is known so that a Doppler rejection filter can be employed that filters out all ground clutter (i.e., all scattered signals from targets that are stationary on the earth). The Doppler filtered return vj() is thus output from the Doppler rejection filter and is assumed to have contributions only from moving ground targets (MGT).
The Doppler processed multi-static data matrix relates the Doppler filtered returns vj() to the excitation signals ek(): v=Ke. The classical time-reversal matrix is simply K+K where the + indicates the Hermitian adjoint.
The Doppler processed multi-static data matrix K is the key essential ingredient to all of TechSat 21. This quantity is measured either by alternately pulsing each antenna module and receiving at all other modules or by using CDMA or similar schemes to obtain this quantity.
The goal of our work is to use the multi-static matrix K in an optimal fashion to detect and located moving ground targets (MGT). Time-reversal processing with the use of MUSIC is one possible way to do this.

## Slide 6: Interpretation of results
April 29, 2003
SMARTS Workshop 2003
<number>
Principle goal of research is the development of algorithms
to located MGT in different range/Doppler bins. This is accomplished
by processing each Doppler and range gated
multi-static data matrix separately.
Doppler
Target Angle
Doppler/angle map of target
location at
fixed range gate
Target Angle
Target angle map in
Fixed Doppler/range bin
All results computed within
fixed Doppler/range bin

## Slide 7: Time-reversal imaging for Tech Sat 21
April 29, 2003
SMARTS Workshop 2003
<number>
In time-reversal imaging the time reversed wave generated from given
target is used to optimally image the target
Ionosphere
Ionosphere
Uncompensated illumination
Compensated illumination
Image generated by
performing the propagation
step computationally
Notes: <number>
Time-reversal imaging is a standard method used in ultrasound medical and industrial imaging. It is customarily performed experimentally where a target is illuminated (insonified) in a first experiment with a plane wave (all transducers pulsed in phase) and then the target is re-illuminated with the transducers now pulsed using the time-reversed measured waves, etc. The net result after such a sequence of experiments is a set of waveforms, one for each transducer element, such that if these waveforms are used to excite the transducers in the array the transmitted wave will focus on the target—irrespective of the properties of the intervening medium between transducer array and target.
Although the name “time-reversal” connotes the use of broad band wave fields (short time pulses) this is not necessary and the method works equally well with narrow band wave fields. For narrow band illumination the time-reversal process is identical to phase conjugation.
Time-reversal imaging can be performed computationally without actually performing the sequence of experiments outlined above. To do this the multi-static response matrix K must be measured. This quantity is an NXN matrix, where N is the number of antenna (or transducer) elements. From this quantity the time-reversal matrix T=K*K (* standing for complex conjugate) is computed and each eigenvalue, eigenvector pair correspond to a different target. The eigenvalues give the scattering strength of the targets and the eigenvectors give the required exciting waveforms to focus on the associated target.

## Slide 8: Computational time-reversal
April 29, 2003
SMARTS Workshop 2003
<number>
Time-reversal processor
Computes time reversed wave that
optimally focuses on isolated target
Multi-static data
Return signals from
moving ground targets
Target detection
Time-reversal processing employs Doppler
processing to isolate returns from
moving targets
Time-reversal compensation determined from multi-static data matrix
Target location estimation
Time-reversal processing works for sparse
three-dimensional and irregular arrays and
both broad band and narrow band wave fields
Notes: <number>
Multi-static data: Measured returns at each antenna element for pulse transmission from each element. Normally obtained by sequentially pulsing each antenna and measuring returns at all other elements. In TechSat 21 it is proposed to measure the multi-static data array K=Ki,j by simultaneously pulsing all elements using orthogonal coded waveforms or similar means. It is important to note that time-reversal processing does not require broad band waveforms and works equally well with narrow band or broad band signals.
Time-reversal processor: Computes eigenvalues and eigenvectors of time reversal matrix which is equal to K*K. Eigenvalues are used for target detection and eigenvectors for target location estimation and imaging.
Doppler: Used to isolate return from moving ground or air targets.
Time reversal processing requires only the measured multi-static array K and, thus, needs no apriori knowledge of propagation medium (e.g., ionosphere), array geometry, etc.
Target detection also requires no knowledge of propagation medium or array geometry, etc. However, target location estimation and other imaging tasks do require such knowledge. In practice (e.g., in ultrasound time-reversal imaging) it is customary to use homogeneous medium estimates of the required background Green functions for these purposes.

## Slide 9: Processing details
April 29, 2003
SMARTS Workshop 2003
<number>
Time-reversal processor
computes singular value decomposition
of multi-static matrix
Multi-static data
Return signals from
ground targets
Singular Values
Singular Vectors
Standard detection scheme
Location estimation
using standard imaging or MUSIC
In simplest case (well resolved targets) each target is associated
with different singular vector. More generally subspace methods
allow different targets to be individually imaged.

## Slide 10: SVD of multi-static matrix
April 29, 2003
SMARTS Workshop 2003
<number>
Receiving antenna
measured response at antenna element
j due to impulse applied at element k
Ionosphere
Transmitting antenna
MGT located at
K
SVD
vj, uj
Target image
Field propagation
Background
Green Function

## Slide 11: Well resolved targets
April 29, 2003
SMARTS Workshop 2003
<number>
Ionosphere
K
SVD
vj, uj, σj>0
Background
Green Function
Computed image
For well resolved targets each target associated with different singular element

## Slide 12: General Case
April 29, 2003
SMARTS Workshop 2003
<number>
Each singular element having non-zero singular value
associated with set of targets
Ionosphere
Blurred image
Can use singular elements having zero singular values
in MUSIC Algorithm
H. Lev-Ari and A.J. Devaney, “The time reversal techniques re-interpreted: Subspace based signal processing for multistatic target location,” Proc. IEEE Sensor Array and Multichannel Signal Workshop, Cambridge, MA March 2000, pp509-513

## Slide 13: MUSIC
April 29, 2003
SMARTS Workshop 2003
<number>
Standard time-reversal procedure uses singular vectors
having non-zero singular values
MUSIC uses singular vectors having zero singular values
K
SVD
vj, uj, σj=0
Ionosphere
Background
Green Function
Pseudo-spectrum
Target images
Background Green function
plays role of steering vector

## Slide 14: Grating Lobes
April 29, 2003
SMARTS Workshop 2003
<number>
Ionosphere
False target
Grating lobes much reduced

## Slide 15: Super-resolution
April 29, 2003
SMARTS Workshop 2003
<number>
Ionosphere
Increased effective
aperture
Properly compensated intervening medium can
increase performance of imaging algorithm

## Slide 16: Computer Simulation Model
April 29, 2003
SMARTS Workshop 2003
<number>
x
x
z
xn
x0
l0
l1
Ionosphere
Fresnel Approximation
Thin phase screen model
Down-going wave
Up-going wave

## Slide 17: Simulation Parameters
April 29, 2003
SMARTS Workshop 2003
<number>

## Slide 18: Single Centered Target Regular Array Time Reversal Image
April 29, 2003
SMARTS Workshop 2003
<number>

## Slide 19
April 29, 2003
SMARTS Workshop 2003
<number>
Simulation Parameters

## Slide 20: Single Target Irregular Array-TR
April 29, 2003
SMARTS Workshop 2003
<number>

## Slide 21
April 29, 2003
SMARTS Workshop 2003
<number>
Simulation Parameters

## Slide 22: Three Targets-TR Images free space
April 29, 2003
SMARTS Workshop 2003
<number>

## Slide 23
April 29, 2003
SMARTS Workshop 2003
<number>
Simulation Parameters

## Slide 24: Three Targets TR images with phase screen
April 29, 2003
SMARTS Workshop 2003
<number>

## Slide 25
April 29, 2003
SMARTS Workshop 2003
<number>
Simulation Parameters

## Slide 26: Three Targets free space MUSIC
April 29, 2003
SMARTS Workshop 2003
<number>

## Slide 27
April 29, 2003
SMARTS Workshop 2003
<number>
Simulation Parameters

## Slide 28: Three Targets with phase screen MUSIC
April 29, 2003
SMARTS Workshop 2003
<number>

## Slide 29
April 29, 2003
SMARTS Workshop 2003
<number>
Simulation Parameters

## Slide 30: Two Targets with Clutter phase screen MUSIC
April 29, 2003
SMARTS Workshop 2003
<number>

## Slide 31: Estimating background
April 29, 2003
SMARTS Workshop 2003
<number>
Imaging algorithms require knowledge of background Green function.
Two approaches to this problem are:
Using early time-gated multi-static data to estimate this quantity using
methods outlined in papers below
2. Using ground based sources to generate “pilot pulses.”
A.J. Devaney, “Imaging and target detection from unstructured and sparse antenna arrays,” ASAP workshop proceedings, Lincoln Lab March 03.
A.J. Devaney and M. Dennison, “Inverse scattering in inhomogeneous
background media, Inverse Problems (submitted)
Pilot pulse
Intervening distorting medium
Antenna

## Slide 32: Summary
April 29, 2003
SMARTS Workshop 2003
<number>
Time reversal based imaging algorithms yield high quality
images of sets of discrete ground based targets
Method works with arbitrary array geometry
Intervening medium can improve on performance
Reduces grating lobes
Increases effective aperture
Requires knowledge of background Green functions
Estimate using early time-gated reflection measurements
Estimate using known ground based sources of “pilot pulses”