## Slide 1: Experimental Time-reversal
Intervening medium
Intervening medium
Without time-reversal compensation
With time-reversal compensation
In time-reversal imaging a sequence of illuminations is used such that each
incident wave is the time-reversed replica of the previous measured return
First illumination
Final illumination
Intermediate illumination
Intervening medium
Goal is to focus maximum amount of energy on target
for purposes of target detection and location estimation
Notes: <number>
Time-reversal imaging is a standard method used in ultrasound medical and industrial imaging. It is customarily performed experimentally where a target is illuminated (insonified) in a first experiment with a plane wave (all transducers pulsed in phase) and then the target is re-illuminated with the transducers now pulsed using the time-reversed measured waves, etc. The net result after such a sequence of experiments is a set of waveforms, one for each transducer element, such that if these waveforms are used to excite the transducers in the array the transmitted wave will focus on the target—irrespective of the properties of the intervening medium between transducer array and target.
Although the name “time-reversal” connotes the use of broad band wave fields (short time pulses) this is not necessary and the method works equally well with narrow band wave fields. For narrow band illumination the time-reversal process is identical to phase conjugation.
Time-reversal imaging can be performed computationally without actually performing the sequence of experiments outlined above. To do this the multi-static response matrix K must be measured. This quantity is an NXN matrix, where N is the number of antenna (or transducer) elements. From this quantity the time-reversal matrix T=K*K (* standing for complex conjugate) is computed and each eigenvalue, eigenvector pair correspond to a different target. The eigenvalues give the scattering strength of the targets and the eigenvectors give the required exciting waveforms to focus on the associated target.

## Slide 2: Multi-static Response Matrix
Scattering is a linear process:
Given impulse response can compute response to arbitrary input
Kl,j=Multi-static response matrix = impulse response of medium
output from array element l for unit amplitude
input at array element j.
Single element
Illumination
Single element
Measurement
= K e
Applied array
excitation vector e
Arbitrary
Illumination
Array output
Notes: <number>

## Slide 3: Computational Time-reversal
Time-reversal processor
Computes measured returns that would
have been received after time-reversal compensation
Multi-static data
Return signals from
targets
Target detection
Time-reversal compensation can be performed without actually
performing a sequence of target illuminations
Target location estimation
Time-reversal processing requires no knowledge
of sub-surface and works for sparse
three-dimensional and irregular arrays and
both broad band and narrow band wave fields
Notes: <number>
Multi-static data: Measured returns at each antenna element for pulse transmission from each element. Normally obtained by sequentially pulsing each antenna and measuring returns at all other elements. In TechSat 21 it is proposed to measure the multi-static data array K=Ki,j by simultaneously pulsing all elements using orthogonal coded waveforms or similar means. It is important to note that time-reversal processing does not require broad band waveforms and works equally well with narrow band or broad band signals.
Time-reversal processor: Computes eigenvalues and eigenvectors of time reversal matrix which is equal to K*K. Eigenvalues are used for target detection and eigenvectors for target location estimation and imaging.
Doppler: Used to isolate return from moving ground or air targets.
Time reversal processing requires only the measured multi-static array K and, thus, needs no apriori knowledge of propagation medium (e.g., ionosphere), array geometry, etc.
Target detection also requires no knowledge of propagation medium or array geometry, etc. However, target location estimation and other imaging tasks do require such knowledge. In practice (e.g., in ultrasound time-reversal imaging) it is customary to use homogeneous medium estimates of the required background Green functions for these purposes.

## Slide 4: Mathematics of Time-reversal
Multi-static response matrix = K
Array excitation vector = e
Array output vector = v
v = K e
T = time-reversal matrix = K† K = K*K
K is symmetric (from reciprocity) so that K†=K*
= K e
Applied array
excitation vector e
Arbitrary
Illumination
Array output
Each isolated point scatterer (target) associated with different m value
Target strengths proportional to eigenvalue
Target locations embedded in eigenvector
The iterative time-reversal procedure converges to the eigenvector
having the largest eigenvalue
Notes: <number>

## Slide 5
Basic Time Reversal Imaging
Superposition of time reversed data from all transmitter/receiver locations
Total time reversed image field
receivers
transmitters
Time reversed multistatic data matrix
Background Green function
Peaks at target locations
Notes: <number>

## Slide 6
Notes: <number>

## Slide 7
Notes: <number>

## Slide 8: CMU 3rd Data Sets 11 & 12
17 dielectric rods
17 dielectric rods + conducting rod
Processed with standard Time Reversal Imaging as well as with TR MUSIC
target
Notes: <number>

## Slide 9
CMU 3rd Data Sets “Setup11” and “Setup12”
Processed with 7 frequencies uniformly spaced between 4.84 and 5.14 Ghz
Notes: <number>

## Slide 10
Processed with 7 frequencies uniformly spaced between 4.84 and 5.14 Ghz
CMU 3rd Data Sets “Setup11” and “Setup12”
Notes: <number>

## Slide 11
Processed with 7 frequencies uniformly spaced between 4.84 and 5.14 Ghz
CMU 3rd Data Sets “Setup11” and “Setup12”
Notes: <number>

## Slide 12
CMU 3rd Data Sets 14 & 15
Processed with standard Time Reversal Imaging as well as with TR MUSIC
30 dielectric rods + conducting rod
30 dielectric rods
target
Notes: <number>

## Slide 13
CMU 3rd Data Sets “Setup14” and “Setup15”
Notes: <number>

## Slide 14
CMU 3rd Data Sets “Setup14” and “Setup15”
Notes: <number>

## Slide 15
CMU 3rd Data Sets “Setup14” and “Setup15”
Notes: <number>

## Slide 16
CMU 3rd Data Set 7
7) 3 solid dielectric rods at position indexes 1,23,36
Setup7.mat
3D ( 23,1,36)
“The dielectric pipe (23) has copper
patches attached to it”
Processed by CMU using A.J. Devaney basic time reversal Algorithm
Notes: <number>

## Slide 17: Target Detection Strategy
K
+
W=AWGN
TR MUSIC
xm
Target amplitude
Inversion
Detection
Algorithm
τm
Detection Algorithm
τ=[τ1,τ2,…, τM]
τ=Min{τm-τ0}
τ>T
Target present
τ<T
Target not present
Time Reversal MUSIC locates the targets using the background
Green function and a time-reversal based non-linear inversion algorithm
developed over the past year computes the target amplitude vector .
τm
Notes: <number>

## Slide 18
Monte Carlo Simulation
xm= target and clutter locations
target
clutter
Target and clutter amplitudes and locations generated randomly,
Program estimates target and clutter amplitudes using
  Linear (DWBA based) time reversal,
  Non-linear (multiple scattering based) time reversal,
  Least squares bench mark algorithm.
Probability of detection Pd=# correct target selections/number of trials
Probability of false alarm Pf=# false target selections/number of trials
Notes: <number>

## Slide 19
Monte Carlo Simulation
5λ
5λ
Target + 4 clutter
S/N = 22 db
6 antennas
Single frequency
50 λ
64 λ
Notes: <number>

## Slide 20
Target + 4 clutter
S/N = 16 db
6 antennas
Single frequency
5λ
5λ
50 λ
64 λ
Notes: <number>

## Slide 21: Imaging
Notes: <number>

## Slide 22
5λ
5λ
50 λ
64 λ
S/N = 13 db
Notes: <number>

## Slide 23: Image
Relationship between image and object
Algorithm point spread function (PSF)
Perfect Image
Notes: <number>

## Slide 24: Cargo scan array
Notes: <number>

## Slide 25: Cable Lengths
Not known
Not known
Notes: <number>

## Slide 26
Computing Cable Filters for Transmission Case
MT frequency domain signal at receiver i from
transmitted signal at transmitter j
Known Green
function
Transmitter Filter (unknown)
Receiver Filter (unknown)
36 array Transmit element j
36 array Receive element i
Signal with target present:
Data Matrix
Product of cable filters
Computing product of cable filters
Data Matrix
Notes: <number>

## Slide 27: Reflection Case
36 array Transmit element j
5 array Receive element i
MT(i,j)=cross talk
MT signal unreliable for filter determination
36 arrayTransmit element j
5 array Receive element i
MT(i,j)
Target
Reflection signal
MT cross talk
6 element filter
36 element filter
Data Matrix
Cannot reliably compute r(i)T(j). Need to compute each separately from Xmission data
Notes: <number>

## Slide 28
Reflection Case Using Mirror
36 arrayTransmit element j
5 array Receive element i
MT(i,j)
Mirror
Mirror image of arrays
Received signals at 5 element receive array look like they come
from mirror image of 36 element transmit array.
Mirror image signal
6 element filter
36 element filter
Green function from mirror image of
transmit array to receive array
MT cross talk
Notes: <number>

## Slide 29
Notes: <number>

## Slide 30
Notes: <number>