## Slide 1: Digital Design: A Systems Approach Lecture 8: Factoring State Machines

## Slide 2: Readings
L8: Chapter 17
L9: Chapter 18

## Slide 3: Review
Lecture 1 – Digital abstraction
Lecture 2 – Combinational logic design
Lecture 3 – Combinational building blocks
Lecture 4 – Numbers and arithmetic
Lecture 5 – Quiz 1 Review
Lecture 6 – Sequential Logic, FSMs
Lecture 7 – Datapath FSMs
Lecture 8 - Factoring FSMs
Lecture 9 - Microcode

## Slide 4: Partitioning
Divide a big problem into several smaller problems
Last lecture - data/control partitioning
This lecture – factoring state machines
Later – system partitioning

## Slide 5: Data/Control Partitioning - Example
Consider a 4-way digital stopwatch
Inputs:
  pb[3:0] - four pushbuttons - high for one clock on each press
    Toggles start/stop for each counter
  reset - resets and stops all timers
  ms - high for one clock each millisecond
Outputs - time3[15:0], time2[15:0], time1[15:0], time0[15:0]
What is the data state of the machine?
Assume you have a single 16-bit adder. What does the datapath look like? What are the control points?
What control FSM is needed to sequence this?

## Slide 6: Specification Of Light Flasher
Inputs: in
Outputs: out
Operation:
  When in = 1, FSM goes through 5 sequences:
  On-Off-On-Off-On
  Each On sequence:
    out = 1
    6 cycles long
  Each Off sequence:
    out = 0
    4 cycles long
  After 5 sequences, FSM goes back to OFF state to wait for new input.

## Slide 7: Light Flasher State Diagram

## Slide 8: Factored light flasher
*Timer loads value 5 or 3, based on tsel

## Slide 9: State diagram of factored light flasher

## Slide 10
module Flash(clk, rst, in, out) ;
input clk, rst, in ; // in triggers start of flash sequence
output out ; // out drives LED
reg out ; // output
wire [`SWIDTH-1:0] state, next ; // current state
reg [`SWIDTH-1:0] next1 ; // next state without reset
reg tload, tsel ; // timer inputs
wire done ; // timer output
// instantiate state register
DFF #(`SWIDTH) state_reg(clk, next, state) ;
// instantiate timer
Timer1 timer(clk, rst, tload, tsel, done) ;
always @* begin
case(state)
`S_OFF: {out, tload, tsel, next1} =
{1'b0, 1'b1, 1'b1, in ? `S_A : `S_OFF } ;
`S_A: {out, tload, tsel, next1} =
{1'b1, done, 1'b0, done ? `S_B : `S_A } ;
`S_B: {out, tload, tsel, next1} =
{1'b0, done, 1'b1, done ? `S_C : `S_B } ;
`S_C: {out, tload, tsel, next1} =
{1'b1, done, 1'b0, done ? `S_D : `S_C } ;
`S_D: {out, tload, tsel, next1} =
{1'b0, done, 1'b1, done ? `S_E : `S_D } ;
`S_E: {out, tload, tsel, next1} =
{1'b1, done, 1'b1, done ? `S_OFF : `S_E } ;
default:{out, tload, tsel, next1} =
{1'b1, done, 1'b1, done ? `S_OFF : `S_E } ;
endcase
end
assign next = rst ? `S_OFF : next1 ;
endmodule

## Slide 11: Waveforms from simulation of light-flasher FSM

## Slide 12: Still redundancy in state diagram

## Slide 13: Factor out “flash number”

## Slide 14: State diagram of twice-factored light flasher

## Slide 15
module Flash2(clk, rst, in, out) ;
input clk, rst, in ; // in triggers start of flash sequence
output out ; // out drives LED
reg out ; // output
wire [`XWIDTH-1:0] state, next ; // current state
reg [`XWIDTH-1:0] next1 ; // next state without reset
reg tload, tsel, cload, cdec ; // timer and countr inputs
wire tdone, cdone ; // timer and counter outputs
// instantiate state register
DFF #(`XWIDTH) state_reg(clk, next, state) ;
// instantiate timer and counter
Timer1 timer(clk, rst, tload, tsel, tdone) ;
Counter1 counter(clk, rst, cload, cdec, cdone) ;
always @(*) begin
case(state)
`X_OFF: {out, tload, tsel, cload, cdec, next1} =
{1'b0, 1'b1, 1'b1, 1'b1, 1'b0,
in ? `X_FLASH : `X_OFF } ;
`X_FLASH:{out, tload, tsel, cload, cdec, next1} =
{1'b1, tdone, 1'b0, 1'b0, 1'b0,
tdone ? (cdone ? `X_OFF : `X_SPACE) : `X_FLASH } ;
`X_SPACE:{out, tload, tsel, cload, cdec, next1} =
{1'b0, tdone, 1'b1, 1'b0, tdone,
tdone ? `X_FLASH : `X_SPACE } ;
endcase
end
assign next = rst ? `X_OFF : next1 ;
endmodule

## Slide 16: Waveforms from simulation of twice-factored light flasher

## Slide 17: Modifying the light flasher
Making the light’s “on” state last 7 cycles
Adding 2 more “on” states
The 3rd “on” lasts 15 cycles
Making the light flash 206 times, which each flash lasting an arbitrary, predetermined number of cycles

## Slide 18: Light Flasher State Diagram

## Slide 19: State diagram of factored light flasher

## Slide 20: State diagram of twice-factored light flasher

## Slide 21: Cynical view of lecture up to now
All we’ve done is build a counter with three subfields
  Each field increments when previous field “wraps”
  Most significant field is count
  Next is on/off
  Least is timer
Lets look at a less trivial problem

## Slide 22: Specification Of A New Traffic-Light Controller
Inputs: car_ew, car_lt
Outputs: nsgyr ewgyr ltgyr
Operation:
  Default: green light for north-south road
  If car_lt: green light for left-turn
    If ~car_lt & car_ew: green light for east-west road
  Green light for left-turn and east-west roads stay on until either:
    No more cars, or
    Green light timer expires
  Each green, yellow, and red light stay on for a time interval
  Lighting sequence: green -> yellow -> red

## Slide 23: Number of states required by ‘flat’ machine
Sequences for NS, EW, LT (3)
States in each sequence Yellow, Red, Green (3)
Time in each state 9, 5, or 4 cycles (6)
Time remaining before return to NS (13)
Total states 3 x 3 x 6 x 13 = 702

## Slide 24: Block diagram of factored machine

## Slide 25: State diagram of master FSM

## Slide 26
//----------------------------------------------------------------------
//Master FSM
// car_ew - car waiting on east-west road
// car_lt - car waiting in left-turn lane
// ok - signal that it is ok to request a new direction
// dir - output signaling new requested direction
//----------------------------------------------------------------------
module TLC_Master(clk, rst, car_ew, car_lt, ok, dir) ;
input clk, rst, car_ew, car_lt, ok ;
output [1:0] dir ;
wire [`MWIDTH-1:0] state, next ; // current state and next state
reg [`MWIDTH-1:0] next1 ; // next state without reset
reg tload ; // timer load
reg [1:0] dir ; // direction output
wire tdone ; // timer completion
// instantiate state register
DFF #(`MWIDTH) state_reg(clk, next, state) ;
// instantiate timer
Timer #(`TWIDTH) timer(clk, rst, tload, `T_EXP, tdone) ;
always @(state or rst or car_ew or car_lt or ok or tdone) begin
case(state)
`M_NS: {dir, tload, next1} =
{`M_NS, 1'b1, ok ? (car_lt ? `M_LT
: (car_ew ? `M_EW : `M_NS))
: `M_NS} ;
`M_EW: {dir, tload, next1} =
{`M_EW, 1'b0, (ok & (!car_ew | tdone)) ? `M_NS : `M_EW} ;
`M_LT: {dir, tload, next1} =
{`M_LT, 1'b0, (ok & (!car_ew | tdone)) ? `M_NS : `M_LT} ;
default: {dir, tload, next1} =
{`M_LT, 1'b0, (ok & (!car_ew | tdone)) ? `M_NS : `M_LT} ;
endcase
end
assign next = rst ? `M_NS : next1 ;
endmodule

## Slide 27: Block diagram of factored machine

## Slide 28: State diagram of light FSM

## Slide 29: Light “handshake”

## Slide 30
module TLC_Light(clk, rst, on, done, light) ;
input clk, rst, on ;
output done ;
output [2:0] light ;
reg [2:0] light ;
reg done ;
wire [`LWIDTH-1:0] state, next ; // current state, next state
reg [`LWIDTH-1:0] next1 ; // next state w/o reset
reg tload ;
reg [`TWIDTH-1:0] tin ;
wire tdone ;
// instantiate state register
DFF #(`LWIDTH) state_reg(clk, next, state) ;
// instantiate timer
Timer timer(clk, rst, tload, tin, tdone) ;
always @(state or rst or on or tdone) begin
case(state)
`L_RED: {tload, tin, light, done, next1} =
{tdone & on, `T_GREEN, `RED, !tdone,
(tdone & on) ? `L_GREEN : `L_RED} ;
`L_GREEN: {tload, tin, light, done, next1} =
{tdone & !on, `T_YELLOW, `GREEN, tdone,
(tdone & !on) ? `L_YELLOW : `L_GREEN} ;
`L_YELLOW: {tload, tin, light, done, next1} =
{tdone, `T_RED, `YELLOW, 1'b1, tdone ? `L_RED : `L_YELLOW} ;
default: {tload, tin, light, done, next1} =
{tdone, `T_RED, `YELLOW, 1'b1, tdone ? `L_RED : `L_YELLOW} ;
endcase
end
assign next = rst ? `L_RED : next1 ;
endmodule

## Slide 31: The Combiner
Notify master when legal to change (green, able to go red)
  ok = on & done
Trigger a red light when master changes direction
  on = (dir == cur_dir)
Update the current direction to input dir when all lights are red and able to go green
  next_dir = (!on & !done) ?
  dir : cur_dir
Trigger a green light when cur_dir has been updated
  on = (dir == cur_dir)
Output red lights for the two directions that are not cur_dir

## Slide 32
//----------------------------------------------------------------------
// Combiner -
// dir - direction request from master FSM
// ok - acknowledge to master FSM
// lights - 9-bits to control traffic lights {NS,EW,LT}
//----------------------------------------------------------------------
module TLC_Combiner(clk, rst, dir, ok , lights) ;
input clk, rst ;
input [1:0] dir ;
output ok ;
output [8:0] lights ;
wire done ;
wire [2:0] light ;
reg [8:0] lights ;
wire [1:0] cur_dir ;
// current direction register
DFF #(2) dir_reg(clk, next_dir, cur_dir) ;
// light FSM
TLC_Light lt(clk, rst, on, done, light) ;
// request green from light FSM until direction changes
wire on = (cur_dir == dir) ;
// update direction when light FSM has made lights red
wire [1:0] next_dir = rst ? 2'b0 : ((!on & !done) ? dir : cur_dir) ;
// ok to take another change when light FSM is done
wire ok = on & done ;
// combine cur_dir and light to get lights
always @(cur_dir or light) begin
case(cur_dir)
`M_NS: lights = {light, `RED, `RED} ;
`M_EW: lights = {`RED, light, `RED} ;
`M_LT: lights = {`RED, `RED, light} ;
default: lights = {`RED, `RED, `RED} ;
endcase
end
endmodule

## Slide 33: Waveforms from simulation of factored machine

## Slide 34: Summary
Factoring state machines
  Separate state into multiple ‘orthogonal’ state variables
  Each is simpler to handle (fewer states)
  Total number of states is product of numbers of sub-states
  “Factors out” repetitive sequences
  Hierarchical structure