## Slide 1: Digital Design: A Systems Approach Lecture 17: Overview and Wrapup

## Slide 2: Restoring logic gives noise margins

## Slide 3: Represent values with bits
Truth values, e.g., door is open
  Single bit
Numbers, temperature (range, precision)
  Integers, fixed-point, floating-point
Sets, e.g., colors
  Encoded one-hot or binary
Compound
  Includes several of above

## Slide 4: Combinational Logic
We compose gates into combinational logic circuits Output depends only on present value of inputs
This circuit realizes the function f= _______________
Why don’t we realize this function with a single gate?

## Slide 5: Functions built from decoders and other blocks
Example – find maximum of 256 small 4-bit numbers
  Decode each number 416 bits (256 times)
  OR these together w/16 256-bit ORs
    (each a 4-level tree of 4-input ORs)
  Use an Arbiter to get highest of 16
  Encode the 164
Need to see if this is more efficient than a tournament
Can this determine which input has the ‘winning’ number?
Decode
OR
Arbiter
Encode

## Slide 6: Building Blocks

## Slide 7: Iterative Circuits

## Slide 8
Arithmetic

## Slide 9: Sequential Logic
Sequential logic circuits have state. Next state and outputs are a function of inputs and present state.

## Slide 10: Sequential circuits work properly if setup and hold time constraints are met
Suppose tdCQ = ts = th = 100ps, tk = 200ps or –200ps,
tmin = 50ps, tmax=2ns.
Is hold time met? What is minimum tcy ?

## Slide 11: Finite-State Machines
Finite-state machines are described by a next-state and output function Can be described with a state diagram or state table.

## Slide 12
//---------------------------------------------
// FSM Example for Lecture 7
// Bill Dally 1/30/03
//---------------------------------------------
// define state assignment - one hot
//---------------------------------------------
`define SWIDTH 4
`define GNS 4'b1000
`define YNS 4'b0100
`define GEW 4'b0010
`define YEW 4'b0001
//---------------------------------------------
// define output codes
//---------------------------------------------
`define GNSL 6'b100001
`define YNSL 6'b010001
`define GEWL 6'b001100
`define YEWL 6'b001010
//---------------------------------------------
// define flip-flop
//---------------------------------------------
module DFF(clk, in, out) ;
parameter n = 1; // width
input clk ;
input [n-1:0] in ;
output [n-1:0] out ;
reg [n-1:0] out ;
always @(posedge clk)
out = in ;
endmodule
//------------------------------------------------------
// Traffic_Light
// Inputs:
// clk - system clock
// rst - reset - high true
// carew - car east/west - true when car is waiting in east-west direction
// Outputs:
// lights - (6 bits) {gns, yns, rns, gew, yew, rew}
// Waits in state GNS until carew is true, then sequences YNS, GEW, YEW
// and back to GNS.
//------------------------------------------------------
module Traffic_Light(clk, rst, carew, lights) ;
input clk ;
input rst ; // reset
input carew ; // car present on east-west road
output [5:0] lights ; // {gns, yns, rns, gew, yew, rew}
wire [`SWIDTH-1:0] state, next ; // current and next state
reg [`SWIDTH-1:0] next1 ; // next state w/o reset
reg [5:0] lights ; // output - six lights 1=on
// instantiate state register
DFF #(`SWIDTH) state_reg(clk, next, state) ;
// next state and output equations - this is combinational logic
always @(state or carew) begin
case(state)
`GNS: {next1, lights} = {(carew ? `YNS : `GNS), `GNSL} ;
`YNS: {next1, lights} = {`GEW, `YNSL} ;
`GEW: {next1, lights} = {`YEW, `GEWL} ;
`YEW: {next1, lights} = {`GNS, `YEWL} ;
endcase
end
// add reset
assign next = rst ? `GNS : next1 ;
endmodule
¬carew
carew

## Slide 13: Data paths are more easily described by realizing the next state function from building blocks

## Slide 14
module Timer(clk, rst, load, in, done) ;
parameter n=4 ;
input clk, rst, load ;
input [n-1:0] in ;
output done ;
wire [n-1:0] count, next_count ;
wire done ;
DFF #(n) cnt(clk, next_count, count) ;
always@(rst, load, in, out) begin
casex({rst, load, done})
3'b1xx: next_count = 0 ; // reset
3'b001: next_count = 0 ; // done
3'b01x: next_count = in ; // load
default: next_count = count-1’b1; // count down
endcase
end
assign done = (count == 0) ;
endmodule

## Slide 15: Factoring
Factor Machines to reduce complexity Divide and conquer

## Slide 16: Most FSMs are a combination of a data path realized from building blocks, and a controller designed from a state diagram.

## Slide 17: Microcode
Microcode, realizing a FSM with a memory - a programmable FSM
Compress the size of the memory by encoding control and output instructions

## Slide 18: System Design – a process
Specification
  Understand what you need to build
Divide and conquer
  Break it down into manageable pieces
Define interfaces
  Clearly specify every signal between pieces
  Hide implementation
  Choose representations
Timing and sequencing
  Overall timing – use a table
  Timing of each interface – use a simple convention (e.g., valid – ready)
Add parallelism as needed (pipeline or duplicate units)
Timing and sequencing (of parallel structures)
Design each module
Code
Verify
Iterate back to the top at any step as needed.

## Slide 19: DES Example

## Slide 20: Pipelining
Modules are composed in pipelines and parallel configurations
Throughput and latency

## Slide 21: How does a typical pipeline handshake work? What signals are used between stages? What values must these signals have for data to move from one stage to the next?

## Slide 22: Flow Control

## Slide 23: Pipelines
Pipelines can stall and idle
When do these happen? How can you prevent them

## Slide 24: Synchronization Failure

## Slide 25: Failure Probability and Error Rate
Each event can potentially fail.
Failure rate = event rate x failure probability

## Slide 26: What is wrong with this picture?

## Slide 27: Asynchronous logic design
Continuous state feedback
Affected by races and hazards
Synthesize/Analyze with flow tables

## Slide 28: Congratulations! You are now a logic designer.
To become a better one:
  Practice, practice, practice…
  Study other designs
  Become a student of the art of digital design
    Stay on top of the latest technology
      New parts, processes, tools, techniques
    Read the trade press
    Take more courses
    Go to conferences
    Build a “network” (of people)
  Continue learning
    What you have now is a “license to learn”
It’s a fun field
  Design lots of neat things – chips, boards, systems
  Play with fun tools, processes, chips, lab equipment
  Meet fun people (mostly)
  Make $$