## Slide 1: Digital Design: A Systems Approach Lecture 14: Sequential Logic Review

## Slide 2: Readings
L14: Sequential Logic Review
L15: 22, 24, & 25

## Slide 3: Outline
Combinational vs. sequential logic
Classic FSMs
Datapath FSMs
Microcode
System decomposition
Timing, concurrency and pipelines

## Slide 4: Combinational Logic
We compose gates into combinational logic circuits Output depends only on present value of inputs
This circuit realizes the function f= _______________

## Slide 5: Sequential Logic
Sequential logic circuits have state. Next state and outputs are a function of inputs and present state.

## Slide 6: Sequential Building Block: D Flip-Flop
Input: D
Output: Q
Clock: ^
Q outputs a steady value
Edge on ^ changes Q to be D
Flip-flop stores state
D
Q
^
d
q
clk
D
Q
^
s
s
clk
d
q

## Slide 7: Example: A Traffic-Light Controller
carew

## Slide 8: Finite State Machines (State Table)

## Slide 9: Finite State Machines (State Diagram)
gns
100 001
yns 010 001
gew
001 100
yew
001 010
¬carew | rst
carew & ¬rst
¬rst
¬rst
*
state output
= gyr gyr
ew
ns
carew = car east-west sensor active
rst = reset
rst
rst

## Slide 10: Draw a State Diagram for a Missing-Pulse Filling FSM

## Slide 11: Draw a State Diagram for a Missing-Pulse Filling FSM
A
B
C
D
E
B
C
D
E
B
C
D
E
B
C

## Slide 12: Draw a State Diagram for a Missing-Pulse Filling FSM
A
B
C
D
E
B
C
D
E
B
C
D
E
B
C
B
C
D
E

## Slide 13: FSM Factoring
Partition problem into smaller problems
  Major theme of circuit design
Separate a multi-dimensional state space into multiple smaller FSMs
  Control and data
  State variables

## Slide 14: Light Flasher FSM Diagram

## Slide 15: Factored Light Flasher

## Slide 16: Data paths are more easily described by realizing the next state function from building blocks

## Slide 17: Most FSMs are a combination of a data path realized from building blocks, and a controller designed from a state diagram.

## Slide 18: Design a DP FSM that computes parity across a block of 16 8-bit words

## Slide 19: Design a DP FSM that computes ‘horizontal’ parity across a block of 16 8-bit words
Inputs
  Start – first word
  In – 8-bit data
Outputs
  P – parity – running parity across 16 words then hold until next start
Two pieces of state
  P – running parity
  N – words to go

## Slide 20: DP FSM is designed by writing equations for each case
Case | P | N
Start | in | 15
~Start & ~Done | in ^ P | N-1
Done | P | N (=0)
P = start ? in : (done ? P : P ^ in)
N = start ? 15 : (done ? 0 : N-1)
Done = (N == 0)

## Slide 21: Check timing with table
Cycle | Start | Done | Next P | N
i-1 | 0 | 1 | P | 0
i | 1 | 1 | ini | 0
i+1 | 0 | 0 | Ini ^ ini+1 | 15
i+j | 0 | 0 | Ini ^ … ^ ini+j | 16-j
i+15 | 0 | 0 | Ini ^ … ^ ini+15 | 1
i+16 | 0 | 1 | Ini ^ … ^ ini+15 | 0
Catches off-by-one errors

## Slide 22: Microcode
Microcode, realizing a FSM with a memory - a programmable FSM
Compress the size of the memory by encoding control and output instructions

## Slide 23
Microcode For Traffic-Light Controller With brx & ldx Instructions
NS
Green
NS
Yellow
to Red
EW or LT?
Wait for NS Red,
make EW
Green
EW to
Red
Back to NS
Wait for NS Red,
make LT
Green
LT to
Red
Back to NS
Until input

## Slide 24: Microcode
Microcode is just FSM implemented with a ROM or RAM
  One address for each state x input combination
  Address contains next state and output
Adding a sequencer reduces size of ROM/RAM
  One entry per state rather than 2i
  uPC, incrementer, branch address, and branch control
Adding instruction types reduces width of ROM/RAM
  Branch or output in each instruction – rather than both
  Type field specifies which one

## Slide 25: Circuit Timing
tcab (contamination delay): minimum time it takes the output B to be contaminated from a contamination of input A
tdab (propagation delay): maximum time it takes the output B to be stable from when input A is stable
ts (setup time): duration signal must be stable before clocking a flip-flop
th (hold time): duration signal must be stable after clocking a flip-flop

## Slide 26: Timing Example
b contaminated at time t=0, stable at t=150
All gates have delay 100ps
AND-OR counts as two gates
t = 0

## Slide 27: Timing Example
b contaminated at time t=0, stable at t=150
All gates have delay 100ps
AND-OR counts as two gates
t = 100

## Slide 28: Timing Example
b contaminated at time t=0, stable at t=150
All gates have delay 100ps
AND-OR counts as two gates
t = 150

## Slide 29: Timing Example
b contaminated at time t=0, stable at t=150
All gates have delay 100ps
AND-OR counts as two gates
t = 200
tcbg = 200ps

## Slide 30: Timing Example
b contaminated at time t=0, stable at t=150
All gates have delay 100ps
AND-OR counts as two gates
t = 250
tcbg = 200ps

## Slide 31: Timing Example
b contaminated at time t=0, stable at t=150
All gates have delay 100ps
AND-OR counts as two gates
t = 350
tcbg = 200ps

## Slide 32: Timing Example
b contaminated at time t=0, stable at t=150
All gates have delay 100ps
AND-OR counts as two gates
t = 450
tcbg = 200ps
tdbg = 300ps

## Slide 33: Setup and Hold Times (back to our friend the DFF)
ts (setup time): duration signal must be stable before clocking a flip-flop
th (hold time): duration signal must be stable after clocking a flip-flop
tcCQ: contamination time of clock to Q
tdCQ: propagation time of clock to Q
D
Q
^
s
s
clk
d
q

## Slide 34: Sequential circuits work properly if setup and hold time constraints are met
Suppose tdCQ = tcCQ= ts = th = 100ps, tk = 200ps or –200ps,
tmin = 50ps, tmax=2ns.
Is hold time met? What is minimum tcy ?

## Slide 35: Pipelining
Modules are composed in pipelines and parallel configurations
Throughput and latency

## Slide 36: Pipelines
Pipelines can stall and idle
When do these happen? How can you prevent them?
Max latency vs. average latency (absorbing bursts)

## Slide 37: Asynchronous Failure
Dealing with asynchrony
  Purely asynchronous signals
  Traversing clock domains
Probability of entering illegal state is the probability that a clock edge lands during setup or hold time:
  PE = (ts + th) / tcy
For reasonable values, error rate is very high:
ts = th = 100ps, tcy = 2ns, PE = 0.1

## Slide 38: Synchronizing
Sample asynchronous signal a
Clock a into intermediate (possibly metastable) value a_w
Clock a_w into synchronized value a_s
Take advantage of exponential decay of metastability
Note ln(10)=2.3 so exp(-18) = 10^(-18/2.3) ~ 10^(-8)

## Slide 39: How do you fix this?

## Slide 40: Questions