## Slide 1: Supplement e04.1: Radar observations of birds

## Slide 2: The misleading bird echoes
Bird echoes come in a few shapes and forms. If your mental image of a spectacular bird echo on radar is a large formation of ducks or geese as above, you could not be farther away from the truth. Though awesome in sight, they are surprisingly hard to spot and relatively unremarkable on radar compared to other examples to follow.

## Slide 3: Large bird formations on radar
This is the best example I have found of daytime migrations, on the day the previous picture was taken. Strong textured echoes are from the ground, speckles moving north to south are flocks of birds, while echoes moving from the WNW are from rain.

## Slide 4: Bird rings in the morning Bat rings in the evening
A more common bird echo sighting is an expanding disk or ring out of a roosting area, occurring just before sunrise (for many birds) or after sunset (for bats). Here is an example of one from Wisconsin, USA, the line appearing from the KGRB radar near the end of the animation being emissions from the rising sun on this low-elevation PPI.
But the most spectacular observation is the nighttime migration of song birds.
Animation courtesy of NOAA

## Slide 5: Migrations of song birds A time-height section
Song birds migrate at night individually or maybe in small groups and are much harder to see visually as a result. But a few birds per cubic kilometer is enough to fill radar displays in a way that is at first somewhat counter-intuitive. And on good nights, like on the example above from Montreal, Canada, there can be many more.

## Slide 6: Migrations of song birds Single radar views
Bird migrations cover most of the radar display on low-level PPIs or CAPPIs. On reflectivity imagery, echoes are weak, and may be a bit speckled if the image is not smoothed. Bird echoes are more visible on longer-wavelength radars such as S-band systems.

## Slide 7: Migrations of song birds Single radar views
In general, bird echoes appear everywhere just after sunset, and gradually disappear before sunrise. Unlike for weather, one does not see movement clearly from these. Only with radars near the coast may one have the chance to see moving echoes.
On this example, we see birds taking off from land and attempting the crossing of a portion of the Gulf of Mexico, many stopping when they spot an island.

## Slide 8: Migrations of song birds The bigger picture
What the previous examples above do not fully convey is the spatial and temporal extent of bird migrations as observed by radar. Shown below is a surface weather map for the US. A low-pressure system in the middle of the continent is bringing south winds to its east and north winds to its west. Also shown is an animation of the US radar composite that night. On it, we see both the rain associated with the weather system (in blue, green, yellow, and orange) and echoes plotted in brown, cyan and blue from migrating birds.

## Slide 9: Migrations of song birds The weather connection
and 2) how they are "limited" to regions of favorable winds.
Note how 1) the echoes pop up around sunset between 00UTC in the east and 03UTC in the west, and come down around sunrise about 10 hours later

## Slide 10: Migrations of song birds The weather connection
In fact, if one animates the radar composite day after day, one can see how the regions where migrations occur change with the weather conditions.