## Slide 1: A Filtered Back Propagation Algorithm for Optical Diffraction Tomography
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
A. J. Devaney and J. Cheng
Department of Electrical and Computer Engineering
Northeastern University
Boston, MA 02115
email: devaney@ece.neu.edu
Examples of inverse scattering problems
Importance of multiple scattering
Potential scattering theory for ODT
  Lippmann Schwinger integral equation
  Born series
  Distorted Wave Born approximation
Born inversion in ideal ODT systems
  Generalized projection slice theorem
  Filtered Back Propagation Algorithm
Born inversion in real ODT systems
  Simple examples
Summary
Notes: <number>
Presented at the “Holographic Workshop 07” held in Leicester UK. It specializes diffraction tomography (Chapters 8 and 9) to optical tomography and discusses the use of phase shifting interferometry to retrieve the phase of the optical field from digital images.

## Slide 2: Optical Microscopy
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Objective Lens
Condenser
Semi-transparent Object
Image
Illuminating light spatially coherent over small scale:
  Complicated non-linear relationship between sample and image
Poor image quality for 3D objects
  Need to thin slice
Cannot image phase only objects:
  Need to stain
  Need to use special phase contrast methods
Require high quality optics
Images generated by analog process
Remove all image forming optics and do it digitally
Notes: <number>

## Slide 3: General Approaches to ODT
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Phase Problem
  Phase Retrieval
  Multiview holography
  Phase shifting holography
Inversion Algorithms
  Standard CT
  Fourier interpolation
  Filtered Back propagation
  Generalized Linear inverse
Forward
Back
Notes: <number>

## Slide 4
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Notes: <number>

## Slide 5: Problems Addressed by Inverse Scattering and DT
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Geophysical
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
Medical
x
x
x
x
x
x
Industrial
Electromagnetic
Acoustic
Ultrasonic
Optical
x
x
x
x
x
x
Electromagnetic
Ultrasonic
Optical
Off-set VSP/ cross-well tomography
GPR surface imaging
induction imaging
Ultrasound tomography
optical microscopy
photon imaging
Ultrasound tomography
optical microscopy
induction imaging
Notes: <number>

## Slide 6
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Real Media
Geophysical
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
Medical
x
x
x
x
x
x
Industrial
Electromagnetic
Acoustic
Ultrasonic
Optical
x
x
x
x
x
x
Electromagnetic
Ultrasonic
Optical
Real experiments
are usually not performed
in homogeneous backgrounds
and include multiple scattering
Notes: <number>

## Slide 7: Why Multiple Scattering
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Simply nature of experiments
Employ to improve linear scattering models
Employ to improve inversion quality
Laser
polarizer
Spatial filter
lens
mirror
mirror
¼  plate
Beam splitter
CCD
sample
Beam splitter
1024X1024
10 bits/pixel
Pixel size=10 
Index matching fluid
Notes: <number>

## Slide 8: Improving the Resolution via Multiple Scattering
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Increases numerical aperture to unity
Multiple scattering in background generates evanescent waves
Oil immersion
Reflecting boundary
Measurement boundary
Glass slide
Cavity with conducting walls
Notes: <number>

## Slide 9
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Historical Survey
X-ray crystallography
Fourier based
Born/Rytov inversion
Computed
tomography
Diffraction tomography
General Linear
Inversion
Distorted Wave
Approximations
Needed for complex media
Notes: <number>

## Slide 10: Back Propagation—the key to inversion
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Notes: <number>

## Slide 11: Total Back Propagation: Point Targets
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Can also sum over temporal frequencies
Notes: <number>

## Slide 12
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Filtered Back Propagation: Extended Targets
Generates a least squares pseudo-inverse of index of refraction distribution
Quantitative
Notes: <number>

## Slide 13: ODT in Free Space
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
CCD
Sample in free space
CCD
sample
Born Approximation
rd
Camera pixel locations
Incident wave directions
Inversion algorithm
Fourier based
Angular spectrum expansion
+
Notes: <number>

## Slide 14: Generalized Projection-Slice Theorem
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
CCD
sample
rd
Ω
Generalized Projection-Slice Theorem
Limiting Ewald Sphere
Ewald Sphere
k
2k
Notes: <number>

## Slide 15: Free Space FBP Algorithm
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
FFT Based: fast and efficient
Can employ Rytov data
Assumes free space background
Notes: <number>

## Slide 16: Multiple Scattering Effects
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Free space
n(r)
Lippmann Schwinger Equation
Notes: <number>

## Slide 17: Distorted Wave LS Equation
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
n0(r)
≡
+
≡
n(r)
n0(r)
n(r)
Notes: <number>

## Slide 18
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Renormalizing Born Series
Linear mapping between incident and scattered field
Non-linear mapping between object function and scattered field
By selecting background properly can minimize multiple scattering
and linearize the mapping from object function to scattered field
Must know background Green function and incident wave in background
Notes: <number>

## Slide 19: Optical Diffraction Tomography
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
CCD
sample
CCD
sample
Fluid filled test tube
Incident wave in background
Object Function
Background Green function
Notes: <number>

## Slide 20: Background Medium
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Background
CCD
sample
Fluid filled test tube
Need to be computed
Notes: <number>

## Slide 21: Distorted wave Born approximation
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Linear mapping between object profile and scattered field
Camera pixel locations
Illumination directions
Apply standard and well developed theories of Linear Inversion
Includes multiple scattering within background
Notes: <number>

## Slide 22
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Mathematical Structure of Inverse Scattering in Complex Media
Non-linear operator (Lippmann Schwinger equation)
Object function
Scattered field data
Linear operator (Distorted wave Born approximation)
Form normal equations for least squares solution
Wavefield Back propagation
Compute pseudo-inverse
Filtered backpropagation algorithm
Data filtering
Back propagation
Notes: <number>

## Slide 23: Implementing FBP Algorithm via the SVD
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Notes: <number>

## Slide 24: Optical Scattering Example
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Notes: <number>

## Slide 25: Scattered Field Data
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Notes: <number>

## Slide 26: Reconstructions
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Notes: <number>

## Slide 27: Resolution Enhancement
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Born with no bottom
DWBA with Bottom
Born with Bottom
Notes: <number>

## Slide 28: Resolution Enhancement
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
PSF with no reflecting bottom
PSF with reflecting bottom
Notes: <number>

## Slide 29: Concluding Remarks
April 30 07
A.J. Devaney Holographic Workshop 07
<number>
Multiple scattering important for many reasons
Present in many experimentals
Can increase inversion resolution
Makes linear models more accurate
Linear based inversion algorithms require knowledge of background
Background well known in controlled experiments such as
3D optical microscopy
Future work concentrated on obtaining optical scattering data
Notes: <number>