## Slide 1: Supplement e05.1: Doppler tutorial Wind profile retrievals

## Slide 2: Geometry of Doppler PPIs
Doppler velocity PPIs show the radial component of the wind going in the direction of the radar (either toward or away). If we take the example of a constant wind from the west, strong approaching velocities will be observed when the radar looks west, strong receding velocities when the radar looks east, and no velocity when the radar looks north or south.

## Slide 3: Doppler PPI displays
This information can then be displayed, generally using progressively colder colors (for example greens and blues) for increasingly strong approaching velocities and progressively warmer colors (for example yellows and reds) for increasingly strong receding velocities.

## Slide 4: Geometry of PPIs, Part 2
Radial velocity images are usually more complicated because:
• The wind is rarely uniform;
• Velocities can only be measured where there are echoes ( limited coverage);
• The height at which radar observes the weather increases with distance because the radar generally points at some elevation over the horizon.
A
B
C
A
B
C

## Slide 5: Result: A typical Doppler PPI
The result is a map that can be intimidating to interpret; yet this image was nevertheless shaped by a dominant wind profile.
The goal of this tutorial is for you to learn how to obtain average wind profiles over the radar from PPIs of Doppler velocity.
In this tutorial, the Doppler patterns to interpret will only be a function of height.

## Slide 6: Introducing the Doppler tutorial
The Doppler images to interpret will look as on the right.
Cold colors (greens, blues…) are used to indicate radial velocities approaching from the radar; warm colors (yellows, reds...) are used to indicate velocities going away from the radar. Near-zero velocities are in gray. The numbers on the color scale correspond to the velocity of the color changes.

## Slide 7: Introducing the Doppler tutorial
Numbers on the image itself correspond to the range rings (20, 40, 60, etc.) in km from the radar on the horizontal line, and the corresponding altitudes (1.1, 2.2, 3.4 km, …) on the vertical line.
In this exercise, you must determine the average wind speed (in m/s) and direction (in degrees from north) at 0, 1.1, 2.2, 3.4, 4.6, and 5.8 km altitude.

## Slide 8: Wind direction reporting Nautical convention
Wind direction reporting in meteorology can be misleading.
In general, in physical sciences, we use the physics convention for measuring angles, i.e., measuring angles with respect to a horizontal line with increasing angles in the counterclockwise direction.
When reporting winds, meteorologists use the nautical convention for direction: angles are measured clockwise from north. Furthermore, the wind direction is the direction the wind comes from. So an east-to-west wind comes from 90° while a wind from 359° would come very slightly west from north.
N
E
W
S
0°
90°
180°
270°
90°
359°

## Slide 9: A method to extract vertical profiles of Doppler velocity
1. For the altitude of interest, for example 3.4 km, identify the data that are at that altitude. In a PPI, these data would make a ring at constant range, in this example at 60 km. One should then mentally filter out everything else. This is important because all other data are at different altitudes, and using them in your thinking will almost always lead to mistakes. This is why on this image all data except at the range of interest have been whitened out.

## Slide 10: A method to extract vertical profiles of Doppler velocity
2. Locate the places where the Doppler velocity is zero. If you have a simple wind pattern and complete data coverage as in all the examples shown here, there should be two of them opposite to each other with respect to the radar location. The axis linking the radar to these zero-velocity regions is perpendicular to the wind at the location where zero velocity is observed. The axis between both zero-velocity regions should be roughly perpendicular to the wind at the radar site.

## Slide 11: A method to extract vertical profiles of Doppler velocity
3. Follow the ring until you find the peak negative Doppler velocity as here and/or the peak positive Doppler velocities.
4. Peak velocities should be observed roughly 90° away from the zero-velocity regions. The wind then blows directly towards the radar in the direction of the peak negative velocity (label “4”) or away from the radar in the direction of the peak positive Doppler velocity (180° away from the label “4”) . Wind speed is hence
the magnitude of that peak velocity, here 17 m/s from the SE (135 °).

## Slide 12: A method to extract vertical profiles of Doppler velocity
5. Repeat for all heights.
The surface wind at "0" range is a bit trickier to estimate. Just assume a tiny ring around the center and proceed as for the other heights.
Once you have your answer for the whole profile, you can verify it against the truth.

## Slide 13: Velocity shear examples Example 2
The following examples have no directional shear, but velocity changing with height.
Follow the approach described in the previous page to determine the wind profile that would cause this stripped pattern on Doppler imagery. Once you have an answer you are confident about, compare it with the solution.

## Slide 14: Velocity shear examples Example 3
Here is the next example.
And its solution.

## Slide 15: Velocity shear examples Example 4
This next example is watching you.
And its solution.

## Slide 16: Directional shear examples Example 5
Now let us add directional change to the mix.
Think about the wind profile that would cause this maelstrom on Doppler imagery.
Once you have an answer you are confident with, compare it with the solution.

## Slide 17: Directional shear examples Example 6
Another example.
And its solution.

## Slide 18: Directional and velocity shear Example 7
Let us try a more hypnotic pattern.
And its solution.

## Slide 19: Directional and velocity shear Example 8
And finally, exercise yourself on this yin-yang pattern.
And here is its solution.

## Slide 20: Yin-yang patterns: More common than you may think
This last case is not as excessive as it may look.
Actually, cases like this are common in approaching low pressure systems.
Consider these real images obtained using 2.7° PPIs in this and the next image.
Note how the coverage is now more limited and how the pattern is not as symmetric as in the tutorial examples.

## Slide 21: Yin-yang patterns: More common than you may think
You may want to practice your skills on these three images. The solution derived by an automatic algorithm is on the lower right corner of each image in 4 columns: Height (km), speed (km/h, not m/s!), direction (°), and standard deviation of the velocity estimate (km/h). Note the change between this and the next image only three hours apart.

## Slide 22: A last challenge
On this image, what is the wind speed and direction at 3 km altitude? As usual you need to think about what wind would have such a radial velocity pattern as a function of azimuth.
I am sorry, I am not providing the answer to that one. Just think! There is only one answer that fits the data, even if it is a bit unexpected.

## Slide 24: Tip on getting speeds right
Color intervals are wide; how do we know where in the interval velocity peaks?
Contrast the 2.2 and the 4.6 km ring. At 4.6 km, the color is just changing at peak velocity, so the peak velocity is near the two color thresholds (13 m/s); at 2.2 km, the color change occurred ~25° away from the peak velocity, so we are well within the orange velocity category (hence ~7 m/s).
[More]

## Slide 25: Tip on getting speeds right
All that being said, with a color scheme such as this, there are limitations to what you can retrieve visually.
Hence, if you are within ± 2 m/s of the correct answer, you are doing fine!
Go back to Example 2

## Slide 26: What you should have found Example 1
Here is the answer to the first wind profile.
On the left, profiles of wind direction and of wind speed are plotted.
On the right, the same information is shown as a table of numbers.
If you did not get it right,
return to Example #1
If you are happy with your answer,
move to Example #2

## Slide 27: What you should have found Example 2
Here is the answer to the second wind profile.
On the left, profiles of wind direction and of wind speed are plotted.
On the right, the same information is shown as a table of numbers.
If you did not get it right,
return to Example #2
If you are happy with your answer,
move to Example #3
Tip on getting speeds right

## Slide 28: What you should have found Example 3
Here is the answer to the third wind profile.
On the left, profiles of wind direction and of wind speed are plotted.
On the right, the same information is shown as a table of numbers.
If you did not get it right,
return to Example #3
If you are happy with your answer,
move to Example #4

## Slide 29: What you should have found Example 4
Here is the answer to the fourth wind profile.
On the left, profiles of wind direction and of wind speed are plotted.
On the right, the same information is shown as a table of numbers.
If you did not get it right,
return to Example #4
If you are happy with your answer,
move to Example #5

## Slide 30: What you should have found Example 5
Here is the answer to the fifth wind profile.
On the left, profiles of wind direction and of wind speed are plotted.
On the right, the same information is shown as a table of numbers.
If you did not get it right,
return to Example #5
If you are happy with your answer,
move to Example #6

## Slide 31: What you should have found Example 6
Here is the answer to the sixth wind profile.
On the left, profiles of wind direction and of wind speed are plotted.
On the right, the same information is shown as a table of numbers.
If you did not get it right,
return to Example #6
If you are happy with your answer,
move to Example #7

## Slide 32: What you should have found Example 7
Here is the answer to the seventh wind profile.
On the left, profiles of wind direction and of wind speed are plotted.
On the right, the same information is shown as a table of numbers.
If you did not get it right,
return to Example #7
If you are happy with your answer,
move to Example #8

## Slide 33: What you should have found Example 8
Here is the answer to the eighth wind profile.
On the left, profiles of wind direction and of wind speed are plotted.
On the right, the same information is shown as a table of numbers.
If you did not get it right,
return to Example #8
If you are happy with your answer,
you are almost done!