## Slide 1: Supplement e05.4: Velocity aliasing and range folding
The Doppler dilemma,
its cause, and its mitigation

## Slide 2: Doppler velocity and change in φ

## Slide 3: Velocity aliasing
Since Dphi = Equation, if |vDOP| is too large or fr too small, DPhi may exceed π. For example, a very strong negative velocity leading to
will look identical to a slower positive velocity.
In this example, as long as the speed of rotation of the dials, or the Doppler velocity, is slow, both dials appear to rotate counter-clockwise.
But when the speed accelerates, the right dial seems to rotate clockwise.
This is velocity aliasing.
Real target phase
Measured target phase

## Slide 4: Velocity aliasing example
In this example where the VAD analysis shows winds aloft in excess of 125 km/h (35 m/s) while the radar’s Nyquist velocity is 31.3 m/s, large areas of aliased velocities (e.g., in purple in the SW) can be seen.

## Slide 5: A velocity aliasing solution?
Given that Equation should not exceed π to avoid aliasing, isn’t a simple solution to increase the pulse repetition frequency fr ?
Not really…
Real target phase
Measured target phase

## Slide 6: Range folding
If the pulse repetition frequency fr is increased too much, the maximum unambiguous range rmax may decrease by such an extent that the next pulse is fired before echoes from the previous pulse have all reached the radar.
These echoes are said to be range-folded.

## Slide 7: Range folding terminology
Echoes originating from within the unambiguous range rmax are known as “first trip echoes”.
Range folded echoes originating from between rmax and 2rmax are “second trip echoes”, while those coming from between 2rmax and 3rmax are “third trip echoes”.
First trip echoes
Second trip echoes

## Slide 8: Example of range folding
Range folded echoes have the same range depth but a narrower cross-range width and height and a lower reflectivity than in reality (wrong r2 assumed when using the radar equation). They however remain difficult to distinguish from first trip echoes.
Four storms (1, 2, 3, 4), and how they appear on a radar with an maximum unambiguous range rmax (1’, 2, 2’, 3, 4’). From Brown and Wood (2006).

## Slide 9: Example of range folding
Range folded echoes have the same range depth but a narrower cross-range width and height and a lower reflectivity than in reality (wrong r2 assumed when using the radar equation). They however remain difficult to distinguish from first trip echoes.
Four storms (1, 2, 3, 4), and how they appear on a radar with an maximum unambiguous range rmax (1’, 2, 2’, 3, 4’). From Brown and Wood (2006).

## Slide 10: The Doppler dilemma: aliasing and/or folding is unavoidable
Given typical radar frequencies (S or C-band), radar ranges (~250 km) and wind speeds (up to 40 m/s), aliasing and/or folding are unavoidable:
fr: | 1500 Hz | 1000 Hz | 600 Hz | fr: | 3000 Hz | 1000 Hz | 600 Hz
rmax: | 100 km | 150 km | 250 km | rmax: | 50 km | 150 km | 250 km
vmax: | 40 m s−1 | 27 m s−1 | 16 m s−1 | vmax: | 40 m s−1 | 13.5 m s−1 | 8 m s−1
S-band (f = 2.8 GHz)
C-band (f = 5.5 GHz)
Approaches must therefore be developed to minimize aliasing, folding, and their impact on radar data quality.
Note that aliasing “simply” adds a multiple of 2vmax to the velocity while range folding displaces and possibly blends echoes together. Folding is hence generally a more serious problem than aliasing.

## Slide 11: Approaches: Different elevation angles, different trade-offs
When thinking of mitigation approaches, it should first be realized that the range up to which echoes are generally seen varies with elevation.
At low elevations, echoes can be observed up to large distances, and both aliasing and folding can occur. At higher elevations, echoes can only be observed at near ranges, naturally limiting the range folding problem; one may hence not have to trade-off between aliasing and folding for those.

## Slide 12: Mitigation approach: Dealiasing using velocity continuity
Given a first guess for the wind at different heights, or by looking for discontinuities
or “jumps” in the wind speeds, one can design an algorithm to dealias velocities especially in large-scale weather systems.
Doppler velocities as measured (aliased)
Doppler velocities after dealiasing
KLGX 3.4° PPI
2015/02/06 7:02

## Slide 13: Mitigation approach: Using more than one fr
Multiple fr can be used to solve two different problems:
a1) Use a very low pulse repetition frequency fr (say, 300 Hz) to detect echoes without folding (rmax = 500 km), deciding to ignore Doppler data quality and the issue of aliasing.
A “clean” reflectivity map is obtained as a result, and is easy to interpret.
The associated (highly aliased) Doppler map is often ignored.

## Slide 14: Mitigation approach: Using more than one fr
Multiple fr can be used to solve two different problems:
a2) Use the clean reflectivity map to determine how echoes will fold when a higher fr is used.
Depending on the relative intensity of the original or the folded echoes, one can establish which will dominate the Doppler measurement; the Doppler velocity can hence be assigned to the correct echo, while the Doppler velocity of the other echo will be declared unknown.
Weaker 2nd trip;
Doppler from 1st trip will dominate
Stronger 2nd trip;
Doppler from 2nd trip will dominate

## Slide 15: Mitigation approach: Using more than one fr
Multiple fr can be used to solve two different problems:
b) Use two fr that have different vmax to determine whether the velocities measured at either fr are aliased or not.
Depending on whether the velocities measured at two fr are similar or not, one can detect and correct for aliasing up to a point.
If fr2 = M/(M+1) fr1, M being a positive integer, it can be shown that the new aliasing velocity for the combination of fr1 and fr2 is equivalent to that obtained with a frequency (M fr1).
Real target phase
Measured target phase

## Slide 16: Mitigation approach: Achieving more than one fr
Multiple fr can be achieved using different approaches, each having slightly different strengths and weaknesses. Staggered PRT are often preferred for velocity dealiasing, while multiple PRFs and successive scans at different PRFs tend to be more often used to deal with range folding at medium and low elevation angles respectively. Also note that one is not limited to using only two frequencies.
1° of azimuth
Firing patterns of transmit pulses
1° of azimuth
1° of azimuth
Scan 1
Multiple PRF
(pulse repetition frequencies) batches
Staggered PRT
(pulse repetition times)
Scan 2
Successive scans at different PRF

## Slide 17: Advanced mitigation approach: Phase coding
Multiple pulse repetition frequencies have limitations, because echoes from multiple pulses often overlay on top of each other, affecting Doppler estimates from all trips.
A technique was hence developed in an attempt to better separate the contribution from each echo: phase coding of transmit pulses.
17
Weaker 2nd trip;
Doppler from 1st trip will dominate
Stronger 2nd trip;
Doppler from 2nd trip will dominate

## Slide 18: Advanced mitigation approach: Phase coding – Without coding
Consider two echoes arriving at the same time at the radar, one from the current transmit pulse, and one from the previous pulse.
For illustration purposes, we will assume that the nearby target is stronger and has a phase slowly increasing with time, while the distant target is weaker and has a phase decreasing more rapidly with time. The combined signal received by the radar blends the two echoes.
Phase of transmit pulse
Signal from the nearby target
Signal from the distant target
Combined signal received

## Slide 19: Advanced mitigation approach: Phase coding – With coding
It is important to remember that target phase is a phase delay φ
that is added to the phase of the transmit pulse.
Therefore, if one adds phase shifts to transmit pulses, first trip echoes will also have their phase shifted by the same amount immediately, while the echoes from previous pulses will have their phase shifted with a delay of M pulses for the (M+1)-trip echoes.
Phase of transmit pulse
Raw signal from the nearby target
Raw signal from the distant target
Combined signal received

## Slide 20: Advanced mitigation approach: Phase coding – Recovering 1st trip
If we now compare the combined signal with respect to (w.r.t.) the phase of the current transmit pulse, the signal from the nearby target will be synchronized with that reference; the combined signal will hence more or less track the velocity of the nearby echo on which is superposed a noisy contribution from the distant target. The velocity of the nearby target can then be retrieved.
Assumed reference phase (current transmit phase)
Raw signal from the nearby target
Raw signal from the distant target
Combined signal w.r.t. assumed reference

## Slide 21: Advanced mitigation approach: Phase coding – Recovering 2nd trip
If we next compare the combined signal w.r.t. the phase of the previous transmit pulse, it is now the signal from the distant target that will be synchronized with that reference; the combined signal now more or less rotates like the velocity of the distant signal despite a strong noisy contribution from the nearby target. The velocity of the weaker distant target can then also be retrieved, although less clearly.
Assumed reference phase (previous transmit phase)
Raw signal from the nearby target
Raw signal from the distant target
Combined signal w.r.t. assumed reference

## Slide 22: Advanced mitigation approach: Phase coding
Phase coding hence allows us to estimate the velocity of echoes from multiple trips all arriving at the same time. It is now being used in many radar systems.
But as the examples here suggest, there are limits: if one echo is much stronger than the other(s), the Doppler velocity of the weaker echo(es) cannot be estimated.
Assumed reference phase (previous transmit phase)
Raw signal from the nearby target
Raw signal from the distant target
Combined signal w.r.t. assumed reference

## Slide 23: Example of Doppler velocities measured using phase coding
Weaker 2nd trip;
Doppler from 1st trip will dominate
Stronger 2nd trip;
Doppler from 2nd trip will dominate
Stronger 2nd trip;
Doppler from 2nd trip dominated
No velocities estimated for 1st trip echoes
Weaker 2nd trip;
Doppler from 1st trip dominated; no velocity was estimated for 2nd trip