## Slide 1: Supplement e02.6: The fluctuating radar signal

## Slide 2: Echoes from distributed targets
Atmospheric targets such as rain and snow are distributed targets.
In a typical radar sampling volume (~ 0.1 km3), one may find of the order of 100 billion raindrops. The returns from each target combine to make a single signal that is received by the radar. Because each drop or snowflake moves, the signal coming from a particular volume evolves in time in complex ways.
To understand what the radar will measure, we need to know what to expect in simpler scenarios. We hence first start to consider what the radar would measure for a single target.

## Slide 3: Signal from a single target
As the transmit wave interacts with the target, a signal is returned back to the radar.
That signal has an amplitude (illustrated by the magnitude of the wave) and a phase
with respect to the transmit wave (illustrated by how far along in the sine function the wave is when it comes back to the antenna).
We can also plot amplitude and phase as a vector, as shown on the left.
Let us see how amplitude and phase will change as the drop moves.

## Slide 4: Signal from a single circling target
While the amplitude of the return signal does not change, its phase does, depending on how quickly the target gets closer or further away from the radar. The rate of phase change can then be used to measure radial velocity.

## Slide 5: Signal from two targets
When two targets are illuminated, their returns combine and interfere. If the returns are in phase, the signal amplitude is maximized; if the returns are 180° out of phase, the signal amplitude is minimized. As targets move with respect to each other, echo amplitude fluctuates.

## Slide 6: Signal from multiple targets
The echo from multiple targets also fluctuates considerably, as targets move in out of configurations where constructive or destructive interference dominates.
The rate of echo fluctuation is dictated by the width of the velocity distribution.

## Slide 7: Signal from multiple targets Consequences
Amplitude measurements provide echo intensity information; phase change measurements are used to compute radial velocity.
A single echo strength measurement is not sufficient to get a good estimate; multiple independent measurements are needed.
It takes some time to get independent measurements: we need to wait for targets to move with respect to each other.
 This limits the maximum scanning speed of weather radars.