## Slide 1: Supplement e02.1: Virtual visit of two radars
The McGill S-band radar and the
U. Massachusetts X-band system

## Slide 2: Two very different systems
Two radar facilities are “visited” to show what radars look like: 1) The large McGill University S-band (10-cm) radar, used for research and weather surveillance near Montreal, Canada; and, 2) the smaller University of Massachusetts X-band (3-cm) system 150 km west of Boston, USA, used as a demonstration for small adaptive radars.
McGill S-band radar tower
X-band radar tower (U. Mass.)

## Slide 3: One common template
Although weather radars may all look very different, they share similar functional blocks.
We shall now follow the travels of a radar pulse from block to block.
Block diagram of a single-antenna pulse radar. This basic design is followed by most weather radars.

## Slide 4: Transmitter
Weather radar transmitters typically generate powerful (10 kW – 1 MW) and short (τ ≈ 1 μs) pulses of microwaves approximately 1000 times per second. The rest of the time, the radar listens for echoes.
At McGill, a weak microwave signal is first shaped into a short transmit pulse lasting one micro-second by the waveform generator boards above the engineer’s hands. That pulse is then amplified to more than 600 kW of power in a few steps that culminates in a big microwave amplifier tube, known as a klystron, located inside the light blue canister on the right.
Location of
transmitter
The S-band klystron transmitter

## Slide 5: Transmitter
Weather radar transmitters typically generate powerful (10 kW – 1 MW) and short (τ ≈ 1 μs) pulses of microwaves approximately 1000 times per second. The rest of the time, the radar listens for echoes.
For small radars such as the one at U. Mass., a single box often contains the transmitter as well as the circulator and the receiver. In this case, the transmitter cannot easily be seen.
The U. Mass. radar inside the radome. The black box on the left contains both the transmitter and receiver.
Location of
transmitter

## Slide 6: Transmitter
Weather radar transmitters typically generate powerful (10 kW – 1 MW) and short (τ ≈ 1 μs) pulses of microwaves approximately 1000 times per second. The rest of the time, the radar listens for echoes.
A comparable transmitter-receiver system is shown on the right. Under the control of the trigger board, a modulator provides short bursts of high current to a magnetron that transforms them into pulses of microwaves.
X-band magnetron transmitter, circulator, and receiver used on McGill vertically pointing radars.
Magnetron
Waveguide
Modulator
Circulator
Receiver
Trigger board
Zoom of the magnetron section (the metal box)
The frequency of the radar is determined by the design of the magnetron. Magnetrons are commonly used as microwave sources in ovens for example.

## Slide 7: Waveguides
The high power radar pulse must be brought towards the antenna. This is achieved by waveguides.
Standard radar waveguides are basically hollow rectangular tubes of metal that can bend or twist. The size of the rectangular section determines the maximum wavelength of the microwaves that can travel within them, while the axis of the narrowest side determines the direction of polarization of the wave.
Brass X-band waveguide
Copper X-band waveguide
Aluminum S-band waveguide

## Slide 8: Circulator
One part of the waveguide is used both to guide waves going out from the transmitter as well as back in towards the receiver. There must be a point where the two paths split. This is done by the circulator.
Its task is to passively redirect what originates from the transmitter towards the antenna, and what comes from the antenna towards the receiver. In the case of the single polarization vertically pointing X-band radar shown before, the circulator is found immediately below the magnetron. The path to the antenna starts into the page and then goes up in the waveguide identified on the image. The path to the receiver goes right of the circulator. To further protect the receiver, a transmit-receive (or T-R) switch is used to prevent transmit power from reaching the receiver.
X-band magnetron transmitter, circulator, and receiver used on McGill vertically pointing radars.
Waveguide
Circulator
Receiver
T-R switch

## Slide 9: Circulator
When a radar sends and receives at two polarizations, the waveguides must also split. There are hence two circulators, one per channel.
On the large S-band system, the transmit pulse traveling from the transmitter (1, flow in red) is first split into two pulses travelling in two waveguide channels (2a and 2b) that ultimately go up (5) towards the antenna. Two circulators (one in 3, one left of 2a) direct the transmitted pulse coming from (2a) to (3) towards (4) and (5), and direct the signal received by the radar (in orange) from (5) and (4) to (3) towards (6).
Location of
circulator
Dual-polarization split and circulators

## Slide 10: Antenna
The final destination of the waveguides is the radar antenna. The role of the antenna is to direct the energy in one direction on transmission, and to capture echoes from that direction on reception.
The photo at right shows the antenna of the S-band system as seen from behind. At longer wavelengths, antennas can be large.
Outside of the photo on the left side is the pedestal that supports the antenna and houses the necessary motors to make it turn. It is from there that the two waveguides come out, run behind the antenna (you can see them), and then go to the front. The radome (the giant golf ball) surrounding the antenna protects the system against the wind and rain.
The parabolic dish of the S-band radar antenna

## Slide 11: Antenna
The final destination of the waveguides is the radar antenna. The role of the antenna is to direct the energy in one direction on transmission, and to capture echoes from that direction on reception.
From the side, we can see the feed of the antenna supported by struts and where the two waveguides converge. The feed is itself a small antenna that directs the energy from the transmitter towards the parabolic dish; the dish then focuses it out in a narrow beam, generally of the order of 1° wide. Echoes on their way back reflect off the dish into the feed, and follow the waveguides back down.
Above: Radar antenna seen from the side. Left: Zoom on the feed with a transparent globe on top.

## Slide 12: Antenna
The final destination of the waveguides is the radar antenna. The role of the antenna is to direct the energy in one direction on transmission, and to capture echoes from that direction on reception.
similar, though the size of the reflector is considerably smaller. Here, the feed is to the right where the two waveguides converge. Note how the two waveguides attach to the feed, the first transmitting and receiving at one polarization, the second at the other polarization.
Dish and feed of the U. Mass. X-band radar
On the University of Massachusetts dual-polarization X-band radar, the set-up is

## Slide 13: Receiver
The echoes travel back via the waveguide to the circulator that directs them towards the receiver. The receiver is designed to amplify the very weak signals received and simplify their digitization and processing.
This is because echoes are weak (as low as 10−15 W) and their frequency too high for direct digitization. The receiver amplifies the signal, and also reduces its frequency f by mixing it with a known wave of frequency fLO to obtain a signal with a frequency f−fLO that can then be digitized.
The image on the right shows, among others, the receiver used at the University of Massachusetts. The S-band receiver at McGill looks very similar.
The black U. Mass. transmitter-receiver box is open, revealing the receiver
Digitizer and signal processor
Receiver

## Slide 14: Digitizer and signal processor
The digitizer then converts the signal into numbers that can then be processed by the signal processor to compute the basic radar measurements such as reflectivity and Doppler velocity.
On the University of Massachusetts system, the digitizer and signal processor are next to the receiver. On other systems such as at McGill, they are located in a building next to the tower, as the lower frequency signal after the receiver can travel “long” distances (several tens of meters).
Once processed, the basic radar measurements can be sent anywhere.
Next to the receiver, the digitizer and signal processor can be found.
Digitizer and signal processor
Receiver

## Slide 15: Product generator and display
Those basic radar measurements are then further processed by a product generator, a specialized software program. The resulting products can then be displayed or used by other programs.
Different radar systems use different approaches. Some radar systems send their basic radar measurements via a network to distant locations where integrated product generator and display systems can manipulate them. Others have product generators at specific locations, such as at the radar site or the weather office, that then send products on request to display systems located anywhere.
A researcher uses the McGill Radar Analysis, Processing and Interactive Display (RAPID) system