## Slide 1: Supplement e02.5: Attenuation formulas

## Slide 2: First, a word of caution
For a variety of applications, a simple way of estimating or parameterizing attenuation is often needed. The following formulas were designed for such purposes. However, be aware that attenuation is particularly difficult to parameterize accurately because:
• The refractive index of water is a complex function of frequency and temperature, as a result of which attenuation can span a large range of values for a given cloud or precipitation amount within a specific radar band. Oxygen attenuation also varies with temperature;
• For precipitation, attenuation is also a function of the hydrometeor size distribution. Expect storm-to-storm variability.
As a result, attenuation varies considerably, and the attenuation tables provided herein can be expected to provide good information only on average.

## Slide 3: Common mistakes
Ignoring that attenuation varies considerably with temperature (at S- and C-band, rain attenuation changes by a factor two between 0°C and 25°C);
Ignoring humidity and clouds (comparable to O2 at C- and X-band);
Oversimplifying the correction of oxygen attenuation (no range or height dependence).

## Slide 4: Process and assumptions used
• The attenuation tables were optimized and simplified to work best within commonly used weather radar bands. They are not designed to work well outside of those bands.
• For attenuation by gas, water vapor, and liquid water, the model of Liebe (1989) was used to compute attenuations in different conditions; these values served as input to generate the relationships to follow.
• For rain, drops were assumed to be spherical with attenuation cross section computed from Bohren and Huffman (1983). The average drop size distribution observed in Montreal, Canada, was used for computations. Montreal has a continental temperate climate, and the calculated attenuations work best for similar conditions. Greatest differences should be expected for areas with maritime climates that generally receive rain with smaller drops.

## Slide 5: Attenuation by oxygen
The first constant is the attenuation in dB/km of dry clean air at sea level for the International Standard Atmosphere (Pref = 101,325 Pa, Tref = 288.15 K (15°C)) at the center of specific radar bands. The correction terms are multiplicative factors to adjust the attenuation for different pressures P (Pa), temperature T (K), frequency f (Hz), and water vapor pressure e (Pa).
Radar band (reference frequency fref)
One-way attenuation at (Pref, Tref, fref)
(dB/km)
Pressure correction term
Temperature correction term
Frequency correction term
S-band (2.8 GHz)
C-band (5.6 GHz)
X-band (9.4 GHz)
Ku-band (13.6 GHz)
Ka-band (35 GHz)
W-band (94 GHz)
0.00700642 (P−0.9e) (P/101325)1.943 / P (T/288.15)-2.93 1 + .103 (f/2.8E9-1)
0.007421098 (P−0.9e) (P/101325)1.98 / P (T/288.15)-2.97 1 + .09 (f/5.5E9-1)
0.007984311 (P−0.9e) (P/101325)1.995 / P (T/288.15)-2.98 (f/9.4E9).207
0.008916323 (P−0.9e) (P/101325)2 / P (T/288.15)-2.97 (f/13.6E9).417
0.02947889 (P−0.5e) (P/101325)2 / P (T/288.15)-2.83 (f/35E9)3.05
0.037341399 (P+1.8e) (P/101325)2 / P (T/288.15)-3.25 (f/94E9)-1.97

## Slide 6: Attenuation by water vapor
Water vapor attenuation has two dominant terms that must be added to get total attenuation by water vapor, one roughly proportional to eP and one to e2, each with somewhat different correction terms for changing temperature, and frequency. There are hence two lines per band on the table.
Radar band (reference frequency fref)
One-way attenuation at (Pref, Tref, fref)
(dB/km)
Pressure correction term
Temperature correction term
Frequency correction term
S-band (2.8 GHz)
C-band (5.6 GHz)
X-band (9.4 GHz)
Ku-band (13.6 GHz)
Ka-band (35 GHz)
W-band (94 GHz)
3.215E-07 e P/101325 (T/288.15)-2.9 (f/2.8E9)2.025
8.08E-11 e2 1 (T/288.15)-9.9 (f/2.8E9)2
1.2895E-06 e P/101325 (T/288.15)-2.88 (f/5.5E9)2.11
3.14E-10 e2 1 (T/288.15)-9.9 (f/5.5E9)2
4.2563E-06 e (P/101325)0.98 (T/288.15)-2.7 (f/9.4E9)2.42
9.303E-10 e2 1 (T/288.15)-10 (f/9.4E9)2.08
1.199E-05 e (P/101325)0.937 (T/288.15)-2.4 (f/13.6E9)3.42
2.026E-9 e2 1 (T/288.15)-10 (f/13.6E9)2.18
5.704E-05 e (P/101325)0.975 (T/288.15)-2.7 (f/35E9)0.18
1.282E-8 e2 1 (T/288.15)-10.1 (f/35E9)1.75
2.773E-04 e P/101325 (T/288.15)-3.16 (f/94E9)2.04
8.797E-8 e2 1 (T/288.15)-10.5 (f/94E9)2

## Slide 7: Attenuation by liquid cloud
Attenuation by liquid cloud is proportional to the cloud liquid water content w (g/m3).
It does not depend on air pressure, but it has a dependence with temperature that is sometimes difficult to parameterize properly, especially when water becomes supercooled at millimetric wavelengths.
Radar band (reference frequency fref)
One-way attenuation at (Pref, Tref, fref)
(dB/km)
Temperature correction term
Frequency correction term
S-band (2.8 GHz)
C-band (5.6 GHz)
X-band (9.4 GHz)
Ku-band (13.6 GHz)
Ka-band (35 GHz)
W-band (94 GHz)
0.0047283 w (T/288.15)-7.3+0.059(T-288.15) (f/2.8E9)2
0.018228 w (T/288.15)-7.2+0.062(T-288.15) (f/5.5E9)2
0.053125 w (T/288.15)-7.16+0.058(T-288.15) (f/9.4E9)1.99
0.11079 w (T/288.15)-7.1+0.058(T-288.15) (f/13.6E9)1.99
0.70588 w (T/288.15)-6.6+0.028(T-288.15) (f/35E9)1.91
4.0189 w (T/288.15)-3.5+0.045(T-288.15) (f/94E9)1.53

## Slide 8: Attenuation by rain
Because raindrops are often at the limit between Rayleigh and Mie scatterers, attenuation is not nicely proportional to the rainfall rate R (mm/hr); it is instead a complicated function that varies considerably with f, R and T, in addition to with the drop size distribution.
In the table, “sqrt()” means √ ; the relationships here fail at very low R (< 0.1 mm/hr).
Radar band (reference frequency fref)
One-way attenuation at (Pref, Tref, fref)
(dB/km)
Temperature correction term
Frequency correction term
S-band (2.8 GHz)
C-band (5.6 GHz)
X-band (9.4 GHz)
Ku-band (13.6 GHz)
Ka-band (35 GHz)
W-band (94 GHz)
0.0003689 (R+0.06)0.94 (T/288.15)-7.4+0.038(T-288.15) (f/2.8E9)2+0.1sqrt(R)
0.0016309 (R+0.1)1.1 (T/288.15)-7.4+0.02(T-288.15) (f/5.5E9)2+0.3sqrt(R)
0.00660 (R+0.11)1.26 (T/288.15)-6.6 exp(-R/7)-0.02(T-288.15) (f/9.4E9)2.4+0.15sqrt(R)
0.019953 (R+0.06)1.24 exp(-0.01*(T-288.15)) (f/13.6E9)2.7-0.1sqrt(R)
0.208305 (1-0.003R)R1.1 1 (f/35E9)2.85-0.25sqrt(R)
1.18 (1-exp(-10R))R0.8-0.001R 1 (f/94E9)2-0.3sqrt(R)
Air density correction term

## Slide 9: Attenuation by snow
A similar challenge occurs with snow rate S (mm/hr). In addition, snow attenuation increases very rapidly near 0°C at centimetric wavelengths, defeating simple parameterizations like these.
In this table, the reference temperature Tref is −5°C; Pref remains 101,325 Pa.
Radar band (reference frequency fref)
One-way attenuation at (Pref, Tref, fref)
(dB/km)
Temperature correction term
Frequency correction term
S-band (2.8 GHz)
C-band (5.6 GHz)
X-band (9.4 GHz)
Ku-band (13.6 GHz)
Ka-band (35 GHz)
W-band (94 GHz)
0.0000318 S0.985 (T/268.15)5 (f/2.8E9)2.3
0.0001583 S1.02 (T/268.15)7.5 (f/5.5E9)2.3
0.0005693 S1.1 (T/268.15)8 (f/9.4E9)2.3
0.0014356 S1.17 .55 + .45 exp[.07(T-268.15)] (f/13.6E9)2.4
0.02075 S1.17 .85 + .15 exp[.06(T-268.15)] (f/35E9)2.9
0. 2786 S1.13 .92 + .08 exp[.03(T-268.15)] (f/94E9)2.5
Air density correction term

## Slide 10: Attenuation parameterization code
On the right (and in the PPT notes) is a subroutine that implements the formulas in the previous tables. You can cut and paste it in your code (please acknowledge if you use it or any other contents of this book or electronic material).
It is written in C. But since it essentially contains only formulas, it should take minutes to convert it to your favorite computer language.
// param_absorp:
// This routine computes an approximation to the one-way attenuation expected
// given microwave frequency, pressure, temperature, vapor pressure, cloud and rain amount
// Input:
// freq: Frequency, in Hz (2-15 GHz, 34-36 GHz, 93-95 GHz)
// atm_pres: Atmospheric pressure (dry + wet), in Pa (10,000-110,000 Pa)
// temp_air: Temperature of the air, in K (180-330 K)
// temp_hydro: Temperature of the hydrometeors (cloud, rain, snow), in K (180-330 K)
// e: Water vapor pressure, in Pa
// w: Cloud liquid water content (g/m3)
// r: Rain rate (mm/hr)
// s: Snow rate (mm/hr)
// Returns: -1 when well outside of the parameter space for which it was designed,
// or the expected one-way attenuation in dB/km.
double param_absorp(double freq, double atm_pres, double temp_air, double temp_hydro, double e, double w, double r, double s) {
double atten_dry ;
double atten_e_lin_term ;
double atten_e_square_term ;
double atten_per_w ;
double atten_r ;
double atten_s ;
double atten_total ;
atten_dry = 0. ;
atten_e_lin_term = 0. ;
atten_e_square_term = 0. ;
atten_per_w = 0. ;
atten_r = 0. ;
atten_s = 0. ;
atten_total = 0. ;
// Part 1: Checks if input parameters are within the range for which this should perform reasonably.
// If not, exit the routine prematurely, returning -1.
if( e < 0. ) e = 0. ;
if( w < 0. ) w = 0. ;
if( r < 0. ) r = 0. ;
if( s < 0. ) s = 0. ;
if( freq < 2.E9 ) return(-1) ; // Leave if: frequency less than 2 GHz
if((freq > 16.E9) && (freq < 34.E9)) return(-1) ; // frequency is between 16 and 34 GHz
if((freq > 36.E9) && (freq < 93.E9)) return(-1) ; // frequency is between 36 and 93 GHz
if( freq > 95.E9 ) return(-1) ; // frequency is above 95 GHz
if( atm_pres < 10000. ) return(-1) ; // Leave if P < 10,000 Pa (100 mb)
if( atm_pres > 110000. ) return(-1) ; // or if P > 110,000 Pa (1100 mb)
if( temp_air < 180. ) return(-1) ; // or if T < 180 K (-93 C)
if( temp_hydro < 180. ) return(-1) ;
if( temp_air > 330. ) return(-1) ; // or if T > 330 K (57 C)
if( temp_hydro > 320. ) return(-1) ;
if( (r > 0.) && (temp_hydro < 260.) ) return(-1) ; // or if rain or clouds are too supercooled
if( (w > 0.) && (temp_hydro < 240.) ) return(-1) ;
// Part 2: Parameterize attenuation at different radar frequencies
// S-band, relationship optimized for 2.7-2.9 GHz
if( (freq >= 2.E9) && (freq < 4.0E9) ) {
atten_dry = 0.00700642 * (atm_pres - .9*e) / atm_pres * (1. + (freq/2.8E9-1.) * .103) * pow(atm_pres/101325., 1.943) * pow(temp_air / 288.15, -2.93) ;
atten_e_lin_term = 3.215e-07 * atm_pres/101325. * pow(freq/2.8E9, 2.025) * pow(temp_air / 288.15, -2.9) ;
atten_e_square_term = 8.08e-11 * pow(freq/2.8E9, 2.0) * pow(temp_air / 288.15, -9.9) ;
atten_per_w = 0.004728313 * pow(freq/2.8E9, 2.) * pow(temp_hydro / 288.15, -7.3+(.059*(temp_hydro-288.15))) ;
atten_r = 0.00036892 * pow(r+.06,.94) * pow(freq/2.8E9, 2.+.1*sqrt(r)) * pow(temp_hydro / 288.15, -7.4+(.038*(temp_hydro-288.15))) * pow(atm_pres*288.15/(101325.*temp_air), 0.5) ;
atten_s = 3.18e-5 * pow(s, .985) * pow(freq/2.8E9, 2.3) * pow(temp_hydro / 268.15, 5.) * pow(atm_pres*268.15/(101325.*temp_air), 0.5) ;
}
// C-band, relationship optimized for 5.4-5.6 GHz
else if( (freq >= 4.0E9) && (freq < 8.0E9) ) {
atten_dry = 0.007421098 * (atm_pres - .9*e) / atm_pres * (1. + (freq/5.5E9-1.) * .09) * pow(atm_pres/101325., 1.98) * pow(temp_air / 288.15, -2.97) ;
atten_e_lin_term = 1.2895e-06 * atm_pres/101325. * pow(freq/5.5E9, 2.11) * pow(temp_air / 288.15, -2.88) ;
atten_e_square_term = 3.14e-10 * pow(freq/5.5E9, 2.0) * pow(temp_air / 288.15, -9.9) ;
atten_per_w = 0.01822807 * pow(freq/5.5E9, 2.) * pow(temp_hydro / 288.15, -7.2+(.062*(temp_hydro-288.15))) ;
atten_r = 0.00163086 * pow(r+.1,1.1) * pow(freq/5.5E9, 2.+.3*sqrt(r)) * pow(temp_hydro / 288.15, -7.4+(.02*(temp_hydro-288.15))) * pow(atm_pres*288.15/(101325.*temp_air), 0.5) ;
atten_s = 0.00015826 * pow(s, 1.02) * pow(freq/5.5E9, 2.3) * pow(temp_hydro / 268.15, 7.5) * pow(atm_pres*268.15/(101325.*temp_air), 0.5) ;
}
// X-band, relationship optimized for 9.3-9.5 GHz
else if( (freq >= 8.0E9) && (freq < 12.0E9) ) {
atten_dry = 0.007984311 * (atm_pres - .9*e) / atm_pres * pow(freq/9.4E9, .207) * pow(atm_pres/101325., 1.995) * pow(temp_air / 288.15, -2.98) ;
atten_e_lin_term = 4.2563e-06 * pow(atm_pres/101325.,.98) * pow(freq/9.4E9, 2.42) * pow(temp_air / 288.15, -2.7) ;
atten_e_square_term = 9.303e-10 * pow(freq/9.4E9, 2.08) * pow(temp_air / 288.15, -10.) ;
atten_per_w = 0.05312521 * pow(freq/9.4E9, 1.99) * pow(temp_hydro / 288.15, -7.16+(.058*(temp_hydro-288.15))) ;
atten_r = 0.0066 * pow(r+.11,1.26) * pow(freq/9.4E9, 2.4+.15*sqrt(r)) * pow(temp_hydro / 288.15, (-6.6*exp(-r/7.)-(.02*(temp_hydro-288.15)))) * pow(atm_pres*288.15/(101325.*temp_air), 0.5) ;
atten_s = 0.00056929 * pow(s, 1.1) * pow(freq/9.4E9, 2.3) * pow(temp_hydro / 268.15, 8.) * pow(atm_pres*268.15/(101325.*temp_air), 0.5) ;
}
// Ku-band, relationship optimized for 13.6 GHz
else if( (freq >= 12.0E9) && (freq <= 16.0E9) ) {
atten_dry = 0.008916323 * (atm_pres - .9*e) / atm_pres * pow(freq/13.6E9, .417) * pow(atm_pres/101325., 2.) * pow(temp_air / 288.15, -2.97) ;
atten_e_lin_term = 1.199e-05 * pow(atm_pres/101325.,.937) * pow(freq/13.6E9, 3.42) * pow(temp_air / 288.15, -2.4) ;
atten_e_square_term = 2.026e-9 * pow(freq/13.6E9, 2.18) * pow(temp_air / 288.15, -10.) ;
atten_per_w = 0.1107939 * pow(freq/13.6E9, 1.99) * pow(temp_hydro / 288.15, -7.1+(.058*(temp_hydro-288.15))) ;
atten_r = 0.019953 * exp(-.01*(temp_hydro-288.15)) * pow(r+.06,1.24+.005*(temp_hydro-288.15)) * pow(freq/13.6E9, 2.7-.1*sqrt(r)) * pow(atm_pres*288.15/(101325.*temp_air), 0.5) ;
atten_s = 0.00143555 * pow(s, 1.17) * pow(freq/13.6E9, 2.4) * (.55 + .45 * exp(.07 * (temp_hydro - 268.15))) * pow(atm_pres*268.15/(101325.*temp_air), 0.5) ;
}
// Ka-band, relationship optimized for 35 GHz
else if( (freq >= 34.E9) && (freq <= 36.0E9) ) {
atten_dry = 0.02947889 * (atm_pres - .5*e) / atm_pres * pow(freq/35.E9, 3.05) * pow(atm_pres/101325., 2.) * pow(temp_air / 288.15, -2.83) ;
atten_e_lin_term = 5.704e-05 * pow(atm_pres/101325.,.975) * pow(freq/35.E9, .18) * pow(temp_air / 288.15, -2.7) ;
atten_e_square_term = 1.282e-8 * pow(freq/35.E9, 1.75) * pow(temp_air / 288.15, -10.1) ;
atten_per_w = 0.7058844 * pow(freq/35.E9, 1.91) * pow(temp_hydro / 288.15, -6.6+(.028*(temp_hydro-288.15))) ;
atten_r = 0.2083054 * (1 - .003*r) * pow(r,1.1) * pow(freq/35.E9, 2.85-.25*sqrt(r)) * pow(atm_pres*288.15/(101325.*temp_air), 0.5) ;
atten_s = 0.02074907 * pow(s, 1.27) * pow(freq/35.E9, 2.9) * (.85 + .15 * exp(.06 * (temp_hydro - 268.15))) * pow(atm_pres*268.15/(101325.*temp_air), 0.5) ;
}
// W-band, relationship optimized for 94 GHz
else if( (freq >= 93.E9) && (freq <= 95.0E9) ) {
atten_dry = 0.037341399 * (atm_pres+1.8*e) / atm_pres * pow(freq/94.E9, -1.97) * pow(atm_pres/101325., 2.) * pow(temp_air / 288.15, -3.25) ;
atten_e_lin_term = 2.773e-04 * atm_pres/101325. * pow(freq/94.E9, 2.04) * pow(temp_air / 288.15, -3.16) ;
atten_e_square_term = 8.797e-8 * pow(freq/94.E9, 2.0) * pow(temp_air / 288.15, -10.5) ;
atten_per_w = 4.018882 * pow(freq/94.E9, 1.53) * pow(temp_hydro / 288.15, -3.5-(.045*(temp_hydro-288.15))) ; /* Poor for supercooled water */
atten_r = 1.18 * (1 - exp(-10.*r)) * pow(r,.8-.001*r) * pow(freq/94.E9, 2.-.3*sqrt(r)) * pow(atm_pres*288.15/(101325.*temp_air), 0.5) ;
atten_s = 0.2785951 * pow(s, 1.13) * pow(freq/94.E9, 2.5) * (.92 + .08 * exp(.03 * (temp_hydro - 268.15))) * pow(atm_pres*268.15/(101325.*temp_air), 0.5) ;
}
// Final correction for very weak rainfalls and drizzles to get 0 attenuation at r = 0
if( r < .1 ) atten_r = atten_r * sqrt(r / .1) ;
atten_total = atten_dry + atten_e_lin_term * e + atten_e_square_term * (e*e) + atten_per_w * w + atten_r + atten_s ;
return(atten_total) ;
}
Notes: // param_absorp:
// This routine computes an approximation to the one-way attenuation expected
// given microwave frequency, pressure, temperature, vapor pressure, cloud and rain amount
// Input:
// freq: Frequency, in Hz (2-15 GHz, 34-36 GHz, 93-95 GHz)
// atm_pres: Atmospheric pressure (dry + wet), in Pa (10,000-110,000 Pa)
// temp_air: Temperature of the air, in K (180-330 K)
// temp_hydro: Temperature of the hydrometeors (cloud, rain, snow), in K (180-330 K)
// e: Water vapor pressure, in Pa
// w: Cloud liquid water content (g/m3)
// r: Rain rate (mm/hr)
// s: Snow rate (mm/hr)
// Returns: -1 when well outside of the parameter space for which it was designed,
// or the expected one-way attenuation in dB/km.
double param_absorp(double freq, double atm_pres, double temp_air, double temp_hydro, double e, double w, double r, double s) {
double atten_dry ;
double atten_e_lin_term ;
double atten_e_square_term ;
double atten_per_w ;
double atten_r ;
double atten_s ;
double atten_total ;
atten_dry = 0. ;
atten_e_lin_term = 0. ;
atten_e_square_term = 0. ;
atten_per_w = 0. ;
atten_r = 0. ;
atten_s = 0. ;
atten_total = 0. ;
// Part 1: Checks if input parameters are within the range for which this should perform reasonably.
// If not, exit the routine prematurely, returning -1.
if( e < 0. ) e = 0. ;
if( w < 0. ) w = 0. ;
if( r < 0. ) r = 0. ;
if( s < 0. ) s = 0. ;
if( freq < 2.E9 ) return(-1) ; // Leave if: frequency less than 2 GHz
if((freq > 16.E9) && (freq < 34.E9)) return(-1) ; // frequency is between 16 and 34 GHz
if((freq > 36.E9) && (freq < 93.E9)) return(-1) ; // frequency is between 36 and 93 GHz
if( freq > 95.E9 ) return(-1) ; // frequency is above 95 GHz
if( atm_pres < 10000. ) return(-1) ; // Leave if P < 10,000 Pa (100 mb)
if( atm_pres > 110000. ) return(-1) ; // or if P > 110,000 Pa (1100 mb)
if( temp_air < 180. ) return(-1) ; // or if T < 180 K (-93 C)
if( temp_hydro < 180. ) return(-1) ;
if( temp_air > 330. ) return(-1) ; // or if T > 330 K (57 C)
if( temp_hydro > 320. ) return(-1) ;
if( (r > 0.) && (temp_hydro < 260.) ) return(-1) ; // or if rain or clouds are too supercooled
if( (w > 0.) && (temp_hydro < 240.) ) return(-1) ;
// Part 2: Parameterize attenuation at different radar frequencies
// S-band, relationship optimized for 2.7-2.9 GHz
if( (freq >= 2.E9) && (freq < 4.0E9) ) {
atten_dry = 0.00700642 * (atm_pres - .9*e) / atm_pres * (1. + (freq/2.8E9-1.) * .103) * pow(atm_pres/101325., 1.943) * pow(temp_air / 288.15, -2.93) ;
atten_e_lin_term = 3.215e-07 * atm_pres/101325. * pow(freq/2.8E9, 2.025) * pow(temp_air / 288.15, -2.9) ;
atten_e_square_term = 8.08e-11 * pow(freq/2.8E9, 2.0) * pow(temp_air / 288.15, -9.9) ;
atten_per_w = 0.004728313 * pow(freq/2.8E9, 2.) * pow(temp_hydro / 288.15, -7.3+(.059*(temp_hydro-288.15))) ;
atten_r = 0.00036892 * pow(r+.06,.94) * pow(freq/2.8E9, 2.+.1*sqrt(r)) * pow(temp_hydro / 288.15, -7.4+(.038*(temp_hydro-288.15))) * pow(atm_pres*288.15/(101325.*temp_air), 0.5) ;
atten_s = 3.18e-5 * pow(s, .985) * pow(freq/2.8E9, 2.3) * pow(temp_hydro / 268.15, 5.) * pow(atm_pres*268.15/(101325.*temp_air), 0.5) ;
}
// C-band, relationship optimized for 5.4-5.6 GHz
else if( (freq >= 4.0E9) && (freq < 8.0E9) ) {
atten_dry = 0.007421098 * (atm_pres - .9*e) / atm_pres * (1. + (freq/5.5E9-1.) * .09) * pow(atm_pres/101325., 1.98) * pow(temp_air / 288.15, -2.97) ;
atten_e_lin_term = 1.2895e-06 * atm_pres/101325. * pow(freq/5.5E9, 2.11) * pow(temp_air / 288.15, -2.88) ;
atten_e_square_term = 3.14e-10 * pow(freq/5.5E9, 2.0) * pow(temp_air / 288.15, -9.9) ;
atten_per_w = 0.01822807 * pow(freq/5.5E9, 2.) * pow(temp_hydro / 288.15, -7.2+(.062*(temp_hydro-288.15))) ;
atten_r = 0.00163086 * pow(r+.1,1.1) * pow(freq/5.5E9, 2.+.3*sqrt(r)) * pow(temp_hydro / 288.15, -7.4+(.02*(temp_hydro-288.15))) * pow(atm_pres*288.15/(101325.*temp_air), 0.5) ;
atten_s = 0.00015826 * pow(s, 1.02) * pow(freq/5.5E9, 2.3) * pow(temp_hydro / 268.15, 7.5) * pow(atm_pres*268.15/(101325.*temp_air), 0.5) ;
}
// X-band, relationship optimized for 9.3-9.5 GHz
else if( (freq >= 8.0E9) && (freq < 12.0E9) ) {
atten_dry = 0.007984311 * (atm_pres - .9*e) / atm_pres * pow(freq/9.4E9, .207) * pow(atm_pres/101325., 1.995) * pow(temp_air / 288.15, -2.98) ;
atten_e_lin_term = 4.2563e-06 * pow(atm_pres/101325.,.98) * pow(freq/9.4E9, 2.42) * pow(temp_air / 288.15, -2.7) ;
atten_e_square_term = 9.303e-10 * pow(freq/9.4E9, 2.08) * pow(temp_air / 288.15, -10.) ;
atten_per_w = 0.05312521 * pow(freq/9.4E9, 1.99) * pow(temp_hydro / 288.15, -7.16+(.058*(temp_hydro-288.15))) ;
atten_r = 0.0066 * pow(r+.11,1.26) * pow(freq/9.4E9, 2.4+.15*sqrt(r)) * pow(temp_hydro / 288.15, (-6.6*exp(-r/7.)-(.02*(temp_hydro-288.15)))) * pow(atm_pres*288.15/(101325.*temp_air), 0.5) ;
atten_s = 0.00056929 * pow(s, 1.1) * pow(freq/9.4E9, 2.3) * pow(temp_hydro / 268.15, 8.) * pow(atm_pres*268.15/(101325.*temp_air), 0.5) ;
}
// Ku-band, relationship optimized for 13.6 GHz
else if( (freq >= 12.0E9) && (freq <= 16.0E9) ) {
atten_dry = 0.008916323 * (atm_pres - .9*e) / atm_pres * pow(freq/13.6E9, .417) * pow(atm_pres/101325., 2.) * pow(temp_air / 288.15, -2.97) ;
atten_e_lin_term = 1.199e-05 * pow(atm_pres/101325.,.937) * pow(freq/13.6E9, 3.42) * pow(temp_air / 288.15, -2.4) ;
atten_e_square_term = 2.026e-9 * pow(freq/13.6E9, 2.18) * pow(temp_air / 288.15, -10.) ;
atten_per_w = 0.1107939 * pow(freq/13.6E9, 1.99) * pow(temp_hydro / 288.15, -7.1+(.058*(temp_hydro-288.15))) ;
atten_r = 0.019953 * exp(-.01*(temp_hydro-288.15)) * pow(r+.06,1.24+.005*(temp_hydro-288.15)) * pow(freq/13.6E9, 2.7-.1*sqrt(r)) * pow(atm_pres*288.15/(101325.*temp_air), 0.5) ;
atten_s = 0.00143555 * pow(s, 1.17) * pow(freq/13.6E9, 2.4) * (.55 + .45 * exp(.07 * (temp_hydro - 268.15))) * pow(atm_pres*268.15/(101325.*temp_air), 0.5) ;
}
// Ka-band, relationship optimized for 35 GHz
else if( (freq >= 34.E9) && (freq <= 36.0E9) ) {
atten_dry = 0.02947889 * (atm_pres - .5*e) / atm_pres * pow(freq/35.E9, 3.05) * pow(atm_pres/101325., 2.) * pow(temp_air / 288.15, -2.83) ;
atten_e_lin_term = 5.704e-05 * pow(atm_pres/101325.,.975) * pow(freq/35.E9, .18) * pow(temp_air / 288.15, -2.7) ;
atten_e_square_term = 1.282e-8 * pow(freq/35.E9, 1.75) * pow(temp_air / 288.15, -10.1) ;
atten_per_w = 0.7058844 * pow(freq/35.E9, 1.91) * pow(temp_hydro / 288.15, -6.6+(.028*(temp_hydro-288.15))) ;
atten_r = 0.2083054 * (1 - .003*r) * pow(r,1.1) * pow(freq/35.E9, 2.85-.25*sqrt(r)) * pow(atm_pres*288.15/(101325.*temp_air), 0.5) ;
atten_s = 0.02074907 * pow(s, 1.27) * pow(freq/35.E9, 2.9) * (.85 + .15 * exp(.06 * (temp_hydro - 268.15))) * pow(atm_pres*268.15/(101325.*temp_air), 0.5) ;
}
// W-band, relationship optimized for 94 GHz
else if( (freq >= 93.E9) && (freq <= 95.0E9) ) {
atten_dry = 0.037341399 * (atm_pres+1.8*e) / atm_pres * pow(freq/94.E9, -1.97) * pow(atm_pres/101325., 2.) * pow(temp_air / 288.15, -3.25) ;
atten_e_lin_term = 2.773e-04 * atm_pres/101325. * pow(freq/94.E9, 2.04) * pow(temp_air / 288.15, -3.16) ;
atten_e_square_term = 8.797e-8 * pow(freq/94.E9, 2.0) * pow(temp_air / 288.15, -10.5) ;
atten_per_w = 4.018882 * pow(freq/94.E9, 1.53) * pow(temp_hydro / 288.15, -3.5-(.045*(temp_hydro-288.15))) ; /* Poor for supercooled water */
atten_r = 1.18 * (1 - exp(-10.*r)) * pow(r,.8-.001*r) * pow(freq/94.E9, 2.-.3*sqrt(r)) * pow(atm_pres*288.15/(101325.*temp_air), 0.5) ;
atten_s = 0.2785951 * pow(s, 1.13) * pow(freq/94.E9, 2.5) * (.92 + .08 * exp(.03 * (temp_hydro - 268.15))) * pow(atm_pres*268.15/(101325.*temp_air), 0.5) ;
}
// Final correction for very weak rainfalls and drizzles to get 0 attenuation at r = 0
if( r < .1 ) atten_r = atten_r * sqrt(r / .1) ;
atten_total = atten_dry + atten_e_lin_term * e + atten_e_square_term * (e*e) + atten_per_w * w + atten_r + atten_s ;
return(atten_total) ;
}

## Slide 11: Going beyond (I)
Despite their sometimes complicated functional relationships, even within the typical radar frequency bands, the formulas above cannot work perfectly in all tropospheric conditions.
For more accurate work, or for better results outside of the usual radar bands and tropospheric temperatures, I recommend a good basic all-purpose attenuation model such as Liebe (1989) for gas and cloud attenuation (http://www.its.bldrdoc.gov/resources/radio-propagation-software/mpm/millimeter-wave-propagation-model-mpm.aspx; though MPM supposedly does rainfall, it does not do a good job of it).
Liebe, H.J, 1989: MPM - An atmospheric mm-wave propagation model. International Journal of Infrared and Millimeter Waves, 10, 631–650.

## Slide 12: Going beyond (II)
For more accurate work on precipitation, given DSD variability and the underrated sensitivity of attenuation to temperature, one is generally forced to first simulate the absorption from individual hydrometeor sizes given their size, shape, and the radar viewing angle, and then sum them for all drop sizes and numbers.
A good starting point to achieve this is Mischenko et al. (2002) that can be used to compute the scattering and attenuation of prolate (sausage-shaped) and oblate (hamburger-shaped) spheroids.

## Slide 13: Going beyond (III)
Finally, for complex mixtures such as melting snow, one must first make an assumption on the morphology of the hydrometeor (what type of mixture shall be assumed, e.g., multi-layered or single layered, and what each layer is made of), compute the equivalent refractive index and size of a melting particle as a function of melted fraction, and then sum of particles as a function of their number and their size given their size-dependent melted fraction.
A good starting point to achieve this is Fabry and Szyrmer (1999), though their work did not specifically focused on attenuation, and papers referencing it.

## Slide 14: References
Bohren, C. F., and D. R. Huffman, 1983: Absorption and Scattering of Light by Small Particles. Wiley, 530 pp.
Fabry, F., and W. Szyrmer, 1999: Modeling of the melting layer. Part II: Electromagnetic. Journal of the Atmospheric Sciences, 56, 3593–3600.
Liebe, H. J, 1989: MPM - An atmospheric mm-wave propagation model. International Journal of Infrared and Millimeter Waves, 10, 631–650.
Mischenko, M.I., L.D. Travis, and A.A. Lacis, 2002: Scattering, Absorption, and Emission of Light by Small Particles, Cambridge University Press, 228 pp.