## Slide 1: Digital Design: A Systems Approach Lecture 12: Timing

## Slide 2: Readings
L12: Chapter 15
L13: Chapter 27 & 28

## Slide 3: Timing
How fast can a system run?
Will it work at any speed?

## Slide 4: Propagation Delay and Contamination Delay
Propagation Delay – Time from last input change until last output change. (Input at steady state to output at steady state.)
Contamination Delay – Time from first input change until first output change. (Input contaminated to output contaminated)

## Slide 5: Example, Contamination and Propagation Delay of Full Adder
Gate | Delay (ps)
Nand2 | 80
OAI21 | 120
min | a,b | cin
g’ | 80 | -
p’ | 120 | -
cout | 200 | 120
U3 | 200 | 80
s | 240 | 120
max | a,b | cin
g’ | 80 | -
p’ | 200 | -
cout | 320 | 120
U3 | 280 | 80
s | 400 | 200
What is
tdas
tcas
tdcs
tccc

## Slide 6: Example, Contamination and Propagation Delay of Full Adder
Gate | Delay (ps)
Nand2 | 80
OAI21 | 120
min | a,b | cin
g’ | 80 | -
p’ | 120 | -
cout | 200 | 120
U3 | 200 | 80
s | 240 | 120
max | a,b | cin
g’ | 80 | -
p’ | 200 | -
cout | 320 | 120
U3 | 280 | 80
s | 400 | 200
What is
tdas
tcas
tdcs
tccc

## Slide 7: Example, Contamination and Propagation Delay of Full Adder
Gate | Delay (ps)
Nand2 | 80
OAI21 | 120
min | a,b | cin
g’ | 80 | -
p’ | 120 | -
cout | 200 | 120
U3 | 200 | 80
s | 240 | 120
max | a,b | cin
g’ | 80 | -
p’ | 200 | -
cout | 320 | 120
U3 | 280 | 80
s | 400 | 200
What is
tdas
tcas
tdcs
tccc

## Slide 8: Note that if a, b goes from 0,0 to 1,1 contamination does occur

## Slide 9: What about an n-bit adder?
Assume delay of FA is 1
What is
tdas
tcas
tdcs
tccs

## Slide 10: 4-bit Prime or one Function in Verilog Code – Result of synthesizing description using case
module prime ( in, isprime );
input [3:0] in;
output isprime;
wire n1, n2, n3, n4;
OAI13 U1 ( .A1(n2), .B1(n1), .B2(in[2]), .B3(in[3]), .Y(isprime) );
INV U2 ( .A(in[1]), .Y(n1) );
INV U3 ( .A(in[3]), .Y(n3) );
XOR2 U4 ( .A(in[2]), .B(in[1]), .Y(n4) );
OAI12 U5 ( .A1(in[0]), .B1(n3), .B2(n4), .Y(n2) );
endmodule

## Slide 11: Synthesis Reports
****************************************
Report : area
Design : prime
Version: 2003.06
Date : Sat Oct 4 11:38:08 2003
****************************************
Library(s) Used:
GS30KA_W_125_1.35_CORE.db (File: /home/imagine/from_ti/gs30ka_1.3/sun5/synop
sys/lib/GS30KA_W_125_1.35_CORE.db)
Number of ports: 5
Number of nets: 9
Number of cells: 5
Number of references: 4
Combinational area: 7.000000
Noncombinational area: 0.000000
Net Interconnect area: undefined (Wire load has zero net area)
Total cell area: 7.000000
Total area: undefined
****************************************
Report : timing
-path full
-delay max
-max_paths 1
Design : prime
Version: 2003.06
Date : Sat Oct 4 11:38:08 2003
****************************************
Operating Conditions:
Wire Load Model Mode: enclosed
Startpoint: in[2] (input port)
Endpoint: isprime (output port)
Path Group: (none)
Path Type: max
Des/Clust/Port Wire Load Model Library
------------------------------------------------
prime 2K_5LM GS30KA_W_125_1.35_CORE.db
Point Incr Path
-----------------------------------------------------------
input external delay 0.000 0.000 r
in[2] (in) 0.000 0.000 r
U4/Y (EX210) 0.191 0.191 f
U5/Y (BF051) 0.116 0.307 r
U1/Y (BF052) 0.168 0.475 f
isprime (out) 0.000 0.475 f
data arrival time 0.475
-----------------------------------------------------------
(Path is unconstrained)

## Slide 12: Timing report from Xilinx tools
Delay: 7.668ns (Levels of Logic = 20)
Source: wave_buffer_inst/Mram_RAM_inst_ramb_0 (RAM)
Destination: vga_blue_reg/q_1 (FF)
Source Clock: clk rising
Destination Clock: clk rising
Data Path: wave_buffer_inst/Mram_RAM_inst_ramb_0 to vga_blue_reg/q_1
Gate Net
Cell:in->out fanout Delay Delay Logical Name (Net Name)
---------------------------------------- ------------
RAMB16_S36_S36:CLKB->DOB0 4 1.500 0.629 wave_buffer_inst/Mram_RAM_inst_ramb_0 (data_read<0>)
LUT2_L:I0->LO 1 0.313 0.000 vga_driver_inst/XNor_stagelut (vga_driver_inst/N2)
MUXCY:S->O 1 0.377 0.000 vga_driver_inst/XNor_stagecy (vga_driver_inst/XNor_stage_cyo)
MUXCY:CI->O 1 0.042 0.000 vga_driver_inst/XNor_stagecy_rn_0 (vga_driver_inst/XNor_stage_cyo1)
MUXCY:CI->O 1 0.042 0.000 vga_driver_inst/XNor_stagecy_rn_1 (vga_driver_inst/XNor_stage_cyo2)
MUXCY:CI->O 1 0.042 0.000 vga_driver_inst/XNor_stagecy_rn_2 (vga_driver_inst/XNor_stage_cyo3)
MUXCY:CI->O 1 0.042 0.000 vga_driver_inst/XNor_stagecy_rn_3 (vga_driver_inst/XNor_stage_cyo4)
MUXCY:CI->O 1 0.042 0.000 vga_driver_inst/XNor_stagecy_rn_4 (vga_driver_inst/XNor_stage_cyo5)
MUXCY:CI->O 1 0.042 0.000 vga_driver_inst/XNor_stagecy_rn_5 (vga_driver_inst/XNor_stage_cyo6)
MUXCY:CI->O 23 0.524 0.779 vga_driver_inst/XNor_stagecy_rn_6 (vga_driver_inst/XNor_stage_cyo7)
LUT3:I2->O 1 0.313 0.533 vga_driver_inst/_AUX_5<0>1 (vga_driver_inst/max_data<0>)
LUT2_L:I0->LO 1 0.313 0.000 vga_driver_inst/XNor_stagelut8 (vga_driver_inst/N11)
MUXCY:S->O 1 0.377 0.000 vga_driver_inst/XNor_stagecy_rn_7 (vga_driver_inst/XNor_stage_cyo8)
MUXCY:CI->O 1 0.041 0.000 vga_driver_inst/XNor_stagecy_rn_8 (vga_driver_inst/XNor_stage_cyo9)
MUXCY:CI->O 1 0.041 0.000 vga_driver_inst/XNor_stagecy_rn_9 (vga_driver_inst/XNor_stage_cyo10)
MUXCY:CI->O 1 0.041 0.000 vga_driver_inst/XNor_stagecy_rn_10 (vga_driver_inst/XNor_stage_cyo11)
MUXCY:CI->O 1 0.041 0.000 vga_driver_inst/XNor_stagecy_rn_11 (vga_driver_inst/XNor_stage_cyo12)
MUXCY:CI->O 1 0.041 0.000 vga_driver_inst/XNor_stagecy_rn_12 (vga_driver_inst/XNor_stage_cyo13)
MUXCY:CI->O 1 0.041 0.000 vga_driver_inst/XNor_stagecy_rn_13 (vga_driver_inst/XNor_stage_cyo14)
MUXCY:CI->O 1 0.525 0.440 vga_driver_inst/XNor_stagecy_rn_14 (vga_driver_inst/_n0002)
LUT4_D:I3->LO 1 0.313 0.000 vga_driver_inst/rgb_mux_select2 (N531)
FD:D 0.234 vga_blue_reg/q_1
----------------------------------------
Total 7.668ns (5.287ns logic, 2.381ns route)
(68.9% logic, 31.1% route)

## Slide 13: And, from the .twr file
================================================================================
Timing constraint: TS_J_TO_J = MAXDELAY FROM TIMEGRP "J_CLK" TO TIMEGRP "J_CLK" 30 ns;
2782 items analyzed, 0 timing errors detected. (0 setup errors, 0 hold errors)
Maximum delay is 7.915ns.
--------------------------------------------------------------------------------

## Slide 14: Contamination delay is not the same thing as minimum delay Contamination delay - is the minimum amount of time from an input signal change to an output signal change Minimum delay - is the minimum amount of time from an input signal change (to its correct value) to an output signal taking on its correct value

## Slide 15: Synchronous Sequential Logic

## Slide 16: Edge-Triggered D Flip-Flop

## Slide 17
Setup Time Constraint

## Slide 18
Hold Time Constraint
tcXY – contamination delay
tdXY – propagation delay
Unsafe at any speed

## Slide 19: Example
tdCQ = tcCQ = ts = 150ps
th = 250ps
tdMax = 850ps
tcMin = 100ps
Is hold time constraint met?
What is the minimum cycle time?

## Slide 20: Clock Skew

## Slide 21: Example
tdCQ = tcCQ = ts = 150ps
th = 250ps
tdMax = 850ps
tcMin = 100ps
tk = 100ps
Is hold time constraint met?
What is the minimum cycle time?

## Slide 22: Another example
You have three flip-flops connected as a shift register
You need to connect the clock to these three flip flops
Your connection must be from flip-flop to flip-flop (no intermediate points)
Each segment of your connection takes tdck=200ps
Assume ts = th = tdcq = tccq = 100ps
How should you connect the clock to these flip-flops (what order?)

## Slide 23: Summary
Delays in digital systems
  Propagation delay
  Contamination delay
Flip-flop timing constraints
  Setup time (ts)
  Hold time (th)
Cycle time determined by maximum delay
Correct operation depends on minimum delay
Clock skew affects both

## Slide 24: A Preview of coming attractions

## Slide 25: Coming Next Lecture
Metastability and synchronization failure
or – When good flip-flops go bad