## Slide 1: Inverse Scattering and Diffraction Tomography in Complex Media
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Anthony J. Devaney
Department of Electrical and Computer Engineering
Northeastern University
Boston, MA 02115
email: devaney@ece.neu.edu
Examples of inverse scattering problems
Importance of multiple scattering
Potential scattering theory
  Lippmann Schwinger integral equation
  Born series
  Born approximation
Born inversion in homogeneous media from plane wave scattering data
  far field data
  near field data—Filtered Back Propagation Algorithm
Born inversion in complex media
  Simple examples
Summary
Notes: <number>
This was a seminar talk presented in 2007 at the Woods Hole Oceanographic Institute in Woods Hole MA.

## Slide 2: Problems Addressed by Inverse Scattering and DT
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Geophysical
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
Medical
x
x
x
x
x
x
Industrial
Electromagnetic
Acoustic
Ultrasonic
Optical
x
x
x
x
x
x
Electromagnetic
Ultrasonic
Optical
Off-set VSP/ cross-well tomography
GPR surface imaging
induction imaging
Ultrasound tomography
optical microscopy
photon imaging
Ultrasound tomography
optical microscopy
induction imaging
Notes: <number>

## Slide 3
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Real Media
Geophysical
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
Medical
x
x
x
x
x
x
Industrial
Electromagnetic
Acoustic
Ultrasonic
Optical
x
x
x
x
x
x
Electromagnetic
Ultrasonic
Optical
Real experiments
are usually not performed
in homogeneous backgrounds
Notes: <number>

## Slide 4: Why Complex Media
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Simply nature of experiments
Employ to improve linear scattering models
Employ to improve inversion quality
Laser
polarizer
Spatial filter
lens
mirror
mirror
¼  plate
Beam splitter
CCD
sample
Beam splitter
1024X1024
10 bits/pixel
Pixel size=10 
Index matching fluid
Notes: <number>

## Slide 5: Improving the resolution
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Increases numerical aperture to unity
Multiple scattering in background generates evanescent waves
Oil immersion
Reflecting boundary
Measurement boundary
Glass slide
Cavity with conducting walls
Notes: <number>

## Slide 6: Designed as-Built as
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Designed as
Built as
“Built-as” = “Designed-as” + Perturbation
Notes: <number>

## Slide 7
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Historical survey
X-ray crystallography
Fourier based
Born/Rytov inversion
Computed
tomography
Diffraction tomography
General Linear
Inversion
Distorted Wave
Approximations
Needed for complex media
Notes: <number>

## Slide 8: Potential Scattering Theory in Homogeneous Media
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Lippmann Schwinger Equation
Object Function
Notes: <number>

## Slide 9: Born Series
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Linear mapping between incident and scattered field
Non-linear mapping between object profile and scattered field
Lippmann Schwinger Equation
Object function
Non-linear operator
Scattered field data
Notes: <number>

## Slide 10: Scattering Amplitude
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Boundary value of the spatial Fourier transform of the
induced source on a sphere of radius k (Ewald sphere)
Induced Source
Inverse Source Problem: Estimate induced source
Inverse Scattering Problem: Estimate object profile
Non-linear functional of Object function
Linear functional of 
Notes: <number>

## Slide 11: Non-uniqueness--Non-radiating Sources
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Inverse source problem does not possess a unique solution
Inverse scattering problem for a single experiment does not possess a unique solution
Use multiple experiments to exclude NR sources
Difficulty: Each induced source depends on the (unknown)
internal field--non-linear character of problem
Notes: <number>

## Slide 12: Mathematical Structure of Inverse Scattering
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Non-linear operator (Lippmann Schwinger equation)
Object function
Scattered field data
Use physics to derive model and linearize mapping
Linear operator (Born approximation)
Form normal equations for least squares solution
Wavefield Backpropagation
Compute pseudo-inverse
Filtered backpropagation algorithm
Successful procedure require coupling of mathematics
physics and signal processing
Data filtering
Backpropagation
Notes: <number>

## Slide 13: Born Approximation
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Boundary value of the spatial Fourier transform of the
object function on a set of spheres of radius k (Ewald spheres)
Generalized Projection-Slice Theorem in DT
Linear functional of O (LO=d)
Free space Born
Fourier based inversion
Notes: <number>

## Slide 14: Free Space Born Inverse Scattering
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Ewald Spheres
Forward scatter data
Back scatter data
z
Limiting Ewald Sphere
Ewald Sphere
k
2k
Notes: <number>

## Slide 15: Born Inversion for Fixed Frequency
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Inversion Algorithms:
Fourier interpolation (classical X-ray crystallography)
Filtered backpropagation (diffraction tomography)
Problem: How to generate inversion from Fourier data on spherical surfaces
Filtering of data followed by backpropagation: Filtered Backpropagation Algorithm
k
2k
Notes: <number>

## Slide 16: Near Field Data
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Weyl Expansion
Filtered Backpropagation
Algorithm
Notes: <number>

## Slide 17
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Potential Scattering Theory in Complex Media
Object Function
Lippmann Schwinger Equation
Background
Object of interest
Incident wave in background
Total wave
Notes: <number>

## Slide 18
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Born Series
Linear mapping between incident and scattered field
Non-linear mapping between object profile and scattered field
Lippmann Schwinger Equation
Object function
Non-linear operator
Scattered field data
Background Green function
Incident wave in background
Notes: <number>

## Slide 19
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Mathematical Structure of Inverse Scattering in Complex Media
Non-linear operator (Lippmann Schwinger equation)
Object function
Scattered field data
New Green function, incident wave and object function
Linear operator (Distorted wave Born approximation)
Form normal equations for least squares solution
Wavefield Backpropagation
Compute pseudo-inverse
Filtered backpropagation algorithm
Everything goes through for complex background media
Data filtering
Backpropagation
Notes: <number>

## Slide 20
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Distorted Wave Born Approximation
Generalized Projection-Slice Theorem , etc., GONE
Linear functional of O (LO=d)
Cannot use Fourier theory for inversion
Free space
Notes: <number>

## Slide 21: Inverse Theory
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
“Inverse scattering in inhomogeneous background media,” Inverse Problems, Part I, Vol. 19 pp.855-870, 2003, Part II, Vol. 20, pp 1307-1324, 2004
“Comparison of reconstruction algorithms for optical diffraction tomography,”
J. Opt. Soc. Am. A., Vol. 22, pp. 2338-2347, 2005
“Inverse scattering and diffraction tomography in cylindrical background media,”
J. Opt.Soc. Am. A., Vol. 23, pp. 1038-1047, 2006
“Inversion procedure for inverse scattering within the distorted wave Born approximation,”
Phys.Rev.Letts. Vol 51, pp. 237-241, 1983
General theory applies to arbitrary data sets
Notes: <number>

## Slide 22
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Inversion from Scattering Amplitude
Scattering amplitude determines the projection
of the object function onto the set of functions
Free space
Notes: <number>

## Slide 23
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
General Linear Inversion
Linear operator (Distorted wave Born approximation)
Filtered backpropagation algorithm
filtering
Backpropagation
Implemented using SVD
Notes: <number>

## Slide 24: Optical Scattering Example
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Notes: <number>

## Slide 25: Scattered Field Data
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Notes: <number>

## Slide 26: Reconstructions
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Notes: <number>

## Slide 27: Resolution Enhancement
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Born with no bottom
DWBA with Bottom
Born with Bottom
Notes: <number>

## Slide 28: Resolution Enhancement
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
PSF with no reflecting bottom
PSF with reflecting bottom
Notes: <number>

## Slide 29: Concluding Remarks
March 29
A.J. Devaney Woods Hole 07 lecture
<number>
Multiple scattering important for many reasons
Present in many experimentals
Can increase inversion resolution
Makes linear models more accurate
Linear based inversion algorithms require knowledge of background
Background well known in controlled experiments such as
3D optical microscopy and “designed as-built as”
Future work concentrated on obtaining optical scattering data
Notes: <number>