## Slide 1: Presentation Slides for Chapter 2 of Fundamentals of Atmospheric Modeling 2nd Edition
Mark Z. Jacobson
Department of Civil & Environmental Engineering
Stanford University
Stanford, CA 94305-4020
jacobson@stanford.edu
March 10, 2005

## Slide 2: Hydrostatic Air Pressure
Weight per unit area of air overhead a given altitude (2.1)
pa = air pressure (1 Pa=1 kg m-1 s-2 = 0.01 hPa=0.01 mb)
a = air density (kg/m3)
g = gravity (m/s2)
z = altitude (m)
Typical sea-level pressures:
  101,325 Pa =1013.25 hPa = 1013.25 mb = 1.01325 bar
  760 mm Hg = 760 torr
  29.9 in. Hg
  14.7 lb in-2
  10,300 kg m-2

## Slide 3: Pressure, Density, Gravity vs. Altitude
Figs. 2.1a-c
Altitude above sea level (km)
Altitude above sea level (km)
Altitude above sea level (km)

## Slide 4: Toricelli's Experiment With Mercury Barometer
1643 Evangelista Torricelli records the first sustained vacuum and demonstrates that air pressure changes daily.
Height of fluid = Air pressure / (fluid density x gravity)
1648 Blaise Pascal and brother-in-law Florin Périer demonstrate that air pressure decreases with increasing altitude at Puy-de-Dôme, France.
Edgar Fahs Smith Collection, University of Pennsylvania Library

## Slide 5: Current Composition of the Atmosphere
Table 2.1

## Slide 6: Carbon Dioxide Mixing Ratio
Carbon dioxide mixing ratio (ppmv)
Fig. 2.2

## Slide 7: Definitions of Temperature
From average thermal speed of an air molecule (m/s) (2.3,2.4)
kB = Boltzmann’s constant (kg m2 s-2 K-1)
T = Absolute temperature (K)
M = mass of a single air molecule (kg molec.-1)
From root-mean-square speed
From most probable speed

## Slide 8: Temperature-Example
Find thermal speeds at T=300 K, T=200K
Average speed
T=300 K --> 468.3 m/s (1685 km/hr)
T=200 K --> 382.4 m/s (1376 km/hr)
Root-mean-square speed
T=300 K --> 508.3 m/s
T=200 K --> 415.0 m/s
Most probable speed
T=300 K --> 415.0 m/s
T=200 K --> 338.9 m/s
Example 2.1

## Slide 9: Temperature Versus Altitude
Altitude (km)
Pressure (mb)
Fig. 2.4

## Slide 10: The Ozone Layer

## Slide 11: Stratospheric Ozone Chemistry
Natural Ozone Production
O2 + h --> O(1D) + O < 175 nm
O2 + h --> O + O 175 nm < < 245 nm
O(1D)+M-->O+M
O + O2 + M --> O3 + M
Natural Ozone Destruction
O3 + h --> O2 + O(1D) < 310 nm
O3 + h --> O2 + O > 310 nm
O3 + O --> O2 + O2
(2.9)-(2.15)

## Slide 12: Temperature Structure

## Slide 13: Zonally-Averaged Temperatures
January
July
Altitude (km)
Altitude (km)
Fig. 2.5a, b

## Slide 14: Boundary Layer
Daytime
Fig. 2.3a, b
Nighttime

## Slide 15: Processes Affecting Temperature
Specific heat (J kg-1 K-1)
Energy required to increase the temperature of 1 kg of a substance 1 K
= 1004.67 for dry air
= 4185.5 for liquid water
= 1360 for clay
= 827 for sand
Lower specific heat
--> substance heats up faster upon addition of energy
--> soil heats up during the day more than does water

## Slide 16: Processes Affecting Temperature Energy Transfer Processes
Conduction
  Transfer of energy from molecule to molecule
Convection
  Transfer of energy by the vertical mass movement of a fluid
Advection
  Horizontal propagation of the mean wind
Radiation
  Energy transferred in the form of electromagnetic waves

## Slide 17: Conduction
Important only near the ground
Conductive Heat Flux (W m-2)
Hc=- T / z (2.8)
= thermal conductivity (W m-1 K -1) = 0.0256 for dry air = 0.6 for liquid water
= 0.92 for clay = 0.298 for sand
 = change in temperature (oC)
z = change in altitude (m)
Near the ground
T / z = -12 K / 0.001 m--> Hc =307 W m-2
Free troposphere
T / z = -6.5 K / 1000 m--> Hc=0.00015 W m-2

## Slide 18: Thermal Conductivity
Dry air (2.5)
Water vapor (2.6)
Moist air (2.7)
n=number of moles

## Slide 19: Turbulence
Wind
Buoyancy: lifting of low-density (warm) air in bath of cold air
Wind shear: variation of wind speed with height or distance
Eddy: swirling motion of air due to wind shear
Turbulence: chaotic air motion from eddies of different sizes
Thermal turbulence: turbulence due to buoyancy
Mechanical turbulence: turbulence due to wind shear or convergence/divergence

## Slide 20: Convergence/Divergence
Convergence: horizontal net inflow of air into a region
L
H
Divergence: horizontal net outflow of air from a region

## Slide 21: Convection
Vertical air motion
Free convection: vertical air motion due to thermal turbulence
Forced convection: vertical air motion due to mechanical turbulence

## Slide 22: Equation of State
Boyle’s Law
    p~1/V at const. T
Charles’ Law
    V~T at const. p
Avogadro’s Law
    V~n at const. p, T
Ideal Gas Law
    pV=n R*T
Lifting of a parcel of air
(2.17)-(2.20)

## Slide 23: Jacques Charles (1746-1823)
June 4, 1783 Montgolfier brothers launch hot-air balloon in Annonay, France
August 27, 1783 Charles launches silk balloon filled with hydrogen in Paris
“The country people who saw it fall were frightened and attacked it with stones and knives so that it was much mangled” - Benjamin Franklin
November 21, 1783 Montgolfiers organize first manned hot-air balloon flight.
December 1, 1783 Charles in hydrogen-balloon flight.
“I had a pocket glass, with which I followed it until I lost sight, first of the men, then of the car, and when I last saw the balloon it appeared no bigger than a walnut” - Benjamin Franklin
Edgar Fahs Smith Collection, U. Penn. Lib.

## Slide 24: Equation of State
(2.20)
p = air pressure n = number of moles of gas
R* = gas const. (cm3 hPa mol-1 K-1) T = absolute temperature (K)
A = Avogadro’s num. (molec. mol-1) N = gas conc. (molec. cm-3)
kB = Boltzmann’s constant
(1.380658x10-19 cm3 hPa K-1)
Example 2.3 p = 1013 hPa
T = 288 K
--> N = 2.55 x 1019 molec. cm-3
p = 1 hPa
T = 270 K
--> N = 2.68 x 1016 molec. cm-3

## Slide 25: Dalton’s Law of Partial Pressure
Total air pressure equals the sum of the partial pressures of all the individual gases in the atmosphere
Total air pressure (hPa) (2.22)
Partial pressure of an individual gas (2.21)
Total air pressure equals partial pressures of dry plus moist air
Number concentration of total air

## Slide 26: Equation of State for Dry Air
Dry air mass density (g cm-3)
Dry air number concentration (molec. cm-3)
Dry air gas constant (Appendix A)
(2.23)
Partial pressure of dry air (hPa)

## Slide 27: Equation of State for Water Vapor
Water vapor mass density (g cm-3)
Water vapor number concentration (molec. cm-3)
Gas constant for water vapor
Partial pressure of water vapor (hPa) (2.25)

## Slide 28: Equation of State Examples
Example 2.4 pd = 1013 hPa
T = 288 K
R’ = 2.8704 m3 hPa kg-1 K-1
--> d = 1.23 kg m-3
Example 2.5 pv = 10 hPa
T = 298 K
Rv = 4.6189 m3 hPa kg-1 K-1
--> v = 0.00725 kg m-3

## Slide 29: Volume and Mass Mixing Ratio
Volume mixing ratio (molec. of gas per molecule of dry air)
Example 2.6 - ozone
 = 0.1 ppmv
mO3 = 48 g mol-1 --> O3 = 0.17 ppmm
T = 298 K
pd = 1013 hPa --> Nd = 2.55 x 1019 molec. cm-3
--> NO3 = 2.55 x 1012 molec. cm-3
--> pO3 = 0.000101 hPa
(2.29)
Mass mixing ratio (mass of gas per mass of dry air)
(2.30)

## Slide 30: Mass Mixing Ratio of Water Vapor
Equation of state for water vapor
Example 2.7
pv = 10 hPa
pd = 1013 hPa
--> v = 0.00622 kg kg-1 (0.622%)
Mass mixing ratio of water vapor (mass-vapor per mass dry air)
(2.27)
(2.31)

## Slide 31: Specific Humidity
= Moist-air mass mixing ratio (mass of vapor per mass moist air)
Example 2.8
pv = 10 hPa
pa = 1010 hPa
--> pd = 1000 hPa
--> qv = 0.00618 kg kg-1 (0.618%)
(2.32)

## Slide 32: Equation of State for Moist Air
Total air pressure (2.34)
Gather terms (2.35)
Total air pressure (2.36)
Gas constant for moist air (2.37)

## Slide 33: Equation of State for Moist Air
Molecular weight of total air less than that of dry air (2.39)
Gas constant for moist air (2.37)

## Slide 34: Virtual Temperature
Virtual temperature
Temperature of dry air having the same density as a sample of moist air at the same pressure as the moist air. (2.38)
Equation of state for moist air (2.36)

## Slide 35: Moist Air Example
Example 2.9 pd = 1013 hPa
pv = 10 hPa
T = 298 K
-->

## Slide 36: Hydrostatic Equation
Use equation to calculate pressure at a given altitude (2.41)
Upward pressure gradient balances downward gravity (2.40)
Vertical equation of motion in absence of vertical acceleration
Example 2.10
At sea level, pa,k+1 = 1013.25 hPa
a,k+1 = 1.225 kg m-3
gk+1 = 9.8072 m s-2
--> At 100 m, pa,100m = 1001.24 hPa
--> Air pressure decreases about 1 hPa per 10 m altitude

## Slide 37: Pressure Altimeter
Assume free-tropospheric lapse rate
Combine hydrostatic equation with equation of state (2.42)
Measures pressure at unknown altitude with aneroid barometer
Assume constant temperature decrease with altitude
Assume standard atmosphere surface pressure, temperature
pa,s = 1013.25 hPa Ts = 288 K

## Slide 38: Pressure Altimeter
Integrate from pa,s to pa (2.43)
Example 2.11
Pressure-altitmeter reading pa = 850 hPa
--> z = 1.45 km
Rearrange for altitude as function of pressure (2.44)

## Slide 39: Scale Height
Combine (2.45) with hydrostatic equation (2.46)
Density of air from equation of state (2.45)
Height above a references height at which pressure decreases to 1/e its value at the reference height
Mass of one air molecule
Scale height (2.47)

## Slide 40: Scale Height Equation
Integrate (2.46) at constant pressure (2.46)
Example 2.12
T = 298 K
--> H = 8.72 km
pa,ref = 1013.25 hPa
zref = 0 km
z = 1 km
--> pa = 903.5 hPa

## Slide 41: Energy
Kinetic energy
Energy within a body due to its motion
Potential energy
Energy that arises due to an object’s position rather than motion
Gravitational potential energy
Potential energy obtained when an object is raised vertically
Internal energy
Kinetic and/or potential energy of atoms or molecules within an object
Work
Energy added to a body by the application of a force that moves the body in the direction of the force
Radiation
Energy transferred by electromagnetic waves

## Slide 42: Latent Heat
Energy required to change a substance from one state to another
  Condensation, freezing, deposition
    release energy --> warm the air
  Evaporation, melting, sublimation
    absorb energy --> cool the air
Fig. 2.6

## Slide 43: Latent Heat of Evaporation
Change of latent heat of evaporation with temperature (2.49)
Example 2.13
T = 273.15 K
--> Le = 2.5x106 J kg-1
T = 373.15 K
--> Le = 2.3x106 J kg-1
Substitute constants (J kg-1) (2.54)
Integrate (2.53)

## Slide 44: Specific Heat of Liquid Water
Fig. 2.7
CW (J kg -1 K-1)

## Slide 45: Latent Heat of Melting
Change of latent heat of melting with temperature (2.50)
Example 2.14
T = 273.15 K
--> Lm = 3.34x105 J kg-1
T = 263.15 K
--> Lm = 3.12x105 J kg-1
Integrate and substitute constants (J kg-1) (2.55)

## Slide 46: Latent Heat of Sublimation
Change of latent heat of sublimation with temperature (2.50)
Integrate and substitute constants (J kg-1) (2.56)

## Slide 47: Clausius-Clapeyron Equation
Change of saturation vapor pressure with temperature (2.57)
Density of water vapor over particle surface (kg m-3)
Combine density with Clausius-Clapeyron equation (2.58)
Substitute latent heat of evaporation (2.59)

## Slide 48: Clausius-Clapeyron Equation
Integrate (2.60)
Substitute constants (2.61)
Example 2.15
T = 253.15 K
--> pv,s = 1.26 hPa
T = 298.15 K
--> pv,s = 31.6 hPa

## Slide 49: Saturation Vapor Pressure
Empirical parameterization (2.62)
Example 2.16
Tc = -20 oC (253.15 K)
--> pv,s = 1.26 hPa
Tc = 25 oC (298.15 K)
--> pv,s = 31.67 hPa
Vapor pressure (hPa)

## Slide 50: Saturation Vapor Pressure Over Ice
Change of saturation vapor pressure with temperature (2.63)
Substitute latent heat of sublimation and integrate (2.64)

## Slide 51: Saturation Vapor Pressure Over Ice
Empirical parameterization (2.65)
Example 2.17
Tc = -20 oC (253.15 K)
--> pv,s = 1.26 hPa
--> pv,I = 1.04 hPa
Vapor pressure (hPa)

## Slide 52: Condensation/Evaporation
Condensation when pv > pv,s
Fig. 2.9a,b
Evaporation when pv < pv,s

## Slide 53: Formation of Rain in Cold Clouds Ice Crystal (Bergeron) Process
pv,s over ice is less than that over liquid water
Water droplets evaporate, vapor flows to ice crystals
Ideal precipitation if 100,000 droplets per ice crystal
Vapor pressure (hPa)

## Slide 54: Relative Humidity
To increase relative humidity,
  increase partial pressure of water
  decrease temperature, which decreases pv,s
To decrease relative humidity,
  lower partial pressure of water
  increase temperature
Relative humidity (percent) (2.66)
Saturation mass mixing ratio (2.67)

## Slide 55: Relative Humidity Example
Vapor pressure (hPa)
Temperature (oC)
If T = 35°C and pv=20 hPa
--> find pv,s and fr
fr = 100% x 20 hPa / 56.2 hPa
= 35.6%
pv,s=56.2 hPa
pv=20 hPa
T=35°C

## Slide 56: Relative Humidity Example
Vapor pressure (hPa)
Temperature (oC)
If T = 24°C and fr =80%
--> at what temperature does fog appear upon cooling the air
pv = 80% x 29.6 hPa / 100%
= 23.7 hPa
pv,s=29.6 hPa
pv=23.7 hPa
T=24°C
T=20°C

## Slide 57: Dew Point
Dew point (K) (2.68)
Ambient water vapor mixing ratio
Temperature to which air must be cooled at constant water vapor partial pressure to be saturated over a liquid water surface
Example 2.17
pv = 12 hPa
--> TD = 282.8 K

## Slide 58: Dew Point Example
Vapor pressure (hPa)
Temperature (oC)
pv=20 hPa
T
TD
T = 30°C and
pv=20 hPa --> find TD

## Slide 59: Dew Point Example
Vapor pressure (hPa)
Temperature (oC)
TD = 16°C and fr =83%
--> find pv and pv,s
pv,s = pv x100% / fr
= 21.3hPa
pv,s=21.3 hPa
pv=17.7 hPa
TD

## Slide 60: Morning/Afternoon Temperature/Dew Point at Riverside, Calif.
Air pressure (hPa)
Air pressure (hPa)
Figs. 2.11a,b

## Slide 61: First Law of Thermodynamics
First law for atmosphere (2.69)
dQ* = change in energy (J) due to energy transfer
dU* = change in internal energy (J) of the air
dW* = work done by (+) or on (-) the air (J)
First law in terms of energy per unit mass (2.71)
Ma = mass of air (kg)

## Slide 62: Change in Work
Work done by air during expansion (dV>0) or contraction of air
Work done per unit mass of air (2.72)
Specific volume of air (2.73)

## Slide 63: Change in Internal Energy
Change in internal energy (2.74)
-->Specific heat moist air at const. volume (J kg-1 K-1) (2.76)
Change in energy required to change temperature of 1 kg air 1K at constant volume
Change in temperature of the gas multiplied by the energy required to change the temperature 1 K, without affecting the work done by or on the gas and without changing its volume.
Conservation of energy (2.75)

## Slide 64: Different Forms of First Law
First law of thermodynamics (2.77)
Equation of state for moist air
Differentiate equation of state (2.78)
Combine (2.77) and (2.78) and cp,m= cv,m +Rm (2.79)

## Slide 65: Different Forms of First Law
Specific heat of moist air at const. pressure (J kg -1 K-1) (2.80)
Energy required to increase the temperature of 1 kg of air 1K without affecting air pressure
Virtual temperature (2.38)
First law in terms of virtual temperature (2.82)

## Slide 66: Different Forms of First Law
Isobaric process (dpa=0) (2.83)
Isothermal process (dT=0) (2.84)
Isochoric process (da=0) (2.85)
Adiabatic process (dQ=0) (2.86)

## Slide 67: Adiabatic/Diabatic Processes
Parcel
of air
Atmosphere
Adiabatic process (dQ=0)
Process by which no energy is exchanged between a system (parcel of air) and its surroundings (atmosphere)
Diabatic processes (dQ>0 or <0)
Condensation/evaporation
Deposition/sublimation
Freezing melting
Radiative heating/cooling

## Slide 68: Dry adiabatic Expansion in Rising Air
1. Rising air expands
2. Expanding air cools
Rising air cools
Unsaturated air cools +9.8 K per 1 km rise in altitude
dry adiabatic lapse rate
d = +9.8 K/km
288 K
278.2 K
1 km

## Slide 69: Stability in Terms of Temperature
Compare parcel temperature with environmental temperature to determine stability
Unstable
Stable
Fig. 2.14

## Slide 70: Dry Adiabatic Lapse Rate
Rewrite first law for adiabatic process
Differentiate with respect to altitude (2.89)
--> Dry adiabatic lapse rate in terms of virtual temperature
Differentiate with respect to altitude (2.89)
--> Dry adiabatic lapse rate in terms of actual temperature
Rewrite first law for adiabatic process

## Slide 71: Potential Temperature
Substitute (2.91)
Integrate (2.92)
Exponential term (2.93)

## Slide 72: Potential Temperature
Potential temperature of moist air (p,m) (2.94)
Assume pa,0=1000 hPa --> T0=p,m
Potential temperature of dry air (p) (2.95)
Example 2.21
pd = 800 hPa
T = 270 K
--> p = 287.8 K

## Slide 73: Temperature vs. Potential Temperature
Air pressure (hPa)
Air pressure (hPa)
Figs. 2.11a, 2.12

## Slide 74: Potential Virtual Temperature
Potential virtual temperature (v) (2.96)
Found by converting all moisture in a parcel to dry air, then bringing the parcel to 1000 hPa and determining its temperature
Virtual potential temperature (p,v) (2.97)
Found by bringing a parcel to 1000 hPa, then converting all moisture to dry air and determining the parcel's temperature

## Slide 75: Stability in Terms of v
Altitude (km)
Fig. 2.15

## Slide 76: Stability Criteria For v
Potential virtual temperature (2.96)
Differentiate (2.101)
Take partial derivative with respect to height (2.102)
and substitute ∂pa /∂z=-a g and v=- ∂Tv /∂z

## Slide 77: Stability Criteria For v
Example 2.21
pa = 925 hPa
Tv = 290 K
v = +7 K km-1
--> v = 296.5 K
--> ∂v / ∂z = 3.07 K km-1 --> stable
Substitute R’/pa=1/aTv and d=g/cp,d (2.103)

## Slide 78: Brunt-Väisälä Frequency
Example 2.25 Tv = 288 K
v = +6.5 K km-1
--> bv = 0.0106 s-1 --> stable
--> period bv = 2π/ bv = 593 s
Rewrite (2.103) (2.105)
Brunt-Väisälä frequency (2.106)
Stability criteria (2.107)

## Slide 79: Isentropic Surfaces
Change in entropy
Isentropic surfaces occur when dS=0, which occurs when dQ=0 (adiabatic process), which occurs when v is constant with distance or height. Isentropic surfaces slant northward in the Northern Hemisphere.
Fig. 2.13