## Slide 1: Presentation Slides for Chapter 6 of Fundamentals of Atmospheric Modeling 2nd Edition
Mark Z. Jacobson
Department of Civil & Environmental Engineering
Stanford University
Stanford, CA 94305-4020
jacobson@stanford.edu
March 10, 2005

## Slide 2: ODEs and PDEs
Ordinary differential equation (ODE)
Equation with one independent variable
Partial differential equation (PDE)
Equation with more than one independent variable
Order
Highest derivative of an equation
Degree
Highest polynomial value of the highest derivative
Initial value problem
Conditions are known at one end of domain but not other
Boundary value problem
Conditions are known at both ends of domain

## Slide 3: ODEs and PDEs

## Slide 4: Operator Splitting Scheme
Fig. 6.1

## Slide 5: Operator Splitting
Operator-split advection-diffusion equations (6.1-6.3)
Operator-split external source/sink terms (6.4)

## Slide 6: Finite-Difference Approximation
Replacement of continuous differential operator (d) with discrete difference analog () written in terms of a finite number of values along a temporal or spatial direction.
Examples:

## Slide 7: Finite Difference Example
Fig. 6.2
First, replace continuous function ux with a finite number of values in the x direction.

## Slide 8: Finite Difference Approximation
Second, define differences of du at point xi
-->
-->
-->
backward difference
forward difference
central difference
Central difference approximation to tangent slope at xi (6.10)

## Slide 9: Finite-Difference Approximations
Fig. 6.3
Central (AC), forward (BC), and backward (AB) approximations to slope of tangent at point B

## Slide 10: Taylor Series Expansion
Taylor series expansion at point x+x (6.11)
Taylor series expansion at point x-x (6.12)

## Slide 11: Finite Difference Approximations
Sum the Taylor series expansions (6.13)
Rearrange (6.14)
Truncation error (neglect 2nd-order terms and higher) (6.15)
2nd-order central difference approx. of 2nd derivative (6.16)

## Slide 12: Finite Difference Approximations
Subtract the Taylor series expansions (6.17)
Rearrange (6.18)
Truncation error (6.19)
2nd-order central difference approx. of 1st derivative (6.20)

## Slide 13: Finite Difference Approximations
1st-order backward difference approx. of 1st derivative (6.22)
First two terms of Taylor series
1st-order forward difference approx. of 1st derivative (6.21)

## Slide 14: Differencing Time Derivative
Central, forward, backward difference approximations (6.23)

## Slide 15: Consistency, Convergence
Convergence of finite difference analog (6.6)
Consistency of finite difference analog (6.7)
Convergence of overall solution (6.8)

## Slide 16: Stability
Stability (6.9)
Conditionally stable: Stable for limited time-step range
Unconditionally stable: Stable for all time steps
Unconditionally unstable: Unstable for all time steps
An unconditionally unstable scheme cannot be convergent overall, but individual finite-difference analogs in an unstable scheme may converge and may be consistent.
In other words, consistency and convergence of individual analogs do not guarantee stability.
Stability is guaranteed if a scheme is convergent overall and its finite-difference analogs are convergent and consistent.

## Slide 17: Numerical Diffusion, Dispersion
Numerically diffusive scheme:
Peaks spread artificially across grid cells
Numerically dispersive (oscillatory) scheme:
Waves appear ahead of or behind peaks
Unbounded scheme:
Transported values artificially rise above the largest existing value or fall below the smallest existing value in domain.
Nonmonotonic scheme:
Gradients are not preserved during transport

## Slide 18: High Order Approximations
Finite difference approximation of ∂mN/∂xm
Order of derivative = m
Approximation expanded across q discrete nodes
Minimum number of nodes = m + 1
Maximum order of approximation = q - m
Example
Order of derivative: m = 1
Number of nodes: q = 5
--> Order of approximation: q - m = 4

## Slide 19: High Order Approximations
Grid spacing where q=5. Derivative is taken at x3. Fig. 6.4
Distance between two nodes
Approximation to the mth derivative across q nodes (6.24)

## Slide 20: High Order Approximations
Taylor series expansion for each node about point x* (6.25)
Combine (6.24) with (6.25) and gather terms (6.26)
Redefine (6.27)
Approximation to the mth derivative across q nodes (6.24)

## Slide 21: High Order Approximations
for n = 0…q - 1 (6.28)
Set Bn=0 for all n, except n = m
Set Bn=1 when n = m
Multiply (6.28) through by n! and set matrix (6.29)

## Slide 22: 2nd-Order Central Diff. Approx.
Find second-order central difference approx. to ∂N/∂x
Order of derivative: m = 1
Order of approximation: q - m = 2
--> Number of nodes: q = 3
Example
Set matrix (6.32)

## Slide 23: 2nd-Order Central Diff. Approx.
Apply the 's to (6.24)
Substitute 's to obtain central difference approx. Table 6.2 (c)
Solve matrix

## Slide 24: 1st-Order Backward Diff. Approx.
Find first-order backward difference approx. to ∂N/∂x
Order of derivative: m = 1
Order of approximation: q - m = 1
--> Number of nodes: q = 2
Example
Set matrix (6.30)

## Slide 25: 1st-Order Backward Diff. Approx.
Apply the 's to (6.24)
Substitute 's to obtain backward difference approx. Table 6.2 (a)
Solve matrix

## Slide 26: 2nd-Order Backward Diff. Approx.
Find second-order backward difference approx. to ∂N/∂x
Order of derivative: m = 1
Order of approximation: q - m = 2
--> Number of nodes: q = 3
Example
Set matrix (6.32)
Solve (Table 6.2d)

## Slide 27: Higher-Order Approximations
Third-order forward difference (m = 1, q = 4) Table 6.2 (g)
Fourth-order backward difference (m = 1, q = 5) Table 6.2 (i)
Third-order backward difference (m = 1, q = 4) Table 6.2 (f)
Fourth-order forward difference (m = 1, q = 5) Table 6.2 (j)

## Slide 28: Fourth-Order Approximations
Fourth-order backward diff. scheme (m = 1, q = 5) Table 6.2 (k)
Discretize around furthest cell
Fourth-order forward difference (m = 1, q = 5) Table 6.2 (l)

## Slide 29: Fourth-Order Central Diff. Approx.
Fourth-order central difference of ∂N/∂x (m = 1, q = 5) (6.33)
Table 6.2 (h)

## Slide 30: Fourth-Order Central Diff. Approx.
Fourth-order central difference of ∂2N/∂x2 (m = 2, q = 5)
Table 6.2 (n)

## Slide 31: Advection-Diffusion Eqn. Solutions
Species continuity equation in west-east direction (6.1)
CFL stability criterion for advection
Stability criterion for diffusion
Example:
xmin=5 km, |umax|=20 m/s --> h=250 s (Hydrostatic model)
xmin=5 km, |umax|=346 m/s --> h=14.5 s (Nonhydrostatic model)
Example:
zmin=20 m, Kmax=50 m2/s --> h=8 s (in the vertical)

## Slide 32: FTCS Solution
Forward in time, centered in space (FTCS) solution (6.35)
1st-order approximation in time
Unconditionally unstable for K=0, large K; otherwise conditionally stable

## Slide 33: Advection-Diffusion Eqn. Solutions
Implicit solution: 1st-order approximation in time (6.36)
Unconditionally stable for all u, K
Rearrange and write in tridiagonal matrix form (6.37)
(6.38)

## Slide 34: Advection-Diffusion Eqn. Solutions
Rearrange and write in tridiagonal matrix form (6.39)

## Slide 35: Tridiagonal Matrix Solution
Matrix decomposition: (6.40)
i = 2..I
i = 2..I
Matrix backsubstitution: (6.41)
i = I -1..1, -1

## Slide 36: Tridiagonal Matrix Solution
Matrix for solution for periodic boundary conditions (6.42)
Values at node I are adjacent to those at node 1

## Slide 37: Crank-Nicolson Scheme
Crank-Nicolson form (6.44)
c = Crank-Nicolson parameter
= 0.5 --> Crank-Nicolson solution (unconditionally stable all u, K)
2nd-order approximation in time
= 0. --> explicit (FTCS) solution
= 1 --> implicit solution

## Slide 38: Crank-Nicolson Scheme
Tridiagonal form (6.45)

## Slide 39: Leapfrog Scheme
2nd-order approximation in time (6.48)
Unconditionally unstable for all nonzero K; conditionally stable for linear equations when K=0; unstable for nonlinear equations

## Slide 40: Matsuno Scheme
Prediction step (6.49)
Correction step (6.49)
1st-order approximation in time
Conditionally stable for all u when K=0 or small; unconditionally unstable for large K

## Slide 41: Heun Scheme
2nd-order approximation in time (6.51)
Unconditionally unstable for all u when K=0 and K large; conditionally stable for other values of K
Prediction step same as first Matsuno step

## Slide 42: Adams-Bashforth Scheme
2nd-order approximation in time (6.52)
Unconditionally unstable for all u when K=0 and K large; conditionally stable for other values of K.

## Slide 43: Fourth-Order Runge-Kutta Scheme
Conditionally stable (6.53-5)

## Slide 44: Fourth-Order Runge-Kutta Scheme

## Slide 45: Convergence of Four Schemes
(Ketefian and Jacobson 2004b) Fig. 6.5
Error

## Slide 46: Fourth-Order in Space Solution
Central difference implicit solution (6.56)
Write in Crank-Nicolson and pentadiagonal form

## Slide 47: Variable Grid Spacing, Winds
Second-order central difference of advection term (6.57)
Solve matrix equation to obtain coefficients (6.58)

## Slide 48: Variable Grid Spacing, Winds
Solve matrix equation to obtain coefficients (6.59)

## Slide 49: Variable Grid Spacing, Diffusion
Expand analytical diffusion term (6.60)
Second-order central-difference approx. to terms (6.61)

## Slide 50: Variable Grid Spacing, Diffusion
Solve matrix equation to obtain coefficients (6.63)

## Slide 51: Variable Grid Spacing Solution
Crank-Nicolson form (c=0.5--> 2nd order time, space) (6.66)
Coefficients for diffusion term (6.65)
Write in tridiagonal form

## Slide 52: Two Dimensional Solution
Advection-diffusion equation in two dimensions (6.67)
Central difference approximation (6.68)
Solve

## Slide 53: Semi-Lagrangian Method
Concentration at current time t and existing node x (6.69)
Values at time x-uh, t-h interpolated from existing nodes

## Slide 54: Finite Element Method
Advection equation at node i (6.70)
Trial function = series expansion approximation to N (6.71)
= linear combination of basis functions
ej(x) = basis function
j = trial space

## Slide 55: Finite Element Method
Minimize residual (6.72)
Force its weighted average to zero over domain
Residual in advection equation (6.73)
ei(x) = weight function
ei(x) = ej(x) --> Galerkin method of weighted residuals
ei(x) ≠ ej(x) --> Petrov-Galerkin technique

## Slide 56: Finite Element Method
Substitute
into
to obtain (6.74)

## Slide 57: Finite Element Method
Take time difference of (6.74) over three nodes (6.75)

## Slide 58: Finite Element Method
Define basis functions as chapeau functions (6.76)
Solve each integral (6.77)

## Slide 59: Finite Element Method
Substitute integral solutions back into (6.75) (6.78)
Solve with tridiagonal matrix solution -->
4th-order in space, 2nd order in time

## Slide 60: Tests with a Finite Element Method
Preservation of a Gaussian peak during finite element transport after eight revolutions around a circular grid when uh/x= 0.02
Fig. 6.8
Concentration

## Slide 61: Tests with a Finite Element Method
Preservation of a Gaussian peak during finite element transport after eight revolutions around a circular grid when uh/x= 0.6
Fig. 6.8
Concentration

## Slide 62: Pseudospectral Method
Advection equation (6.87)
Represent solution with infinite Fourier series (6.88)
For t=0, integrate both sides of (6.88) from 0≤x≤L (6.89)

## Slide 63: Pseudospectral Method
Truncate infinite series (6.90)
Central time-difference approximation of (6.90) (6.91)
Partial derivative of (6.90) with respect to space (6.92)

## Slide 64: Pseudospectral Method
Substitute (6.91) and (6.92) into (6.87) (6.93)
Separate into K equations --> solve (6.94)

## Slide 65: Traits of a Good Advection Scheme
Final shape after six rotations around a 2-D grid. Walcek (2000)
Fig 6.9
Bounded
Nonoscillatory
Monotonic