## Slide 1: Presentation Slides for Chapter 13 of Fundamentals of Atmospheric Modeling 2nd Edition
Mark Z. Jacobson
Department of Civil & Environmental Engineering
Stanford University
Stanford, CA 94305-4020
jacobson@stanford.edu
March 29, 2005

## Slide 2: Sizes of Atmospheric Constituents
Table 13.1
Mode Diameter (m) Number (#/cm3)
Gas molecules 0.0005 2.45x1019
Aerosol particles
Small < 0.2 103-106
Medium 0.2-2 1-104
Large 1-100 <1 - 10
Hydrometeor particles
Fog drops 10-20 1-1000
Cloud drops 10-200 1-1000
Drizzle 200-1000 0.01-1
Raindrops 1000-8000 0.001-0.01

## Slide 3: Particles and Size Distributions
Particle
Agglomerations of molecules in the liquid and / or solid phases, suspended in air. Includes aerosol particles, fog drops, cloud drops, and raindrops
Example 13.1. - Idealized particle size distribution
10,000 particles of radius between 0.05 and 0.5 m
100 particles of radius between 0.5 and 5.0 m
10 particles of radius between 5.0 and 50 m
Example 13.2. Number of size bins needs to be limited
105 grid cells
100 size bins
100 components per size bin
--> 109 words = 8 gigabytes to store concentration

## Slide 4: Volume Ratio Size Structure
Volume of particles in one size bin (13.1)
(13.2)
Volume-diameter relationship for spherical particles

## Slide 5: Volume Ratio Size Structure
Fig. 13.1
Variation in particle sizes with the volume ratio size structure

## Slide 6: Volume Ratio Size Structure
Volume ratio of adjacent size bins (13.3)
Example 13.3.
d1 = 0.01 m
= 1000 m
NB = 30 size bins
---> Vrat = 3.29

## Slide 7: Volume Ratio Size Structure
Number of size bins (13.4)
Example 13.4.
d1 = 0.01 m
= 1000 m
Vrat = 4
---> NB = 26 size bins
Vrat = 2
---> NB = 51 size bins

## Slide 8: Volume Ratio Size Structure
Average volume in a size bin (13.5)
Relationship between high- and low-edge volume (13.6)
Substitute (13.6) into (13.5) --> low edge volume (13.7)

## Slide 9: Volume Ratio Size Structure
Volume width of a size bin (13.8)
Diameter width of a size bin (13.9)

## Slide 10: Particle Concentrations
Number concentration in a size bin (13.10)
Volume concentration in a size bin (13.12)
Number concentration in a size distribution (13.11)
Surface area concentration in a size bin (13.13)

## Slide 11: Particle Concentrations
Mass concentration in a size bin (13.14)
Volume-averaged mass density (g cm-3) of particle of size i (13.15)

## Slide 12: Particle Concentrations
Example 13.5
= 3.0 g m-3 for water
---> = 5.0 g m-3
---> = 4.09 x 10-12 cm3 cm-3
---> = 6.54 x 10-14 cm3
---> = 62.5 partic. cm-3
---> = 4.8 x 10-7 cm2 cm-3
= 2.0 g m-3 for sulfate
di = 0.5 m
= 1.0 g cm-3 for water
= 1.83 g cm-3 for sulfate
---> = 3 x 10-12 cm3 cm-3 for water
---> = 1.09 x 10-12 cm3 cm-3 for sulfate

## Slide 13: Lognormal Distribution
Bell-curve distribution on a log scale
Geometric mean diameter
50% of area under a lognormal curve lies below it
Geometric standard deviation
68% of area under a lognormal curve lies between +/-1 one geometric standard deviation around the mean diameter

## Slide 14: Lognormal Distribution
Fig. 13.2a
dv (m3 cm-3) / d log10 Dp
Describes particle concentration versus size

## Slide 15: Lognormal Distribution
Fig. 13.2b
The lognormal curve drawn on a linear scale
dv (m3 cm-3) / d log10 Dp

## Slide 16: Lognormal Parameters From Data
Low-pressure impactor -- 7 size cuts
0.05 - 0.075 m 0.5 - 1.0 m
0.075 - 0.12 m 1.0 - 2.0 m
0.12 - 0.26 m 2.0- 4.0 m
0.26 - 0.5 m

## Slide 17: Lognormal Parameters From Data
Natural log of geometric mean mass diameter (13.16)
Total mass concentration of particles (g m-3)

## Slide 18: Lognormal Parameters From Data
Natural log of geometric mean volume diameter (13.17)
Total volume concentration of particles (cm3 cm-3)

## Slide 19: Lognormal Parameters From Data
Natural log of geometric mean area diameter (13.18)
Total area concentration of particles (cm2 cm-3)

## Slide 20: Lognormal Parameters From Data
Natural log of geometric mean number diameter (13.19)
Total number concentration of particles (partic. cm-3)

## Slide 21: Lognormal Parameters From Data
Natural log of geometric standard deviation (13.20)

## Slide 22: Redistribute With Lognormal Parameter
Redistribute mass concentration in model size bin (13.21)
Redistribute volume concentration (13.22)
Redistribute area concentration (13.23)

## Slide 23: Redistribute With Lognormal Parameter
Redistribute number concentration (13.24)
Exact volume concentration in a mode (13.25)

## Slide 24: Lognormal Modes
Fig. 13.3
Number (partic. cm-3), area (cm2 cm-3), and volume (cm3 cm-3) concentrations distributed lognormally
dx / d log10 Dp (x=n,a,v)

## Slide 25: Lognormal Param. for Cont. Particles
Table 13.2
Nucleation Accumulation Coarse
Parameter Mode Mode Mode
g 1.7 2.03 2.15
NL (particles cm-3) 7.7x104 1.3x104 4.2
DN (m) 0.013 0.069 0.97
AL (m2 cm-3) 74 535 41
DA (m) 0.023 0.19 3.1
VL (m3 cm-3) 0.33 22 29
DV (m) 0.031 0.31 5.7

## Slide 26: Quadramodal Size Distribution
Size distribution at Claremont, California, on the morning of August 27, 1987
Fig. 13.4

## Slide 27: Marshall-Palmer Distribution
Raindrop number concentration between di and di+di (13.30)
din0 = value of ni at di = 0
n0 = 8.0 x 10-6 partic. cm-3 m-1
r = x Rm-1
R = rainfall rate (1-25 mm hr-1)
Total number concentration and liquid water content

## Slide 28: Marshall-Palmer Distribution
Example 13.6.
R = 5 mm hr-1
di = 1 mm
di+di = 2 mm
---> ni = 0.00043 partic. cm-3
---> nT = 0.0027 partic. cm-3
---> wL = 0.34 g m-3

## Slide 29: Modified Gamma Distribution
Number concentration (partic. cm-3) of drops in size bin i (13.30)

## Slide 30: Modified Gamma Distribution Parameters
Table 13.3

## Slide 31: Modified Gamma Distribution
Example 13.7.
Find number concentration of droplets between 14 and 16 m in radius at base of a stratus cloud
---> ri = 15 m
---> ri = 2 m
---> ni = 0.1506 partic. cm-3

## Slide 32: Full-Stationary Size Structure
Average single-particle volume in size bin (i) stays constant. When growth occurs, number concentration in bin (ni) changes.
Advantages:
    Covers wide range in diameter space with few bins
    Nucleation, emissions, transport treated realistically
Disadvantages:
    When growth occurs, information about the original composition of the growing particle is lost.
    Growth leads to numerical diffusion

## Slide 33: Full-Stationary Size Structure
Demonstration of a problem with the full-stationary size bin structure
Fig. 13.5

## Slide 34: Full-Moving Structure
Number concentration (ni) of particles in a size bin does not change during growth; instead, single-particle volume (i) changes.
Advantages:
    Core volume preserved during growth
    No numerical diffusion during growth
Disadvantages:
    Nucleation, emissions, transport treated unrealistically
    Reordering of size bins required for coagulation

## Slide 35: Full-Moving Structure
Preservation of aerosol material upon growth and evaporation in a moving structure
Fig. 13.6

## Slide 36: Full-Moving Structure
Particle size bin reordering for coagulation
Fig. 13.7

## Slide 37: Quasistationary Structure
Single-particle volumes change during growth like with full-moving structure but are fit back onto a full-stationary grid each time step.
Advantages and Disadvantages:
    Similar to those of full stationary structure
    Very numerically diffusive

## Slide 38: Quasistationary Structure
Partition volume of i between bins j and k while conserving particle number concentration (13.32)
and particle volume concentration (13.33)
Solution to this set of two equations and two unknowns (13.34)
After growth, particles in bin i have volume i’, which lies between volumes of bins j and k

## Slide 39: Moving-Center Structure
Single-particle volume (i) varies between i,hi and i,lo during growth, but i,hi, i,lo, and di remain fixed.
Advantages:
    Covers wide range in diameter space with few bins
    Little numerical diffusion during growth
    Nucleation, emission, transport treated realistically
Disadvantages:
    When growth occurs, information about the original composition of the growing particle is lost

## Slide 40: Moving-Center Structure
Comparison of moving-center, full-moving, and quasistationary size structures during water growth onto aerosol particles to form cloud drops.
Fig. 13.8
dv (m3 cm-3) / d log10 Dp