## Slide 1: Digital Design: A Systems Approach Lecture 3: Combinational Building Blocks

## Slide 2: Readings
L3: Chapters 8 & 9
L4: Chapter 10 & 11

## Slide 3: Review
Lecture 1 – Introduction to digital design:
Representations, noise margins, Boolean algebra, Verilog
Lecture 2 – Combinational logic design
Representations: English, Truth table, Minterm list, Equation, Cubes, K-map, Verilog
K-map minimization: prime implicants, distinguished 1s, coverage
Don’t cares
Product-of-sums
Verilog examples

## Slide 4: Today’s Lecture
Combinational building blocks – the idioms of digital design
  Decoder (binary to one-hot)
  Encoder (one-hot to binary)
  Muliplexer (select one of N)
  Arbiter (pick first of N)
  Comparators
  Read-only memories

## Slide 5: One-hot representation
Represent a set of N elements with N bits
Exactly one bit is set
Example – encode numbers 0-7
Binary One-hot
000 00000001
001 00000010
010 00000100
… …
110 01000000
111 10000000
What operations are simpler with one-hot representation? With binary?

## Slide 6: Decoder
A decoder converts symbols from one code to another.
A binary to one-hot decoder converts a symbol from binary code to a one-hot code.
  One-hot code: exactly one bit is high at any given time and each bit represents a symbol.
Binary input a to one-hot output b
b[i] = 1 if a = i
b = 1<<a
n
m
a
n
m
2
≤
b
Decoder

## Slide 7: Example of a Decoder
2 4 Decoder
a1 | a0 | b3 | b2 | b1 | b0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0

## Slide 8: Can build a large decoder from several small decoders
Example – build a 6  64 decoder from 3 2  4 decoders
Each 24 decodes 2 bits
  a[1:0]x[3:0], a[3:2]y[3:0], a[5:4]z[3:0]
AND one bit each of x, y, and z to generate an output
  b[i] = x[i[1:0]] & y[i[3:2]] & z[i[5:4]]
  Think of each bit of b as a position in a 3-D cube
a5 | a4 | z3 | z2 | z1 | z0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
a3 | a2 | y3 | y2 | y1 | y0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
a1 | a0 | x3 | x2 | x1 | x0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0

## Slide 9: 2-Stage decoders – the picture

## Slide 10: Advantage Of Dividing Large Decoder
6->64 decoder requires:
  64 6-input AND gates (384 inputs)
6->64 decoder using 2->4 decoders requires:
  12 2-input AND gates (24 inputs)
  64 3-input AND gates (192 inputs)
Faster, smaller, lower power

## Slide 11: Verilog implementation of a decoder
// a - binary input (n bits wide)
// b - one hot output (m bits wide)
module Dec(a, b) ;
parameter n=2 ;
parameter m=4 ;
input [n-1:0] a ;
output [m-1:0] b ;
wire [m-1:0] b = 1<<a ;
endmodule
n
m
a
n
m
2
≤
b
Decoder

## Slide 12: Synthesizes to
module dec ( in, out );
input [1:0] in;
output [3:0] out;
wire n2, n3;
NO210 U2 ( .A(n2), .B(n3), .Y(out[3]) );
NO210 U3 ( .A(in[0]), .B(n2), .Y(out[2]) );
NO210 U4 ( .A(in[1]), .B(n3), .Y(out[1]) );
NO210 U5 ( .A(in[0]), .B(in[1]), .Y(out[0]) );
IV110 U6 ( .A(in[1]), .Y(n2) );
IV110 U7 ( .A(in[0]), .Y(n3) );
endmodule

## Slide 13: Can implement an arbitrary logic function with a decoder Example – prime number function
module Primed(in, isprime) ;
input [2:0] in ;
output isprime ;
wire [7:0] b ;
// compute the output as the OR of the required minterms
wire isprime = b[1] | b[2] | b[3] | b[5] | b[7] ;
// instantiate a 3->8 decoder
Dec #(3,8) d(in,b) ;
endmodule
i
n
[
2
:
0
]
3
b
[
7
:
0
]
8
b
[
7
]
b
[
5
]
b
[
3
]
b
[
2
]
b
[
1
]
i
s
p
r
i
m
e
3:8

## Slide 14: Encoder
An encoder is an inverse of a decoder.
Encoder is a logic module that converts a one-hot input signal to a binary-encoded output signal.
Example: a 4 2 encoder.
a3 | a2 | a1 | a0 | b1 | b0
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1
b0 = a3  a1
b1 = a3  a2
a
3
a
1
a
2
a
0
b
1
b
0

## Slide 15: Designing A Large Encoder – 164 from 5 42s
a
[
1
5
:
1
2
]
4
a
[
1
1
:
8
]
4
a
[
7
:
4
]
4
a
[
3
:
0
]
4
2
2
2
2
b
[
1
:
0
]
b
[
3
:
2
]
2
2
Need an ‘any input true’ output on first rank of encoders
First rank encodes low bits, second rank encodes high bits
Repeat as needed
4:2
4:2
4:2
4:2
4:2
High bits
Low bits
One hot

## Slide 16
// encoder - fixed width - with summary output
module Enc42a(a, b, c) ;
input [3:0] a ;
output [1:0] b ;
output c ;
wire [1:0] b ;
wire c ; // c is true if any input is true
assign b[1] = a[3] | a[2] ;
assign b[0] = a[3] | a[1] ;
assign c = |a ;
endmodule
// factored encoder
module Enc164(a, b) ;
input [15:0] a ;
output[3:0] b ;
wire [3:0] b ;
wire [7:0] c ; // intermediate result of first stage
wire [3:0] d ; // if any set in group of four
// four LSB encoders each include 4-bits of the input
Enc42a e0(a[3:0], c[1:0],d[0]) ;
Enc42a e1(a[7:4], c[3:2],d[1]) ;
Enc42a e2(a[11:8], c[5:4],d[2]) ;
Enc42a e3(a[15:12],c[7:6],d[3]) ;
// MSB encoder takes summaries and gives msb of output
Enc42 e4(d[3:0], b[3:2]) ;
// two OR gates combine output of LSB encoders
assign b[1] = c[1]|c[3]|c[5]|c[7] ;
assign b[0] = c[0]|c[2]|c[4]|c[6] ;
endmodule

## Slide 17
# 0000000000000001 0000
# 0000000000000010 0001
# 0000000000000100 0010
# 0000000000001000 0011
# 0000000000010000 0100
# 0000000000100000 0101
# 0000000001000000 0110
# 0000000010000000 0111
# 0000000100000000 1000
# 0000001000000000 1001
# 0000010000000000 1010
# 0000100000000000 1011
# 0001000000000000 1100
# 0010000000000000 1101
# 0100000000000000 1110
# 1000000000000000 1111
# 0000000000000000 0000

## Slide 18: Multiplexer
Multiplexer:
  n k-bit inputs
  n-bit one-hot select signal s
  Multiplexers are commonly used as data selectors
Selects one of n k-bit inputs
s must be one-hot
b=a[i] if s [i] = 1

## Slide 19: Multiplexer Implementation

## Slide 20
// four input k-wide mux with one-hot select module Mux4(a3, a2, a1, a0, s, b) ;
parameter k = 1 ;
input [k-1:0] a0, a1, a2, a3 ; // inputs
input [3:0] s ; // one-hot select
output[k-1:0] b ;
wire [k-1:0] b = ({k{s[0]}} & a0) |
({k{s[1]}} & a1) |
({k{s[2]}} & a2) |
({k{s[3]}} & a3) ;
endmodule
Mux4 #(2) mx(2'd3, 2'd2, 2'd1, 2'd0, f, h) ;
f h
# 0001 00
# 0010 01
# 0100 10
# 1000 11

## Slide 21
module Mux3a(a2, a1, a0, s, b) ;
parameter k = 1 ;
input [k-1:0] a0, a1, a2 ; // inputs
input [2:0] s ; // one-hot select
output[k-1:0] b ;
reg [k-1:0] b ;
always @(*) begin
case(s)
3'b001: b = a0 ;
3'b010: b = a1 ;
3'b100: b = a2 ;
default: b = {k{1'bx}} ;
endcase
end
endmodule

## Slide 22: k-bit Binary-Select Multiplexer
Selects one of n k-bit inputs
s must be one-hot
b=a[i] if s [i] = 1

## Slide 23: k-bit Binary-Select Multiplexer (Cont)
a
0
k
b
a
n
-
1
k
k
s
m
n
a
b
Decoder

## Slide 24: Implementing k-bit Binary-Select Multiplexer Using Verilog
// 3:1 multiplexer with binary select (arbitrary width)
module Muxb3(a2, a1, a0, sb, b) ;
parameter k = 1 ;
input [k-1:0] a0, a1, a2 ; // inputs
input [1:0] sb ; // binary select
output[k-1:0] b ;
wire [2:0] s ;
Dec #(2,3) d(sb,s) ; // Decoder converts binary to one-hot
Mux3 #(k) m(a2, a1, a0, s, b) ; // multiplexer selects input
endmodule
a
0
k
b
a
n
-
1
k
k
s
m
n
a
b
Decoder

## Slide 25
module Primem(in, isprime) ;
input [2:0] in ;
output isprime ;
Muxb8 #(1) m(1, 0, 1, 0, 1, 1, 1, 0, in, isprime) ;
endmodule
s
b
3
i
s
p
r
i
m
e
0
1
1
1
0
1
0
1
0
1
s
b
[
2
]
1
s
b
2
i
s
p
r
i
m
e
Logic with Muxes
Muxb
Muxb

## Slide 26: Arbiter
n
n
Finds first “1” bit in r
g[i]=1 if r[i]=1 and r[j]=0 for j>i
Arbiter handles requests from multiple devices to use a single resource
Arbiter
r
g

## Slide 27: Logic Diagram Of One Bit Of An Arbiter

## Slide 28: Two Implementations Of A 4-Bit Arbiter
Using Bit-Cell
Using Look-Ahead

## Slide 29: Implementing Arbitrary Width Arbiter Using Verilog
// arbiter (arbitrary width)
module Arb(r, g) ;
parameter n=8 ;
input [n-1:0] r ;
output [n-1:0] g ;
wire [n-1:0] c ;
wire [n-1:0] g ;
assign c = {(~r[n-2:0] & c[n-2:0]),1'b1} ;
assign g = r & c ;
endmodule
Bit-slice coding style using
concatenation {a, b}
index ranges c[n-2:0]
c is 1s up to first 1 in r, then 0s

## Slide 30: Priority Encoder
Priority Encoder:
  n-bit input signal a
  m-bit output signal b
    b indicates the position of the first 1 bit in a
n
n
m
m
n
r
g
Arbiter
a
b
Encoder
m = log2n
a
b
Priority
Encoder

## Slide 31: Verilog for Priority Encoder
// priority encoder (arbitrary width)
module PriorityEncoder83(r, b) ;
input [7:0] r ;
output [2:0] b ;
wire [7:0] g ;
Arb #(8) a(r, g) ;
Enc83 e(g, b) ;
endmodule

## Slide 32: Functions built from decoders and other blocks
Example – find maximum of 256 small 4-bit numbers
  Decode each number 416 bits (256 times)
  OR these together w/16 256-bit ORs
    (each a 4-level tree of 4-input ORs)
  Use an Arbiter to get highest of 16
  Encode the 164
Need to see if this is more efficient than a tournament
Can this determine which input has the ‘winning’ number?
Decode
OR
Arbiter
Encode

## Slide 33: Equality Comparator
a
n
b
n
// equality comparator
module EqComp(a, b, eq) ;
parameter k=8;
input [k-1:0] a,b;
output eq ;
wire eq;
assign eq = (a==b) ;
endmodule
eq
Comparator

## Slide 34: Magnitude Comparator
a
n
b
n
// magnitude comparator
module MagComp(a, b, gt) ;
parameter k=8 ;
input [k-1:0] a, b ;
output gt ;
wire [k-1:0] eqi = a ~^ b ;
wire [k-1:0] gti = a & ~b ;
wire [k:0] gtb {((eqi[k-1:0] & gtb[k-1:0]) | gti[k-1:0]), 1’b0} ;
wire gt = gtb[k] ;
endmodule
Magnitude
Comparator
gt

## Slide 35: Another Implementation Of Magnitude Comparator

## Slide 36
// Behavioral Magnitude comparator
module MagComp_b(a, b, gt) ;
parameter k=8 ;
input [k-1:0] a, b ;
output gt ;
wire gt = (a > b) ;
endmodule

## Slide 37: Putting things together – Maximum unit
a
n
b
b
n
a
n
m
a
x
n
n
a > b
1
0
gt
Magnitude
Comparator
Mux

## Slide 38: Read-only memory (ROM)

## Slide 39
Conceptual block diagram

## Slide 40
2-D array implementation

## Slide 41: Summary
Assemble combinational circuits from pre-defined building blocks
  Decoder – converts codes (e.g., binary to one-hot)
  Encoder – encodes one-hot to binary
  Multiplexer – select an input (one-hot select)
  Arbiter – pick first true bit
  Comparators – equality and magnitude
  ROMs
Divide and conquer to build large units from small units
  Decoder, encoder, multiplexer
Logic with multiplexers or decoders
Bit-slice coding style

## Slide 42: Coming in L4
Numbers and Arithmetic