## Slide 1: University of California, Berkeley X-rays and Extreme Ultraviolet Radiation
AST210/EECS213
Fall 2019

## Slide 2: Laser High Harmonic Generation
David Attwood University of California, Berkeley

## Slide 3
Courtesy of Chang-Hee Nam, KAIST

## Slide 4: High Harmonic Generation (HHG)

## Slide 5: Relationships among electric field and intensity for a plane wave in vacuum

## Slide 6: HHG process
1. The high electric field of a coherent, fsec duration, intense laser pulse liberates an electron from the atom.
2. The electron is accelerated in the laser field, first away then in a return towards the parent ion.
3. The electron recombines with the atom (ion) in a very short interaction time, emitting high energy photons
4. The process simultaneously involves many electron-ion pairs, emitting photons in phase. There is an effect where N is the # of recombination events.
5. The spatial coherence of the incident laser field is effectively transferred to the emitted EUV/SXR radiation.
6. The process occurs symmetrically twice per cycle of the incident laser pulse, at well defined phases, resulting in odd-only harmonic emissions.

## Slide 7: Laser High Harmonic Generation (HHG)

## Slide 8: Early HHG Experiments
L’Huillier and Balcou (1993); (b) Macklin, Kmetec and Gordon (1993);
(c) Schulze et al. (1998); (d) Pfeiffer (2004).

## Slide 9: HHG spectra in pursuit of non-linear EUV processes
Ti:sapphire, 780 nm/45 nm bandwidth, 20mJ, 27 fsec, 1 KHz, 2Torr Ar, 6m focus to a 6 cm gas cell. Energy/pulse ~3 nJ in the 29th harmonic at 26.9 nm.
Relative spectral resolution ~ 1/2hN ~ 1/145, thus Δλ ~ 0.2 nm (~Instr. ltd.)
Courtesy of E. Champenois, UC Berkeley, AS&T.

## Slide 10: Step 1: Tunneling of a bound electron in an intense laser field
The tunneling probability is exponential in nature, involving the atoms ionization potential, Ip, and the laser electric field strength, E0. The governing non-dimensional parameter, known as the Keldysh parameter, , is given by
where Ip is the binding potential due the electric field of the
nucleus as felt by the bound electron (shielded by other electrons) and Up =
In the parameter range of interest to HHG « 1, the
laser electric field is comparable but smaller than the nuclear
binding field, and tunneling is the primary mechanism by which
an electron is removed from the atom. Tunneling time experiments are discussed by Camus et al., Phys. Rev. Lett. 119, 023201 (14July 2017).
e2E02/4mω2 is the ponderomotive potential. .

## Slide 11: Three Step HHG Model
Tunneling of a valence electron through the atom’s potential barrier in the presence of an intense laser field
Acceleration of the electron in the intense laser field, and return to the parent ion upon laser field reversal
Radiative recombination with the emission of a photon having an energy equal to the binding energy plus return kinetic energy

## Slide 12: Measured ionization of neon as a function of intensity
T. Auguste, P. Monot, L. A. Lompre, G. Mainfray and C. Manus, J. Phys. B: At. Mol. Opt. Phys. 25, 4181 (1992).
Nd:glass
1053nm
1 psec

## Slide 13: Calculated ionization rates for 4p orbitals of Kr
Calculated ionization rates of Kr,
λ= 800 nm, 40 fsec FWHM
Probability of neutral Kr atoms surviving by the end of the pulse
Courtesy of R Santra (CFEL/DESY), R. Dunford and L. Young (Argonne).

## Slide 14: Electron motion in an intense laser field (continued)
This equation can be solved numerically for the return time, or phase φr, as a function of the time of the electron’s emergence from the tunneling process (“birth”) at phase φ0. If the electron is born at the peak of the laser pulse, φ0 = 0, the electron undergoes a simple oscillation away from, and then back to the ion, with relatively high cycle-averaged kinetic energy, but unfortunately returning with zero kinetic energy and thus not contributing to HHG emission. High return kinetic energies occur for electrons released just after the peak of the pulse, with a maximum return energy at φ0 ≅ π/10, or 18°. For initial phases π/2 ≤ φ0 ≤ π there are no real solutions for φr; the electron never returns to the parent ion and thus cannot generate HHG photons.
.

## Slide 15: Electron motion in an intense laser field (continued)
The process repeats every half cycle, with identical excursion amplitudes and return kinetic energies, but travelling in the opposite direction due to the reversed direction of the laser electric field. A second maximum return energy occurs at an initial phase of 198°; 18° beyond the peak electric field at φ = π.
.

## Slide 16: High harmonics are generated twice per IR cycle
Electron return and EUV/SXR emission
delayed ≈ 2.4 fsec
Conditions: 800 nm (1.55 eV)
Neon, 5 x W/, h = 61
94.8 eV + 21.2 eV = 116 eV
Following Yanwei Liu (UCB/AS&T now at SLAC). Also see T. Pfeifer et al. Optics Lett. 31, 975 1 April 2006).

## Slide 17: University of California, Berkeley X-rays and Extreme Ultraviolet Radiation
AST210/EECS213
Fall 2019

## Slide 18: High Harmonic Generation (HHG)

## Slide 19: HHG spectra in pursuit of non-linear EUV processes
Ti:sapphire, 780 nm/45 nm bandwidth, 20mJ, 27 fsec, 1 KHz, 2Torr Ar, 6m focus to a 6 cm gas cell. Energy/pulse ~3 nJ in the 29th harmonic at 26.9 nm.
Relative spectral resolution ~ 1/2hN ~ 1/145, thus Δλ ~ 0.2 nm (~Instr. ltd.)
Courtesy of E. Champenois, UC Berkeley, AS&T.

## Slide 20: Three Step HHG Model
Tunneling of a valence electron through the atom’s potential barrier in the presence of an intense laser field
Acceleration of the electron in the intense laser field, and return to the parent ion upon laser field reversal
Radiative recombination with the emission of a photon having an energy equal to the binding energy plus return kinetic energy

## Slide 21: Tunneling ionization at moderately high laser intensity
Modest laser intensity provides single electrons for the HHG process without excessive ionization. Excessive plasma electrons would increase the IR wave phase velocity and thus affect phase matching across the interaction region. The plasma electron density profile would also cause refractive divergence of the IR laser pulse.
Augst, Strickland et al., PRL 63, 2212 (13Nov1989)

## Slide 22: Calculated ionization probabilities for a neon atom as a function of laser intensity
Courtesy of C. Ott, MP/INF, Heidelberg
Slowly varying envelope
approximation (svea).
Ne = 21.5645 eV.

## Slide 23: Calculated ionization probabilities for He, Ne, Ar, Kr and Xe atoms as a function of laser intensity
Courtesy of C. Ott, MP/INF, Heidelberg
Slowly varying envelope
approximation (svea).

## Slide 24: Step 2: Electron acceleration in the laser field. Time of birth affects return energy

## Slide 25: Electron motion in an intense laser field
The equation of motion for a bound electron just released in a laser field of E = E0cosωt
a(t) = d2x/dt2 = -[eE0 /m] cosωt
Integrating twice
v(t) = -[eE0/mω] sinωt + v0
x(t) = [eE0/mω2] cosωt + vot + x0
where the constants of integration are set by the initial conditions v(t0) = 0 and x(t0) = 0 at the electron’s time of birth, ωt0 =φ0, within the phase φ=ωt of the laser electric field
ma = -e[E + v x B]

## Slide 26: Electron motion in an intense laser field: applying boundary conditions at t = 0
With the initial conditions v(t0) = 0 and x(t0) = 0
v0= [eE0/mω] sinφ0
and x0 = - [eE0/mω2](cosφ0 + φ0sinφ0)
The time dependent velocity of the electron is then
v(t) = -[eE0/mω](sinφ – sinφ0) (correct Eq.7.6a in book)
and the time dependent amplitude of the electron (away from the parent atom ion) is
x(t) = [eE0/mω2][(cosφ – cosφ0) + (φ-φ0)sinφ0] (Eq.7.6b)
At return to the parent ion x(tr) = 0, thus the bracket on the rhs must be zero
φrsinφ0 + cosφr = φ0sinφ0 + cosφ0
where the return phase is φr = ωtr.

## Slide 27: An HHG example
For atoms irradiated at 5 x 1014 W/cm2, with a wavelength of 800 nm, the peak electric field, E0, is 6.14 x 108 V/cm. From the equations in a previous slide, one has
x(t) = (1.947 nm)[(cosφ – cosφ0) + (φ – φ0)sinφ0)]
The electron return energies are
Ee (tr) = ½ mv2(tr) = [e2E02/2mω2] (sinφr – sinφ0)2
Ee (tr) = (59.76 eV) (sinφr – sinφ0)2
The trajectory for φ0 = 0° (birth at the peak of the laser electric field) corresponds to a simple electron oscillation with excursion distances of nearly 4 nm from the parent ion, gaining a maximum kinetic energy of near 60 eV, but returning to the ion with zero kinetic energy. For neon atoms the ionization energy is 21.6 eV.

## Slide 28: An HHG example (continued)
Of particular interest is φ0 ≅ π/10 = 18°, just beyond the peak of the pulse. This corresponds to the maximum return energy, in this example 94.8 eV at φ0 = 18° and φr = 252°. Note that the cycle averaged kinetic energy is 29.9 eV, demonstrating the 3.17 factor. The highest photon energy emitted equals the return kinetic energy, 94.8 eV, plus the neon ionization energy, 21.6 eV, for a total of 116 eV.

## Slide 29: Electron trajectories for a variety of emission times within the phase of the incident electric field
For an initial phase φ = o, the electron gains significant kinetic energy but returns
with none, simply oscillating with a 4 nm excursion amplitude.
For initial phases of φ = π/10, or 18˚, maximum return kinetic energy is achieved,
94.8 eV in this case. The same is true for 198˚, but travel is in the opposite direction.
Electrons emerging from the tunneling process at initial phases extending from π/2
to π, just before the peak of the pulse, never return to the parent ion.
Note that the same return electron kinetic energy occurs twice in (b). These correspond
to what is known as the short and long return paths.

## Slide 30: Selected trajectories with a limited bandpass
Note that for φ = 18˚ the return kinetic energy is maximum at 94.8 eV. Adding the ionization energy, the total available energy for photon emission is 116 eV, assuming there is a radiative recombination with the parent ion. A 5% spectral bandpas around that peak is emitted within 200 asec.

## Slide 31: Step 3: Radiative recombination with the parent ion
The probability of electron recombination is relatively small due to several factors. Tunneling has an efficiency of order 10-1 to 10-2. Half the photoelectrons never return to their parent ion. The return probability is dominated by the long excursion path (several nm) away from the ion and the divergent nature of the emitted electron wave packet, known as "quantum diffusion". The photoemission process is properly described as diffraction of an electron wave packet as it emerges from the transversely confined, Ångstrom scale atom. Thus the electron moves away from the ion as a divergent electron wave packet, with a lateral divergence of order 5Å/fsec (Corkum and Krausz, Nature Physics, 2007). Thus a 2 fsec return time yields a 1 nm electron wavepacket spread across the 0.1 nm “wide” parent ion, further reducing the probability of recombination. Experimental values or overall HHG conversion efficiency are seen in the next slide.

## Slide 32: Conversion efficiency of high harmonic generation
Coutesy of M. Schnürer, Techn.Univ.Vienna, and F.Krausz, Max Planck Instit. for Quant. Optics and Ludwig Maxmillians Univ., Garching

## Slide 33: Scaling of efficiency, η, with laser wavelength
There is great interest in extending HHG into the soft x-ray region with photon energies of several hundred eV. The photon energies which can be achieve are given by Eqs.(7.1 & 7.2):
where λ is the driving laser wavelength. The choice of longer wavelengths correctly predicts higher achievable harmonic energies.
However, the HHG efficiency is also dependent on the driving laser wavelength, λ, through the liberated electron excursion distance and probability of radiative recombination. The excursion distance of the free electron is given by Eq.(7.6b): x(t) = [eE0/mω2][(cosφ – cosφ0) + (φ-φ0)sinφ0]
thus the excursion distance, x ~ λ2 , and the round trip distance, 2x ~ 2λ2.
The probability of recombination, an important multiplicative factor in the overall conversion efficiency,η, scales inversely with return area. Thus η includes a factor ~ 1/(2x)2 ~ 1/4 λ4 . Quantum mechanical calculations of electron wavefront propagation indicate an efficiency more like λ-5 or λ-6, a high price to pay for increased harmonic generation into the soft x-ray region, indicating that one does not want to push longer wavelengths too far.

## Slide 34: The generation of high harmonics
IR pulse trains generate high harmonics through constructive and destructive interference
There are twice the number of EUV/SXR pulses as IR cycles
The IR pulses each generate a spectral continuum, which by constructive and destructive interference form harmonics.
Symmetric pulse structure (in time) implies only odd harmonics
Even harmonics appear only if the temporal symmetry is broken
Fourier analysis of the EUV wave train reveals high harmonics, limited in photon energy, and thus harmonic number, by Eq.(7.1)
To first order the harmonic pulses contain hN cycles and are of similar duration as the driving IR laser pulse
With a single IR pulse there is no interference, thus no harmonics form, leaving a broad EUV spectral content and thus permitting the formation of very short (asec) pulses

## Slide 35: Spatial and Temporal Coherence of High harmonic Radiation
Spatial coherence is impressed by that of the driving laser field. The condition dFWHM ∙ 2θFWHM ≅ λ/2 implies that the harmonics radiate into narrower angles than the incident IR.
The spatial coherence of HHG radiation is largely imprinted from that of the fully coherent IR laser wavefront. This is true despite the randomness of atoms in the gas. Every participating atom across a uniform IR wave front emits radiation in the forward direction with a fixed phase relative to the laser electric field, and thus to each other. As a consequence of this impressed spatial coherence, the electric fields for a given harmonic add constructively in the forward direction, generating very intense radiation, proportional to the square of the number of participating atoms in the interaction region. Random atomic positions do affect radiation emitted in other directions. Random phases in other directions generally cancel so that there is essentially no HHG at other angles.

## Slide 36: Spectral bandwidth and duration of mid-spectral range HHG pulses
For mid-spectral range harmonics one expects a relative spectral bandwidth λ/Δλ ≈ hN, the product of the # of IR cycles, N, and the harmonic #, h. Relative spectral bandwidths can be of order 0.1%.

## Slide 37: High harmonic spectral bandwidth
We consider two models of HHG spectral bandwidth, a rectangular wavepacket, and a Gaussian wavepacket having an intensity FWHM equal to half the duration of the rectangular wavepacket. In each case we take the Fourier transform of the electric field, E(t), to obtain E(ω), then square to obtain I(ω).
For experimental HHG spectra see, for example, M. Gaarde et al.,PRA 59,1367 (Feb1999),Fig.5; and P. Saliѐres et al. Science 292, 902 (4May2001).

## Slide 38: Spectrally narrow high harmonics
Courtesy of Thomas Pfeifer,
Max Planck Institute for Nuclear Physics, Heidelberg
λ/Δλ 11.6 nm
(h =69, 107 eV)
lcoh= 0.5(11.6 nm)(500) = 2.9 μm
HHG relative spectral bandwidths of order hN/2 are discussed in the literature, e.g., M.B. Gaare et al, Phys. Rev. A 59, 1367 (February 1999); P. Salieres et al., Science 292, 902 (4 May 2001).

## Slide 39: Temporal coherence of HHG
Temporal coherence is set by the harmonic bandwidth lcoh = λ2/2Δλ
For mid-range harmonics one expects a relative spectral bandwidth λ/Δλ ≈ hN, the product of the # of IR cycles, N, and the harmonic #, h.
Relative spectral bandwidths can be of order 0.1%.
For attosecond duration pulses a broad spectral bandwidth is required
thus a 100 asec pulse requires an 18 eV bandwidth
ΔEFWHM ∙ΔτFWHM ≥ 1.825 eV∙fsec

## Slide 40: HHG approaches full spatial coherence
Courtesy R. Bartels, Univ. Colorado, Boulder, now at CSU, Fort Collins,
and Y. Liu, UC Berkeley, now at SLAC.
λ = 760 nm, 25 fsec.
Ar @ 29 torr,
I = 2 x W/
h= 21
= 34 eV (36 nm)
4 x ph/pulse @ 5 kHz
50 μm diameter pinholes @ 142 μm to 779 μm separations; 20 to 240 second exposure times (laser pulses).

## Slide 41: New topic: Generating asec HHG pulses

## Slide 42: Generating asec HHG pulses
For attosecond duration pulses a broad spectral bandwidth is required; not a spectrally sharp harmonic. A 100 asec pulse requires an 18 eV bandwidth
ΔEFWHM ∙ΔτFWHM ≥ 1.825 eV∙fsec

## Slide 43: Generating attosecond duration pulses
… by stabilizing the carrier phase envelope (CPE) and spectrally accepting only the highest intensity
Following F. Krausz and M. Ivanov, “Attosecond Physics” Rev. Mod. Phys. 81, 163(Jan.– March 2009)

## Slide 44: Spectral features reveal pulse structure
Courtesy of F. Krausz and M. Ivanov,
“Attosecond Physics”, Rev. Mod. Phys.
81, 163 (Jan-March 2009)

## Slide 45: Conventional streak camera
R. Kienberger and F. Krausz,
“Attosecond Metrology Comes of Age”,
Physica Scripta, T110, 32 (2004)

## Slide 46: IR laser field/ photoelectron streak camera
Attosecond Streak Recorder (ATR):
R. Kienberger and F. Krausz,
“Attosecond Metrology Comes of Age”,
Physica Scripta, T110, 32 (2004)

## Slide 47: Generating single 80 asec EUV pulses
Courtesy of E. Goulielmakis and F. Krausz, MPI Quantum Optics, Garching; A. Aquila, AST/UCB
720 nm, 3.3 fsec FWHM
80 eV, 0.5 nJ, η
E. Goulielmakis et al.,
“Single-cycle Nonlinear Optics”, Science 320, 1614 (20June2008)

## Slide 48: Attosecond transient absorption spectroscopy: A pump - probe study of electron dynamics in atomic Kr ions
E. Goulielmakis, Z.-H. Loh, A. Wirth, R. Santra, N. Rohringer, V. S. Yakovlev, S. Zherebtsov, T.Pfeifer, A. M. Azzeer, M. F. Kling, S. R. Leone and F. Krausz, “Real-Time Observation of Valence Electron Motion”, Nature 466, 739 (5 August 2010).

## Slide 49: Attosecond streak spectrometry of delayed photoemission in solid state tungsten
A. L. Cavalieri, N. Müller, Th. Uphues, V. S. Yakovlev, A. Baltuška, B. Horvath, B. Schmidt, L. Blümel, R. Holzwarth, S. Hendel, M. Drescher, U. Kleineberg, P. M. Echenique, R. Kienberger, F. Krausz and U. Heinzmann, “Attosecond Spectroscopy in Condensed Matter”, Nature 449, 1029 (25 October 2007).
Photoelectrons liberated from core states are observed to be delayed ~100 asec with respect to electrons from the conduction band in crystalline tungsten (W).

## Slide 50: Broad bandwidth multilayer mirrors can support asec duration pulses
Multilayer mirrors depend on constructive interference from individual interfaces
Higher reflectivity needs more layers
Bandwidth gets narrower with more layers
Attosecond pulse requires a broad spectral bandwidth, thus a limited number of layers.
Multilayer mirror with N<10 layers required for a 200 as pulse (@13nm)
∆E(eV) ∙∆τ(fs) ≥ 1.8 fs∙eV (FWHM)
Courtesy of Yanwei Liu, UCB/AS&T, now SLAC

## Slide 51: What limits IR to EUV harmonic conversion efficiency?
Return efficiency
Effective IR path in the gas

## Slide 52: Laser High Harmonic Generation (HHG); What limits the interaction lengh?

## Slide 53: Differing EUV and IR phase velocities limit HHG generation
The dephasing distance is that where the downstream generated EUV is out of phase by π with the earlier upstream generated HHG. Propagation beyond that is counterproductive, limiting further increases to the harmonic pulse energy. The limiting dephasing distance is given by
(0.5λ/h)/Δn
where Δn is the difference between the IR and EUV refractive indices, and where are IR refractive decrements due to the electrons and atoms, and is the EUV refractive decrement due to atoms. Ion contributions are included with the atoms.
nhh error in book, p.297

## Slide 54: The dephasing limit for effective HHG is due to differences in the IR and harmonic phase velocities
The distance travelled in the medium by the IR and high harmonic waves is (λ is in vacuum)
Lir = Nλir = Nλ/nir
Lh = (hN + ½)λh = (hN + ½)λ/hnh
The dephasing distance is reached when = . Solving for N, the number of IR cycles for dephasing is
so that the dephasing distance can be written as

## Slide 55: Refractive index decrements are small for these IR and high harmonic waves
For the driving IR wave, with contributions from low density neutral atoms (and ions) and from free electrons, the refractive index is nir = 1 + αa – αe , where αa and αe « 1 and positive.
For the higher photon energy harmonic wave, with contributions from the atoms (and ions), the refractive index is nh = 1– αδ ,where αδ « 1 and positive.
Note that the free electron contribution to the harmonic wave is negligible as it scales as 1/ω2.
The factor in the denominator of Lπ is then

## Slide 56: The dephasing distance for HHG
where to a degree of accuracy and and nh 1. .
Eq.(7.13)

## Slide 57: A note on the refractive index of an electromagnetic wave in a plasma
For Ne at 300 Torr & 1.1% ionization, ne = 1.17 x 1017 e/cc. For 800 nm light, nc= 1.73 x 1021 e/cc.
Thus ne / nc << 1 for the IR pulse.The sq root approx. is good. The plasma electrons exert a strong refractive effect, speeding the IR wave and introducing a negative lensing.
Because of its 1/ω2 dependence, the plasma contribution to the higher frequency EUV refractive index is negligible.
where

## Slide 58: An example of dephasing distance
To determine the value of Lπ various refractive index decrements are required. As an example we choose neon at a pressure of 300 Torr (~0.4 atm), illuminated by an 800 nm wavelength, 40 fsec pulse at an intensity of 3.2 x 1014 W/cm2.
For the IR at 800 nm:
Free electrons. With1.1 x 1019 neon atoms/cm3 and 1.1% ionization, the free electron density is 1.2 x 1017e/cm3. With a critical electron density of 1.7 x 1021 e/cm3, the IR refractive index decrement due to free electrons, αe = ne/2nc, is 3.4 x 10-5.
Atoms contribution to the IR refractive index. See the text.
αa = (6.70 x 10-5)(300/760) =2.6 x 10-5 at 800 nm wavelength.

## Slide 59: Dephasing example; high harmonic refractive index
High harmonic refractive indices. Neon at 3.2 x 1014 W/cm2, highest harmonic is h= 53, 15.1 nm, 82.2 eV.
For the atoms at EUV wavelengths, Appendix C, Table C.1, f10 = 5.20 and f20 = 6.12,
αδ = δ = nareλ2f10/2π = 5.6 x 10-6.
For the ions. Far from the K- and L-absorption edges the ions contribute essentially the same to refractive index as the atoms and thus are included with the atoms.
For the free electrons. Due to the 1/ω2 dependence the free electron (plasma) contribution to EUV refractive index is negligible.

## Slide 60: Dephasing distance, continued
The net refractive index increment, Δn, describing the difference in phase velocity for the IR and high harmonic wavefronts for this example is
Δn = αe – αa - αδ = 3.4 x 10-5 – 2.6 x 10-5 – 0.56 x 10-5
Δn = 1.7 x 10-6
Then = 7.5 nm/1.7x10-6 , or Lπ = 4.4 mm
This is a typical value quoted for such experiments (Ne, 300 Torr, 3x1014 W/cm2). At this distance the IR wave has incrementally phase advanced to such a degree that it is generating h = 53 harmonics π out of phase (destructively) with the same harmonic generated at the entrance to the laser-atom interaction region. A small increase in the neon pressure would improve this. But…

## Slide 61: The common description of non-linear harmonic phase matching is in terms of wavenumber mismatch, Δk
Wavenumber matching in non-linear optics is proportional to sinc2(Δk۰L). Maximum conversion efficiency occurs when Δk۰L = 0. The conversion efficiency goes to zero when Δk۰L = π, thus
Showing again t causes a phase mismatch which limits harmonic conversion efficiency.
Δk = kh – hk = Δke + Δka

## Slide 62: The effect of absorption
For neon at 800nm/53 = 15.1 nm, f20 = 6.12, which determines the imaginary component of the refractive index, which according to Eqs.(3.22 & 3.23) gives β = 6.63 x 10-6, and an absorption length labs= λ/4πβ = 0.18 mm.
Thus for this example the harmonic must propagate through several absorption lengths, greatly limiting the achievable conversion efficiency.
Unfortunately this photon energy, 82 eV, is near the peak absorption for neon, as seen in the f20 curve in Table C.1. Clearly tradeoffs need to be explored amongst gas, gas pressure, laser intensity and pulse duration when planning an HHG experiment.
Class project?

## Slide 63: Absorption limited HHG conversion below 100 eV
Coutesy of M. Schnürer, Techn.Univ.Vienna, and F.Krausz, Max Planck Instit. for Quant. Optics and Ludwig Maxmillians Univ., Garching

## Slide 64: Further description of plasma refractive index
8.4.7 Transverse Electromagnetic Waves in a Uniform Plasma
In the interaction region the electron density is maximum on axis (highest IR intensity), thus the refractive index is less than one and the IR wave travels faster than c. Off axis the electron density is lower, the refractive index is close to unity, and the IR travels slower, closer to the speed of light in vacuum, c. Thus the IR is running faster than the EUV, leading to a phase mismatch between the early and later created EUV, as well as divergence of the IR wave. The plasma has much less effect on the EUV due to the dependence. (8.114b)
(8.114b)
(8.112b)

## Slide 65: Transverse electromagnetic waves in a plasma
J = -en0v

## Slide 66: Transverse electromagnetic waves in a plasma (continued)

## Slide 67: Dispersion diagram for transverse electromagnetic waves in a plasma

## Slide 68: Refractive index of an electromagnetic wave in a plasma
for ne/nc «1, where nc = 1.11 x 1021e/cm3 / λ2[µm]